## Slide 1: Time-of-Arrival of hits and resolution better than 2 ms
note: 01/22/2024
G.W.Deptuch

## Slide 2: Typical Charge Processing Chain
ALPIDE/ALICE-ITS3 uses significantly simpler processing chain due to:
power, and
Si area restrictions

## Slide 3: Measurements of Time of Arrival (1)
indeterministic term, depending on noise contained in signal
term depending on slope of rising/falling edge, resulting in delayed crossing of discriminator threshold – can be compensated knowing amplitude
term depending on slope of rising/falling edge (giving overdrive of discriminator’s input), resulting in delayed response of discriminator – can be compensated knowing relation threshold-amplitude
resolution of ToA measurement given by size of “time bucket”, aka “integration time”

## Slide 4: Measurements of Time of Arrival (2)
Leading Edge with amplitude correction
METHOD 1
t0 is real time of occurrence;
t1 or t2 are times when pulses cross threshold f(amp);
knowing amplitude (typically measured peak or Time-over-Threshold of pulse), correction can be made bringing t1 and t2 effectively to t0;
Measurement of amplitude not always available / feasible as additional functionality consumes power and needs more silicon area, vide binary readout.

## Slide 5: Measurements of Time of Arrival (2)
Constant Fraction Discrimination
METHOD 2
t0 is real time of occurrence;
tCFD is time when constructed pulse crosses “zero” f(amp);
new signal is constructed that is fraction of original signal and is compared against delayed original signal;
time at which two signals are equal is amplitude independent;
Effectively bipolar pulse is virtually created that is tested against zero-crossing;
measuring zero-crossing requires additional arming discriminator, to avoid “noise hits”;
Amplitude is not measured directly, but system is complex and there is no ideal delay in Integrated Circuit, vide matched transmission line would be required.

## Slide 6: Is LE of CFD used in ALICE-ITS3?
NO
there is no fast clock distributed to pixels with which LE or CFD threshold crossing could be compared
How hits are registered in ALICe-ITS3 sensors:
matrices of pixels are main parts of RSUs (3 matrices read through one readout channel / RSU);
Analog Front-Ends with Discriminators are continuously active in every pixel;
periodic global to all RSUs signal (STROBE) samples discriminators’ outputs and if pixel possesses activated discriminator is brought to “virtual list” of pixels to be readout;
readout is static (aka snapshotted or framed), i.e., all pixels from “virtual list” are readout and new strobe create new “virtual list”;
frames are caused by STROBE, resulting in grouping all hits in STROBE-period-wide buckets.
C2, D4, I9 new hits,
K3, I5 weak hits, E8, G3 strong hits.
B10, C9, C10, K2 new hits,
C2, E8 weak hits,
D4, I9 strong hits.
strong hit = discriminator ON >TSTROBE
weak hit = discriminator ON <TSTROBE
TSTROBE

## Slide 7: Four cases (1)
CASE 1
CASE 2
Difference in registration of “strong” and weak hits:
discriminator outputs swing rail-to-rail;
duration of discriminator pulse corresponds to magnitude of charge liberated and collected by in-pixel diode;
“weak hit” and “strong hit” may be simultaneous (originate from the same bunch collision), t0, but may be registered at different frames, as “weak hit” may not be yet developed to be snapshot by STROBE that takes “strong hit” ð ToA uncertainty ð complication in analysis;
“strong hit” may have its discriminator active, for one, two or more frames give by pulsed strobe ð multiple readouts of same “strong hit”;
How many times single hit is consecutively read out can becomes equivalent of LE with amplitude correction ToA method; (probability of two distinct hits in pixel following one another is practically non-existent!)
Running STROBE at, e.g. 2 ms or less, ma result in much better timing resolution than resulting from simple time frame duration!

## Slide 8: Summary of Time Walk Issue
Impact of TW on assigning hits to frames
(RO mode agnostic):
“weak hits” and “strong hits” can be mistimed (assigned to consecutive frames-buckets) – having time difference of X ms);
combination of TW (1-3 ms) and “sampling” of time with STROBE (@ 2 ms) results in potential spread of hits from one even between up to three time-frames.

## Slide 9: Four cases (2)
CASE 3
CASE 4
Simplified view:
particle leaves trace in all layers;
“strengths “ of hits even in all layers;
impacts not occurring in coincidence with TROBE pulses;
etc.
STROBEs in all layers are aligned
STROBEs are shifted in phase
Running STROBES with shifted phases per layer, may increase granularity of timing for reconstructed tracks significantly below 1 ms.

## Slide 10: ALPIDE/ALICE-ITS3 FE-DISC-STROBE
assuming 50 mm thick active sensor layer Ü1 MIP produces MPV= 4 ke-/h+ and e- are collected;
charge sharing in corner impact splits collected charge to MPV= 4 × 1 k e-;
taking Landau distribution max – min signals Î (0.3 MPV, 3 MPV) Ü ~(0.3 ke-, 15 ke-)
measured with LGAD 50 mm thick
transient FE + disc
TW and ToT vs. signal
ALICE – ITS3 plenary

## Slide 11: ALPIDE/ALICE-ITS3 Pixel Circuit
ALPIDE is voltage amplifier using independent bias of charge collecting diode, i.e. self-bias;
following every hit, amplifier finds new operating point;
ALPIDE operation manual (ALICE-ITS3 modified circuit)
STROBE selects 1 out of 3 latches to store state of discriminator; then MEMSEL allow reading out 1 out of 3 latches through priority encoder

## Slide 12: Event Rates at ePIC SVT
L. Gonella ePIC SVT collaboration meeting, ANL, 9-13 January 2024
Expected event rates are very;
Additional (repeated) readouts of the same hits should not clog data links but will allow information on signal amplitudes for improved timing
20.8×22.8 mm2 pixel size @ 2 ms STROBE rate

## Slide 13: Summary
Timing resolution is result of:
  Time-Walk “weak” vs. “strong” hits ð 2¸3 ms spread;
  Granularity of snapshotted readout (STROBE) ð create “integration frames”, may spill hit to one or one after frame;
  Out of time hits, incl. fake fractional signals “weak hits”;
Reading duplicated hits (initially planned to reject due to zero-probability of consecutive real hits in the same pixel) may help increasing timing precision by providing amplitude information;
Spreading phase of SROBE signal in SVT layers may allow further increase ToA resolution to significantly below 1 ms;
Requires confirmation of hit registering functionality implemented in ALICE-ITS3 pixel (is it the same as in ALPIDE?);

## Slide 14
Reserve
Slides