## Slide 1: Stave thermal FEA and CFD preliminary studies
Stephanie Yang (Oxford)
ePIC_UK F2F meeting at Birmingham University
15th March 2024

## Slide 2: Introduction
Sensitivity studies have been carried out:
  Steady state thermal FEA to look at temperature profile of a single 5RSU sensor at various convection film coefficient values, and
  To establish a simplified model.
  CFD 2D with porous media to test out the input porous parameters.
  CFD 2D: extend the model to 2 sensors, then 4 sensors, finally full length (8 sensors) model.
  CFD 3D models: to observe their flow patterns.
The assumptions made for the input parameters and boundary conditions were rough estimates as we only look at the effect of cases and their implications.

## Slide 3: Sensor FEA geometry
https://indico.cern.ch/event/1341665/contributions/5648416/attachments/2751648/4789826/20231114-WP2-Report.pdf
114.330
Sensor geometry modelled using shell elements.
LEC
RSU
Source of Power density input
Case1 input
Case2 input

## Slide 4: Material properties for thermal FEA

## Slide 5: Power density input
Boundary conditions:
Initial reference T = 22C;
HTC values from 5 to 1000 W/m2C are applied to the whole sensor surface
Steady state thermal analysis
LEC
Pixel matrix
Data backbone
Readout periphery
Biasing

## Slide 6: Thermal FEA case 1 (sensor detail model)
As expected, the higher the HTC values the smaller the dT.
Chart: Convection film coefficient [W/m2 oC]
| 100 | 175 | 240 | 300 | 350 | 450 | 550 | 650 | 700 | 1000
 | 37.704 | 25.664 | 20.504 | 17.428 | 15.545 | 12.849 | 10.995 | 9.631 | 9.075 | 6.764

## Slide 7: Thermal FEA case 2 (sensor simplified model benchmark)
This result shows that the simplified sensor model with equivalent power input gives the same result as the detail sensor model.
For further CFD studies, the simplified model and power input will be used.

## Slide 8: Thermal FEA case 3 (sensor simplified model with K9 foams)
LEC = 7910W/m2
RSU = 440W/m2
K9 foams
Additional HTC also applied to the end faces of the K9 foams
Delt T =7.5 oC
The additional surface area from K9 foams helps to remove the heat.
HTC area applied to inside faces of K9 foam and sensor area
sensor
K9
K9
Delt T =12 oC
Delta T = 7.53 oC

## Slide 9: CFD 2D model (without K9 foams)
air
Inlet v=5/s
2D geometry and CFD input:
Reference:
https://indico.cern.ch/event/1228295/contributions/5390941/
Fluid material: air
Adiabatic wall boundary conditions applied to the rest of the model

## Slide 10: CFD 2D fluid model without K9 foams
Linear pressure drop along the length
Heat from sensor region has been moved to the right side by the flow, and spread along the channel length.
Global delta T=59K
Delta T btw inlet and outlet =3K

## Slide 11: CFD 2D fluid porous model
Key porous input parameters:
(derived from CERN experiment data on K9 foam: https://indico.cern.ch/event/1228295/contributions/5390941/):
air
K9 foam
Adiabatic wall boundary applied to the rest of the model

## Slide 12: CFD 2D model with K9 foams
Global delta T=9.4K
Delta T btw inlet and outlet =3K
Region between two foams

## Slide 13: Effect of the pressure on heat transport
Without foams
with foams
Pressure remains high between the two foam blocks although pressure difference is the same as the case without foams. However, high pressure means higher inertia of the air there by making the heat transport more efficient.

## Slide 14
Inlet v=5m/s
3 off K9 foams
LEC (red) = 7910W/m2
RSU (yellow) = 440W/m2
Outlet
2D Two sensor length model
Element size: 0.5mm
Delta T btw inlet and outlet = 7K
Top line
bottom line
Middle line

## Slide 15: 2D Four sensor length model
Delta T btw inlet and outlet = 14K

## Slide 16: Full length model (8 sensors)
* Temperature profile at top, middle and bottom of the channel
Delta T btw inlet and outlet = 27K
Middle line
bottom line
top line

## Slide 17: CFD 3D model without foam
Fluid material: Air
Nozzle dia: 2.5mm
The flow pattern without foam

## Slide 18: CFD 3D model with foams
K9 foams
Inlet v = 5m/s
LEC area
RSU area

## Slide 19: Final remark
All work in progress..
Ancillary chip power is not included in the study, it will be added to the later studies.
Simplified sensor model shows the same result as the detail model.
Existence of K9 foams helps remove the heat efficiently.
Continue working on CFD 3D modelling

## Slide 20: Back up

## Slide 21: Porous media coefficients
Chart: K9 foam CERN Test
| 0 | 1 | 3 | 5 | 7 | 9
K9 CERN Test | 0 | 50 | 170 | 345 | 530 | 775
[1].https://indico.cern.ch/event/1228295/contributions/5390941/
[2]. ANSYS Help, section 7.2.8.11
Porous media coefficients for K9 foam are derived from the experimental pressure and velocity data
This yield to the following equation:
Δp = 4.6275ν2+ 44.252ν
where Δp is the pressure drop and ν is the velocity
With ρ =1.225kg/m3, and = porous media thickness which is 6mm, inertial resistance factor C2 is calculated. Likewise, 4.251= ; the μ=1.7894E-5 for air, the viscos inertial resistance factor 1/α is calculated.

## Slide 22: CFD 2D model mesh
CFD 2D model mesh setting:
Element size = 0.1mm
Inflation total thickness =0.1mm, 4 layers
LEC
RSU
Axillary chip
K9

## Slide 23: CFD 3D model with foams (double channel)
K9
RVC foam
K9