## Slide 1
Progress on Cylindrical µRWELL Prototypes
Detector R&D Day Meeting
K. Gnanvo, P. Iapozutto, M. Hohlmann, A. kiselev
on behalf of eRD108 Consortium
March 25, 2024

## Slide 2
eRD108: R&D on Cylindrical µRWELL Prototypes
µRWELL-R/O
Cathode foil
Inner clamp
Outer clamp
Main frame
40 cm
26 cm
Motivation & Design features
Prototype consists of 2 half-cylinder chambers with different readout structures
            2D capaSh proto: µRWELL/readout foil with U-V capacitive-sharing readout
2D zigzag proto: µRWELL/readout foil with U-V :zigzag” readout structure
Goal is to study the performance of the two readout options for cylindrical µRWELL
Design of mechanical structure completed with a set of 3 of frames per chamber
1.35 mm
pitch
1.35 mm
pitch
U-strip
V-strip
U-V zigzag readout concept (BNL)
U-V capacitive-sharing readout (JLab)
Exploded 3D view

## Slide 3
eRD108: Cylindrical µRWELL prototypes
Cyl. µRWELL prototype at Fermilab test beam setup, June 2023
Downstream
GEM Trackers
Cyl. µRWELL
We were unable to operate and take data at the Fermilab 2023 test beam
      Fermilab shut down that week for safety concerns at the lab
      Dents appeared on the Al cathode when HV is applied  HV instabilities
      2024: Fix the dents issues and test the prototype at in Hall D JLab in Fall 2024
Two half cyl. µRWELL prototypes
capaShRO proto
zigzagRO Proto
Florida Tech: Mechanical structure and detector assembly
Curved µRWELL /RO composite PCB
BNL & JLab: Design of uRWELL+ RO composites

## Slide 4
HV stability issues & design upgrade
On the original prototype, the cathode foil shows some dents during operation at Fermilab test bean
HV stabilities issues  Detector could not hold HV
Decide to reinforce the cathode by gluing the Al-Mylar foil on a honeycomb structure
Cathode could sustain up to 1 kV after reinforcement
µRWELL voltage (V)
µRWELL leakage current (nA)
Indicative of dust or
Al flakes on the µRWELL
HV and gas leakage tests
Gas pressure drops from 20 mbar to 10 mbar in two min.
µRWELL: small leakage current up to 350V
above 350V, sudden current increase observed
  New drift cathode reinforced with honeycomb structure
Initial prototype with Al-mylar foil drift cathode
Dents on cathode foil

## Slide 5
eRD108 completed: But - Next steps & plans
Open half cyl. detector and clean µRWELL foil (tacky roller)
Replace Al-Mylar by Cu-Kapton drift cathode
Assemble second detector half cylinder
Implement a larger O-ring to improve gas tightness (right)
Assemble second detector half cylinder
(Re)-assemble both half cyl. prototypes and perform cosmic test at FIT (possibly at JLab)
Conduct an opportunistic beam test at in Hall D JLAB (Fall 2024 run)
Frame with larger O-ring

## Slide 6
Back up

## Slide 7: Gas Testing & HV continued
Bench Top testing of with high voltage and gas pressure was successfully conducted.
-Second gas pressure trial included the µRWELL foil, the detector held gas pressure in the same range for 2 minutes. The leaking is possibly due to the O-ring being too small we plan to use a larger O-ring and modified groove.
-The first trial included a 300 µm mockup foil instead of the µRWELL foil and the structure successfully held gas pressure with a measured drop from 20 to 10 mbar overpressure in 60 minutes.

## Slide 8
Backup Slides