## Slide 1: ePIC/EIC Project Detector R&D Day
25 March 2024
Fernando Barbosa
eRD109 (ASICs/FEEs) – Progress & Outlook

## Slide 2: Outline
eRD109 - ASIC & Electronics R&D Initiatives
    Proposals
    Progress Reports:
        ASIC & Discrete Developments
        3rd Party ASIC Evaluations
        Services
        High Precision Timing
Outlook

## Slide 3: eRD109 Proposals
 | File | Authors | Sub-Detector | Sensor Type | Readout Solution
A | eRD109_pECAL_readout_prototype_FINAL | G. Visser (IU), et al. | Calorimeter | SiPM | Discrete, COTS
B | eRD109CalorimeterReadout | N. Novitzky (ORNL), et al. | Calorimeter | SiPM | H2GCROC
C | eRD109-alcor | M. Ruspa (INFN), et al. | dRICH | SiPM | ALCOR
D | ACLGAD_ASIC_Electronics_FY23 | Z. Ye (UIC), et al. | Central, Far-Forward | AC-LGAD | EICROC, FCFD
E | eRD109_SALSA_proposal_vfinal1 | D. Neyret (CEA), et al. | Micromegas, GEM, MicroRWell | MPGD | SALSA
FY23, FY24 sensibly similar

## Slide 4: eRD109 Progress
eRD109 Addresses EIC ASIC and Electronics R&D needs.
FY23 Proposals - DAC R&D Review August 2022
FY24 Proposals - DAC R&D Review August 2023
FY25 Proposals - DAC R&D Review August 2024 (submissions due by 1 July 2024)
  ASIC & Discrete – Nominal Solutions: (FY23, FY24)
    Discrete/COTS – Calorimeters, SiPMs, 12-14 bit
    CALOROC (H2GCROC revision for EIC) – Calorimeters, SiPMs, 10 bit *
    EICROC - AC-LGAD, pixel *
    FCFD – AC-LGAD, strip**
    ALCOR – dRICH, SiPM, 1 p.e.
    SALSA – MPGD.
  3rd Party Evaluations: (FY23)
      HPSoC, HDSoC – NALU
      ASROC – Anadyne
      FAST – INFN
  Services: Barrel TOF Low-Mass Service Hybrid, (FY23, FY24)
  High Precision Timing, (FY24)
* Considerable commitment of resources by OMEGA/IN2P3.
** Considerable synergy with FNAL

## Slide 5: eRD109 – Discrete/COTS/ASIC (IU)
Calorimeters, SiPMs
Adapter PCB
FEB PCBs
32 ch Waveform Digitizer
12/14-bit TI ADC3422
Microsemi MPF100T-FCVG484E Polarfire (radiation hard FPGA)
CERN DC/DC converter bPOL48V or LTC3601
Cabling, Power, Cooling, Packaging.
  Specs almost complete
  Devices selected
  Signal chain designed, including “dynamic range compressor”.
  Defining FEB-RDO interface
  DC/DC converters under tests, radiation tests coming.
  PCB design is proceeding
  SiPM frontend prototyped
  SiPM Bias distribution established.
Design, Fab: FY23 –FY24
Tests + Beam: FY24 – FY25
Engineering Article: FY25
Production: FY25 – FY26

## Slide 6: eRD109 – H2GCROC Studies (ORNL)
Develop a readout solution for the calorimeters with SiPMs by:
  Employing existing H2GCROCv3 ASIC
  Developing PCBs for full readout chain
  Developing cabling infrastructure
Adapter PCBs
FEB PCBs
RDO PCBs
  H2GCROC & PCBs from OMEGA with KCU105 FPGA eval kit – tests are on-going to validate streaming readout operation algorithms
  Tests confirm data from CMS operation
  Cabling studies for interconnects from FEBs to RDOs are progressing (SAMTEC connectors)
  LFHCAL, Barrel HCAL and ECAL, Bwd HCAL, – SiPM summing studies and FEB design in progress
  Preparing for LFHCAL tests at CERN, 520 ch, May 2024
  Input to OMEGA team for design of CALOROC.
Calorimeters, SiPMs

## Slide 7: eRD109 – CALOROC (OMEGA/IN2P3)
Calorimeters, SiPMs
No Change
Modify trig, mem, CLK dist.
1D, 64 ch.
130 nm CMOS
Charge (ADC+TOT) + Time (TOA)
Cdin: 500 pF - 2.5 nF
Dynamic Range: 1-320 pC
Timing: 100-120 ps
ADC: 10b
39.4 MHz operation from BX 98.5 MHz
Links: 1260.8 Mbps @ 39.4 MHz, multiple
Power: 5-10 mW/ch
Radiation tolerant
Preliminary specifications
Design in progress:
    Analog part complete
    Streaming Readout logic
    Memory
    Clock pre-scaling & distribution.
A (64 ch H2GCROC); B (32 ch, HKROC).
Design Backend: FY23 - FY24
CALOROC1 (A,B): FY24 – FY25
CALOROC: FY26
H2GCROC (not Streaming Readout)

## Slide 8: eRD109 – EICROC (OMEGA/IN2P3/IJCLab/CEA-IRFU/AGH)
AC-LGAD pixel
One pixel – EICROC0
Sensor
2D, 1024 ch (32x32), pixel readout
130 nm CMOS
Preamp, Discriminator, TOA, ADC
Cdin: 1-5 pF
Dynamic Range: 1-50 fC
Timing: 15-20 ps
ADC: 8b
39.4 MHz operation from BX 98.5 MHz
Links: 1260.8 Mbps @ 39.4 MHz, multiple
Power: <1 mW/ch
Packaging: Bump+Wire bonds
Radiation tolerant
EICROC0 (4x4) characterization in progress
  Hybridization with AC-LGAD
EICROC0A – re-spin for lower power
  Simulations in progress
EICROC1 – Layout started
  4x16 or 8x16 or 4x32 or 8x32
  Adding more test capabilities
  Follows EICROC0
EICROC2 – 32x32
EICROC0: FY23
EICROC0A: FY23 – FY24
EICROC1: FY24 – FY25
EICROC2: FY26
4x4 500 um pixels
Bump
Wire
Wire
Plus backend of CALOROC

## Slide 9: eRD109 – FCFD (FNAL)
AC-LGAD strip
2D, 128 ch (8x16), strip readout
65 nm CMOS
Constant Fraction Discriminator
Plus TDC, ADC, interfaces
Cdin: <15 pF
Dynamic Range: 5-40 fC
Timing: 10-30 ps
Links: ~Gbps, multiple
FCFDv0 – characterized with charge injection, laser, beta, and proton beam
  <25 ps @ >6 fC timing.
FCFDv1 – 6 channel designed and submitted (August 2023).
  Received February 2024
  Tests in progress
    All channels functioning with CFDs operational
    Full characterization on-going
Recently met with FNAL designers:
  Adding interfaces
  Designed ETROC for CMS
  Scheduling FCFD work at FNAL
  Proposal soon.
FCFDv1: FY23
FCFDv2: FY24 – FY25
FCFDv3: FY26 – FY27

## Slide 10: eRD109 – ALCOR (INFN)
dRICH – SiPMs, 1 p.e.
2D, 64 ch (8x8), pixel readout
110 nm CMOS
Dual polarity, RCG Amplification, conditioning, inhibit , digitization.
Modes of operation: single-photon tagging or time and charge.
Triggerless and triggered operation.
25 ps TDCs, TOA+TOT, 5 MHz input
4 or 8x 640 Mbps LVDS links.
SPI configuration.
Originally developed by INFN for DARKSIDE.
  ALCOR v2: 32-pixel (8x4), characterization in progress
    Preparing for beam tests (1280 ch), Spring 2024
  ALCOR v3: 64-pixel (8x8), complete design with BGA package – Fall 2024
  Design of RDO prototype – June 2024
    SiPM Bias distribution, LV established; VTRX+ Optical transceiver.
  Readout of RDO - tests – Fall 2024
  Irradiation tests – ALCOR v2 (July 2024), RDO (December 2024)
ALCOR v3: FY25
ALCOR v4: FY26

## Slide 11: eRD109 – SALSA (CEA-Saclay, U. São Paulo)
MPGD
64 Ch
65 nm CMOS
Peaking time: 50 – 500 ns
Inputs: Cdin = 50 - 200 pF; Dual polarity
Gain Ranges: 0 – 50 to 0 – 5000 fC
Rates: <100 kHz/ch
ADC: 12 bits, 5 – 50 MSPS.
Extensive data processing capabilities.
Triggerless and triggered operation.
Power: 15 mW/Ch
Several 1 Gbps links
I2C configuration
Radiation hard, 2T field
SALSA0_analog and SALSA0_digital blocks submitted and received June 2023.
SALSA0_analog
  performance in agreement with simulation. Some stability issues traced to PCB residues.
SALSA0_digital
  Sampling rate too low
  Lower dynamic range, offset issue
  Lower power
    Not resolved
DSP IP block design in progress.
PLL block
  Proper functioning verified
  Jitter tests in progress
SALSA1
  4 ch: FE+ADC+PLL+I2C+test blocks
  Improved pole-zero
  Two ADC versions
  TSMC submission April 2024
SALSA0 (IP blocks): FY23 (June 2023)
SALSA1: FY23 – FY24
SALSA2: FY24 – FY25
SALSAf: FY25 – FY26
SALSA: FY26

## Slide 12: eRD109 – 3rd Party Evaluations (USC/SCIPP, JLab)
  a) HPSoC (SCIPP) & HDSoc (Jlab) (NALU)
HPSoC – AC-LGAD
Waveform, 4 ch, 10 bit, 10 GSPS, 2 mW/ch, Timing precision: 10 ps – 20 ps.
HDSoC - SiPM
Waveform, 32/64 ch, 12 bit, 1 GSPS, 20-45 mW/ch, Timing precision: 80-120 ps.
  b) ASROC (Anadyne)
  c) FAST (INFN)
TDC, 110 nm CMOS, 16/20 ch, ~2 mW/ch, Timing precision: 15 ps – 45 ps.
Discriminator, SiGe BiCMOS, 16 ch, ~ 1 mW/ch, Timing precision: 5 ps – 15 ps.
HPSoCv2
  Fixed digital back-end
  Expected from TSMC March 2024
  Tests soon
ASROC
  Excessive cross-talk
  No further work envisioned.

## Slide 13: eRD109 – Barrel TOF Service Hybrid (ORNL)
Connect 64 ASICs along stave to RDO at end of stave:
  LV, Bias (HV), GND
  Differential e-links, clocks, slow controls (I2C)
  Individual ASIC output data rate is only ~Mbit/s.
Low Mass: 1% X/X0 total barrel material budget
Needs to fit barrel TOF geometry:
  ~1.3 m length.
Kapton flex PCB:
  Custom geometry “sandwich” of Kapton and conductor layers.
  Plan to demonstrate readout of ETROC (CMS endcap TOF ASIC) over long flex PCB with TOF prototype RDO (Tonko).
  Design of TOF prototype RDO is almost complete with fab, tests soon.
  Flex design support from Debrecen
  Some design and fabrication technology issues identified and resolved
  Production is in progress, three processes considered
  High density connectors under consideration – w/ HV or separate.

## Slide 14: Outlook
Finalize specifications:
  Max. rates per channel – almost ready (Jeff)
  ASIC interfaces for FEB-RDO – iterative process with designers, on-going
  SALSA DSP functions – needs input from MPGD group(s)
Considerable resources needed for the next 2 – 3 years:
  Expect a few prototype MPW runs per design ($)
  Pre-production run per design ($$$) (masks: $250k/130 nm, $750k/65 nm)
  Tests are resource intensive (EE, Tech, prototypes)
  Address pfRICH, hpDIRC readout – FCFD, EICROCx
FY23 and FY24 contracts: awards >6 months after start of FY
  Not sure this can be improved.