## Slide 1: Instrumentation Group @Penn
Scientists/Engineers
Paul Keener (Group Leader)
Mitch Newcomer, Nandor Dressnandt, Adrian Nikolica, Bill Ashmanskas
Technical Staff
Godwin Mayers, Mike Reilly, Manny(Emannuel) Morales
MSEE Student workforce
Usually between 3 and 4 Students from the Moore EE School each year
2023 -2024 Xiaokai Ma, Chenjun Li, Meijun Tian (65nm) Analog Design / Layout & verification using parasitic extract NL
Hengji Ye (180nm) Design modification / Verification
MSEE’s working with our group have 100% placement rate in industry on Graduation or go on to PHD studies

## Slide 2: Activities FEE System Design/Development/Production Including Analog & Digital ASICs
  ASIC’s GF 130, TSMC 180, TSMC 65
  ATLAS upgrade ITK Strips 50M channel system GF130
    Leaders with CERN ESE in the design of the readout system including ASICs
    Designed Module readout protocols and most ASIC I/O communication blocks
    Rad and SEU tolerant techniques including TMR
    Implement Design with CI techniques, Test & Produce 35K AMACstar and 35K HCCstar ASICs
  Qpix analog readout for low rate pixel TPC target < 50uW / channel (TSMC 180n)
    Updated Result (p 26,27) showing LN operation
  APP Analog Photon Processor (TSMC 65n)
  COTS electronics
  ATLAS High Speed Readout 128 input HTT Trigger Processor Mother Board
  Dune warm electronics PTC board
  Super Fine Grain Detector SFGD for T2K upgrade RO electronics with U. Geneva
  EOS Detector System design: PMT HV dist. , Analog & NHIT sums, buffer to CAEN RO

## Slide 3: ATLAS ITK Penn /CERN Leadership in System design
P I x e l s
S t r i p s
Credit Thomas Gosart, Bobby MCGovern Penn GS
Module ( 5000 strips)

## Slide 4: Barrel ITK Strip Module & ASICs
CERN Responsibility
Penn ASIC Responsibility

## Slide 5: Wafer Probe Station
AMAC Testing Flow Chart

## Slide 6: ITK ASIC Testing Team

## Slide 7: Probing Yield Distributions

## Slide 8: Analog Feature Extraction Low PE count PMT or SiPM
  Maximum Likelihood studies at Penn using Hamamatsu R5912 have shown that multiple PE signals can be inferred with high accuracy by knowing only a few extracted parameters. The APP is being designed to extract relevant parameters and present extracted analog values to a commercial ADC or an ADC designed by another group.

## Slide 9: The Analog Photon Processor  APP ASIC
Purpose: Dual Readout (Scin & Cherenkov) with PMT or SiPM analog for feature extraction for Underground Neutrino Detectors.
These sensors have an output shape based on their high statistics gain (107-8 ) not determined by the physics of the interaction.
In low statistics (1 to 100PE) readouts APP seeks to extract physics measurements relevant number of PE by capturing:
TOT, Integral Q, T,V first peak, valley and 2nd peak within TOT.
Target Sensor has a 1-2ns Rise time  Chose 65nm node

## Slide 10
PeakDetector
A2D_U1
HOLD_U1
TACx2
aMemoryx2
A2D_U2
A2D_D1
A2D_D2
PMT
Comparator
aMemoryx2
aMemoryx2
aMemoryx2
aMemoryx2
TACx2
aMemoryx2
TACx2
aMemoryx2
Integrator
Counter
Memory
Memory
Memory
HOLD_U2
HOLD_D1
DELAY
TACx2
aMemoryx2
event
64
eventB
TACx2
aMemoryx2
aMemoryx2
Record count at both
rising/falling edges
Timeout Logic
Programmable: ~50ns
Analog Photon Processor Chip
Nandor Dressnandt
CLK
CLK
CLK
CLK
CLK
analogMUX
5:1
Peak1:
A2D_U1 (mV)
HOLD_U1 (ns)
Peak2:
A2D_U2 (mV)
HOLD_U2 (ns)
Valley1:
A2D_D1 (mV)
HOLD_D1 (ns)
PMT Signal
aMemory: Single 400fF Cap
External1
A2D
20 MHz
External2
A2D
20 MHz
OPAMP
Fully Differential
OPAMP
Fully Differential
APP CHIP
External
World
Compiled RTL logic
-Inteface logic
-Integrator controls
(cal, timeout)
-A2D controls (DC services)
-Analog mux control (sample)
-Reset
-PeakDet
(cal, controls)
-DELAY
LVDS
driver
LVDS Receive
-data
-CLK
analogMUX
5:1
A2D Control
Programming
+
-
A2D Control
+
-
A2D Control
CLK
+
-
+
-
+
-
-
+
Differential
Signals only
CLK
SEL/sample
SEL/sample
SEL/sample
100ns/sample:
~600ns to capture
all analog data
DAC
DC services
10
PeakDetector: 4 voltages
Comparator Threshold: 1 voltage
Integrator Cal: 1 voltage
APP CHIP
External
World
TRACK/HOLD
Largely Completed

## Slide 11: Wide BW Opamp NMOS diff pair input
Unity Gain Bandwidth
- 400mV
- 400mV
0dB
-3dB
2.1GHz
Unity Gain Config 1.8GHz -3dB
- 2%
0.6%
Open loop gain | 1400
GBW | 2.3GHz
Closed loop -3dB bandwidth | 1.8GHz
Rise time | 1nS
Dynamic range | 200mV-1000mV
Steady power | 0.63mW
Random out offset (closed loop) | Sigma= 0.82mV

## Slide 12: Prototype Peak Peak Finder
Static power consumption = 1.2V * 3.7mA
2 - 5mV signals,
4.2ns separation
78um(width) * 65um(height) = 5070um^2

## Slide 13: Gated Integrator test bench
Comparator gated input.
When no signal: switch off, source impedance becomes very high, which stops Cap leakage.
Able to integrate successively without reset
Trigger Comp
Delay Block
Source Switch
Vbase(set by DAC)
Vth

## Slide 14: Integrator Simulation:
50mV
300mV
10mV
Comp determining valid integral

## Slide 15: Analog Sampler-Schematic
sample using bottom plate sampler
sample immediately presented to the read port
high output drive
bottom plate sampler
output buffer
switch delay

## Slide 16: Sampler- Range / Precision over process Windows
Read output VS Write input (measure 80nS after sampling)
Percentage Error of measurement
1.6 %
0
100mV
100mV
1V
1V
Input Voltage
Input Voltage
Voltage on Sample Cap after 80ns

## Slide 17: Bottom Sampling Analog Memory
.8mV
-.4mV
-1.6mV
-2.8mV
1V
0V
Input Voltage
Output Voltage
After 1mS
1V
After 100uS
After 1ms
mV Deviation
Readout not Active
Top Plate
Top Bottom Plate
Write Enable
Read Enable
dy = 299.8mV

## Slide 18: TAC Transient Noise Simulation
noise bandwidth: 1MHz~100MHz
temperature: 50 Celcius Degree
clock rate: 40MHz
100runs
Slope ~ 20mV/ns TAC (only) RMS < 10ps
Case1: T_min(0.5CLK) σ=115.64uV(410mV drop) RMS=0.79V
Case2: T_max(1.5CLK) σ=132.33uV(925.3mV drop) RMS=0.275V

## Slide 19: Qpix Analog Front End: An Ionization Current Readout for Pixelated LAr TPC’s
Amplifier Discriminator
Integrator
10uA
Bias
Pixel
4x4mm
No Reset in DAQ mode
50fF
Local Logic
adjustable
fixed current
Clock (~ 40MHz)
external or
Internal Ring Osc
Single Clock Out
Trig if input high
Q = i*Δt

Low Power Diff
Replenish Pulse
One Clock width
50uA
or
500uA
TPC ionization current
Low Power 25 to 45uW
Replenishment eliminates problematic RESETs from the original concept
 REMOVES RESET “noise” UNCERTAINTY observed in Transient Noise Analysis
 Allows the pixel to function as an analog memory for large currents making Q accurate.
RESET dumps incoming charge. In Replenishment only the time between replenishments is
distorted. All charge is counted in units of Replenishment
Notes: Transient Noise Analysis of the “Reset” approach led to questions about it’s accuracy for 1fC or lower measurements. Reset “noise” led to uncertain integrator offsets. The Replenishment approach shown above virtually eliminates the reason for resets as well as the unavoidable masking of the channel while reset takes place.

## Slide 20: Qpix Analog: An Ionization Current Readout for Pixelated LAr TPC’s
Input 0
Ref 0
Input 1
Ref 1
Input 2
Ref 2
…
…
…
…
…
…
…
…
…
…
Input 15
Ref 15
Outp 0
Outn 0
Outp 1
Outn 1
Outp 2
Outn 2
…
…
…
…
…
…
…
…
…
…
Outp 15
Outn 15
16 channel prototype chip divided into 8 “Standard” gain channels (0-7) and 8 “Cgain” (capacitor based gain) channels (8 -15). Each bank of 8 channels has its own services: Serial Interface, Ring Oscillator, POR (Pwr-On Reset), Calibration circuit.
“Standard” gain channels consist of an analog Integrator (20mv/fC), an intermediate amplifier (x3), comparator and programmablereplenishment circuitry. ~ 45uW/channel ignoring prototype’s LVDS drivers
“Cgain” channels have the same functionality but use a different analog Integrator with much higher gain (48mv/fC) to avoid the need for an intermediate amplifier. This reduces unknown offsets, reduces internal delay & power and allows a wider range of bandwidth vs intrinsic noise tradeoffs. Power ~ 25uW/channel ignoring prototype’s LVDS drivers

## Slide 21: Reconstructed Charge Time Resolution Investigation
One Qpix step per sensed fC of Ionization Charge
Physics input Signal
Green Trace
Plot shows Appended results from 2 of 5 Transient Noise Runs
Integral Charge from a Physics simulation of a “proton” event ~80fC
Spectre Simulation Results

## Slide 22: Room Temp Replenish Current Calib. of 6 channels Qpix COB Bd #3
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Channel 1 | 0.30488 | 0.23148 | 0.28986 | 0.29851 | 0.369 | 0.44444 | 0.49505 | 0.63694 | 0.66667 | 0.74074 | 0.4717 | 0.86957 | 0.91743 | 0.96154 | 1.0526 | 1.1236 | 1.2048 | 1.2048 | 1.3333 | 1.3699 | 1.4286 | 1.4706 | 1.5625 | 1.6393 | 1.7241 | 1.7241 | 1.8519 | 1.8868 | 1.9608 | 2.0833 | 2.0833
Chart: Channel 2
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Channel 2 | 0.20284 | 0.19569 | 0.23364 | 0.3012 | 0.31546 | 0.39683 | 0.54945 | 0.60606 | 0.73529 | 0.70423 | 0.7874 | 0.84034 | 0.83333 | 0.82645 | 1.0753 | 1.0417 | 0.96154 | 1.087 | 1.3514 | 1.0989 | 1.3514 | 1.0989 | 1.3889 | 1.3699 | 1.6949 | 1.4706 | 1.5385 | 1.5625 | 1.6129 | 2.2727 | 1.6393
Chart: Channel 3
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Channel 3 | 0.19802 | 0.21413 | 0.29674 | 0.3663 | 0.44843 | 0.53191 | 0.5988 | 0.8 | 0.81967 | 0.92593 | 0.9901 | 1.0638 | 1.1111 | 1.2195 | 1.2821 | 1.3699 | 1.4085 | 1.5152 | 1.5873 | 1.6129 | 1.6949 | 1.7544 | 1.8182 | 1.8868 | 2 | 2.0833 | 2.1277 | 2.2222 | 2.2727 | 2.439 | 2.381
Chart: Channel 5
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Channel 5 | 0.17986 | 0.18553 | 0.23256 | 0.29586 | 0.34965 | 0.42735 | 0.4902 | 0.63694 | 0.68027 | 0.75758 | 0.83333 | 0.88496 | 0.92593 | 0.9901 | 1.0638 | 1.1628 | 1.2346 | 1.2821 | 1.3514 | 1.3699 | 1.4925 | 1.5625 | 1.6129 | 1.6949 | 1.8182 | 1.7857 | 1.9231 | 2 | 2.0833 | 2.1277 | 2.1277
Chart: Channel 6
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Channel 6 | 0.17953 | 0.16584 | 0.2 | 0.24691 | 0.30395 | 0.35971 | 0.41841 | 0.53476 | 0.57143 | 0.64103 | 0.68966 | 0.74627 | 0.8 | 0.86207 | 0.89286 | 0.9901 | 1.0638 | 1.1111 | 1.1628 | 1.2048 | 1.2658 | 1.2658 | 1.4085 | 1.5152 | 1.5385 | 1.6129 | 1.6393 | 1.7241 | 1.7544 | 1.7857 | 1.8519
Chart: Channel 7
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Channel 7 | 0.22124 | 0.24272 | 0.27397 | 0.36364 | 0.45872 | 0.5102 | 0.55866 | 0.71429 | 0.76336 | 0.86207 | 0.93458 | 0.97087 | 1.0526 | 1.1111 | 1.2048 | 1.2987 | 1.3333 | 1.4286 | 1.5385 | 1.6129 | 1.6129 | 1.7544 | 1.8182 | 1.9231 | 1.9608 | 2 | 2.1277 | 2.1277 | 2.2222 | 2.3256 | 2.3256
Internal Ring Osc
Clock 33MHz
Qpix Measurement Results

## Slide 23: 9 Step injection charge at Room Temp. High / Low Leakage
Injector
Q Step ~ 0.5pF*2mV  1fC
Average Count 12.5
Average Cnt NO pulse 6.5
Average Count 5.5
Average Cnt NO pulse .2
Qpix Replenish Output
Qpix Replenish Output
Hi Leakage induced with 1G resistors at the input ~50pA
Reduced Leakage 1G resistors at the input ~1pA
Qpix Measurement Results

## Slide 24: Calibration Circuit
In order to calibrate the size of the replenishment pulses a calibration voltage ramp is generated utilizing a programmable current source and an internal MIM capacitor. This ramp may be connected to individual channels through a 100fF connected to the integrator input. In the example below a 1nA current is generated for 100uS resulting in a 1fC charge injection every microsecond. Since the method depends only on capacitance and voltages it should be able to generate a reasonably precise +/- 10% charge that manifests as ~ 100 charge replenishments. Utilizing this method we should be able to have a high statistics replenishment count to calibrate the replenishment current.
Calibration
RAMP
Vary Slope
To study
Leakage

## Slide 25: Internal Calibration Ramp slope 80uS - 160uS / 100fC
Injection Current 1nA
Injection Current 0.5nA
Calibration Time
Calibration Time
Qpix Measurement Results

## Slide 26: Qpix Operation at LN temp: First Observations

## Slide 27: Qpix LN test showing Ch 15, C-Gain 25uW channel
Pulser Stepping
Integrator monitor point Shows Replenishment
Replenishment Signal
“108.tif shows chan15 (c-gain). The blue is the Integrator output )(spy point) and the yellow shows replenishments. The pink shows an AC coupled descending staircase emulating a 'real' TPC track. The sequence starts with an Integrator reset, followed by the staircase. You can see the Integrator output increase step by step until about 60mV is accumulated... At which time replenishment ensue. after the the first replenishment (actually about 4-5 1fC replenishments) additional steps cause additional replenishment.”
Nandor Dressnandt
“We ran for several hours in the cold, then de-iced, ran at room temp again, the back into the cold for two more hours.”

## Slide 28: ATCA demonstrator Board for ATLAS HTT ATLAS TDAQ
Highest rate eye diagrams for three categories of link. Top: 15Gbps @ 10-14 BER for longest link on mezzanines.
26 Layer Stackup Megatron-6
Eight layers of signal routing (left) and closeup (right). In the closeup, note high speed design techniques: length matching, “necking down” into the FPGA ball grid array, smooth bends. Backdrilled via’s 16 depths.
14x14 backplane mesh:
26 board-to-board links specified at 10 Gbps
  Performance exceeds 10Gbps spec.
RTM with up to 30 fiber links for data transmission plus additional monitoring
32 data links support for mezzanine
Support for 2 mezzanines either:
1 PRM Pattern Recognition Mezzanine with Associative Memory with FPGA I/O
2 TFM Track Fitting Mezzanines
XVCU37P
FPGA
40A @850mV
FPGA core pwr
Lead Engineer
Adrian Nikolica
144 lead Zray
High Level Track Trigger System