## Slide 1: Front-Ends for Extreme Conditions
Carl Grace 5/1/2024
Lawrence Berkeley National Laboratory
HEPIC 2024

## Slide 2: Challenges for Custom ASICs
Physics experiments often create extreme environments for their readout ASICs
High Radiation
ATLAS Detector
Cold Temperature
ProtoDUNE LAr TPC
Liquid Argon

## Slide 3: First Physics ASICs
NMOS process (no P-channel devices) - SLAC - 1984
Microplex – first custom ASIC for Physics Research
Walker, Parker, Hyams, Shapiro, “Development of High Density Readout for Silicon Strip Detectors,” NIM 226 (1984)
SVX – First CMOS ASIC for Physics Research
CMOS process (with P-channel devices) - LBNL - 1987
128 channels
3 mW / channel
Kleinfelder, et al.; “A Flexible 128-Channel Silicon Strip Detector Instrumentation Integrated Circuit with Sparse Data Readout”, TNS 35 (1988)
128 channels
1.25 mW / channel
6.3 mm
6.3 mm
11,000 transistors
CDF experiment used 240 SVX chips  30720 channels
Already at discrete limit
Follow-on versions co-designed with FNAL

## Slide 4: Challenges for Custom ASICs - Radiation
Two main types of radiation damage to integrated circuits that concern us (Single Event Latchup and Single Event Transients of less importance in HEP experiments)
Total Integrated Dose – structural damage to silicon structure that leads to failures
Single Event Upset – transient effects that could modify data or lead to incorrect data

## Slide 5: Radiation -- Total Integrated Dose (TID)
Requirements for TID radiation tolerance for physics far exceed any commercial application
F. Faccio

## Slide 6: Radiation -- Total Integrated Dose (TID)
F. Faccio
Key mitigations:
  use scaled technologies (Microplex and SVX only radiation tolerant to 10s of krad)
  “Hardness-By-Design” techniques (long devices / enclosed layout / guard rings / etc)
  Annealing

## Slide 7: Radiation – Single Event Effects (SEE)
C. Zamantzas
Scaling devices makes ASICs more resilient to TID, but less resilient to SEE
R. Gaillard

## Slide 8: Radiation – Single Event Effects (SEE)
Key mitigations: Triple Modular Redundancy (TMR), Hamming encoding, continuous reconfiguration
K. Berg
Triple Modular Redundancy (TMR)
- Device level? Circuit? Module?
Hamming encoding
Continuous Reconfiguration

## Slide 9: Challenges for Custom ASICs - Cryogenic Environment
Cryoelectronics are typically understood to be electronics that operate at temperatures below what can be found naturally on Earth.
From a practical IC Design standpoint, our cold integrated circuits typically operate in one of two regimes:
Liquid Nitrogen Regime  around 75 K (-200 °C)
Liquid Helium and Below Regime  4 K or less (down to mK)
Key benefits of operating electronics in the cold:
  Enabling technology that allows new system architectures that may offer improved performance
  Promotes scaling by reducing cable plant and cryostat penetrations
  Reduces noise (puts gain physically closer to the sensor / reduces capacitance)
  Reduces overall system complexity and power dissipation

## Slide 10: Cryogenic Electronics Applications
Nobel Liquid Particle Detectors
CMB Studies
Quantum Computation / Science
Superconducting Magnet Instrumentation
ProtoDUNE-SP
South Pole Telescope
BNL Quadrupole magnet
IBM Q-computer

## Slide 11: Cryogenic Operation
Functionality, Threshold Shifts
Negative resistance and hysteresis. Carrier freeze out also an issue.
Reliability and biasing drift
180 nm
180 nm

## Slide 12: Key Challenge - Long-Term Reliability
Reliability and biasing drift
“Hot” carriers cause early device aging
E. Afacan Thesis, 2016
BNL and FNAL conducted lifetime studies and developed design guidelines to assure long-term reliability. Developed custom SPICE models.
UPenn and FNAL developed a cryogenic compatible standard cell library for 65nm CMOS

## Slide 13: Key Challenge – Power Dissipation
Cooling Power
10 µW
100 µW / 1 mW
~ 2 W
100 W
> 100 W
Need low power-per-channel electronics to operate at coldest temperatures
Dilution refrigerator
Oxford Instruments
300 K
70 K
4 K
100 mK
20 mK
Cellphone received signal
LED lamp
Large food fridge
Heat dissipation through finger tip

## Slide 14: Potential Future Cryosensors – mix of CMOS and SC

## Slide 15: Liquid Noble Readout Electronics ~ -200° C
The final DUNE Near Detector will require approximately 350k ASICs to instrument a 100m2 pixel plane (22.4 Mpix)
DUNE Near Detector
Neutrino Pileup Simulation
Pixelated solution solves reconstruction ambiguity problems with wire-plane readout
Front-Ends for Extreme Conditions

## Slide 16: LArPix – Liquid Argon Pixel ASIC
Approach: Integrating Amplifier with Self-triggered Digitization and Readout
Front-end amplifier
Self-triggering Discriminator
Standard SAR Digitizer
Digital Control
Achieve low power: avoid digitization and readout of mostly quiescent data.
64 channels per ASIC
  Charge Sensitive Amplifier
  Discriminator (self trigger)
  ADC (per channel)
  Digital Control logic
Global control logic
2k FIFO
On chip references and bias currents
Only decoupling capacitors needed
Immersed in Liquid Argon (-184° C)

## Slide 17: LArPix Pixel Tile
Tile with 100 LArPix-v2 ASICs (6400 channels)
Closeup of tile
Prototype tiles have 100 LArPix ASICs
(30 cm by 30 cm)
ND Tiles will scale to 160 ASICs/tile
Front of tile with sensor array
Need O(10 Million) pixels for ND

## Slide 18: Liquid Noble Readout Electronics ~ -200° C
Front-Ends for Extreme Conditions
System in operation
Electrical and gas/liquid feedthroughs
Viewport
Test chamber
No boiling with > 3 cm LAr above chip (LArPix running full blast)
18

## Slide 19
Demonstrate system scalability in large LArTPC: ArgonCube 2x2 Demonstrator
System successfully operated.
Demonstrator for DUNE Near Detector
4 modular LArTPCs
Total active mass: ~3 ton
Readout area: 6.4 m2
400k pixels, 6.3k ASICs

## Slide 20
Demonstrate system scalability in large LArTPC: ArgonCube 2x2 Demonstrator
Raw data (no filtering) of cosmics in ArgonCube module0 demonstrator.
Detector delivers unprecedented track fidelity and would be impossible to implement without custom ASICs
The final DUNE Near Detector will require approximately 350k ASICs to instrument a 100m2 pixel plane (22.4 Mpix)

## Slide 21: Final Thought (Courtesy M. Garcia-Sciveres)
1980s
1990s
2000s
2010s – 2020s
2030s?
M. Garcia-Sciveres
(EEs)

## Slide 22: Thank You
This work was supported in part by the U.S. Department of Energy under Contract No. DE-AC02-05CH11231