## Slide 1: Tracking Systems Overview and Requirements
Brian Eng
Jefferson Lab
L3 CAM

## Slide 2: Charge Questions Addressed
Are the technical performance requirements appropriately defined and complete for this stage of the project?
Are the plans for achieving detector performance and construction sufficiently developed and documented for the present phase of the project?
Are the current designs and plans for detector, electronics readout, and services sufficiently developed to achieve the performance requirements?
Are plans in place to mitigate risk of cost increases, schedule delays, and technical problems?
Are the fabrication and assembly plans for the various tracking detector systems consistent with the overall project and detector schedule?
Are the plans for detector integration in the EIC detector appropriately developed for the present phase of the project?
Have ES&H and QA considerations been adequately incorporated into the designs at their present stage?

## Slide 3: Outline
Requirements
Interfaces
Tracking Detector Layout
Risks
Safety
Summary

## Slide 4: Requirements
https://eic.jlab.org/Requirements/index.html
Based physics in Yellow Report
Charge 1
 | Momentum Resolution | Spatial Resolution
Backward (-3.5 to -2.5) | ~0.10%×p⊕2.0% | ~ 30/pT µm ⊕ 40 µm
Backward (-2.5 to -1.0) | ~ 0.05%×p⊕1.0% | ~ 30/pT µm ⊕ 20 µm
Barrel (-1.0 to 1.0) | ~0.05%×p⊕0.5% | ~ 20/pT µm ⊕ 5 µm
Forward (1.0 to 2.5) | ~0.05%×p⊕1.0% | ~ 30/pT µm ⊕ 20 µm
Forward (2.5 to 3.5) | ~0.10%×p⊕2.0% | ~ 30/pT µm ⊕ 40 µm

## Slide 5: Interfaces
https://eic.jlab.org/Interfaces/Interfaces.html
  Outer barrel limited by DIRC
  Disks limited by pfRICH/AC-LGAD
  Inner Barrel first vertex layer 5mm from beampipe
Charge 1

## Slide 6: Interfaces – Beam Pipe
Unique beampipe
  Tapered beampipe, tracking detectors must be installed prior to beampipe installation in central detector
  Beampipe exposed to ambient prior to installation
  Need min 100°C in beampipe to break H2O bonds
    Silicon detector limited to <50°C due to CTE of materials
    Additional details in Nicole’s talk
Charge 1
Only covers 1 m of 3 m beryllium section

## Slide 7: Tracking Detector Layout Modifications
Low number of hits in certain rapidity ranges
  Need more planes
  Red = Si Only, fast simulation
  Blue = Previous layout, full simulation
Solve impact from 5 (2) μs MAPS frame accumulation time
  Need enough hits from faster detectors to form a tracklet with a good pointing resolution, e.g. MPGDs
  Need to utilize ToF and maybe Barrel-ECal AstroPix as possible
    Note: Barrel ToF has good time resolution but not spatial resolution
Current layout finalized in Spring 2023
Charge 2, 3

## Slide 8: Overall Tracking Layout
MPGD
  BOT Length: 340 cm
  BOT Radius: 72.5 cm
Silicon
  Outer Length: 84 cm
  Outer Radius: 42 cm
AC-LGAD
  ToF: Part of PID
μRWELL-ECT
μRWELL-BOT
CyMBaL
AC-LGAD Barrel
AC-LGAD Endcap
SVT OB
SVT IB
SVT Endcaps
SVT Endcaps
μRWELL-ECT

## Slide 9: Simulation – Nhits vs η
Only tracking detectors included, will improve further once calorimeters included which should remove dip at rapidity ±1, details in Matt’s talk

## Slide 10: Silicon
MAPS (monolithic active pixel sensors) in 65 nm CMOS technology, developed with ALICE ITS3 collaboration, details in Laura’s talk
  Inner Barrel: Directly use ITS3 wafer scale sensor
  Outer Barrel: EIC Large Area Sensor (LAS), modification of ITS3 sensor
EIC Project, ePIC SVT Collaboration and CERN ALICE/ITS3 meeting in Q2 23
  Path forward on collaboration (draft completed at BNL legal)
  EIC has hired 2 engineers to work directly with ALICE team on sensor development

## Slide 11: Silicon – Inner and Outer Barrel
Inner: three layers of thin, bent, wafer scale ITS3 based sensors
ITS3 concept adapted to ePIC radii, details in Ernst’s talk
X/X0 % = 0.05
Outer: Traditional stave design
Layer | Radius (mm) | Length (mm) | Sensors
L0 | 36 | 270 | 4
L1 | 48 | 270 | 4
L2 | 120 | 270 | 8
Layer | Radius (mm) | Length (mm) | X/X0%
L3 | 270 | 540 | 0.25
L4 | 420 | 840 | 0.55

## Slide 12: Outer Barrel – MPGD
CyMBaL
  Additional Tracking Points
Single Tile
  65 x 46 cm
  Simplifies production
  More details in Francesco’s talk
μRWELL-BOT
  Provides hits for DIRC
Single module design
  24 modules in total
  More details in Kondo’s talk

## Slide 13: Forward / Backward Disks – Silicon
Foundry rule/limitation, need to limit number of sizes (2-3 total)
  Direct outcome from meeting with ALICE
  More details in Ernst’s talk

## Slide 14: Forward / Backward Disks – MPGD
μRWELL-ECT
  4 disks in total (8 half-disks)
  Diameter ~100 cm with 2 cm overlap
  More details in Annalisa’s talk

## Slide 15: Services
Service volume increases as get further from Interaction Point
  More details in Roland’s talk
RED = power
BLUE = cooling/gas
ORANGE = signal
Charge 3

## Slide 16: Integration
Assembled in stages
  μRWELL-BOT together with hpDIRC
  CyMBaL with TOF
  Silicon barrels and disk clamshell around beampipe (SVT is separate sub-assembly)
  TOF assembly slides over SVT
  μRWELL-ECT are added as last step
More details in Roland’s and Andy’s talks
Charge 6

## Slide 17: Cost / Schedule
Inner Barrel Silicon (ITS3)
  2024-2026
Outer Barrel/Disk Silicon (LAS)
  2025-2027
Stave/Disk Construction Complete
  Q4 29
Ready for integration
  Q2 30
Cost / Schedule is based on engineering estimates from detector experts
Charge 5

## Slide 18: Risks
Currently for the silicon trackers there is a planned engineering run during R&D with the production run taking place during PED
Benefit from ALICE ER1 and ER2 runs and that the EIC runs would be based on the final ER3 design
However, if unforeseen issues arise another engineering run for the sensors might be needed
  The risk register has a proposed risk (ID RT-6-10-014) if a second engineering run is needed which would use contingency
CD-3A Director’s Review comment: “Upfront discussion of risks of R&D not coming to a favorable conclusion, and mitigation plans in this case, should be more clearly documented and presented. Where appropriate, for example for the tracking detector, more detailed plans should be developed.”
  Silicon detectors have external dependency on ITS3 sensors
See later talk for alternative layout discussion
Charge 4

## Slide 19: Safety
Generally the tracking WBS is in the design phase and and such doesn’t have any safety issues
However, there are a few test stands being developed which follow their institution’s safety protocols
  Protocols include required training
  LBNL testing carbon foam cooling: ISM, documented in Work Planning & Control
  JLAB testing beampipe bake-out: ISM, Task List and ePAS (JLab-PR-725)
Equipment going in the BNL Experimental Hall must follow NEC/NFPA 70E, 2021 and electrical safety guidelines: DOE-HDBK-1092-2013
  Defines voltage hazards, cable type requirements, circuit protection, etc
  Equipment must be NRTL listed or approved by BNL Electrical Equipment Inspection program
Charge 7

## Slide 20: Summary
Recent design change to address performance issues, which has been incorporated into the ePIC collaboration’s latest models
Cost and schedule developed with input from ePIC collaborators and ALICE/ITS3 efforts
  Scope change request for additional personnel based on discussions from CERN visit in progress.
Tracking WBS is in the final design stage no major ES&H issues
  Test stands follow the relevant institution’s policies.
Proposed risk added to register for additional engineering runs of silicon sensors