## Slide 1: Barrel Outer MPGD Tracker (BOT)
Incremental Design and Safety Review of the EIC Tracking Detectors March 20-21, 2024
Kondo Gnanvo, Jefferson Lab
Thin-gap GEM-µRWELL hybrid Detector
ePIC MPGD DSL

## Slide 2: Charge Questions Addressed
Are the technical performance requirements appropriately defined and complete for this stage of the project?
Are the plans for achieving detector performance and construction sufficiently developed and documented for the present phase of the project?
Are the current designs and plans for detector, electronics readout, and services sufficiently developed to achieve the performance requirements?
Are plans in place to mitigate risk of cost increases, schedule delays, and technical problems?
Are the fabrication and assembly plans for the various tracking detector systems consistent with the overall project and detector schedule?
Are the plans for detector integration in the EIC detector appropriately developed for the present phase of the project?
Have ES&H and QA considerations been adequately incorporated into the designs at their present stage?

## Slide 3: Outline
Requirements
µRWELL-BOT Detector Layout
Technology Choice & Design Considerations
PED - Engineering Test Article
Assembly Schedule, ES&H & QA
Summary

## Slide 4: Overview of ePIC Tracking Detector
Charge 1
RWELL-ECT
RWELL-BOT
CyMBaL
AC-LGAD Barrel
AC-LGAD Endcap
SVT Barrels
SVT
SVT Endcaps
SVT Endcaps
RWELL-ECT
Technologies
MAPS (Si)
MPGDs (Gaseous)
AC-LGADs (Si)

## Slide 5
Requirements

## Slide 6: Requirements: Tracking needs from hpDIRC in the barrel
ePIC Barrel Outer Tracker (µRWELL-BOT)
Tracking layer close to hpDIRC detector
improved and angular and space point resolution at the DIRC level
Acceptance matching with hpDIRC bars
Spatial resolution: better than150 µm on average over the full eta range in barrel region
Barrel Outer Tracker
hpDIRC (barrel PID)
Impact of tracking angular resolution on hpDIRC performance
Studies from ePIC PID Detector Subsystem Collaboration
Charge 1

## Slide 7: Requirements: Pattern recognition & tracking redundancy
Charge 1
Previous configuration Before June 2023
Current configuration After June 2023
ePIC Barrel Outer Tracker (µRWELL-BOT)
Outer layer for pattern recognition together with the TOF (AC-LGAD) and Inner barrel layer (CyMBaL) trackers
Provide fast timing capabilitiy (~10 ns) to help the slow Si trackers with pattern recognition in high background.
Provide additional hit point to tracking for redundancy
See Matt’s presentations
Tracking simulation and reconstruction

## Slide 8
µRWELL-BOT Detector Layout

## Slide 9: µRWELL-BOT Layout
A1
A12
A11
B1
B12
B11
µRWELL-BOT Layout
24 planar modules arrange in 12-sided polygon shape
  L = 340 cm (−165 cm ≤ 𝑍 ≤ 175 cm)
  R = 72.5 cm
Segmented into
  2 sectors (A & B) in z along beam axis
  12 modules in phi azimuthal direction
µRWELL-BOT specifications
Thin-gap & double amplification (GEM & µRWELL)
2D-strip readout
  Nominal 70 µm (perpendicular tracks)
  On average 150 µm on for tracks in angle range [0, 45 degrees]
Fast timing layer ~ 10 ns
Radiation length < 2% in active area
Charge 2,3
Barrel Outer Tracker
hpDIRC (barrel PID)

## Slide 10: µRWELL-BOT Module:
1800 mm
Back view
1700 mm
340 mm
360 mm
Top view
V-strips
U-strips
µRWELL-BOT module
Thin-gap (1-mm drift) hybrid amplification GEM-µRWELL detector
Capacitive-sharing U-V strips readout layers(45O stereo angle)
Pitch: 1.14 mm (1790 U-strips and 1790 V-strips per modules)
On-detector Front End Boards (FEBs) based on SALSA chips
14 FEB / modules (assuming 4 SALSA chips i.e 256 e-ch / FEB)
Direct connection on the back of the modules (no need for flex cables)
Charge 2,3
2.5 cm
Cross section view
340 mm
360 mm

## Slide 11: µRWELL-BOT Module: Integration considerations
Main integration challenges: Space limitation in ePIC detector environment
µRWELL-BOT detector envelop in ePIC
  In radial direction: 2.5 cm
  Azimuthal direction: 36 cm
Installed in support structure of barrel ECAL in front (from IP) of hpDIRC bar
Optimization of the acceptance matching with hpDIRC
Implications in the design of the µRWELL-BOT module
  FEB cards on the back of the modules  material budget
  Carefully consider how services, cables choices affect maintenance in the future
DIRC bar box
µRWELL-BOT
µRWELL-BOT module
370 mm
Barrel ECAL support structure
Charge 6

## Slide 12
Technology Choice & Design Considerations

## Slide 13: Technology choice: Thin-gap GEM-µRWELL Hybrid Detector
Active area 34 cm
Active area 36 cm
3 mm honeycomb
readout PCB
FEB
G10 frames
GEM
µRWELL
cathode
cross-section view of thin-gap GEM-µRWELL detector
Thin-gap GEM-µRWELL detector concept
hybrid amplification MPGD:
  GEM (preamplification) and µRWELL (main amplification)
  Allow large detector gain and stable operating HV
Readout layer: 3-layer capacitive-sharing U-V strip readout
  Achieve excellent spatial resolution with thin gap detector
Challenges with standard (> 3-mm drift gap) MPGD
Degradation of the spatial resolution with track angle .
E × B in magnetic field negatively impact resolution
Development of Thin-gap MPGDs:
Small drift gap improve spatial resolution at large angle
Small gap  minimize E × B effect in magnetic field
        Improve the detector timing performance
parametrization from EPJ Web of Conferences 174, 06005 (2018)
Charge 2,3
https://wiki.bnl.gov/eic/upload/ERD_tgMPGD_FY22_endOfYearReport_final.pdf

## Slide 14: Technology choice: Thin-gap GEM-µRWELL Hybrid Detector
R&D funded by JLab administered DOE EIC Generic R&D Program as EICGENRandD_2022_23
Efficiency
Residuals
Efficiency
Proof of concept
Concept of thin-gap GEM-µRWELL hybrid prototype demonstrated in beam test at the Fermilab Test beam Facility in Summer 2023 (red plots)
Space resolution < 150 µm and efficiency of 92% on average for 1-mm thin-gap GEM-µRWELL prototype (red dots) and for track in an angle range between 0 – 45 degrees.
Baseline technology for ePIC outer MPGD tracker
Charge 2,3
https://wiki.bnl.gov/eic/upload/ERD_tgMPGD_FY22_endOfYearReport_final.pdf

## Slide 15
PED: Engineering Test Article

## Slide 16: Design consideration: Breakdown of µRWELL-BOT module
Top honeycomb support
Cathode foil
Drift frame
GEM foil
induction frame
µRWELL foil
UV readout PCB
Charge 2,3
FEBs
PED activities 2024–2025: Design of full scale module
Full scale Engineering test article based on 1-mm thin-gap prototype for the choice validation
Design to address integration challenges of ePIC
Test article module fabrication completion end 2024
Will be tested in beam at FNAL summer 2025
Design by the RD & I Group at JLab

## Slide 17: Design consideration: µRWELL-BOT module
Charge 2,3
Front view of the µRWELL-BOT module design
back view of the µRWELL-BOT module design

## Slide 18: Design consideration – µRWELL and GEM foil design
GEM foil: Conceptual design
foil divided into 36 HV sector ~ 160 cm2
Optimization trade-off between active-to-dead area ratio for gap uniformity
Final design with input from GEM experts at CERN MPT workshop - 06/24
Procurement by 12/24
Charge 2,3
µRWELL foil: Conceptual design
Foil divided into 12 HV sector ~ 480 cm2
Final design with input from GEM experts at CERN MPT workshop - 06/24
Procurement by 12/24

## Slide 19: Design consideration: 2D (U-V)-strip readout layer
Readout strip layers
3-layer capacitive-sharing U-V strip readout
  Strip pitch: 0.8 mm (along U and V axis)
  Trace pitch: 1.14 mm along horizontal axis (traces)
All connectors on the back of the rigid µRWELL / readout PCB
U-strips
V-strips
0.8 mm
1.14 mm
U-V strip configuration
Charge 2,3
cross-section view of 3-layers U-V strip capacitive-sharing readout
https://doi.org/https://doi.org/10.1016/j.nima.2022.167782

## Slide 20: Design consideration: µRWELL-BOT Readout Electronics
Charge 2,3
See Irakli’s presentations
MPGD Readout Electronics

## Slide 21
Assembly plans, ES&H & QA

## Slide 22: MPGD-DSC: Organization of ePIC MPGD Subsystem Collaboration
Charge 5
Outer MPGD Tracker: Module assembly
Production sites: University of Virginia (UVa), Florida Institute of Technology (FIT) and Jefferson Lab (JLab)
Vast experience with large scale and large MPGD projects among the 3 institutions
10 modules per site (8 + 2 spares)
Welcome to new institutions to join the effort

## Slide 23: Assembly plans: Equipment at the assembly sites
FIT Clean Room: assembly of
CMS GE1/1 GE2/1 and ME0 GEMs
CMS GEMs
UVa Clean Room: SBS GEMs, MOLLER GEMs, PRad GEMs, CLAS12 µRWELL, Hall D GEM-TRD prototype
Moller GEM foil
JLab MPGD Clean Room: New capacity for large MPGD module assembly
Charge 6
All 3 assembly sites have fully equipped MPGD Detector Lab
  Fully equipped CLASS 1000 Clean rooms for module assembly
  Cosmic tracking telescope setup with coincidence trigger counters and readout & DAQ system
  X-ray setup for high rate studies and long term stability …
  Will setup DAQ and readout system for SALSA – MPGD readout system

## Slide 24: Assembly plans: Quality Assurance (QA)
Test and characterization of µRWELL-BOT modules
  HV test in N2 of GEM and µRWELL sectors before, during and after assembly (in clean room)
  Gas leak test and sealing after module assembly
  Electrical connection capacitance and pedestal noise test of all U & V and strips
  Tag dead strips and replace FEB cards with dead readout channels
  Efficiency and relative gain uniformity studies with cosmic setup
  absolute gain measurement with radioactive source (local measurement)
  Large 2D X-Ray scanner for absolute gain uniformity (JLab)
UVa X-Ray box
Charge 7

## Slide 25: Assembly plans: ES&H
ES&H procedure will derived from past experience in each assembly site with similar system
  Non flammable operation gas mixture Ar / CO2  no special safety concern or implementation procedure needed
  HV supply via simple passive divider  Procedure to isolate any electric point on the detector
  Will follow JLab ES & H procedures for handling radiation sources during QA at the lab
  Similar procedures will be implemented in the various institutions
  Will have all these procedure documented in the appropriate ePIC documentation database (for example EICLOG @ JLab)
Charge 7

## Slide 26: Assembly plans: Planning & schedule
Charge 6
06/2025
06/2026
04/2029
06/2029
PED & validation
Ongoing design of full size µRWELL-BOT module
Procurement of GEM foils, µRWELL PCB – 12 / 2024
Assembly at JLab test in at FNAL - 06/2025
Pre-production
Assembly of one pre-production module (module#0)
Setup of infrastructure and equipment in assembly sites
Production
Assembly and QA of 9 production modules at assembly sites
Full characterization at assembly sites of each module on cosmic stand and with radioactive sources
Shipment to JLab
Shipment of all 24 modules to BNL
Commissioning at BNL cosmic test stand of all µRWELL-BOT as well as µRWELL-ECT
Commissioning & Installation
Commissioning
Installation

## Slide 27: Summary
The ePIC Barrel Outer MPGD Tracker (µRWELL-BOT) is based on thin-gap GEM-µRWELL amplification technology
µRWELL-BOT provides improved tracking option to the hpDIRC and pattern recognition with fast timing hit to Si tracker in the barrel
Design of the µRWELL-BOT is well advanced and integration issues and mechanical constraints are being addressed in the design
The engineering test article pre-production module is under development and expected to be validated by Summer 2025
Preliminary plans and schedule for the production of µRWELL-BOT modules in assembly sites is initiated
The ePIC MPGD DSC is established and very active with several institutions with vast experience with large MPGD productions

## Slide 28
Backup

## Slide 29: Design consideration: Some General considerations
Charge 2,3
Rate Capability
    Not critical ~ 1 kHz/cm2 or less
Radiation Hardness
    Not critical for the detectors
    Important for FEBs and RDO electronics boards
Temperature Stability
    Not critical for the detector performances
    Detector calibration should consider gas pressure variations
Electronics power consumption and cooling
    SALSA ASIC consumption ~ 15 mW/ channel at 1.2V
    Air vs liquid cooling is under study at Saclay – see Irakli’s talk
µRWELL-BOT
1 MeV neutrons
4 × 109