## Slide 1: Silicon: Readout
Joachim Schambach
Oak Ridge National Laboratory
SVT Readout and Powering Work Package Co-Coordinator

## Slide 2: Charge Questions Addressed
Are the technical performance requirements appropriately defined and complete for this stage of the project?
Are the plans for achieving detector performance and construction sufficiently developed and documented for the present phase of the project?
Are the current designs and plans for detector, electronics readout, and services sufficiently developed to achieve the performance requirements?
Are plans in place to mitigate risk of cost increases, schedule delays, and technical problems?
Are the fabrication and assembly plans for the various tracking detector systems consistent with the overall project and detector schedule?
Are the plans for detector integration in the EIC detector appropriately developed for the present phase of the project?
Have ES&H and QA considerations been adequately incorporated into the designs at their present stage?

## Slide 3: Outline
Top Level Readout Design
Inner Barrel Readout Design
Outer Barrel and Disk Readout Design
SVT Numbers
Prototype Developments
Summary

## Slide 4
Top Level Readout Design

## Slide 5: ePIC Streaming DAQ for SVT

## Slide 6: ePIC Streaming DAQ for SVT
Most ePIC detectors have their Readout ASIC on the FEB, connected to the detector via copper cables.
The FEB is then connected to a Readout Board that converts the electrical signals into optical fibers and transmits them to the DAM board in the counting house.

## Slide 7: ePIC Streaming DAQ for SVT
SVT
Most ePIC detectors have their Readout ASIC on the FEB, connected to the detector via copper cables.
The FEB is then connected to a Readout Board that converts the electrical signals into optical fibers and transmits them to the DAM board in the counting house.
In case of the SVT, a lot of the Readout functionality is already integrated in the MAPS ASIC itself, thus SVT does not have an FEB

## Slide 8: SVT Electronics for Data & Control

## Slide 9: SVT Electronics for Data & Control
For the inner barrel, a wafer scale sensor is connected to the RDO via a Flex Printed Circuit (FPC)
The Readout Electronics converts the high-speed data lines into (fiber) optical signals
The slow controls lines of the sensor are controlled individually via fiber-optic/electrical interfaces.
The Inner Barrel RDO also houses the direct powering for the sensors as well as the fiber optic interfaces

## Slide 10: SVT Electronics for Data & Control
For the Outer Barrel staves and the disks, the RDO converts groups of up to 4 SVT LAS high-speed lines to fiber optic signals.
The slow control lines of the whole 4-LAS group are connected to electric/fiber optic interfaces.
The groups of LASs use serial powering, so the power section of the RDO is solely for the RDO electronics itself.

## Slide 11: SVT Electronics for Data & Control
FPGA based “Fiber Aggregation” Boards in the DAQ room aggregate multiple (relatively low bandwidth) individual fibers from the RDOs into single fibers towards the DAM boards

## Slide 12: Backend: ATLAS FELIX Development for Phase-2 Upgrade
FELIX – FLX-182
FPGA: AMD Versal Premium VP1552 FPGA
PCIe Gen5x16 interface (482 Gb/s)
up to 48 bidirectional links
FPGA: AMD Versal Prime VM1802
PCIe Gen4x16 interface (240 Gb/s)
4 FireFly transceivers with 3 possible configurations
  24 links up to 25 Gb/s
  24 links up to 10 Gb/s (CERN-B FireFly)
  One duplex FireFly transceiver with 2 possible configurations with 14 or 25 Gb/s
FELIX – FLX-155

## Slide 13
Inner Barrel: MOSAIX Readout

## Slide 14: MOSAIX Data Flow – From Tiles to Left Endcap

## Slide 15: MOSAIX Data Flow – From Tiles to Left Endcap
MOSAIX is sub-divided into 144 (2 x 72) Tiles
Each Tile has its own pixel matrix read out via a 160 Mbps serial link towards the LEC
MOSAIX thus has 160 Mbps x 144 = 22.5 Gbps arriving at the LEC

## Slide 16: MOSAIX Data Flow – From Tiles to Left Endcap
In the LEC, the tile serial links are received and aligned
Via a switch matrix, the data can then selectively be sent to individual encoders and off-chip serializers

## Slide 17: MOSAIX Data Flow – From Tiles to Left Endcap
The data are then encoded with lpGBT IPs (providing a radiation tolerant protocol) and serialized to be shipped off the sensor via 10.24 Gbps links.
The MOSAIX design contains a total of 8 encoders and serializers, providing a total 80 Gbps bandwidth.
A fallback option is to run the serializers at 5.12 Gbps, thus still providing 40 Gbps.
This provides high redundancy for the 22.5 Gbps payload from the tiles in case of radiation damage; the switch matrix can be programmed with different (fixed) routing to mitigate the impact of failed components.
In case of the SVT LAS, only one serializer is foreseen in the design due to the much lower payload requirements in these sensors.

## Slide 18: lpGBT Protocol
Downlink
Data Uplink

## Slide 19: lpGBT Protocol
Front Ends connect to “e-links”
The fiber protocol includes “Forward Error Correction”

## Slide 20: lpGBT Protocol
Downlink
Data Uplink
Line Rate: 2.56 Gbps
32 out of 64 bits are data:
Payload = 1.280 Gbps
Front Ends connect to “e-links”
The fiber protocol includes “Forward Error Correction”
Downlink runs at 2.56 Gbps
  Downlink frame is 64bit wide, of which 32 bits are payload
  1.28 Gbps payload
  Up to 16 e-links @ 80 Mbps

## Slide 21: lpGBT Protocol
Downlink
Data Uplink
Line Rate: 2.56 Gbps
32 out of 64 bits are data:
Payload = 1.280 Gbps
192 out of 256 bits are data:
Payload = 7.680 Gbps
Front Ends connect to “e-links”
The fiber protocol includes “Forward Error Correction”
Downlink runs at 2.56 Gbps
  Downlink frame is 64bit wide, of which 32 bits are payload
  1.28 Gbps payload
  Up to 16 e-links @ 80 Mbps
Uplink runs at either 10.24 Gbps or 5.12 Gbps
  Uplink frame is either 128bit or 256bit
  256bit frame contains 192bits of payload (7.68 Gbps)
  Up to 24 e-links at either 160 Mbps or 320 Gbps

## Slide 22: MOSAIX Interfaces in the Left End Cap (LEC)
Supplies
I/Os
Supplies
I/Os
Supplies
I/Os
Supplies
Supplies
Supplies
All I/Os are differential
8x 10.24 Gb/s data outputs
1x clock at 160 MHz
2x slow control buses at 5 Mbps (General SC and Power Management)
2x synchronization signals (SYNC and GRST)
(slow controls: 2 links up; 1 clock, 4 links, and 1 spare down)
Global analog and digital supplies per segment
On-chip supply segmentation and control
Reverse biasing of substrate (PSUB)
down
down
down
down
down
down
up
up
Slow control

## Slide 23: ITS3 Flex PC Design: Inspiration for SVT IB FPC design

## Slide 24: Inner Barrel Readout Electronics (inspired by ITS-3 DSE)
Global Timing Unit
(GTU)
FELIX
(DAM Board)
Radiation Area
Counting House
Data : 4 HS lines connected to 1 VTRx+ -> Fiber bundle
VTRx+
lpGBT
5 Mbps
Data
Data
Data

## Slide 25: Inner Barrel Readout Electronics (inspired by ITS-3 DSE)
Global Timing Unit
(GTU)
FELIX
(DAM Board)
Radiation Area
Control
Data : 4 HS lines connected to 1 VTRx+ -> Fiber bundle
Slow Controls: uses lpGBT e-links for one-to-one connection with the LEC SC signals
lpGBTs are also used to control and monitor RDO electronics itself
lpGBTs are connected to individual VTRx+ for fiber up and downlink
VTRx+
lpGBT
5 Mbps
Counting House

## Slide 26
Outer Barrel & Disk LAS Readout

## Slide 27: Outer Barrel and Disk Readout Electronics
Up to 4 LAS connect their H/S data to one VTRx+
Disks & Staves:
VTRx+
Fiber up
H/S Data
LAS
LAS
LAS
LAS

## Slide 28: Outer Barrel and Disk Readout Electronics
Up to 4 LAS connect their H/S data to one VTRx+
Slow Controls is provided via lpGBT e-links to a SC bus
One e-link provides SC to a group of up to four EIC-LAS
Each SC e-link has 3 signals: Clock, SC_in, SC_out
SC up/down
VTRx+
&
lpGBT
Fiber up/down
elink 1
elink 2
elink 16
….
….
SC up/down
SC up/down
Disks & Staves:
VTRx+
Fiber up
H/S Data
LAS
Slow Ctrl
LAS
Slow Ctrl
LAS
Slow Ctrl
Slow ctrl
LAS
LAS
Slow Ctrl
LAS
Slow Ctrl
LAS
Slow Ctrl
LAS
Slow ctrl
LAS
Slow Ctrl
LAS
Slow Ctrl
LAS
Slow Ctrl
LAS
Slow ctrl

## Slide 29
SVT Readout Numbers

## Slide 30: SVT Hit Rate Simulations
10x100 GeV ep,
4.48 x 1033 cm-2s-1, 184 kHz DIS event rate
10 GeV SR
10 GeV e-beam gas, 10000 Ahr
100 GeV proton-beam gas, 100 Ahr
 | Hit Rate (Hz) | Area (cm2) | Hits/s/cm2
L0 | 4.50E+06 | 610.73 | 7.37E+03
L1 | 4.85E+06 | 814.30 | 5.96E+03
L2 | 1.41E+06 | 2035.75 | 6.93E+02
L3 | 8.55E+05 | 9160.88 | 9.33E+01
L4 | 8.89E+05 | 22167.08 | 4.01E+01
 | Hit Rate (Hz) | Area (cm2) | Hits/s/cm2
ED0 | 3.66E+05 | 1767.11 | 2.07E+02
ED1 | 4.00E+06 | 5368.16 | 7.45E+02
ED2 | 3.97E+06 | 5536.32 | 7.17E+02
ED3 | 3.74E+06 | 5532.26 | 6.76E+02
ED4 | 3.35E+06 | 5524.62 | 6.06E+02
 | Hit Rate (Hz) | Area (cm2) | Hits/s/cm2
HD0 | 3.92E+06 | 1767.11 | 2.22E+03
HD1 | 4.45E+06 | 5368.16 | 8.29E+02
HD2 | 4.48E+06 | 5533.75 | 8.10E+02
HD3 | 3.83E+06 | 5513.51 | 6.95E+02
HD4 | 3.25E+06 | 5486.76 | 5.92E+02

## Slide 31: SVT by the numbers
 | width (mm) | length (mm) |  | # pixels per RSU |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Reticle size | 19.564 | 21.666 |  | 827,424 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Pixel size | 0.0208 | 0.0228 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Barrel |  |  |  |  | Sensor |  |  |  |  |  |  |  |  |  |  |  |  | 10x275GeV | 
Layer Index | radius (mm) | z (mm) |  | Area (mm^2) | reticles in width | reticles in length | # of sensors in r-phi | # of sensors in z |  | # pixels | # sensors | Notes | # Readout Links | # Staves | # Data VTRx+ | # SC lpGBTs |  | Hit Rate / s | Hits/pixel/2us frame
L0 | 36 | 260 |  | 58,811 | 3 | 12 | 4 | 1 |  | 119,149,056 | 4 | bent ITS3 | 96 |  | 24 | 5 |  | 2.73E+07 | 4.26E-07
L1 | 48 | 260 |  | 78,414 | 4 | 12 | 4 | 1 |  | 158,865,408 | 4 | bent ITS3 | 128 |  | 32 | 7 |  | 2.94E+07 | 3.44E-07
L2 | 120 | 260 |  | 196,035 | 5 | 12 | 8 | 1 |  | 397,163,520 | 8 | bent ITS3 | 320 |  | 80 | 17 |  | 8.55E+06 | 4.01E-08
L3 | 270 | 520 |  | 882,158 | 1 | 6 | 96 | 4 |  | 1,906,384,896 | 384 | 6 -RSU LAS | 384 | 48 | 96 | 8 |  | 5.19E+06 | 5.06E-09
L4 | 420 | 840 |  | 2,216,706 | 1 | 5 | 148 | 8 |  | 4,898,350,080 | 1184 | 5-RSU LAS | 1184 | 74 | 296 | 25 |  | 5.39E+06 | 2.05E-09
e-endcap |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Disk index | z (mm) | inner r (mm) | outer r (mm) |  |  | 5-RSU LAS | 6-RSU LAS |  |  |  |  |  |  | Readout Groups |  |  |  |  | 
ED0 | -250 | 36.76 | 240 | 176,710 |  | 56 | 40 |  |  | 337,588,992 | 96 | 5-RSU LAS | 96 | 26 | 26 | 3 |  | 2.22E+06 | 1.22E-08
ED1 | -450 | 36.76 | 415 | 536,815 |  | 334 | 0 |  |  | 1,381,798,080 | 334 | 5-RSU LAS | 334 | 96 | 96 | 8 |  | 2.43E+07 | 3.27E-08
ED2 | -650 | 36.76 | 421.4 | 553,632 |  | 334 | 0 |  |  | 1,381,798,080 | 334 | 5-RSU LAS | 334 | 96 | 96 | 8 |  | 2.41E+07 | 3.24E-08
ED3 | -850 | 40.0614 | 421.4 | 552,835 |  | 334 | 0 |  |  | 1,381,798,080 | 334 | 5-RSU LAS | 334 | 96 | 96 | 8 |  | 2.27E+07 | 3.05E-08
ED4 | -1050 | 46.3529 | 421.4 | 551,127 |  | 334 | 0 |  |  | 1,381,798,080 | 334 | 5-RSU LAS | 334 | 96 | 96 | 8 |  | 2.03E+07 | 2.74E-08
h-endcap |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Disk index |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HD0 | 250 | 36.76 | 240 | 176,710 |  | 56 | 40 |  |  | 337,588,992 | 96 | 5-RSU LAS | 96 | 26 | 26 | 3 |  | 2.38E+07 | 1.31E-07
HD1 | 450 | 36.76 | 415 | 536,815 |  | 334 | 0 |  |  | 1,381,798,080 | 334 | 5-RSU LAS | 334 | 96 | 96 | 8 |  | 2.70E+07 | 3.63E-08
HD2 | 700 | 38.52 | 421.4 | 553,216 |  | 334 | 0 |  |  | 1,381,798,080 | 334 | 5-RSU LAS | 334 | 96 | 96 | 8 |  | 2.72E+07 | 3.66E-08
HD3 | 1000 | 53.43 | 421.4 | 548,909 |  | 334 | 0 |  |  | 1,381,798,080 | 334 | 5-RSU LAS | 334 | 96 | 96 | 8 |  | 2.32E+07 | 3.13E-08
HD4 | 1350 | 70.14 | 421.4 | 542,422 |  | 334 | 0 |  |  | 1,381,798,080 | 334 | 5-RSU LAS | 334 | 96 | 96 | 8 |  | 1.97E+07 | 2.65E-08
TOTAL |  |  |  | 8,161,315 |  |  |  |  |  | 19,209,475,584 | 4448 |  | 4976 |  | 1348 | 132 |  | 2.90E+08 | hits/s
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 34.61 | Gbps
 |  |  |  |  |  |  |  |  |  | # of segments: | 4500 |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | # of SC links down | 22500 |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | # of SC links up | 9000 |  |  |  |  |  |  |  | 
… plus noise

## Slide 32
SVT Readout Prototype Developments

## Slide 33: SVT Prototype Developments
A full setup with lpGBT, VTRx+, and FPGA development boards (stand-ins for FELIX) exists at ORNL for evaluation of the various RDO components.
Alternatives to CERN’s lpGBT universe of components using commercial alternatives are being investigated.
First results with these setups have been achieved in the context of an R&D project concerned with the Silicon using EIC project funds.
  Evaluation of the Samtec Optical FireFly as an alternative to VTRx+
  Evaluation of the Microchip PolarFire FPGA as a radiation-tolerant FPGA replacement of the lpGBT
Evaluation of Aggregator Board architectures with commercial FPGA development boards has been started at MIT in the context of the Silicon R&D project.
A test setup for the characterization of CERN Engineering Run chiplets to be used in the MOSAIX and LAS designs is under development.
Investigations on Redundancy issues on the LAS design interfaces has started.
Work is ongoing on defining the details of the LAS physical and protocol interfaces.

## Slide 34: Commercial Alternatives: FireFly & PolarFire

## Slide 35: eRD104 Test Setups
Raspberry Pi for programming and monitoring lpGBT
VLDB+
Zync devel board running GBT-FPGA
VTRx+
lpGBT
Samtec FireFly Eval Board
SiliconLabs Clock Generator Eval Board
PolarFire Gigabit Transceiver Test Setup
lpGBT Test Setup with Samtec FireFly (VTRx+ alternative), Xilinx Ultrascale FPGA evaluation board (“FELIX), and SiliconLabs Clock Generator Board (“GTU”)
Samtec FireFly Test Setup with Fiber Loopback

## Slide 36: Selected Test Results:
Purple: M1 = CLK+ (red) - Clk- (blue)
TIE Source : M1
Clock TIE measurement sigma = 3.36ps
Scope Picture of “Phase Adjustable” recovered clock out of lpGBT
FireFly “Eye” measurement @ 14 Gbps
Bit Error Rate (BER) Measurements

## Slide 37: Summary
An SVT Readout Design has been developed and demonstrated here
Inner Barrel RDO based on ALICE ITS-3 Service Electronics Board Design
  Direct connection of multiple HS data serializers per segment to VTRx+
  One-to-One connection between lpGBT e-links and LEC signals for slow controls
  Direct powering of wafer scale sensor
Outer Barrel RDO concept uses a concept of LAS Readout groups
  Group of up to 4 Single HS Data lines are directly connected to VTRx+
  Slow Controls multiplexed between groups of 4 LAS via AncASICs on each LAS on a single bus
Prototype Setups are being investigated with evaluation boards of various components
  First results have already been shown running all components at the full desired speeds and show that sufficient performance is achieved

## Slide 38
Backup Slides

## Slide 39: “MOSAIX” Stitched Sensor for SVT Inner Barrel
Layer 0: 12 x 3 repeated units + endcaps
Layer 1: 12 x 4 repeated units + endcaps
Layer 2: 12 x 5 repeated units + endcaps
Repeated (Stitched) Sensing Unit (RSU)
SEGMENT
Sensitive z-length
Physical z-length
wafer

## Slide 40: MOSAIX Stitched Sensor Detail
Supplies
I/Os
Supplies
I/Os
Supplies
I/Os
Supplies
Supplies
Supplies
12 x Repeated Sensor Unit
RSU
SEGMENT

## Slide 41: Half Repeated Sensor Unit
Each Half Unit is segmented in Tiles (Domains)
Each tile acts as an independent sensor
Separate Local Power
Configuration
Readout Link (160 Mb/s)
Each Tile data output has direct connection to the left endcap

## Slide 42: Tile Readout Scheme
16 bits
16 bits
16 bits

## Slide 43: Pixel Array Readout Architecture
20.8 μm x 22.8 μm pixel pitch
Continuously active front-end (40 nW typ.)
Global shutter
Zero-suppressed matrix readout
Continuous readout mode
Integration time: 2 / 5 / 10µs
In pixel:
Amplification
Discrimination
Hit integration register
readout register
Test charge injection
Digital pulsing
Masking
442 x 156 pixels / domain
827,424 pixels per RSU
144 domains / segment
9.929 Mpixels / segment
156 columns
442 rows

## Slide 44: ePIC SVT: “Large Area Sensor” (LAS)
Inner Barrel (Layers 0,1,2) will reuse ITS3-like sensors as is
  Layer 0: 4 sensors in r-phi, 3 segments of 12 RSU
  Layer 1: 4 sensors in r-phi, 4 segments of 12 RSU
  Layer 2: 8 sensors in r-phi, 5 segments of 12 RSU
EIC variant for the Outer Barrel ( Layers 3,4) and Endcap Disks
  “Large Area Sensor” (LAS)
  Will be stitched, but not to wafer scale
  Likely 1 Segment of 5 or 6 RSU (no need for right endcap)
  The intention is to multiplex Tile data lines to 1 High-Speed output
  More conventional carbon composite mechanical support with integrated cooling
Supplies
I/Os
5/6x
X
36x
36x
1x
36x
36x
1x
MUX
6-RSU LAS
No Supplies
Backup

## Slide 45: VTRx+ Front-end Module