## Slide 1: Silicon: Cooling
Nicole Apadula
Lawrence Berkeley National Laboratory
SVT Layers & Discs Co-Convener

## Slide 2: Charge Questions Addressed
Are the technical performance requirements appropriately defined and complete for this stage of the project?
Are the plans for achieving detector performance and construction sufficiently developed and documented for the present phase of the project?
Are the current designs and plans for detector, electronics readout, and services sufficiently developed to achieve the performance requirements?
Are plans in place to mitigate risk of cost increases, schedule delays, and technical problems?
Are the fabrication and assembly plans for the various tracking detector systems consistent with the overall project and detector schedule?
Are the plans for detector integration in the EIC detector appropriately developed for the present phase of the project?
Have ES&H and QA considerations been adequately incorporated into the designs at their present stage?

## Slide 3: Outline
Overview/Introduction
  Baseline design
  Sensor power
SVT Cooling
  Inner Barrel
  EIC-LAS cooling
    Outer Barrel
    Endcaps
  System
Summary

## Slide 4
Overview

## Slide 5: SVT Material Overview
Minimized material  mechanics, cooling, power, readout, etc.
Charge 1
Target Specifications
IB
  L0 - L2: 0.05% X/X0
OB
  L3: 0.25% X/X0
  L4: 0.55% X/X0
Endcaps
  ED0-4: 0.25% X/X0
  HD0-4: 0.25% X/X0
Outer Barrel (OB)
Inner Barrel (IB)
Electron/Hadron Endcaps (EE, HE)
Cooling has a big impact on X/X0

## Slide 6: Material Implications
Water cooling pipe: 1 mm ID tube made with 25 mm Kapton walls is ~0.3% X/X0
Average X/X0 of water will be less
  Dependent on number of pipes & coverage
  Non-homogenous material distribution
Difficult to reach target material budget with liquid cooling alone
Air <0.01% X/X0 for relevant thicknesses
Charge 1, 2

## Slide 7: Baseline design
4000 EIC-LAS sensors in the SVT
  Power consumption based on best estimates: up to 1.6 W per EIC-LAS
  Paired with an Ancillary chip (AncASIC) for slow control, serial powering
Baseline cooling design is air  liquid cooling in strategic places as necessary
End goal is operation of sensor at/near room temperature
Measure thermal performance with DT = Tsensor – Tinlet air
“Reasonable” DT is one that achieves room temperature operation with sensible air inlet temperature
  DT < 10°C is used often as a “standard”, but is not a requirement
Charge 1, 3

## Slide 8: Sensor Power Regions
+
IB sensor: MOSAIX
OB/HE/EE sensor: EIC-LAS
LEC: ~0.8 W/cm2
12 RSUs: up to 40 mW/cm2
EIC-LAS LEC ≤ MOSAIX LEC
5-6 RSUs: same power density as MOSAIX
AncASIC:
Size & power TBD
Charge 1

## Slide 9: Sensor Power
Power consumption estimates for LEC & RSUs based on publicly available information  continuing effort with sensor designers
Investigated a range of values for cooling tests/calculations
ER2 crucial for more finite power numbers
LEC:
Highest power density
RSUs: Low power density
Charge 1

## Slide 10
SVT Cooling

## Slide 11: Inner Barrel
Baseline: Air cooling with thermally conductive carbon foam near LEC
  Measurements from ALICE ITS3 show this is reasonable to cool sensor
Forced convection between L0 & L1
L2: Natural convection paired with liquid cooling near LEC (as necessary)
Air inlet and outlet under design
Charge 3

## Slide 12: Beam-pipe Bake-out
Beam-pipe bake-out with SVT installed
Aiming for no additions to cooling
  No extra material (e.g. insulators) or changes (i.e. liquid instead of air)
ANSYS studies at JLab and LBNL
  Flow N2 in beam-pipe to get inner wall >100°C
  Room temperature air between beam-pipe and silicon
  Studies done with both full length of beam pipe and shortened section near SVT IB
Bench setup at JLab verifies results
  Covers 1 m of 3 m Be beam pipe section
Path forward to cool detector
Charge 1, 3

## Slide 13: Beam-pipe Bake-out
Refine temperature envelopes for materials
  ALPIDE (ITS2) can work reliably at 40°C
  Estimates from climate chamber studies at LBNL up to 50°C show 65 nm DPTS performs reliably
Initial thermoelastic study done by ALICE ITS3
  16 cycles between 10 – 48°C on ITS3 layer 2 (includes glue, foam, silicon)  no failures
Similar thermoelastic study upcoming for ePIC SVT IB
  Cycle test, longevity test, bake-it-til-you-break-it test
Charge 1, 3

## Slide 14: Air cooling
Air cooling internal to the mechanical structure offers advantages (air routing, mechanical strength)
Built on previous LBNL LDRD with carbon composite structures and RVC or CVD (thermally conductive) carbon foam
Heaters with two regions to model SVT sensor power dissipation (LEC & RSUs)
DT reasonable (<10°C) to achieve operating temperature, but structure is material “heavy”
Can build upon this concept
*Air velocity calculated at duct
~1 W/cm2
~40 mW/cm2
Charge 2, 3
LEC only

## Slide 15: Outer Barrel
Baseline design has options for both air and liquid cooling
Crossribs  thermally conducting carbon foam
Edges  carbon foam, could contain liquid cooling pipe
Assumptions/Estimates
  4 x 0.5 cm2 cross section
  8 m/s air speed
Max estimate: 400 cfm total
  Work ongoing that can reduce this (liquid, re-routing air, etc.)
Charge 2, 3

## Slide 16: Discs: Corrugated Carbon Fiber
Baseline disc design using corrugated carbon fiber
  Provides a channel for forced air convection
Air cooling sufficient for RSUs
LEC trending in the right direction
LEC: 1 W/cm2
RSUs: 40 mW/cm2
Charge 2, 3

## Slide 17: Discs: Corrugated Carbon Fiber
Studied a range of LEC power densities
DT reasonable for power < 0.6 W/cm2
Charge 2, 3

## Slide 18: Discs: Corrugated Carbon Fiber
Studied a range of LEC power densities
DT reasonable for power < 0.6 W/cm2
DT scales with power density
Charge 2, 3

## Slide 19: Discs: Corrugated Carbon Fiber
Studied a range of LEC power densities
DT reasonable for power < 0.6 W/cm2
DT scales with power density
Carbon foam under LEC provides 10-20% reduction in DT
  Caveat: this is insulating foam. Will be measured with thermally conductive foam
Charge 2, 3

## Slide 20: Discs: Corrugated Carbon Fiber
Center manifold and air metering strip through middle
Volumetric static temperature of air minimal
  Air can be used in multiple channels  reduces total air volume
Under further optimization
Static Temperature of Cooling Channel Outlet at a Velocity of 10 m/s
Max = 34°C
Air in = 25°C
Charge 2, 3

## Slide 21: Discs: Corrugated Carbon Fiber
Corrugated Disc of 6 mm Height – Rev 2 (Mesh size = 2 mm)
Charge 2, 3

## Slide 22: SVT Air
Current baseline estimates
IB: 50 cfm
OB: max 400 cfm
Discs: max 500 cfm
Total system as we understand it is ~1000 cfm
  Requires compressed air
Optimization continues and we expect this number to go down
Charge 6

## Slide 23: EH&S
All work follows local laboratory EH&S requirements & training
  LBNL: ISM, Work Planning & Control
  JLab: ISM, Task List and ePAS (JLab-PR-725)
  NRTL listed electrical equipment
Overall System
Temperature interlock  work with slow control group to ensure detector safety
  Automatic turn-off if temperature goes above designated value
Pressure system  work with engineers for design and safety
  Also monitored with slow control if air system fails (over-temperature)
Liquid/water cooling  flow under atmospheric pressure designed to prevent leaks
  Cooling plant, temperature, flow, etc. monitoring
Charge 6, 7

## Slide 24: Summary
Baseline cooling design is hybrid with the dominant part done by air for material considerations
End goal is operation of SVT at/near room temperature
Thermal performance studied with a range of power dissipation values based on current sensor knowledge
EH&S
  Following local laboratory requirements & training
  Work with system engineers and slow control for monitoring and interlocks
Next Steps
  Incorporating additional heat generating components (AncASIC, RDOs)
  Continuing design of individual components and overall system