## Slide 1: Tracking Systems Overview and Requirements
Brian Eng
Jefferson Lab
L3 CAM

## Slide 2: Charge Questions Addressed
Are the technical performance requirements appropriately defined and complete for this stage of the project?
Are the plans for achieving detector performance and construction sufficiently developed and documented for the present phase of the project?
Are the current designs and plans for detector, electronics readout, and services sufficiently developed to achieve the performance requirements?
Are plans in place to mitigate risk of cost increases, schedule delays, and technical problems?
Are the fabrication and assembly plans for the various tracking detector systems consistent with the overall project and detector schedule?
Are the plans for detector integration in the EIC detector appropriately developed for the present phase of the project?
Have ES&H and QA considerations been adequately incorporated into the designs at their present stage?

## Slide 3: Outline
Requirements
Interfaces
Tracking Detector Layout
Risks
Safety
Summary

## Slide 4: Requirements
https://eic.jlab.org/Requirements/index.html
Charge 1
 | Momentum Resolution | Spatial Resolution
Backward (-3.5 to -2.5) | ~0.10%×p⊕2.0% | ~ 30/pT µm ⊕ 40 µm
Backward (-2.5 to -1.0) | ~ 0.05%×p⊕1.0% | ~ 30/pT µm ⊕ 20 µm
Barrel (-1.0 to 1.0) | ~0.05%×p⊕0.5% | ~ 20/pT µm ⊕ 5 µm
Forward (1.0 to 2.5) | ~0.05%×p⊕1.0% | ~ 30/pT µm ⊕ 20 µm
Forward (2.5 to 3.5) | ~0.10%×p⊕2.0% | ~ 30/pT µm ⊕ 40 µm

## Slide 5: Interfaces
https://eic.jlab.org/Interfaces/InterfaceMatrix.html
  Outer barrel limited by DIRC
  Disks limited by pfRICH/AC-LGAD
  Inner Barrel first vertex layer 5mm from beampipe
Charge 1

## Slide 6: Interfaces – Beam Pipe
Unique beampipe
  Tapered beampipe, tracking detectors must be installed prior to beampipe installation in central detector
  Beampipe exposed to ambient prior to installation
  Need min 100°C in beampipe to break H2O bonds
    Silicon detector epoxy limited to ~30°C due to CTE
Charge 1

## Slide 7: Tracking Detector Layout Modifications
Low number of hits in certain rapidity ranges
  Need more planes
Solve impact from 5 (2) μs MAPS frame accumulation time
  Need enough hits from fast detectors to form a tracklet with a good pointing resolution
  Need to utilize ToF and maybe Barrel-ECal AstroPix as possible
    Note: Barrel ToF has good time resolution but not spatial resolution
Current layout finalized in June 2023
Charge 2, 3

## Slide 8: Tracking Detector Layout
Silicon
MPGD
ToF
  Part of PID

## Slide 9: Simulation – Nhits vs η
Only tracking detectors included, will improve further once calorimeters included which should remove dip at rapidity ±1

## Slide 10: Silicon
MAPS (monolithic active pixel sensors) in 65 nm CMOS technology, developed with ALICE ITS3 collaboration
  Inner Barrel: Directly use ITS3 wafer scale sensor
  Outer Barrel: EIC Large Area Sensor (LAS), modification of ITS3 sensor
EIC Project, Silicon Consortium and CERN ALICE/ITS3 meeting in Q2 23
  Path forward on collaboration (paperwork in process), EIC hiring 2 engineers to work directly with ALICE team on sensor development

## Slide 11: Silicon – Inner Barrel
Three layers of thin, bent, wafer scale ITS3 based sensors
ITS3 concept adapted to ePIC radii
X/X0 % = 0.05
Layer | Radius (mm) | Length (mm) | Segments
L0 | 36 | 270 | 3
L1 | 48 | 270 | 4
L2 | 120 | 270 | 5

## Slide 12: Silicon – Outer Barrel
Traditional stave design
Layer | Radius (mm) | Length (mm) | X/X0%
L3 | 270 | 540 | 0.25
L4 | 420 | 840 | 0.55

## Slide 13: Outer Barrel – MPGD
Micromegas
  Additional Tracking Points
Single Tile
  51.25 x 44 cm
  Simplifies production
  40 Tiles Total
  ~30k Channels
uRWELL
  Provides hits for DIRC
Capacitive-sharing 45° U-V strips
  Pitch: 1.2 mm pitch
  ~140k Channels

## Slide 14: Forward / Backward Disks – Silicon
Foundry rule/limitation, need to limit number of sizes (2-3 total)
  Direct outcome from meeting with ALICE

## Slide 15: Forward / Backward Disks – MPGD
uRWELL Capacitive-sharing 45° r-phi strips
Pitch: 1.2 mm pitch
~2 × 1570 phi-strips + ~ 2 × 400 r-strips
  ~4k strips per disk (32k channels for 8 disks)

## Slide 16: Services
RED = power
BLUE = cooling/gas
ORANGE = signal
Charge 3

## Slide 17: Services
Charge 3
Subsytem | Type | Item | Material | Quantity | Diameter (cm) | Cross Area (cm^2) | +50% Packing for Bundles | Average Length (in)
Red Path IP to pfRICH Inner face |  |  |  |  |  |  |  | 
Vertex Silicon | Power | 18 awg LV Sagita | Aluminium | 12 | 0.8 | 6.03 | 9.05 | 120.00
 | Signal | Signal Bias |  | 34 | 0.2 | 1.07 | 1.60 | 120.00
 | Signal | Data * |  | 204 | 0.6 | 57.68 | 86.52 | 120.00
 | Cooling | * |  | 12 | 0.3 | 0.85 | 1.27 | 
Sagita Silicon | Power | LV serial power |  | 29 | 0.9 | 18.45 | 27.67 | 
 | Signal | Signal Bias |  | 771 | 0.3 | 54.50 | 81.75 | 
 | Signal | Data * |  | 771 | 0.2 | 24.22 | 36.33 | 
 | Cooling | Cooling Pipes * |  | 356 | 0.3 | 25.16 | 37.75 | 
Silicon Disks | Signal | Sensor Bias | Aluminium | 1100 | 0.3 | 77.75 | 116.63 | 120.00
 | Cooling | cooling | tygon | 550 | 0.63 | 171.45 | 257.17 | 120.00
 | Power | LV current | Aluminium | 92 | 0.9 | 58.53 | 87.79 | 120.00
 | Signal | Data |  | 1100 | 0.3 | 77.75 | 116.63 | 
Inner MPGD | Signal | FEE Data | Firefly | 60 | 1 | 47.12 | 70.69 | 120.00
 | Power | Hv |  | 40 | 0.32 | 3.22 | 4.83 | 120.00
 | Power | Lv |  | 20 | 1.163 | 21.25 | 31.87 | 120.00
 | Cooling | Gas | Polyethylene | 20 | 0.4 | 2.51 | 3.77 | 120.00
 | Cooling | Cooling | Polyurethane | 33 | 0.63 | 10.29 | 15.43 | 120.00
EE MPGD Disks | Power | FEE PWR | 20 awg (3 pair) | 11 | 1 | 8.64 | 12.96 | 120.00
 | Signal | FEE data | Fibers | 128 | 0.32 | 10.29 | 15.44 | 120.00
 | Power | 2kv Hv | Coax | 4 | 0.24 | 0.18 | 0.27 | 120.00
 | Signal | Flat Signal Cables |  | 128 | 0.3 | 76.80 | 115.20 | 120.00
 | Cooling | Gas | Tygon | 8 | 0.4 | 1.01 | 1.51 | 120.00
 | Cooling | Cooling | Tygon | 16 | 0.63 | 4.99 | 7.48 | 120.00
Inner most trackers cable path towards Lepton end
~71% space used

## Slide 18: Cost / Schedule
Inner Barrel Silicon (ITS3)
  ER2 – Q1 24
Outer Barrel/Disk Silicon (LAS)
  2025-2027
Stave/Disk Construction Complete
  Q4 28
Ready for integration
  Q2 29
Cost / Schedule is based on engineering estimates from detector experts
Charge 5

## Slide 19: Risks
Currently for the silicon trackers there is a planned engineering run during R&D with the production run taking place during PED
Benefit from ALICE ER1 and ER2 runs and that the EIC runs would be based on the final ER3 design
However, if unforeseen issues arise another engineering run for the sensors might be needed
  The risk register has a proposed risk (ID RT-6-10-014) if a second engineering run is needed which would use contingency
CD-3A Director’s Review comment: “Upfront discussion of risks of R&D not coming to a favorable conclusion, and mitigation plans in this case, should be more clearly documented and presented. Where appropriate, for example for the tracking detector, more detailed plans should be developed.”
  Silicon detectors have external dependency on ITS3 sensors
  See backup slides for alternative layout discussion
Charge 4

## Slide 20: Safety
Generally the tracking WBS is in the design phase and and such doesn’t have any safety issues
However, there are a few test stands being developed which follow their institution’s safety protocols
  Protocols include required training
  LBNL testing carbon foam cooling: ISM, documented in Work Planning & Control
  JLAB testing beampipe bake-out: ISM, Task List and ePAS (JLab-PR-725)
Equipment going in the BNL Experimental Hall must follow NEC/NFPA 70E, 2021 and electrical safety guidelines: DOE-HDBK-1092-2013
  Defines voltage hazards, cable type requirements, circuit protection, etc
  Equipment must be NRTL listed or approved by BNL Electrical Equipment Inspection program
Charge 7

## Slide 21: Summary
Recent design change to address performance issues, which has been incorporated into the ePIC collaboration’s latest models
Cost and schedule developed with input from ePIC collaborators and ALICE/ITS3 efforts
  Scope change request for additional personnel based on discussions from CERN visit in progress.
Tracking WBS is in the final design stage no major ES&H issues
  Test stands follow the relevant institution’s policies.
Proposed risk added to register for additional engineering runs of silicon sensors

## Slide 22
Backup

## Slide 23: Collaboration

## Slide 24: Alternative Tracker
Goal is always to progress towards using ITS3 based sensors
  Only way to meet full performance requirements
Branchpoints – both based on schedule delays
ITS3 (inner barrel) schedule remains compatible with project schedule but LAS (outer barrel & disks) development is delayed
ITS3 (inner barrel) schedule becomes incompatible with project schedule

## Slide 25: Alternative Tracker – Layout
Hadron and Electron Endcap Disks (HE, EE)
Outer Barrel (OB)
Inner Barrel (IB)
Replaced with two MPGD barrel layers derived from the outer MPGD tracker, specifically its innermost (Micromegas) layer
Branchpoint 1 & 2
Replaced by two or three layers based on the existing ITS2 sensor, as used in ALICE and sPHENIX without EIC specific modifications
Branchpoint 2 only
Replaced with (in total up to) seven near-identical MPGD disks on each side, specifically based on existing uRWELL disks
Branchpoint 1 & 2

## Slide 26: Alternative Tracker – Schedule
Will be further refined leading up to CD-2 based on ITS3 development
Branchpoint | Date | Milestones
1 (LAS Delay) | Q2/Q3 2026 | 1 year for MPGD foils + 3 years construction
2 (ITS3 Delay) | Q3/Q4 2027 | Same 3 years construction as current IB
CD-3
04/2025
Apr 2031
early CD-4
09/2032
CD-4
09/2034
Detector Assembled and Ready for Cosmic Data Taking
Start of
Operations
&
Science
Construction
Oct 2028
IR-6 ready
for installation
June 2030
Barrel Detectors
installed
Oct 2030
Hadron Endcap
Detectors
installed
Jan 2031
Electron Endcap Detectors installed
Early start of
Operations
&
Science
Pre-OPS