## Slide 1: Tracking Simulation/Reconstruction
Matt Posik
Temple University
Deputy Technical Coordinator

## Slide 2: Charge Questions Addressed
Are the technical performance requirements appropriately defined and complete for this stage of the project?
Are the plans for achieving detector performance and construction sufficiently developed and documented for the present phase of the project?
Are the current designs and plans for detector, electronics readout, and services sufficiently developed to achieve the performance requirements?
Are plans in place to mitigate risk of cost increases, schedule delays, and technical problems?
Are the fabrication and assembly plans for the various tracking detector systems consistent with the overall project and detector schedule?
Are the plans for detector integration in the EIC detector appropriately developed for the present phase of the project?
Have ES&H and QA considerations been adequately incorporated into the designs at their present stage?
Grey out charge text not being addressed.
GRY RGB HEX CODE: #BFBFBF

## Slide 3: Outline
Software Framework
ePIC Tracking Detector in DD4HEP
  Coverage
  Detector Hits
  Material and Detector Response
Reconstruction
  Workflow
  Seeding
  Tracking Performance
  Tracking in Background
  Vertex Reconstruction
Summary

## Slide 4: Software Framework
Geometry Framework (epic)
  Material and segmentation
  Based on DD4HEP
Reconstruction Framework (EICRecon)
  Based on PODIO/JANA
  Digitization
  Track Reconstruction
    Based on ACTS Combinatorial Kalman Filter (CKF)
    Combined track finding and fitting
    Realistic seeder
ePIC data structure (EDM4eic) modeled after EDM4hep
Charge 2, 3
A Common Tracking Software

## Slide 5: ePIC Tracking Detector in DD4HEP
Charge 2, 3
RWELL-ECT
RWELL-BOT
CyMBaL
AC-LGAD Barrel
AC-LGAD Endcap
SVT Barrels
SVT
SVT Endcaps
SVT Endcaps
RWELL-ECT
electron
proton

## Slide 6: Coverage
Charge 2, 3
GEANT-level tracker hits showing geometric coverage
ePIC 24.2.1
ePIC 24.2.1
electron
proton

## Slide 7: Tracker Hits
Charge 2, 3
Previous configuration
Current configuration
Additional MPGD layers increased number of hits
  Extreme see hits increasing from ~3 to 5
  Hits vs. (Generator Level)

## Slide 8: Tracker Hits: Current Configuration
Charge 2, 3
Additional MPGD layers increased number of hits
  Current configuration
  Hits vs. (Generator Level)

## Slide 9: Detector Material and Response
Detector Response
  Segmentation implemented as to reproduce expected hit resolution
  Digitization based on deposited energy in detector
  Spatial resolutions used in simulation:
Charge 2, 3
ePIC 24.2.1
electron
proton
Detector | Resolution [
SVT Detectors | 5.8
MPGD Detectors | 150
AC-LGAD Barrel | 28.9 x 2,890
AC-LGAD Endcap | 28.9 x 289
Detector | 
SVT Detectors | 5.8
MPGD Detectors | 150
AC-LGAD Barrel | 28.9 x 2,890
AC-LGAD Endcap | 28.9 x 289

## Slide 10: Reconstruction Framework
Charge 2, 3
Sim Hits
Tracker Hits
Digitization
MCparticle
DD4hep
Track finding / fitting (CKF)
Initial Track Params
Trajectory
Track Params
Trak Segment
…
Seed Finder
(triplet)
Primary
Vertexing
Ambiguity Solver
Track Measurements
* Material map
Track Seed
Raw Hits
Truth seed
Real seed

## Slide 11: Track Seeding
Realistic track seeding done using ACTS orthogonal seeder algorithm
  Realistic seeded results consistent with truth seeded results
Tracking studied with generated vertices spanning the beam spot width ()
  Reasonable results for
  Efficiency gaps seen near the edge of the beam spot ()
  Off-beamline () are also reasonable
Additional seed-finder parameter tuning ongoing
Charge 2, 3
Realistic Seed
Truth Seed

## Slide 12: Track Seeding: Realistic Seeding
Charge 2, 3

## Slide 13: Preliminary Tracking Performance: Momentum Resolution
Single particle (*includes AC-LGAD systems, update real seed)
Charge 2, 3
Backward
Forward
Central

## Slide 14: Preliminary Tracking Performance: Pointing Resolution
Single particle (*includes AC-LGAD systems, update to real seed)
Charge 2, 3
Backward
Forward
Central

## Slide 15: Structure for Tracking in Background
HEPMC Admixing code implemented
  merges signal and background files
Considers three main background contributions
  Synchrotron radiation, hadron beam-gas, and electron beam-gas
Charge 2, 3
GEANT/EICRecon
Signal File(s)
Background Files
Merger Code
Analysis

## Slide 16: Tracking in Background
Track reconstruction within a background environment is beginning
DIS signal event:
  ,
Initial exploration of tracking (truth/realistic seeding) in hadron-beam gas background
Charge 2, 3
DIS
Signal
DIS
Signal
Hadron
Admixture
Hadron
Admixture

## Slide 17: Tracking in Background
Ongoing work to:
  Look at other background sources: synchrotron radiation, electron-beam gas, and full background admixture
  Use timing information in track fitting
  Understand better MC Particles that do not get reconstructed
  Pattern recognition algorithm
Charge 2, 3
Yellow=Reconstructed Particles that get matched
Green=MC Particles that get Reconstructed
Red=MC Particles that do not get Reconstructed
Hadron Admixture
Truth Seeded

## Slide 18: Vertex Reconstruction
ACTS Iterative vertex finder algorithm implemented for vertex finding
  Initial vertex reconstruction studies have begun
Vertex object data structure being reviewed for ePIC software framework
Charge 2, 3

## Slide 19: Summary
Reasonable performance in realistic seeded tracking across the beam spot width
  Efficiency drop seen at edge of beam spot being investigated
Preliminary tracking performance with single particles has been assessed
  Current tracker configuration improves upon number of tracker hits, particularly at large
  The tracking system alone meets Yellow Report requirements in some regions, and misses in others
Structure and tools are in place for performing tracking in background environment
  Structure and tools are in place
  On going work to focus on studying impact of background sources,
  implementing timing,
  and pattern recognition algorithm
Vertex reconstruction work has begun
  Initial vertexing algorithm in place
  Vertex object being defined for EDM4EIC

## Slide 20: Detector Material
Charge 2, 3
ePIC 24.2.1
electron
proton