## Slide 1: Initial photon detector sim G4
Ciprian Gal

## Slide 2: Setup
1 vacuum detector to select the initial photon information
“Calorimeter”: material PbWO4
  4 x 9mm (~1 radlen) + 1 x 18mm + 1 x 256mm = 310mm
SiO2 1mm planes in between the calorimeter blocks (with 1mm of air on each side) to mock up the material for a tracker
Two simulations were run with two transverse sizes 10x10 cm and 5x5 cm
initial information (vacuum det)
The photons are randomly sampled up to 8 GeV in energy and thrown in a square 3x3 mm square transversely at the center of the block
  Momentum direction is (0,0,1)
Total of 10k events

## Slide 3: Energy reconstruction PbWO4 (10x10cm2)
The first few segments of the calorimeter don’t offer much here but summing all the deposited energy gives some decent energy reconstruction
1 (1radlen)
2 (1radlen)
3 (1radlen)
4 (1radlen)
6 (28radlen)
5 (2radlen)

## Slide 4: Energy reconstruction (5 vs 10 cm) PbWO4
The 5x5 cm2 blocks still have linearity up to 8 GeV however we can certainly see a worse energy resolution
5 x 5 cm
10 x 10 cm

## Slide 5: Energy reconstruction (5cm PbWO4 vs 10cm BaF)
The BaF doesn’t look much worse than the PbWO4
5 x 5 cm PbWO4
10 x 10 cm BaF

## Slide 6: Position reconstruction (PbWO4)
Looking at the different “tracking” planes for e+/- with energies larger than 1 MeV we can see that even the first layer has on average more than 2 particles
We can calculate the position average per event for each of these layers
  For tracker 1 only ~54% of events has events to do the averaging
Averaging is done by calculating average X, average Y and the getting R from the sqrt(<X>^2 + <Y>^2)
All hits
Avg hits

## Slide 7: Averaging tracking layers (PbWO4)
By the 3rd layer (after ~3radlen) we have about 90% of the events being able to properly average

## Slide 8: Averaging tracking layers – initial position (transversely) (PbWO4)
It looks like the best resolution comes after about 3 radiation lengths
The positive side tail may be due to the averaging method -> will do a proper averaging in the future
However we don’t get much worse if we go to 4 or 6 radlens

## Slide 9: Averaging tracking layers – initial position (transversely) (BaF)
BaF simulation was ran with smaller number of tracking layers based on the results from the PbWO4
It looks like the best resolution comes after about 3 radiation lengths
After 4 we get more of the events and similar resolution
3radLen
4radLen
6radLen

## Slide 10: Averaging tracking layers – initial position (transversely) (BaF)
The events with single or no tracks after 3 radLens are mostly for low energy photons -> we probably will have some energy cutoff in the analysis anyway so this problem is probably going to be less significant
3radLen

## Slide 11: Todos
update averaging by calculating average R from individual R positions
fold in the asymmetry information and look at the resolution impacts on asymmetry extractions