## Slide 1: Synchrotron Radiation (SR) background simulation for the EIC
Andrii Natochii
natochii@bnl.gov
Outline
  Introduction
  Past background studies
  New simulation tool
    Benchmark
  SR mask implementation
  Latest findings
  Summary

## Slide 2: Introduction: Tasks
Estimate SR background rates in ePIC and auxiliary detectors at different machine and beam settings (i.e., machine lattice, beam currents, etc.).
If the detectors have a high SR background (t.b.d.), develop a mitigation strategy through machine lattice adjustment, SR mask implementation, and/or additional shielding installation.
Why SR is a concern?
SR photons produce background hits in vertex detectors that hard or even impossible to filter from the physics signal hits
In addition, the radiation damages sensitive equipment, affecting detector components' longevity.

## Slide 3: Introduction: Issues
So far, we did not have a reliable tool to properly model the SR background in the detectors, including:
  high statistics SR photon production;
  SR photon propagation through the vacuum beam pipe with reflection;
  consistent beam pipe geometry modeling in different frameworks.
The final machine lattice is not fixed, and hence, highly dynamic changes in the magnetic field were not reflected in all simulation frameworks in a timely manner.

## Slide 4: Introduction: Solution
A dedicated Monte-Carlo simulation code based on the Geant4 framework was developed to:
  generate high statistics SR photon flux from machine magnets in the interaction region (IR), including the detector solenoid;
  accurately propagate the photons through the vacuum beam pipe following reflection mechanisms on the vacuum-metallic border;
  produce files with absorbed SR photon coordinates within the region of interest.
The beam pipe geometry modeling was made consistent between different background simulation frameworks.

## Slide 5: Past path for SR background data production
Synrad+
Molflow+
Eic-Shell
Sampling
Eic-Recon
Machine lattice and beam parameters
Vacuum pressure
Detector SR background rates

## Slide 6: Past path for SR background data production
Synrad+
Eic-Shell
Sampling
Eic-Recon
Bugs and software limitations
The outdated eic-shell beam pipe geometry does not match the absorbed SR photon distribution generated with one of the latest beam pipe geometries used in Synrad+/Molflow+.
Therefore, the eic-shell modeling was modified to match the central beam pipe (~10 m around the IP).
Absorbed SR photons (color)
Eic-shell material scan (black)
e– beam
h beam

## Slide 7: Past path for SR background data production
Synrad+
Eic-Shell
Sampling
Eic-Recon
Bugs and software limitations
Before v1.4.33 (Dec 2023), Synrad+ did not have the functionality to store absorbed SR photons on the surface of the vacuum beam pipe.
  In addition, a few minor bugs were recently detected in old versions.
  For more details, see the discussion with Synrad+ developers here.
Furthermore, Synrad+ still cannot store the information of absorbed photons for all facets at a time.
  A user must go through each facet, run the simulation for about one minute, and store the data.
  Since the current beam pipe model contains ~30k facets, this approach does not work for our tasks.
  Therefore, we propose the adoption of a new framework – Geant4.

## Slide 8: New SR simulation code
~30 m
~50 m
IP6
e– beam direction
A dedicated Geant4-based code was developed to
  generate SR photons in the magnetic field of the interaction region, including the detector solenoid;
  track SR photons through the vacuum beam following the photon reflection process;
  generate a high statistics MC sample of absorbed SR photons.
The code was benchmarked against Synrad+ and contains the same geometry of the vacuum beam pipe using an STL file of 3D CAD drawings.
Synrad+
Eic-Shell
Sampling
Eic-Recon
Geant4

## Slide 9: Machine lattice and beam parameters
There are three lattice files available for the simulation:
  Sep-2023 (so-called “new lattice”)
  Jan-2024 (v6.2)
  Mar-2024 (not simulated yet)
The magnet arrangement is the same for all of them:
  Upstream: 3 dipoles (D1eF, D2eF1/2), 2 quads (Q0/1eF)
  Central: solenoid 1.7 T (MARCO)
  Downstream: 2 quads (Q1/2eR), 1 dipole (B2eR)
All simulations were performed for 18 GeV electrons.

## Slide 10: X-ray reflection process in Geant4
Since X-ray reflection as a standard gamma process was missing in Geant4, the Geant4 developers have recently (Dec. 2023) implemented it; see #50 FCC-ee MDI meeting.
  They use the same material reflection database (like Synrad+) prepared by B.L. Henke et al.
  Unfortunately, they consider only specular (mirror-like) reflection with an attenuation factor to include surface roughness.
However, for the EIC, custom-built Geant4 simulation, more advanced models were implemented and compared against available codes:
  Synrad+ (after recent discussions, bugfixes and new features have been implemented by the developers; see Synrad+/Molfow+ Forum) – diffuse reflection
    old reflection model (Synrad [R.Kersevan, SSC 1993, 10.1109/PAC.1993.309821])
    new reflection model (Synrad3D [G.Dugan, D.Sagan, Cornell 2013, 10.5170/CERN-2013-002.117] )
  Custom-built Geant4
    with the Debye-Waller attenuation factor (similar to the geant4-release) – specular reflection
    with the reflection surface normal random tilt (similar to the old model in Synrad+) – diffuse reflection
    with the reflection direction random offset (similar to the new model in Synrad+) – diffuse reflection
  Geant4 release with the Névot-Croce attenuation factor – specular reflection
set as
default

## Slide 11: Background rate scaling
Generator:
Synrad+
Generator:
Geant4
Generator:
Synrad+
Generator:
Geant4
150 facets of the IP beam pipe
  ~3 hours of data collection
  ~1 hour for sampling
Event sampling (Tint): 10 fs/event
# of events (Nevt): 104
Scaling:
Counts / (Nevt x Tint)
~9 hours of simulation for the entire IR region
Beam current (Ibeam): 0.227 A
Elementary charge (Qe): 1.6e-19 C
# of jobs (Njob): 104
# of electrons per job (Ne): 104
Scaling:
Counts x Ibeam / (Qe x Ne x Njob)
Good agreement between Synrad+ and Geant4 results for the v6.2 lattice file.
Extremely high SR background rates in all sub-detectors
Indicating there is direct SR hitting the detector beam pipe
IP beam pipe only

## Slide 12: Improved eic-shell and Geant4 beam pipes on the far-BWD side
e– beam
eic-shell material scan
Geant4 simulated absorbed SR photons
Tagger-2
Tagger-1
Lumi exit window
(for Lumi monitor)

## Slide 13: Detector hit rates: Electron beam lattice v6.2 (Jan. 2024)
Interaction Region
I = 0.227 A
-37m < z < 5m
E𝛄 > 30 eV
I = 0.227 A
-65cm < z < 65cm
E𝛄 > 30 eV
Interaction Point
The majority of background rates are caused by the absorbed SR photons outside the IP beam pipe.
The SR background rates are very high in all sub-detectors.
  Can we reduce these rates?

## Slide 14: SR photon tracks: E > 10 keV, hit the IP beam pipe
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
IP6
e– beam
Nᵧ = 7469 ph.
Indeed, there is direct SR hitting the IR beam pipe and reflected SR hitting the IP beam pipe
 predominantly from the closest dipole magnets.

## Slide 15
e– beam
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
IP6
Nᵧ = 185 ph.
With the two simple masks, the flux of SR photons hitting the IP beam pipe is reduced by a factor of ~40
SR photon tracks: E > 10 keV, hit the IP beam pipe
The best option would be this mask 

## Slide 16: Detector hit rates: Electron beam lattice v6.2 (Jan-2024)
Interaction Region, w/ the SR mask
I = 0.227 A
-37m < z < 5m
E𝛄 > 30 eV
I = 0.227 A
-37m < z < 5m
E𝛄 > 30 eV
A simple SR mask promises to reduce SR background rates for innermost detectors by up to 2 orders of magnitude.
Designing a more sophisticated mask, taking into account wakefields and impedances, is essential.
Interaction Region, w/o the SR mask

## Slide 17: IR beam pipe material
Aluminum beam pipe
Copper beam pipe
w/o the SR mask
w/o the SR mask
w/ the SR mask
w/ the SR mask
Recently, it was discovered that the IR beam pipe material in the eic-shell is aluminum, not copper.
  Is it a bug or outdated code?
Meanwhile, in the Synrad+/Molflow+, the beam pipe is made of copper.
For the region of interest (0.01-0.1 MeV), this discrepancy affects the final background rates.
  Copper reduces the rates by a factor of ~10.

## Slide 18: Summary (1)
The past method to generate absorbed SR photons on the internal surface of the electron beam pipe does not provide reliable results.
  Corresponding codes (Synrad+ and Event-sampling) were updated with bugfixes and new features.
Therefore, to make the simulation process easier and faster, a dedicated custom-built code based on the Geant4 framework was developed.
  The code was successfully benchmarked against i) the well-known software (Synrad+) and ii) analytical calculations.
  The new code contains several SR photon reflection models and uses the most recent and available beam pipe geometry.
The eic-shell code was modified to study the SR background in the ePIC and auxiliary detectors.
  The default code contained outdated beam pipe geometries and materials, as well as magnet arrangement.

## Slide 19: Summary (2)
The latest simulation with the Jan-2024 (v6.2) lattice shows:
  for the aluminum beam pipe, the majority of ePIC rates originate from the region outside the IP beam pipe;
  for the copper beam pipe, the majority of ePIC rates originate from the IP beam pipe;
    the copper beam pipe effectively stops SR photons in the energy region of interest (10-100 keV);
  the overall rate of the SR background in all sub-detectors is extremely high (THz);
  by placing a simple SR mask, we can reduce the background rates by at least two orders of magnitude;
    we need a more sophisticated SR mask to reduce the rate further;
  adding additional shielding around the IR beam pipe could be another option to mitigate the SR background;
  auxiliary detectors will be exposed to the ultrahigh rate of SR (PHz);
    however, the geometry of the far-backward beam pipe needs revision.

## Slide 20: Next steps
We can continue using the manual approach of the beam pipe geometry description in Geant4 and eic-shell.
  However, we should consider the advantages of transitioning to a unified 3D CAD drawing used in both frameworks.
We have to implement a new SR mask and check its impact on the detector background and machine impedance.
Also, it is essential to revisit the entire IR beam pipe used in Geant4 and eic-shell.
  To ensure the accuracy of the beam pipe geometry description.
  Close collaboration with the ePIC software group is desirable.
For more details and materials regarding the custom-built Geant4 simulation code, please refer to backup slides and past EIC IR Synrad meetings [SupplementaryMaterials].
Thanks for your attention!

## Slide 21: Backup

## Slide 22: Past path for SR background data production
Synrad+
Eic-Shell
Sampling
Eic-Recon
Bugs and software limitations
Since Synrad+ SR photons are stored with assigned weights (flux), an additional step to sample these photons is required.
During the sampling, the absorbed photons are re-generated with no weights grouping within the specified time window (typically 100 ns) to shoot the vacuum beam pipe one by one.
  However, this approach ignores the fact that multiple photons from the same electron bunch can hit the pipe simultaneously.
Therefore, the sampling script was modified to provide the correct SR photon distribution before the eic-shell simulation.
1/s
2/s
4/s
For visualization purposes only, not accurate
Old sampling
New sampling

## Slide 23: Past path for SR background data production
Synrad+
Eic-Shell
Sampling
Eic-Recon
Bugs and software limitations
BEFORE
AFTER
Absorbed SR photons (color)
Eic-shell material scan (black)

## Slide 24: Benchmark: Generated e-beam
A set of electron beam tracking campaigns in Geant4 was performed to cross-check the implementation of magnets (position, orientation).
  Courant–Snyder (a.k.a. Twiss) parameters were used to calculate the expected distributions.
There is a good agreement between generated and expected initial beam distributions upstream of the first dipole magnet.
D2EF1
D2EF2
D1EF
Q1EF
Q0EF

## Slide 25: Benchmark: Dipole and Quad fields
A correctly set magnetic field map gives the expected beam distribution at any location along the IR beamline.
Y
X
Z
visualization is left-handed
D2EF1
Y
X
Z
visualization is left-handed
Q0EF
D2EF1
D2EF2
D1EF
Q1EF
Q0EF

## Slide 26: Photon generator
Turn on the SR production process using a dedicated Geant4 class.
Synrad+
electron beam
SR photons
vacuum beam pipe internal walls
Geant4
vacuum beam pipe internal walls
SR photons
electron beam
visualization is left-handed
visualization is right-handed

## Slide 27: X-ray reflection process benchmark: Synrad+ (v1.4.33/v1.4.34 bugfix) vs Geant4 (Gamma, custom-built) vs Geant4 (Xray, adobted from geant4-release-11.2.0)
Surface roughness RMS = 0 nm
Good agreement between all codes and models

## Slide 28: X-ray reflection process benchmark: Synrad+ (v1.4.33/v1.4.34 bugfix) vs Geant4 (Gamma, custom-built) vs Geant4 (Xray, adobted from geant4-release-11.2.0)
Surface roughness RMS = 50 nm
Good agreement
between Geant4 codes for specular reflection
(blue and yellow)
old model Synrad+ vs Geant4 code for diffuse reflection
(magenta vs black)
new model Synrad+ vs Geant4 code for diffuse reflection
(green vs red)
Now, we have a reliable and convenient tool for studying the SR background.

## Slide 29: BWD beam pipe (before)
e– beam
eic-shell material scan
Geant4 simulated absorbed SR photons
Q1eR
Q2eR
B2AeR
B2BeR

## Slide 30: BWD beam pipe (after)
e– beam
eic-shell material scan
Geant4 simulated absorbed SR photons
B2BeR
Q1eR
Q2eR

## Slide 31: Beam pipe and magnets
The electron beam pipe geometry in the STL file (used in Synrad+) extends to only 33.5m and 15.3m in the forward (hadron-going) and backward (electron-going) directions, respectively.
Q1eR
Q2eR
B2AeR
B2BeR
Further steps to updated geometry:
An extended far-BWD electron beam pipe in the SR generator code (use the eic-shell modeling as a reference)
Improved BWD beam pipe geometry in the eic-shell and custom-built Geant4 (make them consistent)
The new lattice file contains only the B2eR magnet
  There is no B2A/BeR

## Slide 32
eic-shell
custom-built Geant4
Eic-shell vs Geant4 simulation geometry
see the heprep file for more details
e– beam
e– beam

## Slide 33: SR photons causing detector hits
Although there are many SR photons hitting the IR beam pipe
  Only a part of them passes through the beam pipe and reaches the detector-sensitive volume.
According to the MC particle analysis, SR photons with E𝛾 > 10 keV produce Vertex detector hits.
  Let’s track the SR photons with E𝛾 > 10 keV that hit the IP beam pipe.
Generated SR photon on the inner surface of the beam pipe
Energy deposition of the VertexBarrel detector hits
XY position of the VertexBarrel detector hits