## Slide 1
Synchrotron Radiation (SR) background in ePIC at the EIC
Andrii Natochii
natochii@hawaii.edu
Outline
Executive summary
Synrad+ limitation
SR reflection in Geant4 (new physics process)
Benchmarking (debugging)
Beam tails (optional for this talk)
Summary and next steps

## Slide 2
The SR background in the ePIC detector is considered one of the most dominant sources of inner tracker occupancy and damage.
  A comprehensive understanding of the SR impact is essential for detector performance and safety.
So far, only preliminary estimates based on a simplified model have been discussed.
  Using the Molflow+ software, one can accurately calculate gas pressure distribution in the IR.
  However, the Synrad+ software is unsuitable for precise and convenient study of the SR background.
  Therefore, the use of the Geant4 software is proposed and studied.
According to the first preliminary results, the newly developed code based on Geant4 is reliable and can be used for a comprehensive SR background study in ePIC at the EIC.
  The code fairly successfully passed benchmark tests.
  It demonstrated satisfactory performance in terms of computational time and resources.
After improving the IR beam pipe geometry in eic-shell, we can start working on the SR background mitigation using the new Geant4-based code.
Executive summary
Andrii Natochii | Dec 2023

## Slide 3
Synrad+ limitation
Andrii Natochii | Dec 2023

## Slide 4
Z
Y
X
Y
X
The vacuum beam pipe geometry is made of an assembly of ~29k facets (triangles and rectangles) imported from 3D CAD.
Unfortunately, the GUI allows the information about the impinging photons hitting the beam pipe to be stored only for one facet at a time.
Although only up to 1k facets are hit by photons, storing this information for each is highly time-consuming.
Synrad+ GUI limitation
Andrii Natochii | Dec 2023

## Slide 5
Possible solution
Instead of collecting photon data from ~1k facets, we can create a phantom/fake beam pipe (an ideal absorber → sticking = 1) with a simple geometry inside the actual pipe and collect the data.
Pros
  Only 36 facets → easy to store the data (~40 min)
Cons
  Detailed information about reflected photons is missing
Proposal
  Use Geant4 instead of Synrad+ for the SR simulation
⌀ 4.4 cm
⌀ 4.2 cm
Phantom pipe
10o
Andrii Natochii | Dec 2023

## Slide 6
SR in Geant4
Andrii Natochii | Dec 2023

## Slide 7
Synrad+ → Geant4: Steps to be done
Convert the vacuum beam pipe structure into the Geant4 model
Create magnetic regions with three dipoles and two quadrupoles
Implement the SR photon reflection from the vacuum-metal interface
Collect absorbed photon hits
electron beam
SR photons
vacuum beam pipe internal walls
Andrii Natochii | Dec 2023

## Slide 8
Synrad+
STL-file from Charles Hetzel:
“Detector chamber 211004 mm.stl”
Vacuum volume
Convert STL → OBJ
Built using CADMesh.hh
Vacuum modelling in Geant4
~30 m
~50 m
IP6
e– beam direction
G4Solid made of vacuum
Geant4
Andrii Natochii | Dec 2023

## Slide 9
Beam pipe vacuum volume
Overlap with the magnet volume
Overlap with the magnet volume
Applied magnetic field to the intersection volume
Subtracted magnet from the vacuum volume
United beam pipe vacuum volume with the locally applied magnetic field
Magnetic field implementation (1)
Andrii Natochii | Dec 2023
In Geant4, the EM-field can be associated only with a logical volume (describes the element properties)
→ Assign the magnetic field to a part of the vacuum (locally)

## Slide 10
Magnetic field implementation (2)
Geant4
Vacuum pipe extension
FWD ESR lattice (Sep 2023)
Andrii Natochii | Dec 2023

## Slide 11
https://doi.org/10.1006/adnd.1993.1013
Reflection process
X-ray reflection process is not implemented in Geant4
  It is available only for optical photons
Solution:
Create “new process” for gammas
Fresnel formulas for reflection probability
  Use an extended CSV table from Synrad+
Specular reflection (mirror-like) including surface roughness [link]
vacuum
metal (Cu, Au)
reflection angles (ϴ, ɸ) are randomly offsetted
Geant4
Andrii Natochii | Dec 2023

## Slide 12
Geant4
Geant4 simulation inputs and outputs
The output ROOT file contains:
  Initial electron coordinates (r, p, E)
  Absorbed SR photons coordinates (r, p, E, t)
  Absorbed SR photons production vertices
  Simulation parameters (geometry configuration)
Geometry configuration is described in the XML file
  Magnet settings
  Beam parameters
  Absorbers
Andrii Natochii | Dec 2023

## Slide 13
Master parameter table
Andrii Natochii | Dec 2023
Beam parameters used for the study

## Slide 14
Benchmarking
Andrii Natochii | Dec 2023

## Slide 15
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
Setup of magnet elements
Focusing in X
K1L (Twiss) > 0
Defocusing in X
K1L (Twiss) < 0
Andrii Natochii | Dec 2023
survey_ir_6m.tfs and ir6forward.18GeV.twi (Sep 2023) are used for magnetic element positioning and field modeling
FWD ESR lattice (Sep 2023)

## Slide 16
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
Benchmark: Initial beam distribution
Geant4
Geant4
Horizontal phase space
Vertical phase space
Good agreement between generated beam distribution in Geant4 and Courant–Snyder (a.k.a. Twiss) parameters
Andrii Natochii | Dec 2023

## Slide 17
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
Benchmark: D2EF1 dipole field
Geant4
Geant4
Electron beam momentum at the magnet entrance
Y
X
Z
By – D-magnetic field
B[T]⍴[m] = 3.33564 pc[GeV]
⍴[m] = L[m]/(2sin[Θ/2]) RBEND
pc[GeV] = mc2[GeV](Ɣ2–1)
visualization is left-handed
D2EF1
Set a uniform magnetic field using G4UniformMagField
Twiss ANGLE > 0 → Geant4 ANGLE < 0
Andrii Natochii | Dec 2023

## Slide 18
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
FL
FL
FL
FL
N
S
S
N
Benchmark: Q0EF quadrupole field
Geant4
Y
X
Z
visualization is left-handed
Q0EF
Set a quadrupole magnetic field using G4QuadrupoleMagField
Twiss K1L > 0 → Geant4 K1L < 0
g – quadrupole gradient
g[T/m] = 3.33564*K1[m–2]*pc[GeV]
K1[m–2] = K1L[m–1]/L[m]
pc[GeV] = mc2[GeV](Ɣ2–1)
Andrii Natochii | Dec 2023

## Slide 19
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
Benchmark: Beam distribution after Q0EF
Geant4
Geant4
Horizontal phase space
Vertical phase space
Good agreement between tracked beam distribution in Geant4 and Courant–Snyder (a.k.a. Twiss) parameters
Andrii Natochii | Dec 2023

## Slide 20
Benchmark: SR process
Andrii Natochii | Dec 2023
Synrad+
electron beam
SR photons
vacuum beam pipe internal walls
Geant4
vacuum beam pipe internal walls
SR photons
electron beam
visualization is left-handed
visualization is right-handed
Turn on the SR production process using the G4SynchrotronRadiation class

## Slide 21
Benchmark: SR photons
 | D2EF1 |  | D2EF2 |  | D1EF |  | Q1EF |  | Q0EF | 
 | <NƔ> [ph/e–] | σNƔ [ph/e–] | <NƔ> [ph/e–] | σNƔ [ph/e–] | <NƔ> [ph/e–] | σNƔ [ph/e–] | <NƔ> [ph/e–] | σNƔ [ph/e–] | <NƔ> [ph/e–] | σNƔ [ph/e–]
Geant4 | 4.79 | 2.07 | 4.79 | 2.07 | 1.05 | 0.74 | 0.71 | 0.47 | 0.67 | 0.42
Theory | 4.29 |  | 4.29 |  | 0.55 |  |  |  |  | 
 | <PƔ> [μW/e–] | σPƔ [μW/e–] | <PƔ> [μW/e–] | σPƔ [μW/e–] | <PƔ> [μW/e–] | σPƔ [μW/e–] | <PƔ> [μW/e–] | σPƔ [μW/e–] | <PƔ> [μW/e–] | σPƔ [μW/e–]
Geant4 | 1.254 | 1.256 | 1.254 | 1.256 | 0.194 | 0.542 | 0.012 | 0.065 | 0.012 | 0.067
Theory | 1.254 |  | 1.254 |  | 0.194 |  |  |  |  | 
Good agreement between simulated SR photon numbers/power per electron in Geant4 and analytical calculations (theory: )
Andrii Natochii | Dec 2023
D2EF1
D2EF2
D1EF
Q1EF
Q0EF

## Slide 22
Geant4 SR simulation results
Average simulation time is about 70 ms/event (1 event ≡ 1 electron)
Applying the E𝛄 cut significantly speeds up the simulation
Andrii Natochii | Dec 2023
Took ~1.6 hours for 108 events using 1000 jobs (105 events/job) on KEKCC
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
IP6
E𝛄 > 4 eV

## Slide 23
Synrad+ hack to collect the absorbed SR photon information at the reflecting facet
Andrii Natochii | Dec 2023
Facet #39
Absorber
Facet #40
Absorber
Facet #19
Reflector
Facet #20
Reflector
Discussion at the Molflow/Synrad forum: https://molflow-forum.web.cern.ch/t/unexpected-absorbed-sr-photon-distribution-in-synrad/584/11

## Slide 24
Benchmark: Energy spectrum of absorbed SR photons
Andrii Natochii | Dec 2023
There is a small disagreement for E𝛄 ≲ 5 keV
Incident to the beam pipe
Reflected from the beam pipe
Absorbed on the beam pipe

## Slide 25
IP6
Geant4
EIC/ePIC
Material scan
X, Z, Px, and Pz coordinates of SR photons should be flipped in HEPMC files before running the eic-shell simulation
Andrii Natochii | Dec 2023
FWD end of the electron ring beam pipe
BWD end of the electron ring beam pipe

## Slide 26
Material scan: IP6 beam pipe
MC particle (SR photons) vertices
Be beam pipe
Au layer
e– beam
Andrii Natochii | Dec 2023
|Z| < 65 cm
E𝛄 > 4 eV
Geant4 SR hits fit the IP beam pipe aperture

## Slide 27
Andrii Natochii | Dec 2023
SR background in ePIC: Geant4 SR photon generator
|Z| < 65 cm
E𝛄 > 4 eV
Only for the IP beam pipe SR photons

## Slide 28
|Z| < 10 m
E𝛄 > 4 eV
Andrii Natochii | Dec 2023
MC particle vertices
  Geant4 SR photon generator using the vacuum geometry from Synrad+
eic-shell material scan
  |Y| < 0.1 cm
Beam pipe geometry inconsistency (1)
X [cm]
Z [cm]

## Slide 29
Andrii Natochii | Dec 2023
Beam pipe geometry inconsistency (2)

## Slide 30
Andrii Natochii | Dec 2023
SR background in ePIC: Geant4 SR photon generator
|Z| < 10 m
E𝛄 > 4 eV
All SR photons within ±10 m from the IP
Beam pipe geometry issue is still here
PRELIMINARY

## Slide 31
Beam tails
(Optional, if time allows)
Andrii Natochii | Dec 2023

## Slide 32
Beam tail model
18 GeV electron beam | P = 10 nTorr
Andrii Natochii | Dec 2023

## Slide 33
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
Beam tails: Initial beam distribution
Tails: 5 – 20σ
Andrii Natochii | Dec 2023
Geant4
Geant4
Horizontal phase space
Vertical phase space

## Slide 34
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
Beam tails: Beam distribution after Q0EF
Tails: 5 – 20σ
Horizontal phase space
Vertical phase space
Andrii Natochii | Dec 2023
Geant4
Geant4

## Slide 35
Andrii Natochii | Dec 2023
SR background in ePIC: Geant4 SR photon generator
|Z| < 10 m
E𝛄 > 4 eV
Beam core
Beam tails
Beam pipe geometry issue is still here
PRELIMINARY
PRELIMINARY

## Slide 36
Summary
Andrii Natochii | Dec 2023
We revisited a new method to simulate the SR background in the ePIC detector.
  It is based on a custom SR photon reflection process embedded in Geant4.
  So now, all simulations (i.e., SR photon generation, tracking, and interaction with the beam pipe and detector) can be performed in the same software environment – Geant4.
The new code was tested and benchmarked (the most time-consuming part).
  There is a fairly good agreement with Synrad+ calculation, especially for E𝛄 > 5 keV.
  However, a significant inconsistency with the eic-shell beam pipe modeling was observed.
In addition, the first step toward the beam tail simulation was discussed.
The results suggest that the new Geant4-based tool is reliable for the SR background simulation in ePIC at the EIC.
  However, further refinements are still needed.

## Slide 37
Simulation improvements
The IR beam pipe modeling in eic-shell must be improved to fit the SR hits distribution that follows the actual vacuum beam pipe structure. [Who can be contacted for details?]
Beam tails should be clarified. [Who can be contacted for details?]
Implement the detector solenoid magnetic field. [Who can be contacted for details?]
SR background mitigation
Study a possible BG mitigation through the SR masking inside the vacuum.
Find the optimal energy cut for SR photon tracking to accurately study SR hit rates in ePIC and speed up the simulation for higher statistics.
Next steps and missing ingredients
Andrii Natochii | Dec 2023

## Slide 38
Backup
Andrii Natochii | Dec 2023

## Slide 39
Andrii Natochii | Dec 2023
Received on September 24th, 2023

## Slide 40
Event generation
output: .hepmc file with events
Read synrad+ output files and prepare events that contain SR photons within the integrated time window (e.g., 100 ns) using photons’ weights (rates)
Detector simulation
output: .root file with hits
Run ddsim (actually npsim) using the input .hepmc file with generated SR photon events and the default ePIC detector geometry
SR photon production
output: .csv file with photons
Produce “technical” single photons (vertexes, momentums, and rate) using synrad+
Reconstruction and analysis
output: .root file with ntuples
Create a dedicated eicrecon plugin to store ntuples and histograms with the detector hit information
Plot the final figures
Vacuum calculation
output: pressure profile data
Calculate the gas pressure profile using molflow+
SR data production and analysis scheme
Let’s focus on this step
Andrii Natochii | Dec 2023

## Slide 41
–67 cm
68.69231 cm
Gold
Copper
Geant4
Synrad+
Gold
Copper
Copper
Copper
Andrii Natochii | Dec 2023
Beam pipe materials

## Slide 42
Geant4
Closer look at magnets
Andrii Natochii | Dec 2023

## Slide 43
Stop photons at the end of the pipe
Photon absorbers
Stop photons that escape the vacuum through the beam pipe ends
Do not add them to the output data (optional)
Y
X
Z
The geometry is visualized in the left-hand coordinate system
Beam pipe ends
Geant4
Andrii Natochii | Dec 2023

## Slide 44
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
Benchmark: Beam distribution after D2EF1
Geant4
Geant4
Horizontal phase space
Vertical phase space
Good agreement between tracked beam distribution in Geant4 and Courant–Snyder (a.k.a. Twiss) parameters
Andrii Natochii | Dec 2023

## Slide 45
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
Benchmark: Beam distribution after D2EF2
Geant4
Geant4
Horizontal phase space
Vertical phase space
Good agreement between tracked beam distribution in Geant4 and Courant–Snyder (a.k.a. Twiss) parameters
Andrii Natochii | Dec 2023

## Slide 46
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
Benchmark: Beam distribution after D1EF
Geant4
Geant4
Horizontal phase space
Vertical phase space
Good agreement between tracked beam distribution in Geant4 and Courant–Snyder (a.k.a. Twiss) parameters
Andrii Natochii | Dec 2023

## Slide 47
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
FL
FL
FL
FL
S
N
N
S
Benchmark: Q1EF quadrupole field
Geant4
Y
X
Z
visualization is left-handed
Q1EF
Set a quadrupole magnetic field using G4QuadrupoleMagField
TWISS K1L > 0 → Geant4 K1L < 0
g – quadrupole gradient
g[T/m] = 3.33564*K1[m–2]*pc[GeV]
K1[m–2] = K1L[m–1]/L[m]
pc[GeV] = mc2[GeV](Ɣ2–1)
Andrii Natochii | Dec 2023

## Slide 48
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
Benchmark: Beam distribution after Q1EF
Geant4
Geant4
Horizontal phase space
Vertical phase space
Good agreement between tracked beam distribution in Geant4 and Courant–Snyder (a.k.a. Twiss) parameters
Andrii Natochii | Dec 2023

## Slide 49
Benchmark: Synchrotron radiation photons (2)
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
Average number of generated SR photons per electron in the given magnet, <NƔ>
Average power of radiated SR per electron in the given magnet, <PƔ>
Andrii Natochii | Dec 2023

## Slide 50
Benchmark: Absorbed SR photon position along Z-axis
Andrii Natochii | Dec 2023
Incident to the beam pipe
Reflected from the beam pipe
Absorbed on the beam pipe
There is a small disagreement, presumably linked to the energy spectrum disagreement

## Slide 51
Beam tail model
10 GeV electron beam | P = 5 nTorr
Andrii Natochii | Dec 2023

## Slide 52
D2EF1
D2EF2
D1EF
Q1EF
Q0EF
Beam tails: Initial beam distribution
Tails: 5 – 20σ
Andrii Natochii | Dec 2023