## Slide 1: Synchrotron Radiation (SR) background in ePIC at the EIC
Andrii Natochii
natochii@hawaii.edu

## Slide 2: Recap
From Dec. 2023 meeting
Received IR beam pipe drawings from Charlie Hetzel
Adjusted the eic-shell modeling
Charlie plans to update the Synrad+ model in 2024
Mike Sullivan shared his calculation of EIC beam tails based on Gaussian approximation  more conservative model
Plan to study the new model's impact on the EIC SR background
Implemented the detector solenoid field. Thanks Elke Aschenauer for providing the details

## Slide 3: Solenoid field

## Slide 4: Solenoid magnet
For ePIC, a new solenoid is developed as the experimental magnet with a central field of 1.7 T with an operational range of up to 2 T. The Magnet has been named MARCO. From Ref. [link].
  Available field maps in a CSV format (as of Dec 2023): 1.7 T and 2.0 T (points are calculated every 2 cm)
  The solenoid field is off-centered by 8 cm towards the electron beam direction, i.e., its center is at (0;0;-8) cm
R(cm) Z(cm) Br(T) Bz(T)
0.0 -800.0 0.0000 -0.0006
0.0 -798.0 0.0000 -0.0006
0.0 -796.0 0.0000 -0.0006
0.0 -794.0 0.0000 -0.0006
0.0 -792.0 0.0000 -0.0006
0.0 -790.0 0.0000 -0.0006
0.0 -788.0 0.0000 -0.0006
0.0 -786.0 0.0000 -0.0006
0.0 -784.0 0.0000 -0.0006
0.0 -782.0 0.0000 -0.0006
0.0 -780.0 0.0000 -0.0006
0.0 -778.0 0.0000 -0.0006
0.0 -776.0 0.0000 -0.0007
...
MARCO

## Slide 5: Material scan (black) vs solenoid field (color)
Electron beam
Hadron beam
R [cm]

## Slide 6: Detector solenoid field in the custom-built Geant4
X-Z (|Y| <= 2cm)
Y-Z (|X| <= 2cm)
Y-X (|Z| <= 2cm)
X-Y-Z

## Slide 7: X-ray reflection process

## Slide 8: X-ray reflection process in Geant4 (updates)
Since X-ray reflection as a standard gamma process was missing in Geant4, the Geant4 developers have recently (Dec. 2023) implemented this process; see #50 FCC-ee MDI meeting
  They use the same material reflection database (like Synrad+) prepared by B.L. Henke et al.
  Unfortunately, they consider only specular (mirror-like) reflection with an attenuation factor to include surface roughness
Compare the following codes developed for X-ray reflection
  Synrad+ (after recent discussions, bugfixes and new features have been implemented by the developers; see Synrad+/Molfow+ Forum) – diffuse reflection
    Old reflection model (based on Synrad [R.Kersevan, SSC 1993, 10.1109/PAC.1993.309821])
    New reflection model (based on Synrad3D [G.Dugan, D.Sagan, Cornell 2013, 10.5170/CERN-2013-002.117] )
  Custom-built Geant4 code
    With the Debye-Waller attenuation factor (similar to the geant4-release) – specular reflection
    With the reflection surface normal random tilt (similar to the old model in Synrad+) – diffuse reflection
  Geant4 release with the Névot-Croce attenuation factor – specular reflection

## Slide 9: X-ray reflection process benchmark: Synrad+ (v1.4.33/v1.4.34 bugfix) vs Geant4 (Gamma, custom-built) vs Geant4 (Xray, adobted from geant4-release-11.2.0)
Surface roughness RMS = 0 nm
Good agreement between all codes and models

## Slide 10: X-ray reflection process benchmark: Synrad+ (v1.4.33/v1.4.34 bugfix) vs Geant4 (Gamma, custom-built) vs Geant4 (Xray, adobted from geant4-release-11.2.0)
Surface roughness RMS = 50 nm
Good agreement
between Geant4 codes for specular reflection
(blue and yellow)
old model Synrad+ vs Geant4 code for diffuse reflection
(magenta vs black)
new model Synrad+ vs Geant4 code for diffuse reflection
(green vs red)
More plots are in Backups

## Slide 11: Beam pipe geometry

## Slide 12
Beam pipe geometry inconsistency
 MCparticles generated in eic-shell (color)
Material scan (black)
It is unclear which beam pipe geometry is correct
Assumption: consider the Synrad+ vacuum model (prepared by Charlie) as a correct geometry since it is given as a single STL file (hard to modify)

## Slide 13
Adjusted beam pipe overlap with ePIC

## Slide 14
compact/definitions.xml
<constant name="ForwardRICHRegion_tan1" value="CentralTrackingRegionP_tan * 0.88 1.20" />
<constant name="ForwardRICHRegion_tan2" value="Eta3_6_tan * 0.89 1.20" />
compact/tracking/definitions.xml
<constant name="ForwardTOFRegion_minR" value=”8 13*cm" />
Adjusted ePIC geometry
Only as a temporary solution

## Slide 15
 MCparticles generated in eic-shell (color)
Material scan (black)
Beam pipe geometry modification
More plots are in Backups
The new beam pipe modeling is now much closer to the Synrad+ geometry.
Although it might not be the final/recent beam pipe geometry, we define it as a reference to compare the simulated SR impact on the detector background.
BEFORE
AFTER

## Slide 16
Adjusted beam pipe geometry
 MCparticles generated in eic-shell (color)
Material scan (black)
This part was not adjusted
This part was not adjusted
Used for the ePIC SR background simulation

## Slide 17: SR background simulation

## Slide 18
-10m < z < 10m
E𝛄 > 4 eV
ePIC SR background: Rates with inconsistent geometries
High SR background rates (> 1 MHz) due to generated SR photons outside the vacuum beam pipe
First custom-built Geant4 SR model
(contained bugs)
From Dec. 2023 meeting

## Slide 19
-4m < z < 5m
E𝛄 > 30 eV
-4m < z < 5m
E𝛄 > 30 eV
-4m < z < 5m
E𝛄 > 30 eV
Custom-built Geant4
(X-ray, Névot-Croce, adopted from geant4-release-11.2.0)
Specular reflection
Custom-built Geant4
(Gamma, Debye-Waller)
Specular reflection
Custom-built Geant4
(Gamma, surf. normal tilt, like the old Synrad+ model)
Diffuse reflection
Improving the X-ray reflection process and tuning the beam pipe in the eic-shell to the CAD/STL model make the SR background in the ePIC detector more realistic with diffuse reflection, i.e., SR background rates ~ 0.1 MHz (e.g., electron beam-gas rates ~3 MHz [ref.])
ePIC SR background: Rates with adjusted geometries
Custom-built Geant4
(Gamma, Debye-Waller + perturbed reflection direction, like the new Synrad+ model)
Diffuse reflection
-4m < z < 5m
E𝛄 > 30 eV

## Slide 20: Beam tail modeling

## Slide 21
Overview
The realistic/actual beam tail distribution modeling is a challenging task
  Usually, one has to include all possible beam-scattering processes with beam dynamics in the machine lattice, possible machine errors, and collimators
So far, we do not have a reliable multi-turn particle tracking code for the EIC
  Therefore, we have to rely on some assumptions and approximations
Christoph Montag’s model [optimistic]:  first trial; see Dec. 2023 meeting
  Non-gaussian tails caused by beam-beam and beam-gas scattering events
  Enhancement of the electron beam population at large amplitude (beam tails) occurs predominantly in the vertical plane
  The core of the model – parametrized simulated beam tails
    No tails in the horizontal plane at Ee- = 18 GeV
    The vertical beam tail integral is about 10—8 of the beam core
Mike Sullivan’s model [conservative]:  next step
  Gaussian beam tails as an equilibrium between beam lifetime (beam particles are scattered out of the core into the tails) and SR damping (beam tail particles are pulled back to the core)
    Especially true for the horizontal plane
  The integral of beam tails should not exceed a certain value to avoid luminosity degradation
    Arbitrary threshold: the tail integral is < 5% of the core integral

## Slide 22
Summary
Last time, we reported on the first developments of SR photon reflection in Geant4.
Since then, several improvements and features to the code have been implemented.
  Solenoid field using MARCO magnetic field map.
  Spectral and diffuse reflection processes based on the recently released Geant4 and documented old/new Synrad+ models were implemented in the custom-built Geant4 code for the SR simulation.
Furthermore, we have identified significant inconsistencies in the vacuum electron beam pipe geometry between the eic-shell (used for the ePIC background rate simulation) and the custom-built Geant4 (CAD/STL drawings imported from Synrad+).
  Since the correct beam pipe geometry is unclear, we adjusted eic-shell modeling following CAD/STL drawings.  We need correct, up-to-date vacuum beam pipe drawings.
  This temporary solution allowed us to study the ePIC SR background rates for different X-ray reflection models.
According to the findings:
  Diffuse reflection based on old and new Synrad+ algorithms works well and gives a realistic estimation of the detector's SR background level (~0.1 MHz).
  We still need to understand which model is the best for our application; each model has pros and cons.
Several Synrad+ code updates (new features and bugfixes) were triggered during the new custom-built Geant4 code development; see the following slides.

## Slide 23
Beam tails
The first optimistic model with non-Gaussian tails was tested with a very low beam halo intensity.
A more aggressive model with Gaussian tails will be tested next.
New machine lattice
Recently, we have received a new machine lattice v6.2
Questions and subjects to be studied with the SR simulation in Geant4
  Do we need to update the masks in front of ePIC?
  What photons pass and hit the beam pipe?
  Updated SR background rates?
  SR photon files?
For the review of the ancillary detectors in February:
  What are the SR background rates for the low-Q2 tagger and the Luminosity monitor?
    This item requires backward beam pipe geometry modification in both eic-shell and custom-built Geant4.
Next steps

## Slide 24
Synrad+ updates
The new custom-built Geant4 code development triggered a few updates to the official Synrad+ software.
An option to log absorbed particles by a given facet is now available.
The logged particle flux is now correctly normalized using the correct number of simulation scans.
Due to a bug in the code, the switch for the new reflection model did not work correctly in the GUI. Now, through global settings, one can switch between old and new reflection models with one click, and it will be correctly prepared to the simulation.
For more details, please refer to the Synrad+/Molflow+ Forum:
All features and bugfixes from above are implemented in the new release v1.4.34

## Slide 25: Backup

## Slide 26: Solenoid field
B = 1.7 T
B = 2.0 T

## Slide 27: Material scan

## Slide 28: Solenoid field (1.7 T)

## Slide 29
Surface roughness = 0

## Slide 30
Surface roughness = 0

## Slide 31
Surface roughness = 50 nm

## Slide 32
Surface roughness = 50 nm

## Slide 33
Synrad+ beam pipe geometry

## Slide 34
Default beam pipe geometry

## Slide 35
Adjusted beam pipe geometry

## Slide 36
ePIC SR background: Vertex Barrel detector hits
-10m < z < 10m
E𝛄 > 4 eV
-4m < z < 5m
E𝛄 > 30 eV
First custom-built Geant4 SR model (contained bugs)
From Dec. 2023 meeting
Custom-built Geant4
(like the old Synrad+ model)
-4m < z < 5m
E𝛄 > 30 eV
Custom-built Geant4
(like the new Synrad+ model)

## Slide 37
From Dec. 2023 meeting
Optimistic model
No tails in the horizontal plane
The vertical beam tail integral is about 10—8 of the beam core

## Slide 38
https://indico.jlab.org/event/714/contributions/12568/attachments/9944/14673/The%20ePIC%20Experiment%20-%20JLUO%20Split.pdf

## Slide 39
Y
Z
X
Z
From eic-shell/epic