## Slide 1: Real-Time Information Distillation with Deep Neural Network-based Compression Algorithms
06-11-2024
Yi Huang
RHIC-AGS at BNL

## Slide 2
Time-Project Chamber Data Compression
Data: simulated 200 GeV Au+Au collisions from the sPHENIX experiment, high-pileup events
TPC

## Slide 3
In this study, we are going to focus on the outer layer group:
16 layers along the radial direction
2304 columns of sensor nodes along the azimuth direction
498 rows along the beam direction
Subdivided into 24 TPC wedges of shape (16, 192, 249)
Time-Project Chamber Data Compression

## Slide 4
Each sensor node output an analog-to-digit converter (ADC) value as an integer in [0, 1023].
All ADC values below 64 are suppressed to 0 to increase sparsity.
In this study, we use log scale ADC value, i.e. . A log scale ADC value is in [0, 10]. There is no value less 6 because of the zero suppression.
TPC wedges of shape (16, 192, 249)
Input to the neural compression algorithm
Fig. Log scale ADC value in a TPC wedge

## Slide 5
Acrophobia neural network
Sparse with curve-shaped objects
NNs like bell-shaped distribution

## Slide 6
https://arxiv.org/pdf/2111.05423.pdf
Online inference
Offline reconstruction

## Slide 7
Performance of BCAE compared with off-the-shelf lossy compression algorithms

## Slide 8
Ultra-deep yet fast Yolo Network for object detection
2D Convolution might be the key to speed!

## Slide 9
Use 2D Convolution to make BCAE Faster
16 layers
The TPC wedge data has shape (16, 192, 249). Comparing to the azimuth and horizontal direction, the radial dimension is thin.
We can treat the radial dimension as the feature dimension and use 2D convolutions

## Slide 10
model | MAE | PSNR | Precision | Recall | Encoder size | Compr. Ratio
BCAE-2D | 0.152 | 11.726 | 0.906 | 0.907 | 169.0k | 31.125
BCAE++ | 0.112 | 14.325 | 0.934 | 0.936 | 226.2k | 31.125
model |  |  |  |  |  | 
BCAE-2D | 0.152 | 11.726 | 0.906 | 0.907 | 169.0k | 31.125
BCAE++ | 0.112 | 14.325 | 0.934 | 0.936 | 226.2k | 31.125
Speed or Performance, but NOT both
Fast but not accurate
More accurate but slow
(3D Conv. Model)

## Slide 11
For sparse convolution, sparse data is a bless, not a curse!
Can we have something Fast and Accurate?

## Slide 12
Model name | Recon. Loss type | Keep ratio | Comp. Ratio | Test reconstruction performance |  |  |  | Encoder size | Throughput
 |  |  |  | L1 | L2 | precision | recall |  | 
BCAE2D | L1 |  | 31.13 | 0.152 | 0.862 | 0.906 | 0.907 | 169,000 | 6.9k
BCAE++ | L1 |  | 31.13 | 0.112 | 0.617 | 0.934 | 0.936 | 226,200 | 2.6k
ME_20_005 | L2 | 0.128 | 35.06 | 0.056 | 0.100 | 0.997 | 0.990 | 382 | 5.6k (RTX 6000ADA)
ME_20_010 | L2 | 0.177 | 25.19 | 0.034 | 0.080 | 0.998 | 0.989 |  | 
ME_30_005 | L2 | 0.119 | 37.70 | 0.052 | 0.163 | 0.994 | 0.976 |  | 
ME_10_005 | L2 | 0.112 | 40.09 | 0.078 | 0.983 | 0.990 | 0.969 |  | 
Comparing BCAE (dense convolution NN) with MinkowskiEngine Models
Sparse models

## Slide 13
Reconstruction Performance vs. Occupancy
Comparison of dense and sparse models
Reconstruction error
Precision
Recall

## Slide 14
Throughput vs. Occupancy
Comparison of dense and sparse models

## Slide 15
How Sparse Model Works
It works by finding the point of interest (PoI). The sparse model assign each voxel in the TPC a value. The higher the value the more valuable (or interesting) the voxel is. For compression, we only save those voxels that have higher value and discard lower-value ones, because we can confidently reconstruct with only high-value voxels.
Note: We can implement this idea with dense convolution. However, the sparse convolution engine (MinkowskiEngine) makes it much faster.
The black dots (PoIs) are what the sparse model decided to save

## Slide 16
How Fast could Compression be on Alternative
AI Hardware Accelerators
GPUs (shared memory)
GraphCore and Groq (on-chip memory)

## Slide 17
BCAE-2D Encoder

## Slide 18
MLP

## Slide 19
Summary
We can develop Deep Neural Network-based compression algorithm for Time-Projection Chamber data. And they works better than off-the-shelf untrainable compression algorithms
We can use the sparse convolution engine like the MinkowskiEngine to achieve both better accuracy and higher throughput.
AI hardware accelerators may help but we need to make them work better for more complicated neural networks.
Yi Huang (me)
Yihui (Ray) Ren
Shinjae Yoo
Jin Huang (PI)
Our Team