## Slide 1: ePIC BIC: Interface Requirements Follow-up
April 26, 2024
Global Mechanical Interfaces

## Slide 2: BIC Sector, End View:

## Slide 3: Fiber Geometry, Layer 1 17 Levels
 | Scheme | Fibers | 
Layer 1 | [2(43)+1] x 9 levels | 783 | 
 | [2(43)] x 8 levels | 688 | 
 |  | 1471 | for Layer 1

## Slide 4: Fiber Geometry, Layer 1, closer look
 | Scheme | Fibers | 
Layer 1 | [2(43)+1] x 9 | 783 | 
 | [2(43)] x 8 | 688 | 
 |  | 1471 | for Layer 1

## Slide 5: Fiber Totals*
 | Scheme | Fibers |  |  | 
Layer 1 | [2(43)+1] x 9 | 783 |  |  | 
 | [2(43)] x 8 | 688 |  |  | 
 |  | 1471 | for Layer 1 |  | 
Layer 2 | [2(45)+1] x 9 | 819 |  |  | 
 | [2(45)] x 8 | 720 |  |  | 
 |  | 1539 | for Layer 2 |  | 
Layer 3 | [2(47)+1] x 9 | 855 |  |  | 
 | [2(47)] x 8 | 752 |  |  | 
 |  | 1607 | for Layer 3 |  | 
Layer 4 | [2(48)+1] x 9 | 873 |  |  | 
 | [2(49)] x 8 | 784 |  |  | 
 |  | 1657 | for Layer 4 |  | 
Layer 5 | [2(50)+1] x 9 | 909 |  |  | 
 | [2(51)] x 8 | 816 |  |  | 
 |  | 1725 | for Layer 5 |  | 
Non-Imaging | [2(58)+1] x 60 | 7020 |  |  | 
 | [2(59)] x 59 | 6962 |  |  | 
 |  | 13982 | for Non-Imaging Layer |  | 
TOTAL FIBERS PER SECTOR = 21981
*assumes non-imaging layer built with uniform width (117 levels)
segmenting into two widths saves about 500 fibers

## Slide 6: BIC Length:

## Slide 7: Changes from April 12:
Reduce active length from 440cm to 435cm
Change offset from -38.75cm to -41.25
Rotated barrel 3.75 degrees to put edge of sector on vertical plane

## Slide 8: BIC Placement in Global Model:
Interference
w/DIRC
East (+Z)
West (-Z)
Facing North
6.75cm gap to
DRICH

## Slide 9: DIRC Interference:
4.74cm
unchanged from 4/12

## Slide 10: DIRC Interference, end view:
New orientation

## Slide 11: DRICH End:
6.75cm gap to DRICH
1.25cm beyond DIRC Bar

## Slide 12: Next Steps for Global Interface:
Finalize length of astropix staves
Adjust length of ScFi/Pb to match astropix
Resolve interference with DIRC