## Slide 1: A possible TPC tracker for DET-II@IP8
Klaus Dehmelt
Open Detector-II Meeting & Discussions
April 09, 2024

## Slide 2: time projection chamber
A Time Projection Chamber for DET-II@IP8
  TPC can serve multi purposes
    Tracking
    Pattern recognition
    Momentum determination
    Particle identification

## Slide 3: time projection chamber
A Time Projection Chamber for DET-II@IP8
    Gas ionization Y drift Y amplification Y sampling on pads
    Reconstruction of z-coordinates from drift time
    Electric field homogeneity important for undisturbed projection

## Slide 4: time projection chamber
A Time Projection Chamber for DET-II@IP8

## Slide 5: time projection chamber
A TPC for DET-II@IP8
  What are the constraints on length and outer radius?
  What field uniformity is required?
  What are the limitations on angular resolution
    At the vertex?
    At rmax?
  What PID capabilities are possible?
  What are the material budgets?
  Integration issues with other detectors?

## Slide 6: time projection chamber
A TPC for DET-II@IP8
  What are the constraints on length and outer radius?
  Typically, one wants to cover central rapidity h ≈  1 Y diameter ≈ length – constraint is magnet
sPHENIX within
Babar magnet

## Slide 7: time projection chamber

## Slide 8: time projection chamber
A TPC for DET-II@IP8
  What field uniformity is required?

## Slide 9: time projection chamber
A TPC for DET-II@IP8
  What field uniformity is required?
    Two field configurations to be considered
      Magnetic field
      Electric field
, : unit vectors along B/E-field

## Slide 10: time projection chamber
A TPC for DET-II@IP8
  Effect of non-parallel alignment of E- and B-field

## Slide 11: time projection chamber
A TPC for DET-II@IP8
  Momentum resolution dictates space point resolution
  Space point resolution (in a TPC) dictates field homogeneity
  Typically, modern experiments require sx of 100 mm or better
  Resolution degradation of at most 5% require
Fixed

## Slide 12: time projection chamber
A TPC for DET-II@IP8
  What are the limitations on angular resolution
    At the vertex?
    At rmax?

## Slide 13: time projection chamber
A TPC for DET-II@IP8
  A TPC has a multitude of point measurements
    ~50 in the sPHENIX TPC
    O(200) in the ALICE TPC
  A TPC measures space points with a ten-fold worse resolution as compared to Si-detectors
  A TPC is a slow readout device
    Distortion of z-position
    Can have impact on entrance/exit point determination in the TPC
    Can be circumvented with the introduction of “fast” entrance/exit point measurement

## Slide 14: time projection chamber

## Slide 15: time projection chamber
A TPC for DET-II@IP8
  What PID capabilities are possible?

## Slide 16: TPC – PID capabilities
Particle Identification via velocity measurement
    Velocity dependent interaction with the detector Y specific ionization

## Slide 17: TPC – PID capabilities
Particle Identification via velocity measurement
    Velocity dependent interaction with the detector Y specific ionization

## Slide 18: TPC – PID capabilities
Particle Identification via velocity measurement
    Velocity dependent interaction with the detector Y specific ionization

## Slide 19: TPC – PID capabilities
Particle Identification via velocity measurement
    Traditional charge counting vs cluster counting

## Slide 20: TPC – PID capabilities
Particle Identification via velocity measurement
    Traditional charge counting vs cluster counting

## Slide 21: TPC – PID capabilities
Particle Identification via velocity measurement
    Count each electron Y GridPix
Ultimate dE/dx device.
  Avalanche grid in front of 55 x 55 mm2 pixels.
  >90% efficiency for single electrons.
  Goals:
    Enough diffusion to get every electron into a different hole.
    Count electrons one-by-one.
  Three generations of development and continuing.
Small area is not particularly expensive.
  1800 chips (order/produce/test 3600) = $716k
  Careful: 1.2-5.4 kW of power (occupancy dependent).

## Slide 22: TPC – PID capabilities
Particle Identification via velocity measurement
    Count each electron Y GridPix
    Anticipated dE/dx resolution

## Slide 23: A TPC for DET-II@IP8
  What are the material budgets?
    Keep material budgets at minimum to avoid multiple scattering, secondary particle production, …

## Slide 24: Babar Magnet and TPC - Material Budget

## Slide 25: A TPC for DET-II@IP8

## Slide 26: TPC - Material Budget
Field Cage  Inner/Outer for sPHENIX
  Hybrid between STAR and ILD

## Slide 27: Gridpix TPC - Material Budget
sPHENIX:
45 kV & 18 layers kapton.
EIC:
10 kV & 5 layers kapton.
End Cap:
Temperature Profiles: 3 kW
Coolant above the dew point
  Conventional Cooling OK at 4%
  CO2 cooling promises ~2% ?
Barrel:

## Slide 28: Sphenix TPC construction
Ready for take-off

## Slide 29: Sphenix TPC construction
We are also building the TPC
  Mandrel
    Inner FC
    Outer FC

## Slide 30: time projection chamber
A TPC for DET-II@IP8
  Integration issues with other detectors?

## Slide 31: Integration issues for a time projection chamber

## Slide 32: Integration issues for a time projection chamber