## Slide 1: Injector status meeting, 4/16/24
OPPIS polarization
  Cooldown and restart 4/12 to 4/14: replacement of magnetic screws
  Polarization on restart high 70’s (better than at turn off), conditioning continues
AGS user 4 (standard tune jump operation)
  Jump quad on/off polarization 71.8/66.7 +/- 1%, gain of about 7.8% relative (intensity 1.7e11)
  Beam extracted to W-dump, ready for injection into RHIC
    Extraction bump supply repaired this morning
  Optimization scans continue
Development users
  Resonance correction (skew quads)
    Orbit improvements continue to allow higher strength operation
  Dual Linac pulses
    Beam established and merged on AGS flattop
    Transverse emittances quite large (εx ~4-5 um)
Intensity
AGS User
Tune jump timing scan
I = 0.7x1011