## Slide 1: Injector Status Time meeting, 5/7/24
AGS operations supporting
  RHIC fills ~1.3x1011/bunch
  High intensity for scrubbing and APEX (up to 3.9x1011/bunch at AGS extraction)
  Polarization development on user 8
Booster input from OPPIS > 6x1011
  Good conditioning progress
Average polarization for stores ~71% (fixed target, AGS extraction)
Intensity
AGS User
RHIC scrubbing
Pol (%)
Fill
~71%
RHIC bunch int (106)
Leftover scrubbing settings

## Slide 2: Resonance correction
Setup a slow horizontal resonance crossing on the flattop Gg = 45.72, Qx ramps from 8.70 to 8.78 over 200 ms
Crossing rate reduced (relative to acceleration ramp) by ~102, polarization loss ~20% (easily measurable compared to resonance on the ramp (~0.1% loss)
Scan three skew squads (with a 200 ms pulse width): one parallel to resonance, one anti-parallel and one orthogonal.
First proof-of-principle correction of partial snake hybrid resonances with betatron coupling!
Resonance crossing
Resonance vectors
Skew quad current scans
Snake drive term

## Slide 3: Resonance correction: Next steps
Power supplies
  5 of 15 supplies modified for optimized switching behavior to reduce heating
  Rest done by end of week (just in time for summer)
Beam work
  Check more scenarios with the flattop crossing
    correction with multiple skew quads
    Try to infer phase/amplitude errors from scans
  Orbit control scripts ready for testing
    Facilitates improved centering during acceleration : will greatly improve ability to do tests on the ramp (where it matters)