## Slide 1: sPHENIX status
Time meeting
May 14, 2024
Kin Yip
sPHENIX Director of Operations

## Slide 2
sPHENIX Magnet was ramped to the top field ~1.4 T last Friday to help TPC operation; and it has remained on ever since
DAQ/trigger: generally in good shape and working to resolve a couple remaining readout issues of INTT & MVTX
Pushing to complete online monitoring (with award)
Also emphasizing to collaborators on looking at the data taken
Status of sPHENIX Commissioning
Magnet Coil Temperature (K)
Magnet/Power Supply Currents (A)
ZDC rates (Hz)

## Slide 3
The magnetic field of 1.4 T has helped stabilize the TPC operation during beam collisions.
The TPC group will further adjust the operating voltages to improve the gains after changing resistors during the Maintenance Day.
TPC (tracking) operation in beam collisions in magnetic filed

## Slide 4: TPC firmware/zero-suppression status
Clock synchronization was successful
  FEE and FELIX communicate at the frequency of 56MHz, instead of 60MHz.
DAQ was stably operated at 1kHz at a threshold of 75 ADU
  pedestal is 60 ADU. Typically, RMS is ~2-3 ADU.
Turned on so-called baseline correction which forces the baseline of a fixed value

## Slide 5: INTT beam-center correction: before and afterwards
Vertices are reconstructed from data successfully by INTT after the magnet is set to full field.

## Slide 6: Examples of reconstructions of ,  and K masses from recent data (before calibration)