## Slide 1: Preinjectors Status
June 04, 2024
D. Raparia
Time Meeting

## Slide 2: Tandem
External Users :
- Last week: No user , MP 7 open for maintenance
Heated wafer issues, send back for investigation
- This week: No user

## Slide 3: EBIS
Last week ions for NSRL : Si+11 Nb+23, Ag+29 , Tb+35, Ta+38 Au+32, Bi+43
16hours/day , 5 days/week
Ion to NSRL
Au development for RHIC
- Power dip on Friday caused EBIS linac down
- Still investigation continue

## Slide 4: Linac 200 MeV Beam to BLIP , NSRL, Booster
BLIP
6/3-6/14: Th, 200 MeV, 150 𝞵A
polarized H-
Down time (<8 HRS)
- Power dip , (6 HRS )
source 1 changed source 2
- RF trips and reset: RFQ, Mod 5, mod2
Tank3, Q33,Q35,Q36 needed may adjustments
RF Mod 3: Frequent mis-pulsing need attention
OPPIS
Normal current and polarization, (conditioning)
Added Rb on Sunday
To Booster
Polarization @ 200 MeV

## Slide 5
Chart: BLIP Integrated Current Comparison
FY 2020 | 0 | 0
FY 2021 | 351.0169 | 1264.0018 | 4194.4484 | 7625.9229 | 7639.4394 | 10684.5563 | 13552.2975 | 16533.5408 | 17844.1378 | 20956.4462 | 24241.1907 | 27742.6889 | 31334.3905 | 34974.1698 | 37161.6071 | 40697.4878 | 42811.3735 | 43833 | 44420.4 | 46528.1282 | 50133.3278 | 53507.2101 | 57341.2825 | 61223.5901 | 63688.69 | 65312.9049 | 66169.7604 | 66997.9541 | 69866.085 | 72792.611 | 75766.2877 | 76764.8871 | 78727.1649 | 82641.3179 | 86600.6839 | 90483.5715 | 94458.5091 | 97920.9523 | 101392.6786 | 105159.6009 | 109111.7554 | 113062.0367 | 116430.877 | 120221.4262 | 121963.6441 | 121965.8631 | 121965.8631 | 123813.8742 | 126698.757 | 129619.5175 | 132549.2453 | 135161.9025 | 136268.9071