## Slide 1: Injector Status, 7/23/24
AGS User
Intensity
Injector Intensity by Fill
Operations overview
AGS Pol by Intensity (for fills)
(not a fit)
RHIC taking 2-2.5e11 out of the AGS
Polarization up around the ‘good ops’ line
  In line with historical good running
  Some incremental changes to polarimetry
  Good transverse emittances
Developments
Resonance correction skew quad development during AGS acceleration
  First observation of polarization gain on the ramp!
  Indication that early resonance correction is harming polarization (to be investigated)
3He development for APEX

## Slide 2: Polarization increase from skew quad resonance correction
 | Ramp Correction, only resonance after transition active |  |  | 
 | Omitting res: 27,28,33,39,40 |  |  | 
 | On |  | Off | 
 | Pol | err | Pol | err
 | 68.958 | 2.2 | 60.995 | 2.2
 | 62.874 | 2.2 | 62.1 | 2.2
 | 68.37 | 2.2 | 54.53 | 2.2
 | 65.56 | 2.21 | 58.87 | 2.27
 | 66.93 | 2.21 | 62.83 | 2.23
 | Averages |  |  | 
 | 66.538 | 0.986 | 59.865 | 0.993
Gain factor | 1.111 |  |  | 
Pre-transition
Transition gap
Full correction function
Correction on/off comparison (GƔ > 17 only)
Measured gain factor comparable to tune jump
Baseline polarization could be higher with normal optimizations
Plan to study dependence on correction amplitude, timing
Characterize intensity dependence after first iteration of optimizations
Start outlining a plan to swapping this user into operation