## Slide 1: Prospective pathways for generating high energy LWIR seeds
William Li, ATF Science Planning Workshop
June 21st, 2024

## Slide 2: Outline
Motivation for high energy LWIR seed
Overview of schemes in literature
  Raman conversion + DFG
  ZGP-based OPCPA
  Nd:YAG pumped BGGSe DFG

## Slide 3: LWIR laser at the Accelerator Test Facility
Polyanskiy et al. OSA Continuum 3, 459 (2020)

## Slide 4: Higher pump energy
Seed: 2 µJ
Two CO2 amplifiers
Amplification ~1011
Seed: 10 mJ
Single CO2 amplifier
Amplification ~103
Polyanskiy, et al. Photonics 8, 101 (2021)

## Slide 5: Raman + DFG
Welch, Opt. Express 26, 5143-5163 (2018)
Use Raman scattering to generate frequency shift equal to desired final frequency
Mix original pump laser with Raman shifted beam to produce desired final color
Typical Raman shifts in solids are on order of 1000 cm-1
Good match for LWIR
Relatively simple setup
Small footprint
Hard to tune

## Slide 6: Raman conversion in calcite
simulated
Note: could potentially switch to MIR pump

## Slide 7: ZGP-based OPA
Chemical formula: ZnGeP2
Broad transmission spectrum (.74 – 12 um)
High nonlinear coefficient (75 pm/V)
Plot and picture of crystal from Inrad Optics
Broad tunability
Complicated setup

## Slide 8: Cr:ZnSe/ZnS pumped OPA
Yin, Sci. Reports 7, 45794 (2017)
Lu, Optica 10, 1567-1570 (2023)
Recently, 200 mJ, sub-ps pulses demonstrated with Cr:ZnS amplifer

## Slide 9: Non-collinear OPCPA
Jutas, CLEO 2024
10 mJ projected output

## Slide 10: Test of ZGP OPO amplification in CO2
Zhu, Photonics 11, 154 (2024)

## Slide 11: Nd:YAG DFG in BGGSe
Yang, Opt. Express 32, 11182 (2024)
Convenient sources
Hard to tune
Relatively untested

## Slide 12: Conclusion
Several promising pathways to generating 10 mJ LWIR seeds
Need community to push this effort forward
 | Raman + DFG | ZGP OPCPA | Nd:YAG BGGSe DFG
Ease of setup | Relatively simple | Complex | Complex
Tunability | Low | High | Low
Size | Small | Large | Medium
Enabling technologies | BGS/BGSe crystal growth (Cr:ZnS/ZnSe lasers) | Cr:ZnS/ZnSe lasers ZGP crystal growth | BGGSe crystal growth