## Slide 1: Two-color Ionization injection of high-quality electrons
Navid Vafaei-Najafabadi

## Slide 2: Synthesis
Plasma accelerators create accelerating gradients that are hundreds of times higher than conventional accelerators
A “plasma photoinjector” for a collider application needs to create
  Low emittance (<100 nm)
  High charge (order of nC)
  Trapezoidal shape for low energy spread in subsequent accelerating plasma stages
By applying the spatiotemporal pulse shaping to two-color ionization injection, such plasma photoinjector can be demonstrated at ATF

## Slide 3: Dream of Compact & Efficient Plasma Collider
Plasma-Based Acceleration
Gradient: 20 GV/m
Plasma
Gradient: 10+ GV/m
SLAC
Gradient: 10-20 MV/m
Slide Courtesy of Dr. J. L. Shaw, LLE, Rochester
Notes: Talking Point:
-My work has focused on improving the electron beam and x-rays from LWFA.

## Slide 4: Luminosity
In addition to energy, beam quality is a critical consideration
In colliders, quality is measured by Luminosity
C.B. Schroeder et al 2023 JINST 18 T06001
DOI 10.1088/1748-0221/18/06/T06001
Beam charge High charge
Focusability low emittance and energy spread
& & Q
Beam collision rate High rate
Plasma Collider: kHz
Plasma Collider: pC ,
Plasma Collider:
Emittance, nm
Energy spread, 1%
Notes: Having a high acceleration gradient is not enough, you also need a high quality beam
Luminosity determines number of events (collisions) per second

## Slide 5: LWIR-driven laser wakefield acceleration
Strength of ponderomotive force scales with , so LWIR drivers can reach with modest intensities (at ~20 TW power)
can be reached by and LWIR laser without triggering self-injection in LWFA*
Bubble created by LWIR driver can be >100 µm, providing the ability for precise alignment of multiple beams with respect to the bubble
P. Kumar, Physics of Plasmas, 28, 013102 (2021)
,
P=20 TW,
𝜏=0.5 ps,
cm-3
* See A. Jain, Proceedings of AAC 2022
Accelerator Facilities Division

## Slide 6: Two-color ionization injection
Yu, PRL 112, 125001 (2014)
Schroeder, European Conference on Lasers and Electro-Optics (2015)
Schroeder, PRSTAB 17, 101301 (2014)
A second laser can trigger ionization injection in the wakefield driven by the LWIR laser, creating a high-quality beam
Drive laser needs large to form plasma wakefield, but we want low field to avoid prematurely ionizing the gas
Injector laser needs high field to ionize the gas, but low to avoid disturbing the plasma
ATF is ideally suited for this experiment:
  ATF CO2 :driver
  ATF Ti:Sapphire: injector
Low emittance
Excellent phase space
Very intense, small
Less intense, large
Accelerator Facilities Division

## Slide 7
Shortcomings
The charge produced is low (3-30 pC)
Lack of beam loading results in relatively large energy spread (few %)
Solutions
Inject a trapezoidal beam and flatten the plasma wakefield through beamloading
M. Tzoufras, Phys. Rev. Lett. 101, 145002 (2008)

## Slide 8: Varying the location of ionization is possible through spatiotemporal control of the ionizing laser
By varying the chirp, the region of peak intensity (focus) can be made to travel at any velocity

## Slide 9: Motion of the focus with corresponds to an “ionization wave” in the co-moving coordinate
Used as ionizing laser, this results in injection of ~ trapezoidal profile as electrons are injected where , and the function has a parabolic profile
A. Jain, in preparation

## Slide 10
This “Photoinjector” produces an e-beam that is perfectly suited for acceleration in subsequent plasma wakefield “stages”
The luminosity value attributed to such a beam would be compatible with all proposed plasma wakefield collider schemes and competitive with conventional collider beams

## Slide 11: Quad Chart
Scientific/Technical Outcomes Outcomes: Very bright, high-charge electron beams Approach: Spatiotemporal control over NIR laser to initiate ionization injection in a plasma wakefield driven by a CO2 laser | Lasers/e-beam Parameters Required 20 TW CO2 laser pulse ~ 25 mJ of (second harmonic of) Ti:Sapphire Need stable synchronization e-beam for alignment capability (transverse probe)
Facilities Upgrade Roadmap Upgrade CO2 laser to enable 20 TW with pulse length <0.5 ps | Beyond the Current Roadmap N/A

## Slide 12: Summary
Plasma accelerators create accelerating gradients that are hundreds of times higher than conventional accelerators
A “plasma photoinjector” for a collider application needs to create
  Low emittance (<100 nm)
  High charge (order of nC)
  Trapezoidal shape for low energy spread in subsequent accelerating plasma stages
By applying the spatiotemporal pulse shaping to two-color ionization injection, such plasma photoinjector can be demonstrated at ATF

## Slide 13: The End

## Slide 14
a
b
c
d
e
f
g
d
pC
nC

## Slide 15
Injected Charge Evolution due to Flying Focus
ff laser- , / 0.18,
CO2 laser- , , s, ,

## Slide 16
Slope= 0.22
,

## Slide 17: Beam Loading Physics

## Slide 18
Krypton Ionization Rates