## Slide 1
EIC beam (crossing) structure
 | Electron Storage Ring (ESR) | Hadron Storage Ring (HSR) (Nb=290) | HSR (Nb=1160)
Circumference C [m] | 3833.940 | match Trev | match Trev
Revolution period Trev=C/c [µs] | 12.7886 |  | 
RF harmonic number h [-] | match HSR | 2520 | 7560
RF bucket spacing Tb=Trev/h [ns] NOT bunch spacing!!! | match HSR | 5.075 | 1.692
Number of bunches Nb | match HSR | 290 | 1160
Bunch spacing Tbun [ns] | match HSR | 40.599 | 10.150
Gap length [ns] | match HSR | 1015 | 1015
Beam crossing: 98.5MHz
Orbit period: 12.7886 µs
 | ESR | HSR
RMS bunch length sz [mm/ps] | 7-9/23-30 | 75-60/250-200
RMS momentum spread [10-4] | 5.8-10.9 | 10.3-6.8
RMS horiz beam size sx [um] | 100-250 | 
sz/sx ratio [-] | 28-90 | 240-750
Electron Beam Energy: 5 – 18 GeV
Proton Beam Energy: 41, 100, 275 GeV
Luminosity: 1034 cm-2s-1

## Slide 2
EIC beam (crossing) structure
1 2 3 4 5 6 7 8
3 4 5 6 7 8 9 0 1 2 3 4
5 5 5 5 5 5 5 6 6 6 6 6
1 1 1 1 1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 1 1
2 2 2 2
1 1 1 1
7 8 9 0
5 5 5 6
2 2 2 2
1 1 1 1
7 8 9 0
5 5 5 6
1 2 3 4
1160 (all or 1/4 with beam)
100 (no-beam /gap)
Orbit period: 1260*10.150 ns = 12.7886 µs
The natural streaming readout time slice: N*12.7886 µs
Streaming Data
Beam crossing ( * electron ion collision )
Time Slice M+5
Time Slice M-1
Time Slice M+4
Time Slice M+3
Time Slice M+2
Time Slice M+1
Time Slice M
SRO data header:
Packet number,
Data source ID,
Starting orbit count
SRO data trailer:
Ending orbit count
Sync/Error/buffer status
Total word count
*If this is used, there will be less data overlapping in between the time slice (the overlap can still occur if the detector response time is longer than 1 µs). There will be easier synchronization check.
* * * * * * * *
* * * * * * * *
* * * * * * * *

## Slide 3
2. ePIC Design - general structure
GTU: Global Timing Unit
  control encoding, status decoding.
  The interface for machine clock source,
  Data acquisition control and monitor etc.
DAM: Data Aggregation Module:
  The clock/control fanout, and status/busy accumulation.
  local control over the RDO boards connected, though the main function of the DAM is for Data Acquisition.
RDO: optical interface of detector ReaDOut
  control decoding, status encoding.
  The clock/control interface to the front end electronics.
  Data collection from Frontend boards, and data transmission to the DAM
FEB:
  Detector dependent Front End / ASIC carrier boards.
GTU
Clock
Control
Status
DAM
DAM
RDO
RDO
RDO
RDO
Data Acquisition
DAM
(O)100
RDO
(O)1000
GTU (O)1
ePIC
EIC
Common
Platform
Online computer
4
FEB
FEB
FEB
System Clock: 98.5 MHz (100MHz nominal)

## Slide 4
3. Detailed signal implementations
3.1 Clock Distribution
EIC
common platform
GTU
RunControl computer
System clock
(98.5MHz)
Two-level fanouts
Beam orbit
Ethernet
DAM
Clock fanout
(optional jitter cleaner)
DAQ
PCB and fanouts:
Additive Jitter <1ps
Phase: fixed
Fiber cable:
Additive Jitter <1ps
Phase: fixed
PCB and fanouts:
Additive Jitter <1ps
Phase: fixed
RDO
Clock recovery
(optional iitter cleaner)
Clock fanouts
Control
Config
DAQ
Optic fiber cable:
Additive Jitter <1ps
Phase: fixed
GTY REC Clock:
Additive Jitter <3ps
Phase: stable, but NOT fixed;
Automatic Reset to fix.
RunControl: Run_Start/Stop, Run_type, config, Reset, Synchronization, SRO time_start/stop, Trottling…
Status: Buffer busy, out of sync …
GTY
Control config, status
Host PC
TX/RX
RefClk
Beam Orbit synchronized RunControl
GTY
TX/RX
RefClk
RecClk
FEB/ASIC
3.2 RunControl and DAQ
RunControl: forward or ‘hijack’ the GTU control;
DAM, RDO, FEB/ASIC configuration, readout backpressure
Status: Buffer, sync, etc.
Config synchronized with beam orbit, FEB/ASIC readout and control
Status: Buffer, sync, etc.
Beam Crossing phase aligned
Beam orbit phase aligned

## Slide 5
Problem:
We are assuming that the clock from EIC Common Platform is precise (0 ps jitter, fixed phase relative to the BeamCrossing), but it is not true.
Slow drift as the temperature changes (day, season…)
EIC
common platform
GTU
RunControl computer
System clock
(98.5MHz)
Two-level fanouts
Beam orbit
Ethernet
DAM
Clock fanout
(optional jitter cleaner)
DAQ
RDO
Clock recovery
(optional iitter cleaner)
Clock fanouts
Control
Config
DAQ
GTY
Control config, status
Host PC
TX/RX
RefClk
Beam Orbit synchronized RunControl
GTY
TX/RX
RefClk
RecClk
FEB/ASIC
Beam Crossing phase aligned
Even the dedicated clock distribution will have the same problem

## Slide 6
Proposal:
Beam pickup, and digital feedback to GTU
EIC
common platform
GTU
RunControl computer
System clock
(98.5MHz)
Two-level fanouts
Beam orbit
Ethernet
DAM
Clock fanout
(optional jitter cleaner)
DAQ
RDO
Clock recovery
(optional iitter cleaner)
Clock fanouts
Control
Config
DAQ
GTY
Control config, status
Host PC
TX/RX
RefClk
Beam Orbit synchronized RunControl
GTY
TX/RX
RefClk
RecClk
FEB/ASIC
Beam pickup
RDO(area) Clock
Phase#1
Phase#2
Phase#1160
Phase#1
PhaseOrbit (average)
GTU: Phase Correction
RF-SoC (?)

## Slide 7
ppRDO
Clocking scheme
Optic transceiver
RX
TX
1:4 fanout
Out1
Out0
FPGA
GTY
RX
TX
Si5345
Out0
Out2
Out1
IN2
RxRECclk
Phase difference detection
Fiber
optional emergency circuit I2C
RDO
(N/M)* 98.5 MHz
197 or
394 MHz
control
ClkRef
pseudoClock
98.5 MHz
Out9
IN3
Zero Delay FB
DAM
W16/Y16
W17/W18
K5/K6
M5/M6
H1/H2
G3/G4
14/15
23/24
27/28
30/31
ePIC_Clock
( Pll_cc )
(reset)
Si53302
RED/RED: FPGA package pins, or Si5345 package pins
Data/control
To/from MGT
TX
RX
ClkRef0
ClkRef1
RxPLL
AA4/AA3
Y6/Y5
P6/P5
V6/V5
Optic transceiver
RX
TX
Si5338
17/18
9/10