## Slide 1
Agenda
Revisit Far Backward Detectors over next few weeks: today low Q2 tracker – Simon Gardner
MAPS calibration and impact on RDO – Jo Schambach
June 10-11: PDR2 and lpGBT / VTRX+ FDR
Internal RDO review for dRICH RDO & Fiber protocol document
  Discussed at last two DAQ meetings
  High priority, but still needs to be done
AOB

## Slide 2
Intro to the revisit of the far backward overviews…
Revisit Far Backward Detectors (Current situation as regards full DAQ group, but I think there have been advances)
Detector | Subdetector | Channels | Sensor | Readout | ASICs | FEB | RDO | Fiber Pair | FELIX | RDO Data Rate (gbps) | TAPE Data Rate (gbps) | 
Low Q2 | 2 x Trackers | 33,030,144 | Timepix4 | Timepix4 | 144 | n/a | 12 | 120 | 5 | 150 | 10 | Software Trigger to reduce tape rate May not fully handle high luminosity Special 12 TX fiber RDO (SPIDR4)
 | 2 x Calorimeters | 2x144 | SiPM | Discrete? |  |  | 1 | 1 | 1 | n/a | n/a | 
Lumi Pair Spectrometer | 2 x Calorimeter | 2x900 | SiPM/ Flash | H2GCROC/ Discrete? |  |  | 1 | 1 | 1 | 19.2 | 6.4 | Magnet / converter / magnet removes ep pairs, then creates new ones, then spreads them out Controls Rates but still high
 | 2 x Tracker | 2x64,000 | AC-LGAD Strips | FCFD/ EICROCx? | 1000 | 100 | 10 | 15 | 1 | 45 | 2 | 
Direct Photon Calorimeter | 2 x Calorimeter | 2 x 100 | (SciFI/Crystal) - SiPM | 200 MHz Streaming Flash? |  |  | 2 | 2 | 1 | 200 | 6.4 | Channel streaming Flash readout Aggregated by BX Channels aggregated over time (1s) 1 Calorimeter in use at a time
Today: Low Q2 --- Simon Gardner

## Slide 3
DET | lpGBT(SC) | VTRX+(SC) | VTRX+(TX) | VTRX+(TOTAL) | TX | RX
IB | 24 | 24 | 136 | 160 | 664 | 24
OB | 55 | 55 | 440 | 495 | 1815 | 55
EE | 52 | 52 | 410 | 462 | 1692 | 52
HE | 52 | 52 | 410 | 462 | 1692 | 52
 | 183 | 183 | 1396 | 1579 | 5863 | 183
Fibers / VTRX+ | TX | RX
SC (Slow Controls) | 1 | 1
TX (Data Transfer) | 4 | 0
Concept | Count | Aggregate Rate Available to DAQ
96 simplex fiber / DAM boards | 63 FELIX boards ($1.2M) | 6,300 gbps
32 simplex fiber / RDO (aggregator as of Jan Collab Meeting) | 190 RDO ($450k) / 4 DAM ($72k) | 400 gbps
Intro to MAPS calibration and impact on RDO discussion:
During a recent MOSAIX (current prototype of the ITS3 MAPS sensor) review some time estimates were presented regarding configuration and calibration of this sensor:
Assuming need to mask 1% of the pixels, time to configure 1 tile (base unit of the pixel matrix): 0.03 seconds
Same assumptions, time to configure 1 segment (one “row” of stitched sensors): 4 seconds
Assuming parallel scans are possible, a threshold scan with a DAC resolution of 256, pulses per settings: 50, integration window 100us, gap between rows 1000us, readout polling 500us, will take 20 minutes
Same assumptions, but sequential (rather than parallel readout): 29 hours

## Slide 4
DET | lpGBT(SC) | VTRX+(SC) | VTRX+(TX) | VTRX+(TOTAL) | TX | RX
IB | 24 | 24 | 136 | 160 | 664 | 24
OB | 55 | 55 | 440 | 495 | 1815 | 55
EE | 52 | 52 | 410 | 462 | 1692 | 52
HE | 52 | 52 | 410 | 462 | 1692 | 52
 | 183 | 183 | 1396 | 1579 | 5863 | 183
Fibers / VTRX+ | TX | RX
SC (Slow Controls) | 1 | 1
TX (Data Transfer) | 4 | 0
Concept | Count | Aggregate Rate Available to DAQ
96 simplex fiber / DAM boards | 63 FELIX boards ($1.2M) | 6,300 gbps
32 simplex fiber / RDO (aggregator as of Jan Collab Meeting) | 190 RDO ($450k) / 4 DAM ($72k) | 400 gbps
Intro to MAPS calibration and impact on RDO discussion:
During a recent MOSAIX (current prototype of the ITS3 MAPS sensor) review some time estimates were presented regarding configuration and calibration of this sensor:
Assuming need to mask 1% of the pixels, time to configure 1 tile (base unit of the pixel matrix): 0.03 seconds
Same assumptions, time to configure 1 segment (one “row” of stitched sensors): 4 seconds
Assuming parallel scans are possible, a threshold scan with a DAC resolution of 256, pulses per settings: 50, integration window 100us, gap between rows 1000us, readout polling 500us, will take 20 minutes
Same assumptions, but sequential (rather than parallel readout): 29 hours
Questions:
RDO scheme – Does the calibration need affect the RDO concept
  Is the 29 hours driven by data volume? If so which Data Volume?
  What calibration? Is this a frequent event?
There needs to be a synchronization of the 2us strobes. Is this (can this?) be done by the SC links. If not, how is it done?

## Slide 5
June 10th and 11th Review
This review is, and should be thought of as 2 different reviews:
PDR2 – for electronics and DAQ in general
FDR – for VTRX+ and lpGBT
Page turns / rehearsal week of June 3
Final Talks posted June 7th

## Slide 6
EIC - Electronics & DAQ – Preliminary Design Review (PDR) Charge Questions
Are the technical performance requirements appropriately defined and complete for this stage of the project?
Are the plans for the various detector electronics and data acquisition systems appropriately documented and complete for this stage of the project?
Are the current plans from front-end electronics to data acquisition for the detector likely to achieve the technical performance requirements, with a low risk for cost increases, schedule delays, and technical problems?
Are the schedule assumptions for the fabrication of the various electronics and data acquisition systems and assembly plans reasonable and consistent with the overall detector schedule?
Have ESH&Q and QA considerations been adequately incorporated into the plans at their present stage?
PDR Charge and Schedule:

## Slide 7
PDR Charge and Schedule:
10 June 2024
8:00 Introduction Elke/Rolf 15 min
8:15 Electronics Overview Fernando 20 min
8:35 DAQ Overview Jeff 20 min
9:55 DAQ Overview 2 David 20 min]
10:15 Coffee 15 min
10:30 RDO ppRDO Tonko 20 min
10:50 RDO dRICH Fabio 20 min
11:10 Timing William 30 min
11:50 Coffee 25 min
Final Design Review for lpGBT/VTRX+
12:15 Requirements Fernando 20 min
12:35 lpGBT/VTRX+ [Tracking] Jo 20 min
12:55 VTRX+ [dRICH] Pietro 20 min
13:15 Discussion 15 min
13:30 Adjurn
11 June 2024
8:00 Readout/ASIC Overview Fernando 20 min
8:20 Discrete Readout Gerard 30 min
8:50 EICROC Christophe 30 min
9:20 Coffee 15 min
9:35 CALOROC Frederique 30 min
10:05 FCFD Artur 30 min
10:35 Coffee 15 min
10:50 ALCOR Fabio 30 min
11:20 SALSA Damien 30 min
11:50 Discussion 15 min
12:05 Summary Elke/Rolf 15 min
12:20 Adjurn

## Slide 8
EIC - VTRx+/lpGBT - Final Design Review (FDR) Charge Questions
Are the technical performance requirements and subsystem interfaces complete, documented, and understood?
Are the plans for achieving VTRx+ and lpGBT performance and construction sufficiently developed and documented for the present phase of the project, i.e., are they commensurate with the planned initiation of the procurement?
Do the design and specifications meet the performance requirements with a low risk of cost increases, schedule delays, and technical problems?
Are the fabrication and assembly plans consistent with the overall project and detector schedule and sufficiently developed to initiate the procurement?
Are the plans for integration in the ePIC detector appropriately developed to initiate the procurement?
Have previous review recommendations been adequately addressed to initiate the procurement?
Have ES&H and QA considerations been adequately incorporated in the design and procurement planning?
Is the procurement approach sound and the procurement schedule credible?
Final Design Review for lpGBT/VTRX+
12:15 Requirements Fernando 20 min [procurement, EH&S and QA, Cost/Schedule]
12:35 lpGBT/VTRX+ [Tracking] Jo 20 min - What depth needed for this review?
12:55 VTRX+ [dRICH] Pietro 20 min - What depth needed for this review?
13:15 Discussion 15 min
13:30 Adjourn
FDR Schedule: (on June 10th)

## Slide 9
EIC - VTRx+/lpGBT - Final Design Review (FDR) Charge Questions
Are the technical performance requirements and subsystem interfaces complete, documented, and understood?
Are the plans for achieving VTRx+ and lpGBT performance and construction sufficiently developed and documented for the present phase of the project, i.e., are they commensurate with the planned initiation of the procurement?
Do the design and specifications meet the performance requirements with a low risk of cost increases, schedule delays, and technical problems?
Are the fabrication and assembly plans consistent with the overall project and detector schedule and sufficiently developed to initiate the procurement?
Are the plans for integration in the ePIC detector appropriately developed to initiate the procurement?
Have previous review recommendations been adequately addressed to initiate the procurement?
Have ES&H and QA considerations been adequately incorporated in the design and procurement planning?
Is the procurement approach sound and the procurement schedule credible?
Final Design Review for lpGBT/VTRX+
12:15 Requirements Fernando 20 min [procurement, EH&S and QA, Cost/Schedule]
12:35 lpGBT/VTRX+ [Tracking] Jo 20 min - What depth needed for this review?
12:55 VTRX+ [dRICH] Pietro 20 min - What depth needed for this review?
13:15 Discussion 15 min
13:30 Adjourn
FDR Charge and Schedule: (on June 10th)
These questions relate to VTRX+ and lpGBT themselves. How, and to what extent to we address them directly?

## Slide 10
EIC - VTRx+/lpGBT - Final Design Review (FDR) Charge Questions
Are the technical performance requirements and subsystem interfaces complete, documented, and understood?
Are the plans for achieving VTRx+ and lpGBT performance and construction sufficiently developed and documented for the present phase of the project, i.e., are they commensurate with the planned initiation of the procurement?
Do the design and specifications meet the performance requirements with a low risk of cost increases, schedule delays, and technical problems?
Are the fabrication and assembly plans consistent with the overall project and detector schedule and sufficiently developed to initiate the procurement?
Are the plans for integration in the ePIC detector appropriately developed to initiate the procurement?
Have previous review recommendations been adequately addressed to initiate the procurement?
Have ES&H and QA considerations been adequately incorporated in the design and procurement planning?
Is the procurement approach sound and the procurement schedule credible?
Final Design Review for lpGBT/VTRX+
12:15 Requirements Fernando 20 min [procurement, EH&S and QA, Cost/Schedule]
12:35 lpGBT/VTRX+ [Tracking] Jo 20 min - What depth needed for this review?
12:55 VTRX+ [dRICH] Pietro 20 min - What depth needed for this review?
13:15 Discussion 15 min
13:30 Adjourn
FDR Schedule: (on June 10th)
To what extent does this exist?
This is complicated by tax issues and import controls issues. Have the specific transfers been defined, or can they be defined at this stage, and are they consistent with the detector assembly plans?

## Slide 11
AOB?