## Slide 1: EndCap Tracker Strip Pattern
Seungjoon Lee

## Slide 2: Half disc – full length
900 mm
460 mm
Direction | # of Channel
Vertical | 1800
Horizontal | 920
Total (Half circle) | 2720
Total (Full circle) | 5440
FEB (256ch) | 22
Max strip length = 900 mm
Strip pitch = 0.5 mm

## Slide 3: Half disc – half length (similar with quarter disc)
450 mm
460 mm
Direction | # of Channel
Vertical | 1800
Horizontal | 1840
Total (Half circle) | 3640
Total (Full circle) | 7280
FEB (256ch) | 30
Max strip length = 460 mm
Strip pitch = 0.5 mm

## Slide 4: Half disc – half length
770 mm
Direction | # of Channel
+45 degree | 1540
- 45 degree | 1540
Total (Half circle) | 3080
Total (Full circle) | 6160
FEB (256ch) | 24 (6144 ch) not 6160
Max strip length = 640 mm
Strip pitch = 0.5 mm
450 mm

## Slide 5: Spacing of the connector
Perimeter of 450 mm diameter MPGD outer frame = 2800 mm
Hirose FX20 (140pin, 90 degree) connector length = 50 mm
FEB requires two FX20 connectors = 100 mm
We can have 28 FEBs around the full disc. Without any extra space.
We need space for service cable in/out, mounting, etc.
Realistic FEB can be around 24.
We probably need to sandwich FEBs for E-ECT.