## Slide 1
ePIC Timing Implementation for the Readout Chain
William Gu
Introduction: EIC beam (crossing) structure
Requirements
Overall hardware design
Detailed signal implementations
Clock distribution test results
Status and Summary

## Slide 2
EIC beam (crossing) structure
 | Electron Storage Ring (ESR) | Hadron Storage Ring (HSR) (Nb=290) | HSR (Nb=1160)
Circumference C [m] | 3833.940 | match Trev | match Trev
Revolution period Trev=C/c [µs] | 12.7886 |  | 
RF harmonic number h [-] | match HSR | 2520 | 7560
RF bucket spacing Tb=Trev/h [ns] NOT bunch spacing!!! | match HSR | 5.075 | 1.692
Number of bunches Nb | match HSR | 290 | 1160
Bunch spacing Tbun [ns] | match HSR | 40.599 | 10.150
Gap length [ns] | match HSR | 1015 | 1015
Beam crossing: 98.5MHz
Orbit period: 12.7886 µs
 | ESR | HSR
RMS bunch length sz [mm/ps] | 7-9/23-30 | 75-60/250-200
RMS momentum spread [10-4] | 5.8-10.9 | 10.3-6.8
RMS horiz beam size sx [um] | 100-250 | 
sz/sx ratio [-] | 28-90 | 240-750
Electron Beam Energy: 5 – 18 GeV
Proton Beam Energy: 41, 100, 275 GeV
Luminosity: 1034 cm-2s-1

## Slide 3
EIC beam (crossing) structure
1 2 3 4 5 6 7 8
3 4 5 6 7 8 9 0 1 2 3 4
5 5 5 5 5 5 5 6 6 6 6 6
1 1 1 1 1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 1 1
2 2 2 2
1 1 1 1
7 8 9 0
5 5 5 6
2 2 2 2
1 1 1 1
7 8 9 0
5 5 5 6
1 2 3 4
1160 (all or 1/4 with beam)
100 (no-beam /gap)
Orbit period: 1260*10.150 ns = 12.7886 µs
Beam crossing ( * electron ion collision )
* * * * * * * *
* * * * * * * *
* * * * * * * *

## Slide 4
2. Requirements
Streaming Data
Time Slice M+5
Time Slice 1 …
Time Slice M+4
Time Slice M+3
Time Slice M+2
Time Slice M+1
Time Slice M
START
RE-START
RE-START
START
RE-START
RE-START
STOP
RE-START: STOP and START at the same Beam Crossing
Whole detector dead time
RE-START
2.1 The whole detector has a single clock source to align the streaming data slices;
2.2 jitter of the FEE/ASIC received clock: less than 5ps;
2.3 For TOF detectors, the phase of the clock relative to the beam crossing center point is stable (< 5ps)
2.4 For ? detectors, the phase of the clock relative to the beam crossing center point is stable (zero suppression)

## Slide 5
3. Overall Hardware Design
GTU: Global Timing Unit
  control encoding, status decoding.
  The interface for machine clock source,
  Data acquisition control and monitor etc.
DAM: Data Aggregation Module:
  The clock/control fanout, and status/busy accumulation.
  local control over the RDO boards connected, though the main function of the DAM is for Data Acquisition.
RDO: optical interface of detector ReaDOut
  control decoding, status encoding.
  The clock/control interface to the front end electronics.
  Data collection from Frontend boards, and data transmission to the DAM
FEB:
  Detector dependent Front End / ASIC carrier boards.
GTU
Clock
Control
Status
DAM
DAM
RDO
RDO
RDO
RDO
Data Acquisition
DAM
(O)100
RDO
(O)1000
GTU (O)1
ePIC
EIC
Common
Platform
Online computer
4
FEB
FEB
FEB
System Clock: 98.5 MHz (100MHz nominal)

## Slide 6
3. Overall hardware design
GTU fanouts (1:~200):
Additive Jitter <1ps; Phase: fixed
Dedicated (clock only, 197 Mbps) fiber
Additive Jitter <1ps; Phase: fixed
DAM fanouts (1:12):
Additive Jitter <1ps; Phase: fixed
1:1 (Clock/Control, 7.88 (/3.94)Gbps) fiber:
Additive Jitter <1ps; Phase: fixed
RDO RECovered Clock:
Additive Jitter <3ps; Phase: stable,
fixed with PseudoClock
Clock Distribution
Beam Crossing phase aligned
Beam orbit phase aligned
  MGT Clock/Control encoding (1:4):
  Additive Jitter <~ps; Phase: stable, can be fixed
Control
EIC
common platform
GTU
RunControl computer
System clock
(98.5MHz)
Two-level fanouts
Beam orbit
Ethernet
DAM
Clock fanout
(optional jitter cleaner)
DAQ
RDO
Clock recovery
(optional iitter cleaner)
Clock fanouts
Control
Config
DAQ
GTY
Control config, status
Host PC
TX/RX
RefClk
Beam Orbit synchronized RunControl
GTY
TX/RX
RefClk
RecClk
FEB/ASIC
8-bit, 24-bit, 32-bit, 48-bit, 64-bit every clock cycle (10.15ns)

## Slide 7
4. Detailed signal implementations
4.1: Fiber link between GTU and DAM:
Using FireFly TX/RX modules will save power than regular QSFP optic transceivers, but the fiber connection/mapping can be challenging (easy to make mistake).
It is ok to send more (than 8-bit) data between GTU and DAM per clock cycle, but not needed.
GTU
DAM
Clock @ 98.5 MHz
GTU_CONTROL, 8-bits (+ 1 k_bit) @ 98.5 MHz
DAM/RDO Status, 8-bits (+ 1 k_bit) @ 98.5 MHz
Clock feedback @ 98.5 MHz, 197 MHz, or maybe 394 MHz (optional)
Receivers
Transmitters
Receivers
Transmitters
Downlink
Uplink
The GTU will have ~150 ports (four fiber per port). Each port can connect to one DAM.

## Slide 8
4. Detailed signal implementations
4.2: Fiber link between DAM and RDO:
Fiber length/signal delay to be measured, and delay compensated on RDO
RunControl (from GTU) is guaranteed every beamcrossing cycle (98.5MHz). It can be hijacked by the DAM for sub-system test
The RDO/FEB configuration depends on the specific DAM (which comes from the host computer).
The DOWNLINK can be 3.94 Gb/s (40 bits @ 98.5 MHz) to accommodate the VTRX+ optic transceivers
The UPLINK can be 10 Gb/s (up to 12 Gb/s) if needed.
The ¼ clock period of 0...01…1 I should be reserved for alignment, which is also compatible with the pseud_oclock patterns
DAM
RDO
DOWNLINK @ 7.88 Gb/s (80 bits @ 98.5 MHz)
UPLINK @7.88 Gb/s (80bits @98.5 MHz)
MGT_RX
MGT_TX
MGT_TX
MGT_RX
1:2
System Clock Generation
(and Phase
Detection)
Rx_REC_Clk
Pseudo_Clock: 0x0000_0003_FFFF_FFFF_FC00 (LSB first)
CONTROL: DAM3_DAM2_DAM1_DAM0_GTU1_GTU0_FFC00
* DAMn, GTUn are 8b10b encoded
IDLE: 0x0000_0003_FFFF_FFFF_FC00 (LSB first)
STATUS: STAT3_STAT2_STAT1_STAT0_STAT_ENABLE_FFC00
DATA: 64-bit Frontend data with 8b10b encoding
CDR_reset
FEB/ASICs
Each DAM will have 48 ports (one pair of fibers per port). Each port can connect to one RDO.

## Slide 9
5. Clock distribution test results
5.1: RDO RECovered clock: jitter σ < 3ps, no jitter cleaner is required.

## Slide 10
5. Clock distribution test results
5.1: RDO RECovered clock: jitter and phase.
RxRECclk jitter < 3 ps
RxRECclk phase can be fixed at ~(0)ps precision
(by measuring the phase difference between the RxRECclk and the pseudoClock, and resetting the RxRECclk CDR.)
Si5344H  FLX182  KCU105/XEM8320

## Slide 11
5. Clock distribution test results
5.2: DAM MGT Tx phase stability
Si5344H KCU105_MGT_TX

## Slide 12
5. Clock distribution test results
5.3: PseudoClock from DAM (FLX182) to RDO (pre-prototype RDO): the ADCLK944 1:4 fanout
FLX182
ppRDO
(ADCLK944)
Si5344H
(ref Clock)
More tests (similar to 5.1 and 5.2) are expected

## Slide 13
5. Clock distribution test results
5.4: Dedicated Clock from GTU to DAM
5.5: Other clocks from RDO to FEB/ASIC:
Jlab’s 12GeV upgrade
Trigger SuperVisor
Signal Distributor
Trigger Distributor
Trigger Interface
PCB and backplane
Copper traces
Optic Transceivers
Multi-Mode fibers
PCB and backplane
Copper traces
Clock Jitter (from Trigger Interface) σ < 3ps
Used on the Trigger Interface modules to generate SYNCHRONIZED /2, /4, /6 and /8 lower frequency clocks
Analog Devices
AD9510
Additive output jitter (rms)
LVPECL: 225 fs
LVDS/CMOS: 275 fs

## Slide 14
6. Status and Summary
FLX155: Designed for ATLAS FELIX upgrade
DAM: Prototype FLX155 (ePIC DAM) is expected this year
RDO: preprotype RDO, six in hands, being tested
GTU: prototype is being considered
6.1: Status

## Slide 15
6. Status and Summary
6.1: Summary

## Slide 16
Backup slides

## Slide 17
What if:
6.1: The DAM can NOT send phase determined serialized clock/control (MGT TX phase undetermined)
Answer: Dedicated fiber connection from GTU to RDO to distribute the clock to Time Of Flight detector
6.2: The EIC common platform delivered clock is not as good as expected
Answer: There will be jitter cleaner chip on the GTU to receive the clock from EIC common platform;
We can (should) build the beam monitoring circuits to monitor and correct the phase (clock edge relative to the center of beam crossings) shift

## Slide 18
EIC
COMMON PLATFORM
EIC/ePIC clock & beam orbit info
Online computer
Run control
GT
Clock buffers
RDO (TOF)
RDO (TOF)
SFP
DAM
RDO
RDO
DAM
RDO
RDO
Could be a separate clock fanout PCB, if needed
GTU
FPGA
DAM
1 : ~200
May be needed, RDO(TOF) , DAM(dRICH)
CLOCK
RunControl
STATUS
GTU: Global Timing Unit

## Slide 19
LTI
FireFly
Tx/Rx
PCIexpress GEN4x16
2* GEN5x8
Clock
buffer
FPGA
Xilinx Versal
CLOCK
98.5MHz
RunControl
STATUS
GTU
100 GBE
RJ45
GigaBitEth
Fabric
Clock
RefClks
GTYs
(24/48)
TXs
RXs
FireFly
TX
FireFly
RX
RDO
RDO
Host Computer/DAQ
Network Switch/DAQ
RunControl
RDO/FEE config
Status merging
DataProcessing
DAM: Data Aggregation Module

## Slide 20
Optic transceiver
RX
TX
1:2 fanout
O1
O2
FPGA
GTY
RX
TX
Si53x5
O1
O0
O2
IN
RxRECclk
GENIO
FEB
Phase difference detection
Fiber
FEB
optional emergency circuit I2C
RDO
(N/M)* 98.5 MHz
197 or
394 MHz
control
ClkRef
pseudoClock
98.5 MHz
OUT
IN3
Zero Delay FB
DAM
RDO: ReadOut card
optional clock buffer

## Slide 21
Beam orbit cycle and ASIC clock requirement:
One orbit cycle = 1260 Beam Crossing (or ePIC system clock cycles)
1260 = 2x2 x 3x3 x 5 x 7
98.5 x 2 / 5 = 39.4 (MHz)
98.5 / 2 = 49.25 (MHz)
……

## Slide 22
Proposal:
Beam pickup, and digital feedback to GTU
EIC
common platform
GTU
RunControl computer
System clock
(98.5MHz)
Two-level fanouts
Beam orbit
Ethernet
DAM
Clock fanout
(optional jitter cleaner)
DAQ
RDO
Clock recovery
(optional iitter cleaner)
Clock fanouts
Control
Config
DAQ
GTY
Control config, status
Host PC
TX/RX
RefClk
Beam Orbit synchronized RunControl
GTY
TX/RX
RefClk
RecClk
FEB/ASIC
Beam pickup
RDO(area) Clock
Phase#1
Phase#2
Phase#1160
Phase#1
PhaseOrbit (average)
GTU: Phase Correction
RF-SoC (?)

## Slide 23
Phase/Jitter of the clock measuring method:
EIC/Common Platform/GTU clock: Si5344H as reference;
Oscilloscope Probes
Si5344H
KCU105
Si5394A
FLX182
Clk_98.6
Fiber_7.89
RxRecClk_197.3
ClkSys_98.6
ClkPD_98.6
Phase
Detect
CH#1
CH#2
CH#3
CH#3
MGT
1:2
Beam Crossing/Reference Clock
DAM MGT_TX output: FLX182/KCU105 pseudoClock
Encoded Clock
RDO/FEB Recovered Clock: XEM8320/KCU105 plus Si5394A
Recovered Clock
Phase/Jitter measuring method using a scope (Tektronix MSO64):
Phase difference == WIDTH of the difference of the two signals
Jitter == uncertainty of the WIDTH of the difference of the two signals assuming the reference clock is perfect.