## Slide 1: Electronics and DAQ Overview WBS 6.10.08 & 6.10.09
Electronics & DAQ PDR2 Review
June 10-11, 2024
Jeff Landgraf (BNL) & Dave Abbott (JLAB)
WBS 6.10.09 Data Acquisition (DAQ)
Fernando Barbosa(JLAB)
WBS 6.10.09 Data Acquisition (DAQ)

## Slide 2: Charge Questions Addressed
Are the technical performance requirements appropriately defined and complete for this stage of the project?
Are the plans for the various detector electronics and data acquisition systems appropriately documented and complete for this stage of the project?
Are the current plans from front-end electronics to data acquisition for the detector likely to achieve the technical performance requirements, with a low risk for cost increases, schedule delays, and technical problems?
Are the schedule assumptions for the fabrication of the various electronics and data acquisition systems and assembly plans reasonable and consistent with the overall detector schedule?
Have ESH&Q and QA considerations been adequately incorporated into the plans at their present stage?

## Slide 3: Outline
Documentation status
The readout technology and scale of the EPIC DAQ
  Collider environment
  Readout Technologies
  Streaming architecture
  System components and operational concepts
  Component counts & expected data flow
  Fiber protocol and operation
(Fernando Barbosa)
Electronics
(Dave Abbott)
DAQ and Computing related tasks for 2024
  Evaluating and defining timing and data protocol
  Development of RDOs
  FELIX boards
Echelon 0 (DAQ Computing)
Scientific computing Interface
Schedule
QA and ES&H
Summary

## Slide 4: Available Documentation
Prior review closeout documentation
2 documents with a more detailed overview of the electronics and DAQ
Project Requirements Doc
Project Interfaces Doc
Detector technology, channel counts, electronics board counts
Detailed data volume document broken down to component level
P6 electronics / DAQ
Schedule
Charge 2

## Slide 5: EIC Collider DAQ Environment
1260 Bunches arriving at 98.5Mhz (10.15ns bunch separation)
1.015us abort gaps (100 bunches)
⇒ 20 – 141 GeV
𝓛max ⇒ 1034 cm-2 s-1
Electron, proton, and light nuclei beams can be polarized.
  DAQ must tag data to specific bunch crossings
  Need to track luminosity for each bunch crossing
Charge 1&3

## Slide 6: Readout Technologies
~30 Detectors
Spread over +/- 40 meters
(13 bunch crossings @ C)
Many technologies, but effort has been made to make use of possible synergy…
Charge 1&3

## Slide 7: Readout Technologies
13 Calorimeters:
7 x SiPM – CALOROC
5 x SiPM – Discrete
1 x SiPM – Commercial fADC250
Charge 1&3

## Slide 8: Readout Technologies
Tracking:
4 x ITS3 – VTRX+ / lpGBT
3 x uRWELL – SALSA
1 x Micromegas – SALSA
AC-LGAD time of flight
Charge 1&3

## Slide 9: Readout Technologies
AC-LGADs:
6 x Pixels: EICROC
2 x Strips: FCFD / EICROCx
Charge 1&3

## Slide 10: Readout Technologies
3 RICH Detectors:
dRICH: SiPM – ALCOR
(needs single photon sensitivity)
pfRICH: HRPPD – FCFD / EICROCx
hpDIRC: MCPPMT – FCFD / EICROCx
(same FCFD / EICROCx as for
AC-LGAD strip detectors)
Charge 1&3

## Slide 11: Readout Technologies
MAPS (non-ITS3):
Imaging Barrel Calorimeter – Astropix
Low Q2 Tracker – Timepix4
Charge 1&3

## Slide 12: Streaming in ePIC
DAQ
Definition of streaming is “No L0 trigger”
  All data is zero suppressed by the front end electronics
  No system wide deadtime in normal operation
  Collaboration should have the full ability to make data selection cuts on the widest possible criteria
    Flexible event selection, data selection and background characterization
  But subject to an overall throughput budget of ~100Gb/sec
ePIC Streaming will include
  Capabilities for hardware and firmware based triggering
  Capability for flow control
  Zero suppression & aggregation within data packets
Greater sensitivity to noise than triggered system
Greater sensitivity to backgrounds than triggered system
Computing
Definition of streaming is “Process data as it arrives”
  Fast Analysis (~3 weeks not months or years) using automation of calibration and reconstruction.
Requires some overlap between DAQ/computing
  Automation of calibrations
    Mapping calibration dependencies
    Mapping application of calibrations
    Mapping evolution of calibrations
  QA and monitoring can make use of full offline structure
  Consistent schemes and language for data/metadata
  Event selection / tagging / and accounting
ePIC DAQ uses streaming architecture
Charge 3

## Slide 13: EIC Streaming DAQ/Computing Architecture
ePIC DETECTOR
BW O(100Tbps)
BW O(10Tbps)
BW O(100Gbps)
Bunch Crossing ~ 10.2 ns/98.5 MHz
Interaction Rate ~ 2 us/500 kHz
Low occupancy
GTU/Distributed clock
(jitter ~5ps)
Charge 1&3

## Slide 14: ePIC Readout Chain
Name
Design
Function
Attributes
Adapter
Detector Specific
-HV/Bias Distribution
-HV divider
-Interconnect Routing
-Sensor Specific
-Passive
Sensor
Detector Specific
Multi-Channel Sensor
MAPS, AC-LGAD
MPGD, MCP-PMT
SiPM, LAPPD
Front End Board
(FEB)
Detector Specific
-Amplification
-Shaping
-Digitization
-Zero Suppression
-Bias Control & Monitoring
-ASIC/ADC
-Discrete
-Serial Link
Readout Board
(RDO)
Few Variants
-Communication
-Aggregation
-Formatting
-Data Readout
-Config & Control
-Clock & Timing
-FPGA
-Fiber Link
Data Aggregation Module (DAM)
Common
-Computing Interface
-Aggregation
-Software Trigger
-Config & Control
-Clock & Timing
-Large FPGA
-PCIe
-Ethernet
Computing
Common
-Data Buffering and Sinking
-Calibration Support
-QA/Scalers
-Collider Feedback
-Event ID/Building
-Software Trigger
-Monitoring
-COTS
-Ethernet
Global Timing Unit (GTU)
-Interfaces to Collider, Run Control & DAM
-Config & Control
-Clock & Timing
On Detector
SMT BGA
Charge 3

## Slide 15: ePIC Readout Chain
Name
Design
Function
Attributes
Adapter
Detector Specific
-HV/Bias Distribution
-HV divider
-Interconnect Routing
-Sensor Specific
-Passive
Sensor
Detector Specific
Multi-Channel Sensor
MAPS, AC-LGAD
MPGD, MCP-PMT
SiPM, LAPPD
Front End Board
(FEB)
Detector Specific
-Amplification
-Shaping
-Digitization
-Zero Suppression
-Bias Control & Monitoring
-ASIC/ADC
-Discrete
-Serial Link
Readout Board
(RDO)
Few Variants
-Communication
-Aggregation
-Formatting
-Data Readout
-Config & Control
-Clock & Timing
-FPGA
-Fiber Link
Data Aggregation Module (DAM)
Common
-Computing Interface
-Aggregation
-Software Trigger
-Config & Control
-Clock & Timing
-Large FPGA
-PCIe
-Ethernet
Computing
Common
-Data Buffering and Sinking
-Calibration Support
-QA/Scalers
-Collider Feedback
-Event ID/Building
-Software Trigger
-Monitoring
-COTS
-Ethernet
Global Timing Unit (GTU)
-Interfaces to Collider, Run Control & DAM
-Config & Control
-Clock & Timing
On Detector
SMT BGA
Readout Board Flavors
Charge 3
Detector | Characteristics
TOF | Highest Timing Requirement (Generic)
dRICH | Small Footprint (VTRX+ optics)
ITS-3 | Detector side uses fiber (VTRX+)
Imaging Calorimeter | Integrated with ASTROPIX Sensor
Low Q Tracker | High Rates, 20 TX fibers expected / RDO
Direct Photon Calorimeter | Pure 200MHz Streaming (bypass DAQ protocol)

## Slide 16: Simulations of Data Volumes
The ePIC background group has evaluated background sources.
For data volume evaluation we have used:
18x275 DIS events, scaled to the maximum event rates to be seen in 10x275GeV DIS
10 GeV Electron beam gas events scattered from realistic vacuum under 10000Ahr of pumping
275 GeV Proton Beam gas events scattered from realistic vacuum under 10000Ahr of pumping
Synchrotron radiation is still under evaluation. Recent results have shown both that Synchrotron radiation
is a potentially serious issue with the currently implemented beam line, but also that relatively simple remediation schemes can lower the rate significantly.

## Slide 17: Summary of Channel Counts and Data Flow
FEB
RDO
Readout Computer
Detector
DAM
PCI/Eth
Fiber
Copper
100% Occupancy | 27.5-1760 Pb/sec
Aggregate | 2.3 Tb/sec
Noise | 1.6 Tb /sec
Signal from Physics + Background | 700 Gb / sec
Aggregate | 2.3 Tb/sec
Per RDO (Avg) | 0.8 Gb/sec
Eth
Aggregate | Gb/sec
Collision Signal | 41.6 Gb/sec
Synchrotron Rad | Under design
Electron Beam | 4.5 Gb/sec
Hadron Beam | 1.0 Gb/sec
Noise | 40 Gb/sec
Summary of Data Flow
Charge 3

## Slide 18: Data Bottlenecks
Charge 3
Detector | Noise (hz/channel)
ITS3 | 0.01
Astropix | 0.01
Timepix | 0.01
AC-LGAD | 30
HRPPD | 230
dRICH(initial) | 3000
dRICH(Max) | 300,000
All others | 4σ = 311
Evaluated Data Bottlenecks by tiling detector regions with RDO/ASIC combos
RDO data volume spec 10 gbps
  CALOROC expected to have inefficient readout (single hit reads out N samples x 18 channels)
  Remediate by readout 1 sample,
  By suppressing empty channels in RDO
  By using fewer populated FEB per RDO in strategic locations
dRICH dark currents handled by firmware trigger
Preliminary Noise Assumptions
Direct Photon Detector ~100 channels direct streaming, readout only summary

## Slide 19: Fiber Protocol / DAQ operation
Synchronous Commands:
64 bits (80 bits 8b/10b encoded) per bunch
Reconstructed clock
Redundant BCO
Distinct synchronous commands (eg)
  RC
  Time Frame Control & Definition
  Flow Control
  Trigger
    Request special events
    Data filter (firmware trigger)
  Configuration (ASIC / RDO firmware)
  Data Formatting
  Data Transfer
    Hits
    Slow Controls
Time Frame Definition:
16 bits BCO (0.66ms -> 8MB @ 100Gbps)
Flexible formatting
  Filtered & Unfiltered data can coexist
Time Frames are built, they contain the full set of detectors for the time period
Tiered Data Format.
  High level flexible, named navigation via banks (e.g. star SFS, sPHENIX DAQRC)
  Low level supports direct, detector specific (eg ASIC) formats.
Trigger Operation:
Support Max Data Volume to DAM / Readout computer Buffers
Generate Trigger Signals in DAM
Communicate triggered crossings via synchronous cmds through GTU
Charge 3

## Slide 20: Summary
Described an overview of the readout system for ePIC
Described the expected data volumes expected from noise, background and collisions.
Listed the technologies, and the scale of the ePIC Electronics and DAQ systems, to put the following talks into context

## Slide 21: Back-up

## Slide 22: Echelon 0 Computing
COTS DAQ computing
~200 computers
130 for reading out DAM boards
70 for:
  Building time frames
  Low level QA / logging
  Interface to Slow Controls
  Configuration and Conditions Databases
  Buffering of data files
  Transfer of data files to Echelon 1

## Slide 23: Streaming DAQ Concept
Triggered DAQ
Streaming Readout (SRO)
Features of ePIC SRO
No global trigger
  No custom trigger electronics
  Zero-suppress early (ASICs)
Hits identified by time stamp rather than by event
Flexibility in event selection
  Can be performed with all channels available
  Can be performed in CPU, FPGA, or GPU
Cons
  SRO has greater sensitivity to noise and background

## Slide 25: Requirements Flow Down

## Slide 26: ePIC Software & Computing Review Summary
On October 19–20, the EIC Computing and Software Advisory Committee (ECSAC) assessed the ePIC computing model in preparation for the EIC RRB meeting in December 2023.
The scope of this review also included the organization of the EIC Computing and Software Joint Institute (ECSJI), which has been formed by BNL and JLab.
The documents from the review, including the closeout report, can be accessed publicly on the ePIC Indico.
All five charge questions answered in the affirmative with three recommendations shared:
  Q1 (… comprehensive and cost-effective long-term plan …):
    We recommend that ECSJI verify the readiness of simulation and reconstruction for the TDR by May 2024.
    We recommend that ePIC document a first computing needs assessment by the next ECSAC review, in roughly one year.
  Q3 (… integrated with the HEP/NP community developments …):
    We recommend that the ePIC collaboration starts, by the time of next year’s ECSAC review, an evolving list of software dependencies that includes: the packages, who the primary supporters are, and what the ePIC collaboration contributes to them.

## Slide 27: Detailed DAQ Schedule
Releases:
PICODAQ:
  Communicate with electronics test setup
MICRODAQ:
  readout detector data in test stand
MINIDAQ:
  readout detector data using full timing chain
Final:
  Full functionality DAQ

## Slide 28: Introductions
Jeffery M. Landgraf
L3 co-CAM for 6.10.09
Senior Technology Architect at Brookhaven National Laboratory
Physics Ph.D. from University of Michigan, 1995
Developed and supported the DAQ, Trigger and online computing systems for the STAR detector since 1999
co-Convener for ePIC Electronics and DAQ WG
David J. Abbott
L3 co-CAM for 6.10.09
Staff Scientist at Jefferson Lab
Nuclear Physics Ph.D. from UNC Chapel Hill, 1990
Developed and supported the data acquisition systems for all JLab experiments as part of the Physics DAQ and Fast Electronics support groups (33 years).

## Slide 29: EIC SRO Community
The EIC Streaming Readout (SRO) Consortium
  Formed in 2018 with the goals of engaging the nuclear physics community to explore a streaming readout architecture for the EIC detectors.
  Series of ten workshops so far since 2018 (next in Dec 2023)
  Led to adoption of SRO for Yellow Report the physics program for EIC.
ePIC Electronics/DAQ Working Group
  Conveners: F. Barbosa (JLab), J. Huang (BNL), J. Landgraf (BNL)
  Regular meetings to focus on design and requirements specifically for the new ePIC detector
  Interface to detectors, readout, DAQ, online processing, monitoring and control.
ePIC Software/Computing Working Group
  Conveners: M. Diefenthaler (Jlab), S. Joosten (ANL), T. Wenaus (BNL), W. Deconinck (UM)
  Coordinate software development for EIC physics
ePIC Software/Computing Streaming DAQ Working Group
  Conveners: M. Battaglieri (JLab), J. Huang (BNL)
  Streaming Reconstruction
Charge 1

## Slide 30: System Component Status
Optical Protocol
Defines the data flow between the GTU, RDO, and DAM boards
Optical Protocol Requirements
  Timing (<=5ps Hi-Res Detectors)
  Timing (<=100ps Lo-Res Detectors)
  Timing phase stability on power cycle
  Configuration and slow control monitoring passthrough for ASICS/FEBs
  Real-Time Command / Control
  Data Transfer (>=10Gb/s per RDO)
Optical protocol choices under evaluation
  ePIC – simple custom protocol
  GPT in FPGA
  Dedicated Clock/Reconstructed Clock (2 or 3 fibers per RDO)
RDO Status:
Mocking up with devkits for initial studies
Nominal 2.5” x 2.5” for common elements + connector space
FPGA defined by price (Artix Ultrascale+ Class)
Power 3-5 Watts. 2 LV +5V for optical interfaces, lower for FPGA/digital components
Accept 2 or 3 fibers for potential Hi-Res Timing
GTU status:
Mocking up with devkits for initial studies
Interface to collider (Bunch crossing clock, Spin Patterns per bunch crossing)
Distribution of timing to ~100 DAMs + ~220 RDOs of Hi-Res Timing Detectors
User command interface & distribution
Interface to Run Control
DAM Status:
FELIX engineering article obtained
Xilinx Versal FPGA
PCIe Gen4 x16 or 100Gb Ethernet output
24 Firefly links up to 25Gb/s options
48 link upgrade planned
Additional front panel I/O
Detailed Electronics Design starts with CD3.
The current status is that we are evaluating system design and interactions between components.
Charge 1

## Slide 31: DAQ Computing - Streams
Time Frames (~1ms)
  Up to ~500 events per Frame
  ~10MB data per Frame
  ~2.0MB input per DAM
  ~100kB output per DAM
Routing data
Formatting data
Processing data
  DAM FPGA & CPUs
  Cluster finding
  Software triggering
  Sanity Checkers
  QA Monitoring
  Metadata
  Slow controls integration
Scalers / continuously running DAQ components
Charge 1

## Slide 32: DAQ/Online Schedule
The DAQ and computing schedule is planned to be accelerated in relation to the full detector construction.
A functional DAQ will be necessary for small scale detector testing as well as commissioning and pre-ops.
Computing resources are staged to make purchases when the hardware is needed, taking advantage of price savings and performance improvements in time.
Hardware and software development early in the construction phase will produce a series of releases with increasing functionality.
Detector Install: FY29Q2 - FY31Q2
Cosmics: FY31Q3
Early CD-4: FY32Q1
DAQ Releases:
PicoDAQ FY26Q1
  Readout test setups
MicroDAQ: FY26Q4
  Readout detector data in test stand using engineering articles
MiniDAQ: FY28Q1
  Readout detector data using full timing chain
Full DAQ-v1: FY29Q2
  Full functionality DAQ ready for full system integration & testing
Production DAQ: FY31Q3
Ready for cosmics
Charge 3
Mini
DAQ
Production
DAQ

## Slide 33: EIC Streaming DAQ/Computing Architecture
ePIC DETECTOR
BW O(100Tbps)
BW O(10Tbps)
BW O(100Gbps)
RDO
RDO
RDO
RDO
RDO
RDO
RDO
RDO
RDO
Bunch Crossing ~ 10.2 ns/98.5 MHz
Interaction Rate ~ 2 us/500 kHz
Low occupancy
GTU/Distributed clock
(jitter ~5ps)
Charge 3

## Slide 34: ES&H Considerations
Both JLab and BNL have EHS&Q processes for “in-kind” Electronics
At JLab, custom electronics built by collaborators for use in experiments must go through a registration process first. This includes any equipment that is NOT certified by a Nationally Recognized Test Lab (NRTL) like UL and recognized by OSHA.
The JLab EHS&Q Manual has a supplement guide for construction and/or modification of any custom or non-NRTL equipment.
BNL Experimental Safety Review Process
  The experimental details and hazards are submitted to the ESH Coordinator
  An ESR form must be submitted to the C-A department
  The local representative must give a formal presentation to an ESH committee
  Before operations, the equipment must be inspected by the review committee and approved for operation
Charge 4