## Slide 2: Current and future Pu validation experiments
J. Hutchinson, T. Cutler, N. Kleedtke, G. McKenzie, I. Michaud, D. Neudecker, K. Stolte, N. Thompson, R. Little
8/13/24: Mini CSEWG

## Slide 3
Overview
Historic Pu validation experiments
Recent NCERC benchmarks
  EUCLID
Future experiments
  Lilith
  PARADIGM
  Others

## Slide 4
Historic Pu validation experiments
Table at right shows benchmarks sorted in order of descending Pu239 fission sensitivity.
Integrated over all energy, ENDF/B-VIII.0 nuclear data.
List mostly filled with historic LANL (blue) and Russian (red) experiments.
LANL has a history of Pu239 validation experiments.
  We are continuing to add new experiments.
Experiment | Fission | Elastic | Inelastic | n,gamma | total nu
pu-met-fast-022-001 | 0.743 | 0.064 | 0.041 | -0.008 | 0.987
pu-met-fast-025-001 | 0.731 | 0.051 | 0.033 | -0.009 | 0.988
pu-met-fast-035-001 | 0.729 | 0.051 | 0.033 | -0.009 | 0.988
pu-met-fast-040-001 | 0.729 | 0.048 | 0.033 | -0.010 | 0.988
pu-met-fast-039-001 | 0.727 | 0.045 | 0.032 | -0.010 | 0.988
pu-met-fast-001-001 | 0.727 | 0.063 | 0.040 | -0.008 | 0.966
pu-met-fast-001-004 | 0.726 | 0.063 | 0.040 | -0.008 | 0.966
pu-met-fast-001-002 | 0.726 | 0.062 | 0.040 | -0.008 | 0.966
pu-met-fast-001-003 | 0.726 | 0.063 | 0.039 | -0.008 | 0.966
pu-met-fast-023-001 | 0.725 | 0.046 | 0.032 | -0.010 | 0.988
pu-met-fast-045-005 | 0.718 | 0.035 | 0.026 | -0.014 | 1.000
pu-met-fast-026-001 | 0.718 | 0.039 | 0.022 | -0.011 | 0.988
pu-met-fast-045-004 | 0.718 | 0.034 | 0.026 | -0.014 | 1.000
pu-met-fast-045-006 | 0.718 | 0.038 | 0.024 | -0.015 | 1.000
pu-met-fast-045-003 | 0.717 | 0.035 | 0.024 | -0.014 | 1.000
pu-met-fast-024-001 | 0.716 | 0.048 | 0.038 | -0.020 | 0.988
pu-met-fast-045-001 | 0.715 | 0.034 | 0.024 | -0.016 | 1.000
pu-met-fast-045-002 | 0.713 | 0.034 | 0.023 | -0.015 | 1.000
pu-met-fast-045-007 | 0.712 | 0.035 | 0.021 | -0.017 | 1.000
pu-met-fast-036-001 | 0.710 | 0.042 | 0.037 | -0.021 | 0.988
pu-met-fast-015-001 | 0.707 | 0.033 | 0.018 | -0.013 | 0.985
pu-met-fast-009-001 | 0.706 | 0.044 | 0.032 | -0.010 | 0.964
EUCLID_3x2x64 | 0.702 | 0.043 | 0.025 | -0.011 | 0.965
pu-met-fast-003-103 | 0.701 | 0.039 | 0.018 | -0.008 | 0.962
pu-met-fast-021-002 | 0.700 | 0.040 | 0.027 | -0.016 | 0.968
pu-met-fast-005-001 | 0.699 | 0.035 | 0.025 | -0.012 | 0.965
pu-met-fast-013-001 | 0.696 | 0.023 | 0.018 | -0.019 | 0.986
pu-met-fast-021-001 | 0.696 | 0.042 | 0.028 | -0.019 | 0.968
pu-met-fast-018-001 | 0.696 | 0.033 | 0.030 | -0.016 | 0.965
pu-met-fast-014-001 | 0.695 | 0.025 | 0.019 | -0.018 | 0.985
pu-met-fast-008-001 | 0.695 | 0.035 | 0.025 | -0.012 | 0.955
pu-met-fast-029-001 | 0.690 | 0.059 | 0.036 | -0.008 | 0.915
EUCLID_8x1x130 | 0.685 | 0.022 | 0.010 | -0.011 | 0.965

## Slide 5
Recent NCERC benchmarks
Of the 17 ICSBEP evaluations of experiments performed at NCERC, 8 are Pu systems.
Many of these are included in our modern validation suite.
Fast, intermediate, and thermal systems.
Most of the Pu benchmarks are WG Pu.
  Some upcoming benchmarks with high Pu240.
Subcritical BeRP experiments:
  Still need to make validation easier for these experiments.

## Slide 6
Jupiter High-240 experiment
Collaboration with JAEA to help validate Accelerator Driven Systems (ADS).
Similar to the WG Pu Jupiter experiments.
Performed at NCERC in 2019.
ICSBEP evaluation currently underway.
Jupiter High-240
Jupiter

## Slide 7
EUCLID
designed validation experiments optimized to reduce 239Pu compensating errors & adjusted nuclear data to experiments
Neutron Transport
Simulation (MCNP)
Validation Experiments
ML-Augmented
Search for Compensating Errors
Experiment Refines Nuclear Data to Improve Simulations
ML-Optimally Designed Experiment to Resolve Compensating Errors

## Slide 8
Experiment Optimization
Results of the D-Optimality analysis led us to two configurations:
  Both utilize WG Plutonium-Aluminum No-Nickel (PANN) ZPPR plates as fuel
  Non-nuclear components can be used for future experiments as well
3 X 2 (Low Mass/Cube)
Critical with 384 ZPPR plates (41 kg Pu)
8 X 1 (High Mass/Slab reactor)
Critical with 1033 ZPPR plates (109 kg Pu)
8x1 H/”D” ratio is 5.4

## Slide 9
Experiment execution
7 weeks at NCERC: Nov 28 2022 - Jan 26 2023
The most Plutonium ever used in an NCERC Experiment

## Slide 10
Measurement Responses
Six responses were measured for each configuration:
  Critical: ICNC 2023
  Subcritical (neutron noise): ANE
  Neutron leakage spectra: NIM A and APS 2023
  Rossi-α: future work
  Reactivity coefficients: ICNC 2023
  Reaction rate ratios: NSE

## Slide 11
Calculated keff is mostly below experiment and varies with 239Pu library by 10s to 100s of pcm
Results when switching Pu239 nuclear data (all other nuclides are ENDF/B-VIII.0)
3x2 exp: 1.00029 +/- 0.00200
8x1 exp: 1.00038 +/- 0.00300
Library | keff | keff unc | C-E (pcm)
ENDF/B-VIII.0 | 1.00012 | 0.00003 | -17
ENDF/B-VII.1 | 1.00072 | 0.00003 | 43
JEFF-3.3 | 0.99999 | 0.00003 | -30
JENDL-4.0u | 0.99953 | 0.00003 | -76
JENDL-5.0 | 1.00103 | 0.00003 | 74
Pu9VIII1beta1-11c | 0.9991 | 0.00003 | -119
Pu9LANL10172022-10c | 1.00011 | 0.00003 | -18
e81b2 | 0.99992 | 0.00003 | -37
Library | keff | keff unc | C-E (pcm)
ENDF/B-VIII.0 | 0.99838 | 0.00003 | -200
ENDF/B-VII.1 | 0.99886 | 0.00003 | -152
JEFF-3.3 | 0.99938 | 0.00003 | -100
JENDL-4.0u | 0.99712 | 0.00003 | -326
JENDL-5.0 | 0.99852 | 0.00003 | -186
Pu9VIII1beta1-11c | 0.99757 | 0.00003 | -281
Pu9LANL10172022-10c | 0.99802 | 0.00003 | -236
e81b2 | 0.99815 | 0.00003 | -223

## Slide 12
Future experiments: Lilith
Much more than just a “Jezebel replacement”
New enduring Pu assembly
  Design goal of 100 years of operation
Ability to change part of the Pu fuel
Will become the “default experiment” for Pu239 nuclear data validation
Benchmark can be updated over time as new technologies become available
Can be used to measure changes over long periods of time
Would provide new clean Pu assembly for spectral indices, reactor kinetics parameters, etc.
ND validation
AM validation
Dosimetry
Reactor kinetics
Materials
Lilith

## Slide 13
Future experiments: PARADIGM
Reduce Pu-239 nuclear data uncertainty in the intermediate region
  And reduce the timeline of the pipeline
Design differential (LANSCE) and integral experiments (NCERC) simultaneously using machine learning (see Christi Thompson talk)
  Differential, integral, and theory in single optimized process
Two validation experiments targeting Pu239 uncertainty reduction for:
  1-30 keV
  30-600 keV
More sensitive to Pu239 fission in these energies than any existing experiments
Additional responses (beyond keff) will be measured

## Slide 14
Future experiments: other
IER 607: Thales
  Tantalum reflection
  Validation for Ta for Pu processing
IER 296: TEX Mox
  Mox fuel with high Pu240
  Validation for Mox operations in France
Flattop Pu
  Updated evaluation
  General Pu validation and basis for other experiments
IER 551: EUROPA
  Intermediate energy Pu (WG and elevated Pu240)
  Complementary to PARADIGM and TEX experiments

## Slide 15
Lessons learned and challenges
Some lessons learned along the way:
  AI/ML can be very useful in experiment design
  Measurement of additional responses can help further constrain nuclear data
  Integral experiments should be designed in parallel to differential experiments (PARADIGM approach)
  Performing benchmark evaluation directly after experiment completion is both cost effective and results in better benchmarks
Some challenges:
  Funding of benchmark evaluations is similar to the TRL “valley of death”. Outside of NCSP, we have had challenges securing funding
  Documentation for other responses of historical experiments is lacking
  “New” material is hard to acquire

## Slide 16
Conclusions
Recent and planned NCERC experiments provide rich opportunities for validation of Pu nuclear data
Including keff benchmarks as well as many other responses
Very interested in future Pu validation
  Pu239 and Pu240
  Fast
  Intermediate
  All reactions
Interested in collaboration with CSEWG regarding new validation experiments

## Slide 17
Acknowledgments
Research reported in this publication was supported by the U.S. Department of Energy LDRD program at Los Alamos National Laboratory.
NCERC is supported by the DOE Nuclear Criticality Safety Program, funded and managed by the National Nuclear Security Administration for the Department of Energy.
Los Alamos National Laboratory is operated by Triad National Security, LLC, for the National Nuclear Security Administration of the US Department of Energy under Contract No. 89233218CNA000001.