## Slide 1: TSL Style Covariances
Chris W. Chapman, Jordan McDonnell, Goran Arbanas
Oak Ridge National Laboratory
Mini-CSEWG meeting – 14 August 2024

## Slide 2: Goal
What this is
  Discussion points to consider over the next few months regarding the storage, processing, and usage of a TSL covariance
What this is not
  A final decision on any sort of format or procedure
  A discussion about how to produce the covariance

## Slide 3: Broad questions to answer
What to store the covariance of?
  Implied that processing codes will be able to process this covariance to an eventual covariance of DDXS
How to handle temperature dependence?
  TSL temperature dependence is not necessarily analytical as other forms of nuclear data
How will transport codes use this covariance?
  Sampling? Sensitivity calculations?

## Slide 4: What to store covariance of
MD/DFT Parameters
Pros
  Most faithful representation of physics
  Relatively few parameters to store
Cons
  Difficult to analytically propagate uncertainties through to cross section (maybe impossible)
  Code-dependent (some of which are proprietary)
  Confusing to users
  Special care needed to include nuclear reaction contribution
LEAPR/NCrystal/FLASSH/etc. Input Parameters
Pros
  Intuitive for users to comprehend
  Relatively few parameters to store
  Easier to account for temperature dependence
Cons
  Code-dependent (some of which are not publicly available)
  Difficult to analytically propagate uncertainties through to cross section (but not impossible)
S(𝛼,𝛽)
Pros
  Intuitive for users to comprehend
  Analytical link to double differential scattering cross section
Cons
  Very large (~40 GB for 1 temperature of ENDF8.0 light water), so compression algorithm required
  Even with compression algorithm, temperature dependence difficult

## Slide 5: What to store covariance of (cont.)
MD/DFT Parameters
Extensive Processing Burden
Moderate Processing Burden
Minimal Processing Burden
LEAPR/NCrystal/FLASSH/etc. Input Parameters
S(𝛼,𝛽)
Minimal On Disk Storage
Moderate On-Disk Storage
Extensive On-Disk Storage

## Slide 6: How will transport codes use this covariance?
Stochastic Sampling
  Might not necessarily require a DDXS covariance
  Could work for either CE or MG calculations
Deterministic Calculations
  Will require a DDXS covariance for sensitivity calculations
  Could work for MG; CE would be difficult (if even possible)

## Slide 7: Discussion
What do we as a community need to do over the next few months?
  Methods improvements?
  Develop benchmark(s) to test efficacy of covariance methodology?
Who outside of the CSEWG community do we need to reach out to?
Do we need to simultaneously consider how covariances are generated?

## Slide 8: Acknowledgements

## Slide 9: Extra Slides – What we’ve done @ ORNL
DNCSH funded task
Start with covariance matrix created by Chapman in 2017
  Known flaws with covariance methodology, but currently better than nothing
Focus on two different methodologies:
  Covariance of LEAPR input parameters (most notably PDOS & bound scattering cross section)
  Matrix decomposition of S(𝛼,𝛽) covariance matrix

## Slide 10: Extra Slides – TSL Covariance Propagation
MD
Potential
Param’s.
PDOS
PDOS
Force
Constants
Phonon
Dispersion
Legendre
Moments
S(a, b)
DDXS
CE
Transport
Codes
MG
Transport
Codes

## Slide 11: Extra Slides – Cunningham’s Law
“If you want to get the right answer, don’t ask a question, post the wrong answer”
So…

## Slide 12: Extra Slides – My proposal
Store N largest diagonal & off-diagonal values of S(𝛼,𝛽)
  bogosort, of course
LCOMP=2
Store 1 temperature; use linear interpolation to other temperatures