## Slide 1
AncASIC and EIC-LAS: Power and Size Update
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.

## Slide 2
Introduction
EIC-LAS Power Consumption
  Updates based on better understanding of MOSAIX voltage levels
  Updates from Engineering Review
AncASIC Power Consumption
  Simulation set-up
  Balancing currents with R3
  Stave Simulations
  Overall Power Numbers
  Caveats
AncASIC Sizing
  Sizing based on assuming SLDO is the largest part
  Caveats

## Slide 3
MOSAIX Power Consumption
MOSAIX Engineering Specification Review
  Current consumption numbers for MOSAIX were updated in the engineering review.
  What does this mean for EIC-LAS and the Ancillary ASIC

## Slide 4
LAS Power Consumption
 | Typ Current Consumption (mA) |  |  | Max Current Consumption (mA) |  | 
 | RSU | LEC | EIC-LAS | RSU | LEC | EIC-LAS
GAVDD | 28 |  | 168 | 45 |  | 270
GDVDD | 71 | 100 | 526 | 111 | 150 | 816
GSVDD | 1.6 | 30 | 40 | 2.4 | 45 | 59.4
TXVDD |  | 200 | 200 |  | 300 | 300
Total |  |  | 934 |  |  | 1445
Converting to EIC-LAS
  Assume 6 RSU LAS
  Numbers in red do not have “Max” estimates in the previous slide, so assumed +50% on typ number (since this is true for supplies that do have it)
  EIC-LAS is one LEC and 6 RSU

## Slide 5
AncASIC Power Consumption
GlobalDigital
GlobalAnalog
Services
+10% shunt overhead based on https://cds.cern.ch/record/2292628/files/CR2017_385.pdf
LAS<3>
LAS<2>
LAS<1>
LAS<0>
Serialiser
AncASIC (0A)
Programmable Output Voltage
  Compared to earlier presentations (v7 and before), need to simulate case where GA=GD=Services=1.32V and Serialiser=1.2V. Requires adjustable SLDO output.
  Implemented 4 bit variability. Should give swing between 1.1 – 1.5V

## Slide 6
Balancing currents with R3
Power Optimisation
  R3 must be different per supply
  Otherwise current divides evenly and is very power in-efficient (extra is shunted)
  Also different for different LAS power conditions
  Will require real world tuning (perhaps per stave?)
  Include MOSAIX to check if testing ER2 with SLDO will be possible (no plan for IB serial powering)
Supply | R3 Typ | R3 Max | R3 MOSAIX
Global Analog | 17k | 11k | 8.5k
Global Digital | 5.5k | 3.5k | 3k
Services | 72k | 48k | 58k
Serialiser | 14.4k | 9.6k | 14.4k

## Slide 7
Ancillary Chip Power Consumption

## Slide 8
Overall Power Consumption
 |  | AncASIC |  | EIC-LAS | 
 | Unit | Expected 25 | Max 45 | Expected 25 | Max 45
Global Analog | mW | 80 | 105 | 235 | 378
Global Digital | mW | 195 | 279 | 737 | 1144
Services | mW | 22 | 32 | 56 | 84
Serialiser | mW | 129 | 188 | 248 | 371
Total | mW | 426 (33%) | 604 (31%) | 1276 | 1977
Chain Current | A | 1.5 | 2.5 | N/A | N/A
- PSRR trade-off with drop out voltage/power
- All still simulated in 65nm process
- Low dropout at high current is not free…
- RD53B PT: 22,500um2
- AncASIC PT: 36,480um2 (0.00036cm2)
Improvement of ~60% in AncASIC power and 30% in EIC-LAS power c.f previous (GA=GD=Serialiser=1.2V and TDR currents) case

## Slide 9
Power Caveats…
Caveats to the numbers
  Best estimate from MOSAIX. Not a warranty.
  Possibility that LEC value will rise (additional functions)
  For GAVDD, it is likely that EIC-LAS will be in the Max case, since we want the fastest frontend speed
  We may be able to reduce TXVDD consumption if we don’t need all the transmitters (or can run slower)
  Need to add consumption of non-SLDO AncASIC
  Mis-match in GAVDD, GDVDD consumption may require different input voltages (waste of power in serial powering chain)
  Irradiation
Future Updates
  May be future releases from MOSAIX
  AncASIC will need to be updated once porting to XT011 is completed
  Test results from ER2

## Slide 10
AncASIC Size
PADS
PADS
PADS
PADS
SLDO
1mm
200um
SLDO
SLDO
SLDO
SLDO
NVG
Slow Control
???
???
???
500um
500um
500um
500um
>7mm
>1.5mm
Preliminary – Treat as fully subject to change

## Slide 11
Very preliminary
  Only producing at this stage to assist with requests for stave design
  Not discussed with other designers yet
  Chip has 3 components:
    Negative Voltage Generator
      Size unknown
    Slow Control Multiplexing
      Size unknown
    SLDO
      Size unknown, but will probably dominate
      Size dominated by a few transistors, so some guess at chip size can be made
      However:
        Design at early stage
        Sizes taken from 65nm design (not 110nm)
  Of course, this also means we can be open to comments
  Need someone to do thermal FEA – now that size and power are known
Size Caveats
Preliminary – Treat as fully subject to change

## Slide 12
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.

## Slide 13
Backup

## Slide 14
MOSAIX Supply Complexities
GA, GD and Services
  Remaining voltages are all driven at 1.32V
  It is necessary that services should always be above the other two, but this is handled internally by assuming that only GA and GD droop.
  Therefore we assume GA, GD and Services at 1.32V.
Testing MOSAIX with AncASIC
  James suggested it would be useful to be able to test the AncASIC powering MOSAIX when ER2 returns
  Ran some simulations to check if it is possible
  Seems that it is (for the Expected 25 case) because designing for Max45 EIC-LAS leaves a lot of headroom

## Slide 15
MOSAIX Supply Complexities…
The 1.8V Problem…
  MOSAIX requires not just a 1.2V supply, but also 1.8V to run the serialisers
  The AncASIC itself will need a 1.8V supply for logic and the NVG
  However, all SLDOs need to be in parallel, and if we run them at 1.8V, the 1.2V supplies will waste considerable power
What can we do?
  Run the SLDOs at 1.8V
  Two serial powering chains
  Use the NVG?
  Tap power from the next stage?
  Remove serialiser LDO from 65nm IP (serialiser itself is 1.2V)
  Supply 1.8V externally to each LAS
Considerable waste of power - ~1.1W
Impossible – shared ground at various points
Could it step 1.2V up to 1.8V? Noise issues?
Routing complexity. Stability? Still a power waste - ~300mW. What about the last one?
1.2V
1.2V
0.4V
EIC-LAS
1.2V
1.2V
EIC-LAS
V=0V
V= ~1.4V
Would need 8 lines (supply and return for each of 4 LAS).

## Slide 16
MOSAIX Supply Complexities…
The 1.8V Solution?
  João’s idea to edit the 65nm database to skip the LDO seems like a good one.
  We do not yet have a solution to powering the AncASIC circuits that run at 1.8V.
  It does seem that the serialiser could be separated from it’s LDO
  So for the rest of this presentation, I will assume that the serialiser can be powered at 1.2V in order to get an overall power number.
  We should perhaps suggest to the higher SVT that they think about point-to-point powering of the 1.8V system just in case (would mean 8 extra wires)
https://indico.cern.ch/event/1376523/contributions/5785064/attachments/2789901/4865135/ALPIDE_65_30_01_2024.pdf

## Slide 17
LAS Power Consumption – Earlier Estimates
 |  | Power Consumption |  | 
 | Unit | 5 RSU LAS | 6 RSU LAS | MOSAIX
LEC | mW | 696 | 696 | 696
RSUs | mW | 543 | 651 | 1303
Total | mW | 1240 | 1348 | 2000
 |  | Power Consumption |  | 
 | Unit | 5 RSU LAS | 6 RSU LAS | MOSAIX
LEC | mW | 696 | 696 | 696
RSUs | mW | 889 | 1066 | 2133
Total | mW | 1585 | 1763 | 2829
 |  | Power Consumption |  | 
 | Unit | 5 RSU LAS | 6 RSU LAS | MOSAIX
LEC | mW | 696 | 696 | 696
RSUs | mW | 1280 | 1536 | 3072
Total | mW | 1976 | 2235 | 3768
Expected 25
Max 25
Max 45
2 published sources of data (power densities, and supply current breakdown)
LEC does not vary at all in the power density figures
Separation into supplies does not include Expected/Max variation
How to reconcile?

## Slide 18
LAS Power Consumption – Earlier Estimates
Towards individual supply estimates
  Can only really make worst case assumptions:
    6 RSU LAS
    Expected 25 to Max 45 is 65% variation.
    Apply this also to the LEC and assume published number is Expected 25.
    Worst case numbers are then 1536mW for the RSUs and 1148mW for the LEC.
    Total 2684mW
  How does this compare to the published supply numbers (MOSAIX – 12RSU)?
N.B. We can make better case assumptions if we like, but we should do it consciously
272mW
648mW
1643mW
360 mW
XXXXXX
Total: 2923mW 1723mW 2842mW
Scale to EIC-LAS ->
272mW
270mW
821mW
360 mW
XXXXXX
+65% ->
449mW
445mW
1354mW
594 mW
XXXXXXX
Good match to our worst case Max45 estimate, so can probably assume the original numbers are for the Expected 25 case

## Slide 19
LAS Power Consumption – Earlier Estimates
LAS, Best and Worst
  Knowing the EIC-LAS current requirements is key for the SLDO design
  Since the SLDO dominates the AncASIC (we need a better name…) power consumption, it is also key to get a power number for that chip
  Current numbers needed for simulation
272mW
270mW
821mW
360 mW
449 mW
445 mW
1354 mW
594 mW
Expected 25
Max 45
Services
Global Analog
Global Digital
Serialisers
Power
206 mA
205 mA
622 mA
300 mA
340 mA
337 mA
1026 mA
495 mA
Expected 25
Max 45
Current
Assume 1.2V for serialisers (if we can skip the on-chip LDO)
Voltage
1.32V
1.32V
1.32V
1.2V

## Slide 20
Ancillary Chip Adjustability
Programmable Output Voltage
  Compared to earlier presentations (v7 and before), need to simulate case where GA=GD=Services=1.32V and Serialiser=1.2V. Requires adjustable SLDO output.
  Since we also want some control over SLDO output to allow adjustment in real world, prefer to implement real circuit.
  Implemented variable resistor (4bit) to allow this. Should give swing between 1.1 – 1.5V