## Slide 1
SLDO Update
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.

## Slide 2
Introduction
Work at RAL
  Schematic design complete in 65nm
  Porting to XT011
  Full Verification
Work at LBNL
  Porting of sub-blocks for September run
  Layout

## Slide 3: 65nm Simulation Results
Vout 1.2v

## Slide 4: SLDO Port

## Slide 5: SLDO Simulation
Vout 1.2v

## Slide 6: EIC—AncASIC SLDO initial work at LBNL
Amanda Krieger
ePIC SVT DSC June 11, 2024

## Slide 7
LBNL work on SLDO: Completed to date
Install xt011 PDK
  Siemens tools—Calibre, Eldo, ADE interface
  Cadence—Eldo and Spectre models, primitives, process docs, etc.
Pilot design cells: n_amp, preReg
  Schematic simulation in Eldo and Spectre is up and running
  Layout n_amp— DRC, LVS clean

## Slide 8
LBNL work on SLDO: Near term to do
Layout of preReg (pass transistor, decoupling, compensation)
Schematic simulation
  Write extract scripts for n_amp and preReg (LDO) performance
  Write corner recipe for automated simulation (PVT)
Backannotated simulation
  Compare schematic performance to full parasitic extraction with devices

## Slide 9
LBNL work: Sept submission
Start a community pinlist for the padring I/O (imminent)
Desirable: add BGR to the SLDO test structures
Time permitting: design a basic padframe schematic + layout for MPW
  Find xt011 pad + IO module(s) and install—simple
  Periphery rules, pads, etc. need to be understood—might be easy or complicated (power domains, generate sealring, corner stress rules, etc.)
Get Design Sharing Agreement signed (?)