## Slide 1: Recent developments in uncertainty quantification and model validation for complex systems
Roger Ghanem, USC
New York Scientific Data Summit 2024: Addressing Data Challenges in Digital Twins
Brookhaven National Laboratory September 16–17, 2024

## Slide 2: MOTIVATION
RESOLVED MODELS OF PHYSICAL PHENOMENA CANNOT BE EXECUTED IN REALTIME.
WE TYPICALLY INTRODUCE ERRORS TRYING TO RUN FASTER:
  MUST REALIZE THAT ERRORS ARE INTRODUCED
  IDENTIFY THE ERRORS
  ANALYZE THE ERRORS (math or heuristics)
  ASSESS CONSEQUENCES OF ERRORS

## Slide 3: THRUST AREAS
STOCHASTIC MODELING
FASTMATH
AUTONOMY

## Slide 4: EXAMPLE THAT RUNS ACROSS THRUSTS: MODEL VALIDATION
VERIFICATION: Ascertain that we are solving the equations correctly.
TEST PREDICTIONS AGAINST EXACT SOLUTION OF EQUATIONS
VALIDATION: Ascertain that we are solving the correct equations.
TEST PREDICTIONS AGAINST DATA
More reasonably: Determine to what extent the data does not invalidate the model.

## Slide 5: TRADITIONAL THINKING ABOUT VALIDATION
COMPARES MODEL PREDICTION TO EVIDENCE
USING UNCERTAINTY QUANTIFICATION TO PROVIDE A CLOUD OF PREDICTIONS THAT IS REASONABLE

## Slide 6: TRADITIONAL THINKING ABOUT VALIDATION
COMPARES MODEL PREDICTION TO EVIDENCE
USING UNCERTAINTY QUANTIFICATION TO PROVIDE A CLOUD OF PREDICTIONS THAT IS REASONABLE
WE OFTEN DO NOT HAVE MODELS (COMPLETELY DATA DRIVEN)
OR
OPERATING CONDITIONS BETWEEN MODELS AND EVIDENCE ARE DIFFERENT AND CANNOT BE RECONCILED

## Slide 7: TRADITIONAL THINKING ABOUT VALIDATION
COMPARES MODEL PREDICTION TO EVIDENCE
USING UNCERTAINTY QUANTIFICATION TO PROVIDE A CLOUD OF PREDICTIONS THAT IS REASONABLE
WE OFTEN DO NOT HAVE MODELS (COMPLETELY DATA DRIVEN)
OR
OPERATING CONDITIONS BETWEEN MODELS AND EVIDENCE ARE DIFFERENT AND CANNOT BE RECONCILED
WE SHOULD STILL BE ABLE TO VALIDATE A MODEL

## Slide 8: APPROACH
INSIGHT FROM THE HUMAN BODY:
WE CAN RELATE BODY TEMPERATURE AND BLOOD PRESSURE TAKEN AT THE WRIST TO SPECIFIC AILMENTS.
NECESSARILY WITH SOME LEVEL OF UNCERTAINTY.
NO NEED TO HAVE A COMPLETE CHARACTERIZATION OF CELLS AND ORGANS – WHICH MAY BE EXPENSIVE AND NOT NECESSARILY RELATABLE TO THE AILMENT IN A CAUSAL FASHION.

## Slide 9: APPROACH
DEPENDENCE BETWEEN FEATURES OF THE MODEL MAY BE SUFFICIENT INDICATION OF REALISM

## Slide 10: APPROACH
DEPENDENCE BETWEEN FEATURES OF THE MODEL MAY BE SUFFICIENT INDICATION OF REALISM
WE MUST IDENTIFY WHICH FEATURES
WE MUST IDENTIFY THE REALISTIC SHAPE OF DEPENDENCE (NOT JUST CORRELATION !)
WE MUST IDENTIFY WHAT WE MEAN BY SUFFICIENT

## Slide 11: EXAMPLES SYNTHESIS

## Slide 12: Rotary Detonation Engines (RDE)
Continuous thrust (propulsion)
Supersonic detonation wave and shock front
Thermodynamic efficiency 36.9% → 59.3%

## Slide 13: Rotary detonation engines (RDE)
Given measurements on Boundary
Pressure,
Temperature
Density
Velocity

## Slide 14: Rotary detonation engines (RDE)
Given measurements on Boundary
Infer state inside the tube
Pressure,
Temperature
Density
Velocity
p, t, rho, v, Q, w, and gradients
Space/time features

## Slide 15: Training SET:
Explore sensitivity of each QoI to following features:
Distance between ”meta” droplets
Inclination to horizontal
H/O Composition of droplets
Size of droplets
USING A LOW-FIDELITY LES MODEL,
we generate 1000 samples.

## Slide 16: RESULTS: Representing the SENSOR data (Temperature data)
CHALLENGE: TEMPERATURE DATA IS POSITIVE
CONSTRAINED LEAST SQUARES PROMOTED POSITIVITY
NON-NEGATIVE MATRIX FACTORIZATION (NMF) ENSURED POSITIVITY

## Slide 17: RESULTS: Representing the FEATURE data:
TEST FEATURE
RECONSTRUCTED
PARAMETERIZED
TEST FEATURE
PCE OF
RECONSTRUCTED
FEATURE
FEATURE
INFERRED FROM
SENSOR DATA
AT A GIVEN INSTANT OF TIME

## Slide 18: RESULTS: Sensing a different experiment:

## Slide 19: RESULTS: Sensing a different experiment:

## Slide 20: POLYNOMIAL CHAOS FRAMEWORK
EXERCISING THE FORWARD MODEL

## Slide 21: POLYNOMIAL CHAOS FRAMEWORK

## Slide 22: POLYNOMIAL CHAOS FRAMEWORK
ACCURATE MAPPINGS FROM SDOF TO Q1 and Q2 ARE CRITICAL FOR Q1 <-> Q2 TO BE USEFUL.
WE USED A HIGH ORDER PCE TO DESCRIBE THE MAPPING FROM SDOF TO Q1 and Q2.
EFFECTIVE INFERENCE HINGES ON SUITABLE PARAMETERIZATION OF SIGNAL AND FEATURES.

## Slide 23: Oxidation in a hydrogen environment
Train on about 100 experimental specimens:
11 variables characterizing the morphology of oxidation:
Thickness, length, depth, area
of various key features

## Slide 24: Oxidation in a hydrogen environment
Train on about 100 experimental specimens:
11 variables characterizing the morphology of oxidation:
Thickness, length, depth, area
of various key features
NO TRUSTED GOVERNING EQUATIONS

## Slide 25: Oxidation in a hydrogen environment
During Operation
Observe some of the known variables
Infer other key variables

## Slide 26: Oxidation in a hydrogen environment
During Operation
Observe some of the known variables
Infer other key variables
NO CLOSURE FOR THESE VARIABLES (missing information a.s.)
ONLY PROBABILISTIC INFERENCE IS REASONABLE

## Slide 27: Oxidation in a hydrogen environment
A SENSOR PACKAGE IS A SET OF CONDITIONNING VARIABLES ( A SUBSET OF THE 11 FEATURES WE TRAINED ON)
PREDICTING MICROVOID DEPTH (FOR A TEST CASE) CONDITIONAL ON A VARIETY OF SENSING PACKAGES

## Slide 28: Oxidation in a hydrogen environment
STATISTICAL DEPENDENCE AMONG THE KEY 5 VARIABLES

## Slide 29: PLOM FRAMEWORK: MODEL-FREE
DETECT AN INTRINSIC STRUCTURE IN DATA
  e.g. DIFFUSION COORDINATES
CONSTRUCT A PROBABILITY FLOW FROM (SMALL) TRAINING SET TOWARDS A COLLECTIVE MEASURE
CONSTRUCT AN ITO EQUATION WHOSE INVARIANT MEASURE IS THIS COLLECTIVE MEASURE
SOLVE A PROJECTED ITO EQUATION TO OBTAIN CONSTRAINED SAMPLES
NON-PARAMETRIC CONDITIONAL DENSITY ESTIMATION PROVIDES THE INFERENCE ENGINE

## Slide 30: Hybrid Composites
Train on numerical samples of a hybrid composite lamina:
Observe:
Glass, carbon, resin properties
Effective Stress, strain relations
During Operation:
Given microscale properties
Infer stress-strain relations
or
Given stress-strain relations
Infer microscale properties

## Slide 31: Hybrid Composites
Stress-strain curves from training data

## Slide 32: Hybrid Composites
Inferred stress-strain relationships

## Slide 33: REMOTE SENSING: PACE Data
TRAINING DATA: (1516 features)
149 Satellite images:
Instrument properties
Irradiance at 4 wavelengths and 90 view angles.
Wind speed
Surface pressure
Aerosol properties

## Slide 34: REMOTE SENSING: PACE Data

## Slide 35: Turbulence
DATA SOURCE:
JOHNS HOPKINS TURBULENCE BOX
OBSERVE:
Velocity, pressure as spatial processes on the boundary of a 3D cube
INFER:
Subgrid stress over cube,
Q-Criterion, …

## Slide 36: Turbulence
CONDITIONAL INFERENCE
PDF of subgrid stress tensor conditional on local spatial values of
velocity
Pressure
temperature

## Slide 37: Turbulence
JOINT PDF OF SUBGRID STRESS COMPONENTS

## Slide 38: Turbulence
INCLUDING DISTANCE TO WALL AS A CONDITION
ELIMINATES BI-MODALITY AND
SHRINKS SUPPORT OF CONDITIONAL PDF

## Slide 39: Turbulence
The specific relationship that our probe discovers informs it how close it is to a feature :
  Proximity to a wall
  Proximity to vortices
  Proximity to specific reacting chemicals

## Slide 40: Sovereign ratings and GDP
Train on 50 years of data:
Batches of 5 consecutive years of data.
NO FIRST PRINCIPLES MODEL
GOVERNANCE INDICATORS
Voice and Accountability
Government Effectivness
Political Stability
Regulatory quality
Rule of law
Control of Corruption
GDP
S&P Ratings

## Slide 41: Sovereign ratings and GDP
During Operation:
Observe 4 consecutive years of some variables
Predict 5th year of some other variables

## Slide 42: Sovereign ratings and GDP
Figures below:
Observe the ratings and GPD in a four years sequence
Predict GPD and ratings in 5th year

## Slide 43: Extremes on Powergrid
Train on few years of data:
Daily Cost of operation
Hourly Generation at 326 generators
Hourly Demand at 118 buses
During Operation:
Anticipate shutdowns:
Anticipate operational topology associated with high cost

## Slide 44: Extremes on Powergrid
PDF of generation at No.22 under various operating cost scenarios
High cost is associated with blackout.

## Slide 45: SYNTHESIS
DATA ACQUISITION UNIT:
  CHOICE OF SENSORS
  CHOICE OF SAMPLE SIZE
DATA INTERPRETATION UNIT:
  PCE / PLOM / NN ETC…
AUTONOMY:
  CHOICE OF VARIABLES TO CONDITION ON
  DESIGN OF EXPERIMENT
  DESIGN OF SENSORS

## Slide 46: SYNTHESIS
ANALYSIS METRICS:
  LEARNING POTENTIAL (WHETHER WE CAN LEARN ANYTHING)
  LEARNING CAPACITY (WITH UNLIMITED RESOURCES)
  CONSTRAINT VIOLATION/PENALTY
FRAMEWORK OF STATISTICAL LEARNING IS USED TO EVALUATE THESE METRICS
WE ARE PURSUING THE OPTIMAL DESIGN OF THESE KNOLWEDGE EXTRACTION PROBES