## Slide 1: Digital Twins in Large Scale Scientific Instruments: Improving Particle Accelerator Performance and Operation
Weijian (Lucy) Lin
Collider Accelerator Department, BNL
New York Scientific Data Summit 2024
September 17, 2024

## Slide 2
Motivation
Particle accelerator – kilometer-scale machine with thousands of coupled components to generate and preserve beam with very precisely defined qualities (e.g., energy, emittance, luminosity etc.)
Traditionally maintained with many hours of manual tuning, taking time away from data collection
Constantly varying complex system – no constant set of routine, needs real-time adjustments

## Slide 3
Alternating Gradient Synchrotron (AGS) and its Booster serve as part of the injector compound for RHIC and future EIC
Motivation
 | Max Energy [GeV] | Pol. At Max Energy [%]
Source+Linac | 1.1 | 82-84
Booster | 2.5 | ~80-84
AGS | 23.8 | 67-70
RHIC | 255 | 55-60
Loss in polarization along the chain
Difficulty in improving beam quality:
polarimeter measurement is slow and has big error bars
tuning is an empirical process, due to the lack of accurate models for the machines
Digital Twin can be used to optimize beam luminosity, quality, and polarization in RHIC and EIC

## Slide 4: Digital twin at CBETA
Multi-turn energy recovery linac (ERL) developed by BNL and Cornell
Had success in building digital-twins for CBETA: combine physics simulation model with EPICS control system
CBETA-V: measure beam trajectories and compare to the digital twin in real time on control-system screens

## Slide 5
Improve Accelerator Operations with DT
Figure-of-merits (FOM) for machine learning (ML) algorithms (“experimental outputs”): beam position, beam size, emittance, beam intensity, polarization
  real measurements can be expensive
Improved modeling Digital Twin
Digital twin can be used for:
  fast real-time predictions for operators
  error detection and correction
  offline development of optimization and tuning routines

## Slide 6: Automatic orbit correction
Traditional orbit correction
  obtain mapping (orbit response matrix) from corrector settings to orbit measurements
  inverse mapping to get corrector settings needed to cancel orbit deviations
  Problem: time-assuming measurement, system drift over time
Orbit correction with DT
  train neural network models for fast correction routine, no need for matrix inversion
  update with new data and stay accurate

## Slide 7: Orbit response in AGS Booster
Script development with Collider Accelerator Department (CAD) Controls Group to measure orbit data
Good agreements between data and model are reached, despite some faulty monitors (i.e., C8)
Good candidate for incorporating digital twin into the control system

## Slide 8: AGS orbit response NN model
Simulation model can be used to train neural network model for the orbit response matrix
48 vertical corrector kick 72 y orbit measured at beam position monitors
Trained models accuracy > 99%
NN models can be trained for fast orbit correction routine given accurate digital twin model
ORM NN
Inverse ORM NN

## Slide 9: Error detection with orbit response
Actual machine with errors (e.g. quadrupole gradient errors, corrector calibration errors, etc.) produce different orbit response from model/reference machine
Considering all possible sources of errors as a vector , digital twin can be used to build response error model . Any can be reconstructed given known and

## Slide 10: Virtual Diagnostics
Many diagnostic measurements (i.e., quadrupole scan, polarimeter measurement) are very time consuming and disrupt normal accelerator operations
  Example: Coherent electron Cooling experiment at RHIC scans >100 quadrupole settings, and takes > 1 hour for an entire scan routine
Digital twin can replace real measurements with faster virtual measurements, without taking away valuable operation time
Digital twin can also provide virtual diagnostic information at locations where monitors cannot be placed in real machine

## Slide 11: Offline optimization routine development
Digital twin can be used to test and develop optimization algorithms without the need to take away beam time or the risk of sabotaging beam quality
Example: Bayesian optimization algorithm for optimizing AGS Booster injection was first tested on a model of beam intensity response with regards to corrector settings. Subsequent real machine tests achieved satisfactory results.

## Slide 12: Challenge for accelerator digital twins
Physics simulation models have been / are being developed at BNL
Injection and extraction processes are more difficult to model require geometry and physical coordinates of transfer line elements
Model calibrations are necessary to match with real machine
  Require large amount of measured data within limited operation time
  Measurements can be taken at different frequencies time synchronization is difficult
  Disagreement between model and measurements would require further error source investigation

## Slide 13: Summary
Particle accelerators are large scale machines with very complicated tuning and maintenance needs
Majority of particle accelerators still rely on empirical tuning by human operators
Digital twins can be hugely beneficial for improving accelerator performance and operations by providing:
  Foundation to develop tuning and correction routines which can involve other machine learning techniques (e.g., neural network, Bayesian optimization etc.)
  Fast real-time virtual diagnostics for operators to make quick and efficient adjustments
Building digital twins for particle accelerators requires more carefully planned beam studies and script development

## Slide 14: Thank you! Questions?