## Slide 1: Modular Rich Detector Simulation Cherenkov Ring Radius obtained from Circular Hough Transform
Cheuk-Ping Wong
Georgia State University
2016-09-12

## Slide 2: Outline
Obtain Cherenkov Ring Radius from simulation results using Circular Hough Transform.
Monte Carlo result
  Infinite pixel size
  Finite pixel size (6x6mm2)
Simulation result

## Slide 3: Ring Finder Algorithm Update
When filling 3D (a,b,r) histogram
Center position(a,b) cut:
  If (|a|>3mm or |b|>3mm) skip;
✘
✘
Not considered

## Slide 4
Monte Carlo

## Slide 5: Monte Carlo
10,000 events
Infinite pixel size / finite pixel size (6x6mm2)
In each events
  Number of hits
    Total number of Hit= Nsignal+Nnoise <15
  Ring radius
    Radius = Gaussian distribution function
    Mean of radius=20mm
    Sigma of radius=0.1mm

## Slide 6: Event by Event Display (infinite pixel)
strong noise
low noise
Signal
noise

## Slide 7: Radius (in each event) Distribution (infinite pixel)
20.0±0.129 mm

## Slide 8: Event by Event Display (finite pixel)
loud noise
low noise
● Signal
○ noise
Fitted rings are generally smaller than the actual rings
Fitted rings are close to the actual rings, even with loud noise

## Slide 9: Radius (in each event) Distribution (finite pixel)
r
3.54mm
measured value of radius
=r+3.54
=18.94mm
Sensor 1
Sensor 2
Sensor 3
Sensor 4
r=15.4±0.12 mm
Smaller than the actual value (20mm).
difference due to pixel size

## Slide 10
Simulation Result

## Slide 11: Simulation Setup
Beam
  120GeV proton
  1,000 events
  Launched perpendicularly toward center of the detector
  Beam diameter 1cm
Detector
  Aerogel gel: 3.3cm thick, n=1.03
  Fresnel lens: f=3 inches
  Sensor plane : at Fresnel lens focal plane, 1mm gap between glass windows (or 5mm between sensors)

## Slide 12: Detector Setup
Sensor plane

## Slide 13: Event by Event Display
strong background
low background

## Slide 14: Radius (in each event) Distribution
r
3.54mm
Actual measured value of radius
=r+3.54
=18.94mm
Radius of each photon hit from simulation result.
No Q.E. applied
r≈15.4±0.15 mm
r≈18.7±0.60 mm

## Slide 15: Center Position (in each event) Distribution

## Slide 16: Summary
Ring Finder Algorithm has be tested using Monte Carlo method
Ring Finder Algorithm is implemented in simulation analyses

## Slide 17
Back Up

## Slide 18: Ring Finder Analysis Procedure
Accumulated Data

## Slide 19: Detector Setup

## Slide 20: Detector Setup
Sensor plane