## Slide 1: Prototype stave design and tooling review - outcome

## Slide 2: Key observations and reaction
…manufacture of such a structure is probably attainable but we felt that the project was challenging, particularly given the short timescales and our general feeling that the team has limited effort available to it..
  increasing effort is a major goal – stronger invovlement from the North would be very much appreciated
…concerned that the use of 2-ply (inherently asymmetric) facings could be difficult to consolidate fully …
  will use symmetric 3 ply lay-up, K13C2U to start with, will investigate thinner prepreg in the future
…suggest the team evaluate using an “open-mould” technique with a suitable intensifier as a back-up…
  we are changing tooling design to an open-mould (see Adam’s talk)
…gluing of sensor modules onto the bare stave and the necessity to control of the bond-lines to achieve a gas-tight seal is a major challenge…
  changes to tooling should address this
… other aspects of the project, eg FPC and TAB bonding development work, would benefit from having reasonable mechanical mock-ups (perhaps ¼ length staves) to work with and the stave development team should seek to make these available for as an output of their programme…
  This was planned already