## Slide 1: ProtoDUNE News
Wenqiang Gu

## Slide 2: Recent progress
Restarted beam run now, overnight 7GeV run nice and stable
This week’s activities:
  PDS: noise investigation, if coincident with TPC activities
  High pressure Cherenkov: not enough light reaching PMTs, will replace it with another Cherenkov from the East Area
  CE gain: unexpected undershoot at 14mV/fC (see next slide), confirmed by Roger with pulser run. Issue not obvious with 7.8mV/fC, will keep this gain for the coming data taking. “Should be only 2% change in noise”
  Beam run plan: operate at 1GeV/c, changing polarity every two days

## Slide 3: Unexpected undershoot
Stakeholders: noise filter (Xuyang et al.),
Plan to run at 7.8mV/fC
Stakeholders:
  Noise filter (Xuyang et. al)
  CE calibration (Karla)
  Signal processing (e.g., threshold for ROI)
  Simulation

## Slide 4: The Cherenkovs
Only low-pressure Cherenkov is currently working
It’s okay for +/-1GeV/c pion data
Only 1GeV/c electron is vetoed by low-pressure Cherenkov
1GeV/c proton is vetoed using TOF

## Slide 5: Progress on APA1’s field response (FR)
For the v1, a standard 6-electron-path simulation is converted to the wirecell FR format
To-dos:
  Use a fine-grained 26-path simulation from Yichen
  How to take care of the charge normalization? PDSP normalized to 1 electron on a W wire, now we just take the value from GARFIELD for PDHD
Yichen

## Slide 6
Total electrons | Grid collected | U | V | W | Others
26 | 0 | 0 | 19 | 5 | 2
Total electrons | Grid collected | U | V | W | Others
26 | 0 | 1 | 19 | 4 | 2
G
U
V
W

## Slide 7: 2D field response: PDHD APA1
central electron path
central electron path
central electron path
Mostly induction in W now

## Slide 8: Signal processing frames
Barely see ROIs in the signal processing with the new v1 FR
  See tracks in the initial deconvolution (“loose_lf”)
  Maybe noisy, is S/N ratio good enough? Check with simulation
  Problems in the ROI finding? see next slide
original sigproc with wrong field response
Noisy deconvolution?
Field response issue?

## Slide 9: Use the induction-specific workflow for W
X