## Slide 1: Polarized Protons at BNL and some Run 24 results
8/21/24
Machine Learning Collaboration Workshop, BNL, Aug 2024
V. Schoefer

## Slide 2: Overview
Facility overview
Digressions about
  ML work to date
  Challenges for digital twin
  Recent operations

## Slide 3: RHIC Physics Program
To date: 12 different species combinations in collision
Polarized p-p and p-ion collider operation
Energy scan of Au-Au collisions from 100 GeV/N (max) down to sub-injection energies as low as 3.85 GeV/N
Polarized beam operation
Beam energy scan at low energies

## Slide 4
RHIC Accelerator Complex
Tandem van de Graaff
~1.2 km
 | Au | Pol. Protons
Linac (H-) | -- | 1.1
Booster | 1 | 2.3
AGS | 10 | 23.8
RHIC | 100 | 255
Typical Top Energies [Total, GeV/N]
 | Circumference [m]
Booster | 201
AGS | 807
RHIC | 3833
Accelerator Rings
4
Heavy Ions | Protons
E-beam Ion Source (EBIS) | OPPIS (polarized)
Tandem Van de Graaf | High-intensity H- (unpolarized)

## Slide 5: Collider performance
Luminosity: instantaneous rate of collisions, related to the beam density, depends on
  Intensity : number of particles in a bunch
  Emittance: a measure of the beam volume
We’re also concerned with:
Polarization: degree to which the (quantum mechanical) spin of all the particle in the beam are aligned along some direction, usual vertical
  In general, the beam starts highly polarized, then motion in the accelerator fields scrambles them (depolarizing resonance). You can either
    Manipulate the fields to avoid or cancel resonance
    Make the beam size (emittance) small, which weakens the resonance effects

## Slide 6: Polarized collider performance
Collider luminosity,
N = intensity/ bunch
= tran. emittance
Polarized collider figure of merit (for polarization P):
FOM =
Since both emittance and polarization degrade with intensity figure of merit decreases rapidly
FOM dependence on intensity closer to linear in N than quadratic.
Pol vs Intensity
Emittance vs Intensity
AGS extraction
Polarized beam collider FOM
transverse spin
longitudinal spin
Impact of intensity increase on FOM given emittance and polarization dependence at AGS extraction

## Slide 7: RHIC Polarized Beam Complex
 | Max Energy [GeV] | Pol. At Max Energy [%] | Polarimeter
Source+Linac | 1.1 | 82-84 | 
Booster | 2.5 | ~80-84 | 
AGS | 23.8 | 67-70 | p-Carbon
RHIC | 255 | 55-60 | Jet, full store avg*
 | Relative Ramp Polarization Loss (Run 17, full run avg)
AGS | 17 %
RHIC | 8 %
* Includes both ramp loss and store decay
PHENIX
AGS
LINAC
BOOSTER
Pol. H- Source
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
2 Siberian Snakes/ring
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR
AGS Polarimeter
Spin flipper

## Slide 8: RHIC Injector Cycle: The supercycle
The “supercycle” is the collection of all the injectors cycles (sources, Booster, AGS)
Typically 4-6 seconds long
Single pulse of Linac protons becomes a single bunch at AGS extraction
Each RHIC ring (blue and yellow) takes 111 bunches for a fill
  Fill setup take 1-2 hours
A RHIC proton store lasts ~8-9 hours
RHIC per bunch intensity 2.5-3x1011
Booster main magnet cycles
AGS main magnet
Booster NSRL cycle
hysteresis

## Slide 9: Booster injection
Booster injection/early acceleration process sets maximum beam brightness for rest of acceperation though RHIC
Linac pulse of 300 us, H- beam ~6-9x1011 protons
  Multi-turn, frev ~ 1 us
Strip injected through a carbon foil
Beam steered off foil after pulse finished
Coasting beam adiabatically captured by RF and accelerated
Intentional horizontal and vertical scraping reduce emittance (and intensity) to RHIC requirements ~2.5x1011 protons
Intensity
Main Magnet
injection
Capture
Hor scrape
Ver scrape
Extraction
Booster cycle

## Slide 10: Booster injection
Injection
Capture/Early acc
Intensity
Main mag
Injection
Capture
H scrape
V scrape
Extraction
Booster injection/early acceleration process sets maximum beam brightness for rest of acceleration though RHIC
Many ”knobs”
  Linac to Booster trajectory/optics matching
  Optimization of time on foil (Linac pulse length vs height)
  Linac RF phases affect capture and acceleration efficiencies
  Booster RF capture rate affects longitudinal emittance (and transverse, via space charge)
  Booster orbit and optics affect foil scattering, matching and intensity transmission.
  Betatron ‘stop band’ correctors for intensity, emittance preservation.
Difficult instrumentation
  WCM, BPMs don’t work until after capture
  No transverse profile monitor in Booster
    Scraping efficiency as proxy
    Measurable in the extraction line via multiwire
Difficult model
  Linac to Booster longitudinal effects
  Space charge
  Stripping foil
See Lucy’s talk for progress on this front.
Space charge tune spreads

## Slide 11: AGS, Polarization and Snakes
Proton energy range 2.5 GeV -> 23 GeV
Polarization preserved using
  helical dipole snakes
  + horizontal tune jump
  Resonance correction in development (would replace tune jump)
AGS Warm snake
AGS Cold snake
AGS Optics (low energy)
No snakes
Snakes +compensation
Requires “near integer” tune
  Orbit, optics unusually sensitive to errors
Helical dipoles are complicated magnets
  Large optical effects at low energy
  Many related magnetic elements for compensation orbit/optics
The complex fields and lattice + high tune requirements are a challenge to modeling (Eiad’s talk)

## Slide 12: AGS Orbit
First resonance (lowest rigidity)
Representative of post-transition orbits
Challenge underlying all experimental efforts, optics assessments, machine learning efforts
  Large, difficult to address horizontal orbit
  Makes even modeling difficult
Necessary excursions for:
  Snake trajectory
  Injection/extraction
  Remainder driven by misalignments
Control is currently distributed to different devices, controlled separately
No definition of target orbit
No automated corrections (one minor exception)
Coordinated orbit control that includes snakes, backleg windings, orbit steerers and a target seems like a pre-requisite for digitial twin (and for reliable normal operation, actually…)
Original design orbit for injection with snakes
Measured orbits
from Tsoupas, “Acceleration of polarized protons in AGS”

## Slide 13: AGS Performance
Highest AGS performance is difficult to achieve and maintain
Value in just holding a known optimum
A combination of maintaining emittances and direct polarization interventions
(Not a fit)
Known good performance line
Good performance achievable, but hard to keep
AGS Polarization vs intensity for RHIC fills (Run 24)

## Slide 14: ML efforts in the injectors
Injection and transfer (Lucy Lin’s talk)
Booster injection with Bayesian optimization
Natural extension of Booster injection work to AGS injection
Merge optimization (Yuan Gao’s talk)
Accelerating low intensity bunches and merging later avoids intensity dependent problems
High energy merging is a delicate process, ML finding/maintaining an optimum is useful
Energy measurement (NO talk)
Polarization interventions usually rely on precise measurement of energy as a function of time in ramp
Multiple methods cross-calibrated
Inverse problem / data assimilation to determine unknown parameters
Skew quad spin resonance correction optimization (NO talk)
New system being commissioned
Many variables, weak signal, expensive measurement (5-10 min)

## Slide 15: Measuring Energy (Ɣ)
From field
In RED:
Measured quantities
f = RF frequency
dR = radial shift from ’zero’
Bclock = Field reported by Gauss clock
In BLUE:
Machine parameters (not known to sufficient precision)
Ɣtr = transition gamma
R0 = true central radius of AGS
ρ0 = avg bend radius of AGS main magnet
Cscal = Gauss clock calibration (gauss/tick)
Binj = Dipole field at injection
Bdfactor = [NOT IN FORMULA] Gauss measurement sensitive to dB/dt (B-dot), not well understood
Calibration of the Ggamma meter consists of measuring Gg(B) and Gg(f) at the same times in the cycle and fitting parameters until they agree to sufficient precision
Dedicated calibration ~2 weeks
Essentially an inverse problem with data assimilation, good candidate for uncertainty quantification (how well can we determine these parameters, which is responsible for most variation?
From RF frequency
AgsGgammaCal application

## Slide 16: AGS Spin Resonance Correction Skew Quadrupoles
A set of 15 pulsed skew quadrupoles, each with an individual power supply
Designed to excite coupling resonance to compensate the 82 depolarizing resonances associated with horizontal betatron motion in the AGS partial snakes
15 knobs, 82 different resonances
  Expected effect is 10-15% gain in polarization
  A +/-2% measurement takes 5-10 minutes
Run 24: Observation of polarization gain factor (+10%) during acceleration (similar to existing tune jump), with ~half the pulses enabled)
Further improvements (enabling more pulses, +5-10% gain):
  Addressing model inaccuracies at low energy
  Iteration on orbit centering
  Possible optimizations based on ML methods
    No solid plan for how to approach this
Skew quad current pulses
Correction amplitude scan
Zero correction
Skew quad current pulses
Partial correction

## Slide 17: RHIC Run 24
RHC Injected Intensity
STAR Integrated Lumi
Planned
  14 weeks of p^ physics, 100 GeV
  6 weeks of Au, 100 GeV
Currently finishing week 13
  Extended +3 weeks of p^
  3 weeks of Au
Nominal switchover date is 9/16
Operations
  Commissioning of brand new sPHENIX detector
    Superconducting solenoid
    New time projection chamber
    Collision crossing angle
  Luminosity ramp-up delays (and restarts)
    Emittance blowup from 56 MHz SC cavity
    Transfer function/optical error

## Slide 18: Prospects for remainder of Run 24
Six remaining weeks
  3 wks colliding polarized protons
  3 wks setting up and colliding Au
    Protons still available in the injectors
What do we want to do?
  Booster/AGS injection
    Dedicated model validations?
    Tests of optimization with different (optimized?) knobs?
    How to determine optimal set of knobs?
  Skew quads
    Demonstrate an optimized configuration. Maybe in time to extract to RHIC
    Measure 1-2 more single resonance flattop responses
  Bunch merging?
  AGS/snake model validations
    Vertical dispersion predictions/measurements
Other?