## Slide 1: Experimental examples of Bayesian Optimization at BNL
August 21-22, 2024
Lucy Lin
Machine Learning Collaboration Meeting

## Slide 2: Bayesian Optimization
A powerful tool for finding the extrema of objective functions that are expensive to evaluate
Bayes’ theorem: probability of event based on previous knowledge of conditions
Tune hyperparameters of to maximize likelihood of getting data

## Slide 3: Gaussian Process
A probability distribution over possible functions that fit a set of points
GP model consists of mean function + covariance function
The probability distribution of the model output is given by a normal distribution

## Slide 4: Kernel Function
Kernel: covariance function describes how the objective varies (e.g. smoothness) in terms of the changes in the input space
Kernel function is chosen based on prior knowledge of the objective function

## Slide 5: Acquisition Function
Guide how input space should be explored during optimization
Combine predicted mean and variance from Gaussian Process model
  Probability Improvement (PI)
  Expected Improvement (EI)
  Upper Confidence Bound (UCB)

## Slide 6: Booter injection
From Linac
bend
To Booster
Booster injection process sets maximum beam brightness for rest of acceleration through RHIC
Known emittance effect on polarization loss
Intentional horizontal and vertical scraping reduce emittance to RHIC requirements
Goal: minimize emittance / maximize beam intensity after scraping
Controls: Linac to Booster (LtB) transfer line optics
Method: Bayesian optimization
scrape

## Slide 7: ML package for BO: Xopt
https://github.com/ChristopherMayes/Xopt
Flexible framework for optimization of arbitrary problems using python
Independent of problem type (simulation or experiment)
Independent of optimization algorithm & easy to incorporate custom algorithms
Easy to use text interface

## Slide 8: Xopt structure
Note: this process can also be done asynchronously

## Slide 9: LtB controls and measurement
13 quadrupoles and 16 correctors between Linac and Booster
Common practice to improve Booster injection efficiency: tune last few correctors at the end of the LtB line
Criteria to check injection efficiency: Booster early and late intensity
Booster

## Slide 10: LtB corrector scan
All 16 correctors were scanned on Jan 25, 6:55pm – 8:20pm, on PPM user 4 until Booster late intensity dropped by 50%

## Slide 11: NN model for LtB scan
15 correctors (lhn-d009 is excluded due to insensitivity) 2 intensities (Bstr_Early, Bstr_Late)
2 hidden layers: ReLU + Tanh
Training data 75% (893 points), testing data 25% (297 points), score = 0.85

## Slide 12: Test on LtB scan NN model
Controls: Power supply currents of three correctors (two horizontal, one vertical) at the end of the LtB line
Booster late beam intensity (after scraping, before extraction to the AGS)
BO algorithm developed using Xopt, using 242 LtB scan data points as training data
Algorithm converged within 50 samples

## Slide 13: Test Xopt on real machine
Controls: Power supply currents of correctors and quadrupoles at the end of the LtB
Goal: maximize Booster late beam intensity (after scraping, before extraction to the AGS)
Objective function: send PS current to selected magnets, wait 5 seconds (each Booster cycle/injection pulse lasts ~ 4 seconds), read and return Booster intensity measurement
BO algorithm developed using Xopt, with added features such as interpolated optimization and trust region BO (tuRBO)
https://christophermayes.github.io/Xopt/examples/single_objective_bayes_opt/turbo_tutorial/

## Slide 14: Case 1: 2 correctors
Feb 26, PPM user 4, 7pm – 9pm
Controls: Power supply currents of two correctors (one horizontal, one vertical) at the end of the LtB line
Algorithm converged within 100 samples (15-20 minutes)
Operator: Petra Adams

## Slide 15: Case 2: 4 correctors
Feb 27, PPM user 4, 7pm – 9pm
Controls: Power supply currents of four correctors (two horizontal, two vertical) at the end of the LtB line
Algorithm converged within 120 samples (20-25 minutes)
Operator: Petra Adams

## Slide 16: Case 3: 2 correctors + 2 quadrupoles
Mar 4, PPM user 3, 7pm – 9pm
Controls: Power supply currents of two correctors and two quadrupoles at the end of the LtB line
Beam size decrease in both planes in the BtA line in correspondence with intensity increase
Operator: Petra Adams

## Slide 17: Case 4: horizontal only
Mar 13, PPM user 4, 9:30am – 10am
Controls: Currents of two horizontal correctors and two horizontal quads
Maximize Booster late intensity / input intensity (to reduce noise)
Initial beam was sabotaged by changing magnets in the middle of LtB line
Multiple solutions for optimization: objective value converges but input values don’t
Operator: Vincent Schoefer

## Slide 18: Case 5: vertical only
Mar 14, PPM user 4, 12:30pm – 1pm
Controls: Power supply currents of two vertical correctors and two vertical quads
Maximize Booster late intensity / input intensity (to reduce noise)
Initial beam was sabotaged by changing magnets in the middle of LtB line
Same problem with multiple solutions
Operator: Vincent Schoefer

## Slide 19: LtB BO: next step
In the process of creating operational interface for running BO in the control room
More input options can be considered: Linac Tank 9 phase etc.
Averaging option for objective to reduce noise/obtain error bars
Allow user to set BO hyperparameter choices: Step size, Acquisition function, GP kernel & prior function etc.

## Slide 20: Booster to AGS transfer line
Extraction septum at F6 in Booster, injection septum at L20 in AGS, no scraping
15 quadrupoles, 2 major bends (15 DH2 & 3), 3 small bends (2 DH1, 1 DH4, 8 DH5)
Multi-wires MW006, MW060, MW125, MW166

## Slide 21: BtA controls and measurement
Booster
AGS
5* (horizontal) bends
2 (horizontal) correctors
4 (vertical) correctors
7 (focusing) quads
8 (defocusing) quads
Objective (beam intensity ratio): ags_Early / bst_Late (no scraping in BtA injection, optimal value should be ~1)
*only 4 power supplies

## Slide 22: First attempt (07/08 inconclusive)
Horizontal steering + focusing
(…, correctorH, quadD, quadF, correctorH, quadD, quadF, bend, correctorV, quadD]
Used for optimization
Turned ON
Detune #1
Detune #2:
BtA vacuum valve closed
Reset

## Slide 23: Second attempt (07/09 successful)
Horizontal + vertical steering
(…, correctorV, quads, correctorH, quads, correctorH, quads, bend, correctorV, quad]
Used for optimization
Turned ON
Detune #1
Bayesian Optimization

## Slide 24: 07/09 BtA BO results
Convergence speed can be better (~1 hour for 4 inputs), could be due to small step sizes
Algorithm finds different solution from previous optimal settings
Objective ratio bigger than 1: calibration error
Horizontal correctors
Vertical correctors

## Slide 25: BtA BO: next step
Currently, the optimization is ignoring the following measurements:
  Turn-by-turn orbit coherence (AGS F18 BPM)
  Emittance/beam size (AGS eIPM)
  Polarization (AGS pCNI polarimeter)
The first two could be included by using multi-objective Bayesian optimization (MOBO), or by defining a custom a reward function. Before this, it is important to write some data preparation and data pipelining scripts for proper handling of all the ADO data + timing.

## Slide 26: Summary
Bayesian optimization algorithm has been demonstrated to work well to improve and maintain Booster injection efficiency in both planes under different system settings (PPM users)
If controls include upstream and downstream LtB magnets, changes made in the middle can be compensated to bring Booster beam intensity back up
Decrease in beam size in the BtA is observed in both planes in correspondence with intensity increase, which signals decrease in emittance
Preliminary results show the algorithm also works for AGS injection, further studies are needed to improve performance
Software development is underway to incorporate the algorithm into the control system