## Slide 1: Status of ePIC µRWELL-BOT + PED Test Article
TIC Weekly Meeting
August 19, 2024
Kondo Gnanvo, Jefferson Lab
On behalf of the ePIC MPGD DSC

## Slide 2: Outline
µRWELL-BOT Detector Layout: Requirements & Design Considerations
PED - Engineering Test Article
Plans & schedule of the production µRWELL-BOT modules assembly
Summary

## Slide 3: Overview of ePIC Tracking Detector
RWELL-ECT
RWELL-BOT
CyMBaL
AC-LGAD Barrel
AC-LGAD Endcap
SVT Barrels
SVT
SVT Endcaps
SVT Endcaps
RWELL-ECT
Technologies
MAPS (Si)
MPGDs (Gaseous)
AC-LGADs (Si)

## Slide 4: µRWELL-BOT to enhance tracking for hpDIRC: Improve angular resolution?
ePIC Barrel Outer Tracker (µRWELL-BOT)
Tracking layer close to hpDIRC detector to help improved and angular and space point resolution at the DIRC level
Acceptance matching with hpDIRC bars
Good spatial resolution?: simulation results resolution improvement with μRWELL not conclusive
Barrel Outer Tracker
hpDIRC (barrel PID)
Impact of angular resolution on hpDIRC performance
Matt Posik simulation angular resolution slides

## Slide 5: µRWELL-BOT for pattern recognition: Fast timing and additional hit point
ePIC Barrel Outer Tracker (µRWELL-BOT)
Fast timing layer together with the TOF & Inner MPGD (CyMBaL) to assist the slow Si trackers with pattern recognition.
What timing requirement? 10 - 20 ns or worse?
  Need clarification here from simulation  detector design choices depend on that
Additional hit point to tracking for redundancy
  If hit point resolution is not required, how bad of the resolution is acceptable

## Slide 6: µRWELL-BOT Layout
µRWELL-BOT Layout
Coverage: L = 340 cm (−165 cm ≤ 𝑍 ≤ 175 cm) & R = 72.5 cm
24 planar modules configured in 12-sided polygon shape trackers
  Segmented into 12 sectors along azimuthal direction (phi)
  2 modules (left) & (right) per sector in z along beam axis
Technology:
Thin-gap & double amplification (GEM & µRWELL)
Capacitive-sharing U-V strip readout
  Nominal 70 µm for perpendicular tracks i.e. along phi direction
  On average 150 µm on for tracks in angle range [0, 45 degrees]
Fast timing layer ~ 10 ns
Radiation length < 2% in active area
Barrel Outer Tracker
hpDIRC (barrel PID)
Left module
Right module

## Slide 7: µRWELL-BOT Module: Services & Integration in ePIC
Installation
Removal & Service
dRICH have to be moved out 4 meters to remove BOT Or Remove DIRC
Service line
Seung Joon’s talk at ePIC Coll. Meeting (July 2024)
https://indico.bnl.gov/event/20727/contributions/93669/attachments/56059/95920/BOTandECT.Integration.SeungjoonLee.pdf
Main integration challenges:
Space limitation in ePIC detector environment
µRWELL-BOT detector envelop in ePIC
  In radial direction: 2.5 cm
Installed in support structure of barrel ECAL in front (from IP) of hpDIRC bar

## Slide 8: µRWELL-BOT Module: Integration & Services & integration in ePIC
Dimension: 180 cm x 38 cm x 2.5 cm
MPGD chamber
SALSA-FEB
B2B connector
FEB support bracket
Service area
F
Main integration challenges:
Space limitation in ePIC detector environment
µRWELL-BOT detector envelop in ePIC
  In radial direction: 2.5 cm
Installed in support structure of barrel ECAL in front (from IP) of hpDIRC bar
Optimization of the acceptance matching with hpDIRC
Seung Joon’s talk at ePIC Coll. Meeting (July 2024)
https://indico.bnl.gov/event/20727/contributions/93669/attachments/56059/95920/BOTandECT.Integration.SeungjoonLee.pdf

## Slide 9: µRWELL-BOT Module: Thin-gap GEM-µRWELL Hybrid Detector
1800 mm
Back view
1700 mm
330 mm
360 mm
Top view
V-strips
U-strips
µRWELL-BOT module
Thin-gap (1-mm drift) hybrid amplification GEM-µRWELL
Capacitive-sharing U-V strips readout layers(45O stereo angle)
Pitch: 1.14 mm (1790 U-strips and 1790 V-strips per modules)
On-detector Front End Boards (FEBs) based on SALSA chips
14 FEB / modules (assuming 4 SALSA chips i.e 256 e-ch / FEB)
Connectors on the back of the modules (no need for flex cables)
Active area 330 mm
3 mm honeycomb
readout PCB
FEB
G10 frames
GEM
µRWELL
cathode
cross-section view of thin-gap GEM-µRWELL detector

## Slide 10: Technology choice: Thin-gap GEM-µRWELL Hybrid Detector
Active area 34 cm
Active area 36 cm
3 mm honeycomb
readout PCB
FEB
G10 frames
GEM
µRWELL
cathode
cross-section view of thin-gap GEM-µRWELL detector
Technology: Thin-gap GEM-µRWELL hybrid detector
hybrid amplification MPGD:
  GEM (preamplification) and µRWELL (main amplification)
  Large detector gain & stable operating HV
Readout layer: 3-layer capacitive-sharing U-V strip readout
  Achieve excellent spatial resolution with thin gap detector
Challenges with standard (~3 mm drift gap) MPGDs
Degradation of the spatial resolution with track angle .
E × B in magnetic field negatively impact resolution
Development of Thin-gap MPGDs (~1 mm drift gap):
Improve spatial resolution at large angle
Reduce E × B effect in magnetic field
        Improve the detector timing resolution
        Trade off  lose a couple of % in detector efficiency
https://wiki.bnl.gov/eic/upload/ERD_tgMPGD_FY22_endOfYearReport_final.pdf
3 mm μRWELL prototype

## Slide 11: Technology choice: Performance of thin-gap GEM-µRWELL in test beam
R&D funded by JLab administered DOE EIC Generic R&D Program as EICGENRandD_2022_23
Proof of concept
Concept of thin-gap GEM-µRWELL hybrid prototype demonstrated in beam test at the Fermilab Test beam Facility in Summer 2023 (red plots)
Space resolution < 150 µm and efficiency of 92% on average for 1-mm thin-gap GEM-µRWELL prototype (red dots) and for track in an angle range between 0 – 45 degrees.
Efficiency
Residuals
Efficiency
https://wiki.bnl.gov/eic/upload/ERD_tgMPGD_FY22_endOfYearReport_final.pdf
Baseline technology for ePIC Barrel Outer MPGD tracker

## Slide 12: Few consideration on technology choice options: based on personal experience
 | efficiency | spatial resolution | Timing resolution | E × B
Thin (1 mm) gap hybrid amplification – 2D readout |  (need to be demonstrated) |  |  |  (optimized)
Standard (3 mm) gap single amplification – 2D readout |  |  |  |  (acceptable)
Standard (3 mm) gap hybrid amplification – 2D readout |  |  |  |  (acceptable)
“Slow” gas mixture like Ar-iC4H10 (90/10)
 | efficiency | spatial resolution | Timing resolution | E × B
Thin (1 mm) gap hybrid amplification – 2D readout |  (~90% for perpendicular tracks) |  |  |  (minimized)
Standard (3 mm) gap single amplification – 2D readout |  |  |  | 
Standard (3 mm) gap hybrid amplification – 2D readout |  |  |  | 
“Fast” gas mixture like Ar/CO2 (70/30)
Efficiency:
 < 95% < 
Spatial resolution:
< 150 µm < 
timing resolution:
< 20 ns < 
E× B effect:
< 20 degree < 

## Slide 13: PED Engineering Test Article: Design of µRWELL-BOT module
Top honeycomb support
Cathode foil
Drift frame
GEM foil
induction frame
µRWELL foil
UV readout PCB
FEBs
PED engineering test article module (2024–2025):
Full scale 1-mm thin-gap GEM-µRWELL prototype
Validation of the concept on large area detector
Will address production and integration challenges of ePIC
Design at JLab and CERN MPT workshop ongoing
Test article module fabrication completion 2024
Expect to be tested in beam at FNAL summer 2025

## Slide 14: Design consideration: µRWELL PCB and GEM foil (JLab & CERN MPT)
µRWELL PCB:
Active area divided into 36 HV sectors (~ 156 cm2)
Same segmentation pattern as the GEM foil  minimize dead area
GEM foil:
foil divided into 36 HV sector ~ 156 cm2
Trade-off between active-to-dead area ratio for gap uniformity (~1% dead area)
New concepts to be tested to enhance performance:
Random HV segmentation of both GEM and μRWELL
Higher hole density (pitch 100 µm instead of 140 µm)
Design of both uRWELL and GEM is being finalized a lot of back and forth between CERN MPT workshop and JLab RD & I Group
Parts delivery is expected by December 2024 – January 2025

## Slide 15: Design consideration: 2D (U-V)-strip readout layer
3-layer capacitive-sharing U-V strip readout
Strip pitch: 0.8 mm (along U and V axis)
Trace pitch: 1.14 mm along horizontal axis (traces(
Max strip length is 46.7 cm
1780 U-strips + 1780 V-strips
7 FEBs / U (V) planes  14 FEBs / µRWELL-BOT modules
140-pins Hirose connectors
All connectors on the back of the rigid µRWELL / readout PCB
U-strips
V-strips
0.8 mm
1.14 mm
U-V strip configuration

## Slide 16: Design consideration: 2D (U-V)-strip capacitive-sharing readout options
cross-section view of 3-layers capaSh readout
ASACUSA-like R/O design
https://doi.org/https://doi.org/10.1016/j.nima.2022.167782
U-strips
V-strips
0.8 mm
1.14 mm
COMPASS-like R/O design
cross-section view of 3-layers capaSh readout
ASACUSA-like design: preferred option
Equal U-V charge sharing guaranty
Perfect one-to-one matching with pads capacitive sharing layer 3 pad
But large number of vias  challenging fabrication issues.
COMPASS-like design: alternative option
Fabrication easier for Rui’s workshop
Need to fine tune parameter for equal U-V sharing  width of top and bottom strips
Might require a couple of iteration
No vias in the active area

## Slide 17: Design consideration – Support frames
Honeycomb support: Top frame
2 mm wide spacers divide the active area into 6 sectors
GEM top support: Drift Frame
36 × 500 µm wide spacers to keep uniform gap in drift region  match the 36 HV sectors
GEM bottom support: Induction Frame
No spacers in induction frame  no contact with µRWELL
Capacitive-sharing X-Y strip readout
µRWELL foil
GEM foil
Cathode foil
Honeycomb support
Fully assembled detector

## Slide 18: Plans & timeline for PED Engineering Test Article: µRWELL-BOT module
Jan 2024 – Dec 2024: Mechanical drawing of all parts of the detector almost completed
Dec. 2024 – Jan. 2025: Complete design of GEM foils, μRWELL PCB and U-V capacitive-sharing readout  JLab RD&I – CERN MPT
October 2024 – March 2025: Setup class 1000 Clean Room at JLab with all required equipment and infrastructure for test and assembly of the μRWELL-BOT engineering test article module
End January 2024: Expect delivery of the GEM foils, μRWELL PCB and U-V capacitive-sharing readout
March 2025 – June 2025: HV test of the GEM foils, μRWELL PCB and assembly into a detector in clean room
June / July 2025 – : Characterization of μRWELL-BOT engineering test article in cosmic and in beam test (Fermilab or CERN)

## Slide 19: Assembly plans for the production modules: Equipment at the assembly sites
FIT Clean Room: assembly of
CMS GE1/1 GE2/1 and ME0 GEMs
CMS GEMs
UVa Clean Room: SBS GEMs, MOLLER GEMs, PRad GEMs, CLAS12 µRWELL, Hall D GEM-TRD prototype
Moller GEM foil
JLab MPGD Clean Room: New capacity for large MPGD module assembly
3 assembly sites with fully equipped MPGD Detector Lab
  Fully equipped CLASS 1000 Clean rooms for module assembly
  Cosmic tracking telescope setup with coincidence trigger counters and readout & DAQ system
  X-ray setup for high rate studies and long term stability …
  Will setup DAQ and readout system for SALSA – MPGD readout system

## Slide 20: Assembly plans: Planning & schedule
06/2025
06/2026
04/2029
06/2029
PED & validation
Ongoing design of full size µRWELL-BOT module
Procurement of GEM foils, µRWELL PCB – 12 / 2024
Assembly at JLab test in at FNAL - 06/2025
Pre-production
Assembly of one pre-production module (module#0)
Setup of infrastructure and equipment in assembly sites
Production
Assembly and QA of 9 production modules at assembly sites
Full characterization at assembly sites of each module on cosmic stand and with radioactive sources
Shipment to BNL
Shipment of all 24 modules to BNL
Commissioning at BNL cosmic test stand of all µRWELL-BOT as well as µRWELL-ECT
Commissioning & Installation
Commissioning
Installation

## Slide 21: Summary
The ePIC Barrel Outer MPGD Tracker (µRWELL-BOT) is based on thin-gap GEM-µRWELL amplification technology
µRWELL-BOT provides improved tracking option to the hpDIRC and pattern recognition with fast timing hit to Si tracker in the barrel
Design of the µRWELL-BOT is well advanced and integration issues and mechanical constraints are being addressed in the design
The engineering test article pre-production module is under development and expected to be validated by Summer 2025
Preliminary plans and schedule for the production of µRWELL-BOT modules in assembly sites is initiated
The ePIC MPGD DSC is established and very active with several institutions with vast experience with large MPGD productions

## Slide 22
Backup

## Slide 23: MPGD-DSC: Organization of ePIC MPGD Subsystem Collaboration
Outer MPGD Tracker: Module assembly
Production sites: University of Virginia (UVa), Florida Institute of Technology (FIT) and Jefferson Lab (JLab)
Vast experience with large scale and large MPGD projects among the 3 institutions
10 modules per site (8 + 2 spares)
Welcome to new institutions to join the effort

## Slide 24: Design consideration: µRWELL-BOT module
Front view of the µRWELL-BOT module design
back view of the µRWELL-BOT module design

## Slide 25: Design consideration: Honeycomb frame
3 – 5 mm honeycomb
honeycomb
3 mm
1720 mm
1700 mm
330 mm
360 mm

## Slide 26: Design consideration: Drift frame
3 – 5 mm honeycomb
2 mm
1720 mm
360 mm
89 mm
0.4 mm
283 mm
165 mm
0.4 mm
Active area 330 mm
Active area 1700 mm

## Slide 27: Design consideration: Induction frame
3 – 5 mm honeycomb
1720 mm
1700 mm
330 mm
360 mm

## Slide 28: Assembly plans: ES&H
ES&H procedure will derived from past experience in each assembly site with similar system
  Non flammable operation gas mixture Ar / CO2  no special safety concern or implementation procedure needed
  HV supply via simple passive divider  Procedure to isolate any electric point on the detector
  Will follow JLab ES & H procedures for handling radiation sources during QA at the lab
  Similar procedures will be implemented in the various institutions
  Will have all these procedure documented in the appropriate ePIC documentation database (for example EICLOG @ JLab)

## Slide 29: Assembly plans: Quality Assurance (QA)
Test and characterization of µRWELL-BOT modules
  HV test in N2 of GEM and µRWELL sectors before, during and after assembly (in clean room)
  Gas leak test and sealing after module assembly
  Electrical connection capacitance and pedestal noise test of all U & V and strips
  Tag dead strips and replace FEB cards with dead readout channels
  Efficiency and relative gain uniformity studies with cosmic setup
  absolute gain measurement with radioactive source (local measurement)
  Large 2D X-Ray scanner for absolute gain uniformity (JLab)
UVa X-Ray box

## Slide 30: Design consideration: Some General considerations
Charge 2,3
Rate Capability
    Not critical ~ 1 kHz/cm2 or less
Radiation Hardness
    Not critical for the detectors
    Important for FEBs and RDO electronics boards
Temperature Stability
    Not critical for the detector performances
    Detector calibration should consider gas pressure variations
Electronics power consumption and cooling
    SALSA ASIC consumption ~ 15 mW/ channel at 1.2V
    Air vs liquid cooling is under study at Saclay – see Irakli’s talk
µRWELL-BOT
1 MeV neutrons
4 × 109