## Slide 1
SRO Application:
Streamlined Generic DAQ Tool for Detector R&D
Hanjie Liu
Streaming Readout Workshop SRO-XII

## Slide 2: Outline
Overview of Jefferson Lab
Motivation of the project
Development plan
Summary

## Slide 3: Jefferson Lab
Continuous Electron Beam Accelerator Facility (CEBAF)
5 Arcs: 2.2 GeV, 4.4 GeV, 6.6 GeV, 8.8 GeV, 11 GeV
Four experimental halls (A, B, C, D): fixed-target nuclear physics experiments
Two running period per year: Spring, Fall (~ 4 months each period)
For each running period, each hall focuses on one or two experiments that are approved by the PAC committee

## Slide 4: Experimental Halls A and C
Hall C Standard Spectrometers: SHMS, HMS
But it’s like LEGO …...

## Slide 5: Experimental Halls A and C
Experiments bring in new detectors
NPS experiment (2023)
HKS experiments (~2027)

## Slide 6: Experimental Halls A and C
Beam test for detector R&D: rates, backgrounds, radiation tolerance
HMS
SOLID detectors beam test (2023)

## Slide 7: Experimental Halls A and C
Hall A experiments
SBS experiments (2021 – 2023)
Moller experiment (2026 – 2029)
SBS GEP5 experiment
(2024 – 2025)

## Slide 8: Motivation
All the new detectors R&D (testing, commission etc.) need DAQ systems
Not even mention all those detectors in EIC …...

## Slide 9: Standard JLab DAQ system
DAQ modules and CODA
VXS crate
VME CPU (ROC)
VTP (trigger processor, ROC)
SD (signal distribution)
TI (trigger interface)
FADC (flash ADC)
TDC etc….
CODA
https://coda.jlab.org/drupal/
Current two ways of running:
NIM trigger TI ROC read out ADC/TDC data that are associated to the trigger
VTP generates trigger using FADC trigger path data. TI ROC read out associated data

## Slide 10: Motivation
Users are heavily involved in the detector R&D
Building physical triggers requires extra modules and setup time (repetitive work )
NIM triggers usually require scintillators (size limitation etc.)
SRO that allows online trigger, it would reduce the setup time and provide more flexibility on the readout data
Note: in these situations, normally the trigger rate is few Hz and the data rate is small

## Slide 11: A Generic SRO DAQ tool for detector R&D
The current DAQ modules support SRO (Chris Cuevas talk this morning)
First version of SRO CODA is ready (David Abbott talk this morning)
Need a plugin program that allows user designed online triggers
FADC
VTP
Event Builder
VXS backplane
QSFP links
Event Transfer
Hardware
Software
Event Transfer
Event Recorder

## Slide 12: A Generic SRO DAQ tool for detector R&D
Information provide to the user: time slice data that shows hit or not hit at a channel
User writes a C++ program to determine the channels and algorithms that generates a trigger using multiple time slices’ data
Filter and reorganize the time slices’ data that are associated to the trigger, and build them into an event
Pass the event to the ET for recording
Users will program the trigger
Users keep using their familiar decoder
Development

## Slide 13: A Generic SRO DAQ tool for detector R&D
FADC
VTP
Event Builder
VXS backplane
QSFP links
Event Transfer
Hardware
Software
Event Transfer
Event Recorder
NIM trigger
TI
VMECPU
Validation and Monitoring
Compare NIM trigger events and online trigger events
Online trigger
(designed to be same as the NIM trigger logic)
Monitoring
Monitoring

## Slide 14: Current Status and Plan
Test stand with a simple detector
Active Analyzer:
4 by 8 blocks, each block is detected by a PMT
The signals coming from the PMTs are sent to the FADCs
NIM trigger:
(1 || 2 || 3 || 4) || (29 || 30 || 31 || 32 )
Rate ~ 10 Hz

## Slide 15: Current Status and Plan

## Slide 16: Collaborators
David Lawrence
EPSCI group
Nathan Brei
EPSCI group
Brad Sawatzky
SCI
Dmitry Romanov
EIC group
Bryan Moffit
FEDAQ group
Hanjie Liu
Hall A/C

## Slide 17: Summary
SRO is not only useful for large setups, but also can be useful for small detector R&D stands, which will save setup time and provide flexibility on data taking
The SRO generic DAQ tool can be deployed anywhere on/off site for four Halls, EIC etc.