## Slide 1: ePIC DAQ Overview
ePIC Electronics and DAQ WG Conveners
Fernando Barbosa (JLab), Jin Huang (BNL), Jeff Landgraf (BNL)
WBS 6.10.08 Electronics
Fernado Barbosa (Jlab)
WBS 6.10.09 DAQ
David Abbott (Jlab), Jeff Landgraf (BNL)

## Slide 2: Contents
EIC Collider/DAQ Environment
ePIC Detector Electronics and DAQ
  Readout Technologies
  Streaming Concept
  Components and Architecture
  Scale of DAQ system and data
  Readout chain and protocols
  Component Status
  Schedule

## Slide 3: EIC Collider & DAQ Environment
Collider Parameters
Located at Brookhaven National Lab, NY
1260 Bunches arriving at 98.5Mhz (10.15ns bunch separation)
1.015us abort gaps (100 bunches)
⇒ 20 – 141 GeV
𝓛max ⇒ 1034 cm-2 s-1
Electron, proton, and light nuclei beams can be polarized
Each bunch can have different polarization states
  DAQ must tag data to specific bunch crossings
  Need to track luminosity for each bunch crossing
Physics Performance
Maximum DIS rate ~500kHz
Large number of Channels
Low occupancy

## Slide 4: ePIC Detector Readout Technologies
~30 Detectors
Spread over +/- 40 meters
(13 bunch crossings @ c)
5 main digitization ASICs, as well as dedicated sensors and discrete readouts (See Fernando Barbosa’s Talk Tomorrow!)
Many technologies, but effort has been made to make use of possible synergy…

## Slide 5: ePIC Detector Readout Technologies
13 Calorimeters:
7 x SiPM – CALOROC
5 x SiPM – Discrete
1 x SiPM – Commercial fADC250

## Slide 6: ePIC Detector Readout Technologies
Tracking:
4 x ITS3 – VTRX+ / lpGBT
3 x uRWELL – SALSA
1 x Micromegas – SALSA
AC-LGAD time of flight

## Slide 7: ePIC Detector Readout Technologies
AC-LGADs:
6 x Pixels: EICROC
2 x Strips: FCFD / EICROCx

## Slide 8: ePIC Detector Readout Technologies
3 RICH Detectors:
dRICH: SiPM – ALCOR
(needs single photon sensitivity)
pfRICH: HRPPD – FCFD / EICROCx
hpDIRC: MCPPMT – FCFD / EICROCx
(same FCFD / EICROCx as for
AC-LGAD strip detectors)

## Slide 9: Streaming in ePIC
DAQ
Definition of streaming is “No L0 trigger”
  All data is zero suppressed by the front end electronics
  No system wide deadtime in normal operation
  Collaboration should have the full ability to make data selection cuts on the widest possible criteria
    Flexible event selection
    Flexible data selection
    Full background characterization
  But subject to an overall throughput budget of ~100Gb/sec
ePIC Streaming will include
  Capabilities for hardware and firmware based triggering
  Capability for flow control
  Zero suppression & aggregation within data packets
Greater sensitivity to noise than triggered system
Greater sensitivity to backgrounds than triggered system
Computing
Definition of streaming is “Process data as it arrives”
  Fast Analysis (~3 weeks not months or years) using automation of calibration and reconstruction.
Requires some overlap between DAQ/computing
  Automation of calibrations
    Mapping calibration dependencies
    Mapping application of calibrations
    Mapping evolution of calibrations
  QA and monitoring can make use of full offline structure
  Consistent schemes and language for data/metadata
  Event selection / tagging / and accounting

## Slide 10: ePIC Readout Chain
Name
Design
Function
Attributes
Adapter
Detector Specific
-HV/Bias Distribution
-HV divider
-Interconnect Routing
-Sensor Specific
-Passive
Sensor
Detector Specific
Multi-Channel Sensor
MAPS, AC-LGAD
MPGD, MCP-PMT
SiPM, LAPPD
Front End Board
(FEB)
Detector Specific
-Amplification
-Shaping
-Digitization
-Zero Suppression
-Bias Control & Monitoring
-ASIC/ADC
-Discrete
-Serial Link
Readout Board
(RDO)
Few Variants
-Communication
-Aggregation
-Formatting
-Data Readout
-Config & Control
-Clock & Timing
-FPGA or lpGBT
-Fiber Link
Data Aggregation Module (DAM)
Common
-Computing Interface
-Aggregation
-Software Trigger
-Config & Control
-Clock & Timing
-Large FPGA
-PCIe
-Ethernet
Echelon 0
Computing
Common
-Data Buffering and Sinking
-Calibration Support
-QA/Scalers
-Collider Feedback
-Event ID/Building
-Software Trigger
-Monitoring
-COTS
-Ethernet
Global Timing Unit (GTU)
- Interfaces to Collider
Run Control & DAM
- Config & Control
- Clock & Timing
On Detector
SMT BGA
WBS 6.10.08
WBS 6.10.09
(BNL)
(JLAB)
Echelon 1
Computing
Common
- Archive
- Reconstruction
- Analysis
Off Project
ECSJI – Joint Institute
WBS 6.10.x

## Slide 11: Summary of Channel Counts and Data Flow
FEB
RDO
Readout Computer
Detector
DAM
PCI/Eth
Fiber
Copper
Aggregate | 2.0 Tb/sec
Noise | 1.6 Tb /sec
Signal from Physics + Background | 400 Gb / sec
Aggregate | 2.0 Tb/sec
Per RDO (Avg) | 0.7 Gb/sec
Eth
Aggregate | 109 Gb/sec
Collision Signal | 62 Gb/sec
Synchrotron Rad | Under design
Electron Beam | 4.5 Gb/sec
Hadron Beam | 1.0 Gb/sec
Noise | 41 Gb/sec
Summary of Data Flow
Scale of the system:
Electronics
  ~ 24 detectors
  ~ 5 Readout Technologies
  ~ 3000 RDOs (on detector/in racks)
  ~ 100 DAM boards (DAQ room)
  GTU (with interface boards)
Detailed simulations of DIS events, Proton and Electron beam gas lead to maximum Data Volume
  ~ 2 Tb/sec digitized
  ~ 100Gb/sec recorded
Synchrotron Radiation Simulations ongoing

## Slide 12: Data Bottlenecks
Detector | Noise (hz/channel)
ITS3 | 0.01
Astropix | 0.01
Timepix | 0.01
AC-LGAD | 30
HRPPD | 230
dRICH(initial) | 3000
dRICH(Max) | 300,000
All others | 4.5σ = 340
Evaluated Data Bottlenecks by tiling detector regions with RDO/ASIC combos
RDO data volume spec 8 gbps
  Several detectors with max RDO rate ~1/4 bandwidth
  Potential data reduction in RDO
  Use fewer populated FEB per RDO in strategic locations
dRICH dark currents handled by firmware trigger
Preliminary Noise Assumptions
Lumi Monitoring:
  Direct Photon Calorimeter ~100 channels direct streaming, readout only summary
  Track lumi by bunch
Polarimetry
  Readout by collider DAQ, not directly by detector

## Slide 13: Readout Chain: lpGBT & VTRX+
Additional factors:
  ITS-3 integrates lpGBT
  ITS-3 needs lpGBT for control interfaces
  Targeted ASICs not tied to the EIC Clock (EICROC, CALOROC, possibly FCFD will digitize at 39.4MHz, SALSA will digitize at 49.25MHz)
CERN developed readout lpGBT and VTRX+ present opportunity for ePIC:
Existing electronics
Radiation hard
Small footprint in space and material
They also represent challenges:
VTRX+
Will be obsolete soon: final production run orders by 2025!
EIC Project CD-2 (baseline) targeted for early 2026
EIC Project CD-3 (construction) targeted for late 2026
lpGBT
Operation frequency tied to 40MHz (has been tested at 39.4MHz = 2:5 harmonic of EIC frequency)
  Prevents features such as time windows centered on bunch crossings
  Complicates assignment of collisions to bunch crossings
Maps ASIC links to a through serial links to a parallel interface.
  Avoids need for flow control as deterministic ASIC output rates supported by definition
  Complicates further aggregation for ePIC (large numbers of channels, small data rates!)
Meet performance specs
Low-cost relative to commercial options
Operate independently, but designed to co-exist
Decisions:
  CD-3B request for VTRX+ (and some lpGBT)
  VTRX+ and lpGBT to be used for central detectors (SVT, MPGDs, eTOF, bTOF, dRICH, pfRICH) and similar readouts (B0, RP, OffM)

## Slide 14
 | Link | Frame Rate (MHz) | Bit Rate (MHz) | Comments
 | Digitization | 39.4, 49.25, 197 |  | 
 | ASIC Downlink | 39.4, 98.5 | 80,160,320,788 | Still documenting choices by ASIC
 | ASIC Uplink | 39.4, 98.5 | 320,640,788,1000,1280 | Still documenting details by ASIC, including number of links per ASIC
 | lpGBT Fiber Downlink | 39.4 | 2560 | lpGBT protocol carries reconstructed clock
 | lpGBT Fiber Uplink | 39.4 | 10240 | lpGBT protocol
 | RDO Fiber Downlink | ?39.4?, 98.5 | 4925, 9850 | VTRX+, Firefly, or SFP+ transceivers. ePIC DAQ common protocol carries reconstructed clock
 | RDO Fiber Uplink | ?39.4?, 98.5 | 9850 | VTRX+, Firefly, or SFP+ transceivers. ePIC DAQ common protocol
 | GTU DAM Up/Downlinks | 98.5 | 9850 | Synchronized to Beam Clock, but does not need to carry reconstructable clock
 | Clock Interface | 9.85 | 9.85 | Dedicated Clock from GTU --> DAM (suggested value: awaits GTU design)
RDO
FEB
(lpGBT)
ASIC/
Sensor
Sensors
RDO
ASIC/
Discrete
Sensors
FEB
(Stave)
(Module)
FEB
(lpGBT)
ASIC
Sensors
DAM
DAM
DAM
RDO
Readout Chain Links
GTU
E.g. bTOF, eTOF
E.g. SVT
E.g. Forward ECAL

## Slide 15: Fiber Protocol / DAQ operation
Synchronous RDO Commands:
Fit low level protocol to RDO links
  64/32 bits (80/40 bits 8b/10b encoded) per clock
  Carries reconstructed clock
Redundant bunch crossing counter
Time Frame Control & Definition
Flow Control
  FEB links (lpGBT) are deterministic
  RDO_DATA link throughput depends upon expected data volumes
(Firmware) Trigger control
Data Readout / formatting
Configuration
Slow Controls (routed to EPICS IOCs)
Document Started – requires significant revision
Time Frame Definition:
16 bits BCO (0.66ms -> 8MB @ 100Gbps)
Flexible formatting
  Filtered & Unfiltered data can coexist
Time Frames are built, they contain the full set of detectors for the time period
Tiered Data Format.
  High level flexible, named navigation via banks (e.g. star SFS, sPHENIX DAQRC)
  Low level supports direct, detector specific (eg ASIC) formats.
Synchronous ASIC Commands:
DAQ requires
  SYNC_RESET – Defines reference for time
  SYNC_READ – Read current time
  RUN_START – Set internal state for readout
Collecting Requirements from ASICs
  E.g. fire pulser, set pedestal mode, etc…
Expect to require 5 BX synchronization boundaries

## Slide 16: Global Timing Unit Functional Design
GTU idea
FPGA Based Motherboard
Daughter cards with optical interfaces to DAM boards
Plan Engineering Design During 2025 @ JLab

## Slide 17: System Components Status
FPGA/SFP+
Pre-prototype now available for timing studies and firmware development (TOF)
FPGA: Artix Ultrascale+ Class
Reconstructed Clock Timing Tests:
Mocked up with dev-kits
< 5ps timing measured with Ultracale+ FPGA and with lpGBT/VTRX+
FLX-182
Developed by ATLAS (Omega Group at BNL)
2 FELIX engineering articles obtained
RDO
GTU
DAM
FPGA/VTRX+
dRICH
Electronics design progressing, engineering article early 2025
FPGA: Artix Ultrascale+ Class
Fiber Aggregation (MAPS)
(ITS3/AC-LGAD/others)
Component Counts
Astropix / Timepix
Existing designs need adaption for integration
Electronics Design:
Defined data paths
Component selection / Block Design ongoing
Form Factor
Protocol
Data paths defined
Mapping to hardware
Time frames defined
  .66 ms -> 8MB @ 100Gbps)
Functions defined
FLX-155
Targeted for ePIC use
Undergoing testing in Omega Group
Test articles late 24/early 25
Developing many aspects
Integration of 40Mhz/100Mhz systems
Integration of lpGBT & ePIC protocol
Flow control detail
Firmware trigger & Data Reduction detail

## Slide 18: System Components Status
FPGA/SFP+
Pre-prototype now available for timing studies and firmware development (TOF)
FPGA: Artix Ultrascale+ Class
Reconstructed Clock Timing Tests:
Mocked up with dev-kits
< 5ps timing measured with Ultracale+ FPGA and with lpGBT/VTRX+
FLX-182
Developed by ATLAS (Omega Group at BNL)
2 FELIX engineering articles obtained
RDO
GTU
DAM
FPGA/VTRX+
dRICH
Electronics design progressing, engineering article early 2025
FPGA: Artix Ultrascale+ Class
Fiber Aggregation (MAPS)
(ITS3/AC-LGAD/others)
Component Counts
Astropix / Timepix
Existing designs need adaption for integration
Electronics Design:
Defined data paths
Component selection / Block Design ongoing
Form Factor
Protocol
Data paths defined
Mapping to hardware
Time frames defined
  .66 ms -> 8MB @ 100Gbps)
Functions defined
FLX-155
Targeted for ePIC use
Undergoing testing in Omega Group
Test articles late 24/early 25
Developing many aspects
Integration of 40Mhz/100Mhz systems
Integration of lpGBT & ePIC protocol
Flow control detail
Firmware trigger & Data Reduction detail
William Gu: ePIC Timing and Synchronization: (Tomorrow)
Hao Xu: Felix DAM (Tomorrow)
Luca Pontisso: Data filtering on GPU for dRICH (Yesterday)
Cristian Rossi: Noise reduction for dRICH (Yesterday)

## Slide 19: System Components Status
Echelon 0
Compute
Echelon 1
Compute
Interface
Detector Test Support
Echelon 0 location
Firmware Support for Commercial Development Boards as FELIX substitutes for test stands (to be developed)
2 Port VD100 ($800)
48 port VMK180 ($10k)
DAQ Computing:
~100 Readout computers in DAQ Room
~100 computers located anywhere with sufficient network
Splitting farm reduces DAQ room renovations but increases network requirements, space in SDCC, and complicates access
Cost/benefit analysis to be done
Scientific software and computing is off project dependency:
RRB
ECSJI
Latest Collaboration Review Sept 26-27, 2024
Interface:
Full Data to be streamed to JLAB/BNL echelon 1
Full Data to be archived at both facilities for redundancy
Readout Computers
Frame Building Computers
Data Reduction
  Filters
  Compression
  High Level Triggering
DAQ Logging
DAQ Monitoring
DAQ QA
Configuration / Run Control
Slow Controls interface (IOC)
Buffering and Data Transfer

## Slide 20: System Components Status
Echelon 0
Compute
Echelon 1
Compute
Interface
Detector Test Support
Echelon 0 location
Firmware Support for Commercial Development Boards as FELIX substitutes for test stands (to be developed)
2 Port VD100 ($800)
48 port VMK180 ($10k)
DAQ Computing:
~100 Readout computers in DAQ Room
~100 computers located anywhere with sufficient network
Splitting farm reduces DAQ room renovations but increases network requirements, space in SDCC, and complicates access
Cost/benefit analysis to be done
Scientific software and computing is off project dependency:
RRB
ECSJI
Latest Collaboration Review Sept 26-27, 2024
Interface:
Full Data to be streamed to JLAB/BNL echelon 1
Full Data to be archived at both facilities for redundancy
Readout Computers
Frame Building Computers
Data Reduction
  Filters
  Compression
  High Level Triggering
DAQ Logging
DAQ Monitoring
DAQ QA
Configuration / Run Control
Slow Controls interface (IOC)
Buffering and Data Transfer
Markus Diefenthaler: ePIC SRO Calibration and Computing (next)
Torre Wenaus: Orchestration of Streaming Data Processing (next)

## Slide 21: Schedule
The DAQ and computing schedule is planned to be accelerated in relation to the full detector construction.
A functional DAQ will be necessary for small scale detector testing as well as commissioning and pre-ops.
Computing resources are staged to make purchases when the hardware is needed, taking advantage of price savings and performance improvements in time.
Hardware and software development early in the construction phase will produce a series of releases with increasing functionality.
Detector Install: FY29Q2 - FY31Q2
Cosmics: FY31Q3
Early CD-4: FY32Q4
DAQ Releases:
PicoDAQ FY26Q1
  Readout test setups
MicroDAQ: FY26Q4
  Readout detector data in test stand using engineering articles
MiniDAQ: FY28Q1
  Readout detector data using full hardware and timing chain
Full DAQ-v1: FY29Q2
  Full functionality DAQ ready for full system integration & testing
Production DAQ: FY31Q3
Ready for cosmics
MiniDAQ
Production
DAQ
PicoDAQ
MicroDAQ
PDR2
Full DAQ-V1
Non-LLP pre-baseline schedule is in progress
PDR1
PDR3

## Slide 22: Summary
Description of the streaming ePIC DAQ
  Scale of the system
  It’s architecture
  Components
  Status and Schedule

## Slide 23
Backup

## Slide 24: EIC Streaming DAQ/Computing Architecture
ePIC DETECTOR
BW O(100Tbps)
BW O(10Tbps)
BW O(100Gbps)
Bunch Crossing ~ 10.2 ns/98.5 MHz
Interaction Rate ~ 2 us/500 kHz
Low occupancy
GTU/Distributed clock (jitter ~5ps)

## Slide 25: ePIC Detector Scale and Technology Details

## Slide 26: Simulations of Data Volumes
The ePIC background group has evaluated background sources.
For data volume evaluation we have used:
18x275 DIS events, scaled to the maximum event rates to be seen in 10x275GeV DIS
10 GeV Electron beam gas events scattered from realistic vacuum under 10000Ahr of pumping
275 GeV Proton Beam gas events scattered from realistic vacuum under 10000Ahr of pumping
Synchrotron radiation (SR) is still under evaluation
Recent results have shown:
  SR is a potentially serious issue with the currently implemented beam line
  Relatively simple remediation schemes can lower the rate significantly
With the currently available CPU resources and still ongoing simulation optimization, we can not yet study SR background rates below ~1 GHz

## Slide 27: Readout Chain: FEB & RDO
Name
Design
Function
Attributes
Adapter
Detector Specific
-HV/Bias Distribution
-HV divider
-Interconnect Routing
-Sensor Specific
-Passive
Sensor
Detector Specific
Multi-Channel Sensor
MAPS, AC-LGAD
MPGD, MCP-PMT
SiPM, LAPPD
Front End Board
(FEB)
Detector Specific
-Amplification
-Shaping
-Digitization
-Zero Suppression
-Bias Control & Monitoring
-ASIC/ADC
-Discrete
-Serial Link
Readout Board
(RDO)
Few Variants
-Communication
-Aggregation
-Formatting
-Data Readout
-Config & Control
-Clock & Timing
-FPGA
-Fiber Link
Data Aggregation Module (DAM)
Common
-Computing Interface
-Aggregation
-Software Trigger
-Config & Control
-Clock & Timing
-Large FPGA
-PCIe
-Ethernet
Computing
Common
-Data Buffering and Sinking
-Calibration Support
-QA/Scalers
-Collider Feedback
-Event ID/Building
-Software Trigger
-Monitoring
-COTS
-Ethernet
Global Timing Unit (GTU)
-Interfaces to Collider, Run Control & DAM
-Config & Control
-Clock & Timing
On Detector
SMT BGA
Readout Board Flavors
Detector | Characteristics
TOF | Highest Timing Requirement (Generic)
dRICH | Small Footprint (VTRX+ optics)
ITS-3 | Detector side uses fiber (VTRX+)
Imaging Calorimeter | Integrated with ASTROPIX Sensor
Low Q Tracker | High Rates, 20 TX fibers expected / RDO
Direct Photon Calorimeter | Pure 200MHz Streaming (bypass DAQ protocol)

## Slide 28: Timing Resolution with Reconstructed Clock
The timing requirement for ePIC DAQ is currently ~5ps, for selected detectors. This is driven by TOF with desired timing of ~25ps
Timing tests have been done at JLAB/ORNL
  Promising results for both lpGBT and XiLINX Ultrascale+ FPGA
  (See William Gu’s Talk tomorrow!)
5ps is still very challenging because of multiple interfaces between delivered clock and digitization!

## Slide 29: DAM Board – FLX-155
FELIX (Front-End Link Exchange) hardware for future ATLAS experiments at HL-LHC is being developed at BNL (Omega Group)
  Long term support is insured. Development timelines are compatible with EIC.
  ePIC is collaborating with Omega to use this design as our DAM board.
  FLX-155 currently being tested by Omega
  See Hao Xu’s talk tomorrow!

## Slide 30: RDO development Activities
The Readout Board (RDO) is the first processing interface of the DAQ with the front-end electronics/digitizers.
There are currently 6 identified “flavors” of RDO - dependent on the detector subsystems (see Pietro’s for dRICH example)
It must support both a common DAQ communication protocol as well as manage configuration and control with the different front-ends
A pre-prototype board has been produced to support early DAQ and detector development (See Tonko’s talk for more details)
Readout Board Flavors
Detector | Characteristics
TOF (ppRDO) | Artix Ultrascale+
dRICH | Small Footprint (VTRX+ optics)
ITS-3 | Aggregates Fiber from lpGBT
Imaging Calorimeter | Integrated with ASTROPIX Sensor
Low Q Tracker | High Rates, 20 TX fibers expected / RDO
Direct Photon Calorimeter | Pure 200MHz Streaming (bypass DAQ protocol)
ppRDO

## Slide 31: Implementation of Firmware Trigger
48
dRICH DAM
dRICH DAM
FWD HCAL RDO
FWD HCAL RDO
FWD HCAL RDO
FWD HCAL DAM
FWD HCAL DAM
Given the requirement for a backup triggered readout for RICH, it is necessary to carefully define the physics trigger rate, trigger conditions, and trigger latency in order to facilitate design of the RICH front-end.
FWD HCAL RDO
FWD HCAL DAM
RDO_DATA
Activitiy | Notes
Data Arrives at DAM | <=10us from Bunch Crossing
Data Evaluation (DAM) | 100ns
TRG_STATUS to GTU | Data transmitted to GTU after fixed delay from source crossing O(10us)
Trigger Evaluation on GTU | Fixed Latency O(100ns)
Keep/Drop Bit to DAM | Fixed Latency O(40ns)
Drop data / forward data | Drop Forward after fixed time O(11us)
DAM Buffer | 16GB
Buffer Time available | 2.6 seconds
TRG_STATUS
64 bits
Bunch Data
Fixed delay O(10us)
dRICH DAM
DAM_CTRL
GTU
(Keep/Drop
Bunch bit)
48
3
30
Ex: Hcal generates trigger
dRICH is triggered
Hardware Trigger Option
Fixed delay O(10us)
FWD HCAL RDO
FWD HCAL RDO
FWD HCAL RDO
dRICH
RDO
ePIC depends upon a flexible scheme in which sufficient bandwidth is available for data to the dRICH DAM in the worst case. (> 4x safety). The selecting detectors (ex FWD HCAL) generate information characterizing beam in O(10us). The decision is made by the GTU and returned to DAM boards with fixed latency. The maximum latency is orders of magnitudes less than available buffering in DAM board memory. A hardware trigger is supported by the GTU but uses the same dRICH buffering scheme and delays as the firmware trigger option.
48
48
48
48

## Slide 32: Slow Controls Status
Slow Controls Components and architecture are identified
EPICs Base
  Allows use of existing tools
  Synergy with EIC Controls

## Slide 33: Slow Controls Status
Detector DSCs have been surveyed for detector requirements
Resource Requirements have been Documented
  ~ 500k variables to be tracked
  ~ 55 TB/year
  ~ 73 Mbps network traffic
Preliminary hardware recommendation policies / lists drafted
PLC schemes have been investigated
Hiring slow control’s expert to continue these efforts

## Slide 34: Boundary between Online and Offline
The streaming architecture allows for some blurring of the offline and online processing with respect to calibrations, QA monitoring, and potential seed analysis to improve reconstruction turn around.
Require an interface to allow sharing of code between offline / online processing
Local buffering (Echelon 0) provides elasticity in the transfer of data to computing facilities
Offline procedures (Echelon 1) will allow several weeks for calibration and reconstruction. (The computing will be discussed by Markus Diefenthaler in the next talk)
Is a dependency for the project handled in conjunction with host labs.
The Resource Review Board (RRB) looks at the international detector and computing resources.
The ePIC computing groups are actively implementing scientific software as well as working with the DAQ to define the interface with the streaming DAQ system.
ePIC Scientific Computing