## Slide 1: ePIC Timing and Synchronization
The requirements
The designs
Test results
Summary

## Slide 2
Streaming Data
Time Frame M+5
Time Frame 1 …
Time Frame M+4
Time Frame M+3
Time Frame M+2
Time Frame M+1
Time Frame M
START
RE-START
RE-START
START
RE-START
RE-START
STOP
RE-START: STOP and START at the same Beam Crossing
Whole detector dead time
RE-START
1.1 Synchronized control
1.2 Jitter of the FEB/ASIC received clock: less than 5ps;
  1.3 For TOF detectors, the phase of the clock relative to the beam crossing center point is stable (less than 5ps);
  1.4 For dRICH detector, the phase of the clock relative to the beam crossing center point is stable (< ~100ps) for shutter implementation (zero suppression)
1. The requirements

## Slide 3
 | ESR | HSR
RMS bunch length sz [mm/ps] | 7-9/23-30 | 75-60/250-200
RMS momentum spread [10-4] | 5.8-10.9 | 10.3-6.8
RMS horiz beam size sx [um] | 100-250 | 
sz/sx ratio [-] | 28-90 | 240-750
2. The designs
2.1 The EIC beam crossing
 | Electron Storage Ring (ESR) | Hadron Storage Ring (HSR) (Nb=290) | HSR (Nb=1160)
Circumference C [m] | 3833.940 | match Trev | match Trev
Revolution period Trev=C/c [µs] | 12.7886 |  | 
RF harmonic number h [-] | match HSR | 2520 | 7560
RF bucket spacing Tb=Trev/h [ns] NOT bunch spacing!!! | match HSR | 5.075 | 1.692
Number of bunches Nb | match HSR | 290 | 1160
Bunch spacing Tbun [ns] | match HSR | 40.599 | 10.150
Gap length [ns] | match HSR | 1015 | 1015
        Beam crossing: 98.525 MHz or 10.150ns
        Orbit period: 12.7886 µs or 1260 Beam Crossing
Electron Beam Energy: 5 – 18 GeV
Proton Beam Energy: 41, 100 – 275 GeV
Luminosity: 1034 cm-2s-1

## Slide 4
2. The designs
2.2 The ePIC clocks:
1 2 3 4 5 6 7 8
3 4 5 6 7 8 9 0 1 2 3 4
5 5 5 5 5 5 5 6 6 6 6 6
1 1 1 1 1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 1 1
2 2 2 2
1 1 1 1
7 8 9 0
5 5 5 6
2 2 2 2
1 1 1 1
7 8 9 0
5 5 5 6
1 2 3 4
1160 (all or 1/4 with beam)
100 (no-beam /gap)
Streaming Data
Beam crossing ( * electron ion collision )
Time Slice M+5
Time Slice M-1
Time Slice M+4
Time Slice M+3
Time Slice M+2
Time Slice M+1
Time Slice M
SRO data header:
Packet number,
Data source ID,
Starting orbit count
Starting BX count
SRO data trailer:
Ending orbit count
Ending BX count
Sync/Error/buffer status
Total word count
* * * * * * * *
* * * * * * * *
* * * * * * * *
BX_Clock, 98.5 MHz
GTUDAM, 9.85 MHz
lpGBT_Clock, 39.4 MHz
Any other clocks
Nominal Time Slice: 65530 (~216) BX, ~0.6 ms, settable in GTU (Synchronization check)
All the clocks are phase aligned (fixed)
Single clock source, distributed to the whole system

## Slide 5
2. The designs
2.3 The ePIC Timing/Control distribution
GTU
Clock
Control
Status
DAM
DAM
RDO
RDO
RDO
RDO
Data Acquisition
DAM
(O)100
RDO
(O)1000
GTU (O)1
EIC
Common
Platform
Online computer
FEB
FEB
FEB
GTU: Global Timing Unit
  control encoding, status decoding.
  The interface for machine clock source,
  Data acquisition control and monitor etc.
DAM: Data Aggregation Module:
  The clock/control fanout, and status/busy accumulation.
  local control over the RDO boards connected, though the main function of the DAM is for Data Acquisition.
RDO: optical interface of detector ReaDOut
  control decoding, status encoding.
  The clock/control interface to the front end electronics.
  Data collection from Frontend boards, and data transmission to the DAM
FEB:
  Detector dependent Front End / ASIC carrier boards.
System Clock: 9.85 MHz
GTU distributes 9.85 MHz clock, and DAM reconstructs the 98.5 MHz, (and) 39.4 MHz clock

## Slide 6
2.3: Synchronization
DAM/RDO to implement time measurement, so that RDOs can compensate the fiber length delay to within one clock period; but, it is easier to use same-length fibers.
GTU/DAM to keep a 11-bit beam crossing counter (terminates at 1260), synchronization check with streaming readout time slice (start/stop) commands; online/offline check with beam orbit structure (collision or no collision);
RDO to keep a 11-bit beam crossing counter (terminates at 1260), or a 9-bit beam crossing counter (terminate at 504 for lpGBT protocol), and a 6-bit (min. ~818 ms), 21-bit (preferred, ~26seconds), or 32-bit (over 15 hours) beam orbit counter;
GTU and DAM should keep a larger beam orbit counter;
RDO to keep a 16-bit (min), or 32-bit (preferred) time slice counter. This counter should not overflow for the maximum DAQ computer buffer.
RDO should assert buffer high_marker no later than one orbit period before it is full and starts to lose data.
RDO starts a new data packet upon receiving time-slice_start, and end the current packet upon receiving time-slice_end or upon receiving a new time-slice_start.
RDO to hold data if the DAM is busy (potential buffer full), and the DAM to hold data if the host computer/Network switch is busy.
The GTU can record dead time by sending TimeSlice_end, and holding TimeSlice_start in responding to RDO busy.
RDO should generate one packet on every readout time slice. The RDO can discard detector data to avoid buffer overflow, or out of synchronization, but this occurrence must be recorded in the data package/trailer.
GTU
RDO
DAM
DAQ
Data Buffer ‘FULL’ backpressure
Status accumulation:
Data Buffer conditions, Out of Sync, Reset_request, etc.
Run_control:
SRO_time_start/stop, RESETs, etc.
Data flow
2. The designs

## Slide 7
2.4 The hardware design
  2.4.1 GTU
GTU required:
EIC common platform interface;
Run Control;
~150 DAM interface
Risk mitigation:
Beam vs clock phase monitoring;
Dedicated clock fanout to TOF
2. The designs
Clock @ 9.85 MHz
GTU_CONTROL
DAM/RDO Status
Optional/extra
Between GTU and DAM
Same-length Multimode fibers: 4 Tx/4 Rx (inexpensive, standard, commercially available)
GTU
DAM

## Slide 8
2. The designs
2.4 The hardware design
  2.4.2 DAM
DAM clock reconstruct,
98.5 MHz and 39.4 MHz,
Phase aligned with the 9.85 MHz clock,
Additive Jitter ~1ps;
Phase: fixed
The DAM will have one MTP fiber port connects to GTU, 48 ports (duplex) connect to 48 RDOs (one port each), and PCIexpress to host PC.
Run control
SYNC the run control from GTU and repack in lpGBT format at 39.4 MHz, or non-lpGBT format at 98.5 MHz
ASIC setup, and RDO/FEB monitoring

## Slide 9
2. The designs
2.4 The hardware design
  2.4.3 RDO
The RDO will have one fiber port (two fibers) connect to the DAM, and several ports connect to FEB/ASIC
RDO MGT RECovered Clock:
Additive Jitter <3ps;
Phase: stable,
fixed with PseudoClock (serialized clock/control from DAM)
The RDO de-codes the control synchronously, and the RDO/FEB/ASIC configuration;
Assemble time-frame data, also RDO/FEB/ASIC status
  VTRX+ on the RDO for radiation
    This (3.94 Gb/s stream) can also be received by 7.88 Gb/s receivers
For lpGBT (on the RDO or FEB), the RDO will pass on the downlink (in lpGBT format) from DAM to lpGBT
(non-lpGBT data format)
For non-lpGBT,

## Slide 10
2.5 The risk mitigation
2. The designs
2.5.1 Clock phase (RDO/lpGBT recovered clock versus electron beam) monitoring:
e- Beam pickup
RDO(area) Clock
Phase#1
Phase#2
Phase#1160
Phase#1
PhaseOrbit (average)
GTU: Phase Correction
RF-SoC (?)
Optic Transceiver plugin module
Clock fanout
Optic transmitter
Power
regulators
4 U high
Optic transmitter
Optic transmitter
Optic transmitter
Optic transmitter
Optic transmitter
GTU_Optic Transmitter plugin modules
Clock only, to TOF_RDO (optional)
Possible choice of Optic Transmitters:
Samtec FireFly, 12 ch TX,
MTP_12 at GTU
LC at RDO
2.5.2 Dedicated clock from GTU to TOF_RDO

## Slide 11
2.6 The data format
2. The designs
GTU
DAM
Clock @ 9.85 MHz
GTU_CONTROL, “(min) 8-bits (+ 1 k_bit) @ 98.5 MHz” & “480-bits @9.85 MHz”
DAM/RDO Status, “(min) 8-bits (+ 1 k_bit) @ 98.5 MHz” & “480-bits @9.85 MHz”
To fully use the DAM connection
FPGA MGT Transceivers
PCB Transmitters
PCB Receiver
FPGA_MGT Transceiver
Downlink
Uplink
FPGA IOB Transceivers
FPGA_MGT Transceiver
2.6.1 Between GTU and DAM
The 9.85 MHz clock is also used to align the DAM boards by using the same (length, type) fibers (Synchronization)
DAM
RDO
64-bit at 39.4 MHz for lpGBT, or 64-bit @ 98.5 MHz (for example) for non-lpGBT
256-bit at 39.4 MHz for lpGBT, or 64-bit @ 98.5 MHz (for example) for non-lpGBT
FPGA MGT Transceivers
lpGBT or FPGA_MGT Transceiver
Downlink
Uplink
2.6.2 Between DAM and RDO/FEB (one-pair of fibers)
DAM aligns and repacks the packet (from GTU), and sends the relevant information to the RDO at 39.4 MHz, or 98.5 MHz. The RDO receives the ‘downlink’ after a fixed (same) delay (relative to the GTU generation).

## Slide 12
3. Test results
3.1 Clock distribution
Si5344H
Clk: 98.5 MHz
Clk: 39.4 MHz
Si5394A
(x10) Clk: 98.5 MHz
(x4) Clk: 39.4 MHz
Jlab TI
(/10) 9.85 MHz
SYNC
Optic Tx, Rx
Clk: 9.85 MHz
EIC_Clock
GTU
DAM
Copper
cable
Copper
cable
MM
fiber
Copper
cable
Test SETUP

## Slide 13
3. Test results
3.1 Clock distribution
Test SETTING
/10 SYNC: on the Jlab’s TI (GTU simulator) every 1,073,741,830 Clock_98.5 MHz cycles  ~ 11 seconds,
The Si5394A (DAM simulator) needs ~ 2 seconds to synchronize (0x001E[2], R divider reset) the X10, X4 clocks
Results:
The “/10” or 9.85 MHz distribution works (DAM can recover the 98.5 MHz and 39.4 MHz clock synchronously)
The phase stability (jitter): std: < 1.5 ps
The tails (10s ps) are caused by the cable noises (more in BACKUP slides)

## Slide 14
3. Test results
3.2 non-lpGBT RDO recovered clock
3.2 DAM TX serialized clock/control
Pseudo_Clock (TxSerializer and RDO_fanout): Jitter: 3ps; Phase: stable
Si5344  FLX182  ppRDO
(Reference_Clock  Txserilizer  PseudoClock)
FLX182
ppRDO
(ADCLK944)
Si5344H
(ref Clock)
RxRECclk (from FPGA’s MGT) jitter < 3 ps. RxRECclk phase can be fixed at ~(0)ps precision (by measuring the phase difference between the RxRECclk and the pseudoClock, and resetting the RxRECclk CDR.)

## Slide 15
3. Test results
3.3 test results from others
3.3.1 results from Jlab’s 12 GeV upgrade: dedicated clock distribution
Trigger SuperVisor
Signal Distributor
Trigger Distributor
Trigger Interface
PCB and backplane
Copper traces
Optic Transceivers
Multi-Mode fibers
PCB and backplane
Copper traces
Clock Jitter (from Trigger Interface) σ < 3ps
The synchronization (run control, busy feedback, etc.) works
3.3.2 results from CERN (related) on the lpGBT
schambachjj@ornl.gov
lpGBT recovered clock (through VTRX+ optic transceiver):
TIE: σ = 1.0 ps
Phase difference (jitter) : σ = 1.78 ps

## Slide 16
4. Summary
4.1.1 GTU: prototype is being considered
  we plan on finalizing the development in 2025.
4.1 Status
FPGA
Power
supplies
Clock
Receiver, control, distribution
Run Control
Memory
‘services’
GTU base board
Optic Transceiver plugin module
Clock fanout
Possible buffers
Quad optic TRX
Power
regulators
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
16.8 inch wide (max)
4 U/7” high (max)
All the electrical signals are differential signals (PCB and connector). Three FPGAs with fast interconnect.
FPGA (SOM)
FPGA
Clock fanout
Possible choice of Optic Transceivers: Finisar FTL410Q, or SAMTEC firefly B04-14
Possible choice of plugin connector: PCIe x16
A 4U (high, 19 inch wide) rack mounted box consisting of one GTU base board (16.8 inch wide max), and many Optic transceiver plugin modules (4U high max, to DAM)

## Slide 17
4. Summary
FLX155: Designed for ATLAS FELIX upgrade,
  it is consistent with EIC/ePIC schedule.
4.1.2 DAM: FLX155 (ePIC DAM) engineering article is expected early next year (after the tests in BNL going on right now)
4.1 Status
RDO
GTU
PCIe to host computer

## Slide 18
4. Summary
4.1.3 RDO: preprotype RDO
4.1 Status
Clock reconstruction is tested. Moving on to VTRx+ and lpGBT compatible design and testing

## Slide 19
4.2 Conclusion
  4.2.1 The design can satisfy all these four requirements, the tests and other experiments’ implementations proved that the requirements can be met.
  4.2.2 More tests are needed to see if the risk mitigations (designed for requirement 1.3) are needed. The tests are expected to finish in 2025 with the new hardware.
4. Summary

## Slide 20
Thank you

## Slide 21
2. The designs
2.2 The ePIC clocks
BX_Clock, 98.5 MHz
GTUDAM, 9.85 MHz
lpGBT_Clock, 39.4 MHz
Any other clocks
One orbit cycle = 1260 Beam Crossing
1260 = 2x2 x 3x3 x 5 x 7 ; 1160 + 100 = 2x2 x 5 x (58 + 5)
BX: 98.525 MHz,
lpGBT: 98.525 x 2 / 5 = 39.41 (MHz)
SALSA: 98.525 / 2 = 49.26 (MHz)
dRICH: 98.525 *4 = 394.1 (MHz)
……
Single clock source, distributed to the whole system

## Slide 22
EIC, RF
GTU
RunControl computer
System clock
(98.5MHz /10)
Two-level fanouts
Beam orbit
Ethernet
DAM
Clock reconstruct
(Si5395A, ZDM)
DAQ
PCB and fanouts:
Additive Jitter <1ps
Phase: fixed
Dedicated fiber:
Additive Jitter <1ps
Phase: fixed
PCB and fanouts:
Additive Jitter <1ps
Phase: fixed
RDO
Clock recovery
(optional iitter cleaner)
Clock fanouts
Control
Config
DAQ
Optic fiber cable:
Additive Jitter <1ps
Phase: fixed
GTY Rec Clock:
  Additive Jitter <3 ps
lpGBT rec Clock:
  Additive jitter < 3 ps
RunControl: Run_Start/Stop, Run_type, config, Reset, Synchronization, SRO time_start/stop, Throttling…
Status: Buffer busy, out of sync …
GTY
Control config, status
Host PC
TX/RX
RefClk
Beam Orbit synchronized RunControl
GTY
TX/RX
RefClk
RecClk
FEE/ASIC
2.3 RunControl and DAQ
RunControl: forward or ‘hijack’ the GTU control;
DAM, RDO, FEE/ASIC configuration, readout backpressure
Status: Buffer, sync, etc.
Config synchronized with beam crossing /10, FEE/ASIC readout and control
Status: Buffer, sync, etc.
2. The designs
2.3 The ePIC Timing Control distribution
9.85 MHz
7.88 Gbps
9.85 MHz, 98.5 MHz, 39.4 MHz
lpGBT compatible: Tx: 2.52 Gbps, Rx: 10.09 Gbps
Non-lpGBT: Tx: 3.94/7.88 Gbps, Rx: 7.88 Gbps
lpGBT

## Slide 23
Synced CONTROL Distribution
Fixed latency from GTU to DAM, and RDO
The fibers from GTU to DAM will be the same length/delay routed in the DAQ computer racks.
The fiber delays from DAM to RDO will be measured individually, and saved on the RDO. The RDO will delay the received GTU control commands (compensating for the fiber latency), so that all the RDOs will send the GTU commands at the SAME time. It is easier using the same length fibers.
Beam orbit information is embedded in GTU control command
The GTU, DAM and RDO will all keep (at least) two counters, Beam Crossing counter (11-bit from 1 to 1260, 9-bit from 1 to 504 with lpGBT), and Beam Orbit counter (at least 5-bit, for a total time period of about 400 µs)
The GTU will send SRO (Streaming ReadOut) time window start command and some other SYNC commands on the first, eleventh, …(every tenth) beam crossing of the orbit. The size of RDO time window can be set on the GTU.
DAQ data flow control
There are data buffers on DAMs and RDOs. The buffer status is monitored by GTU, DAM and RDO.
2.3: Synchronization

## Slide 24
Beam synced Clock, orbit
EIC common platform
Online computer
GTU
2.4.1. GTU design: Inputs and Outputs
GBE
Run Control
CLOCK distribution
MTP
DAM
Clock, Control, status
MTP
DAM
Clock, Control, status
MTP
DAM
Clock, Control, status
~150
LC
TOF_RDO
Clock
LC
TOF_RDO
Clock
LC
TOF_RDO
Clock
~600
Risk mitigation for extremely stringent requirement by TOF
Beam monitor
RDO clock phase
MTP fibers, ~10 meters
LC fibers, ~100 meters
Clock @ 9.85 MHz
GTU_CONTROL
DAM/RDO Status
Optional/extra
MTP: 4 Tx/4 Rx

## Slide 25
2.4.1 GTU detailed design: clock ‘area’
EIC common platform interface
OSC
AD9510
Si5395
FPGA (SOM)
IN1
IN0
OUT0
IN0
Orbit
BXclock
98.5 MHz
9.85 MHz
SPI
Clock_Sync
OUT4
OUT5
Fanout
To FPGAs
I2C
OUT0
OUT1
OUT2
OUT3
OUT4
OUT9
IN3
ZDM
To plugin optic transceivers
To plugin optic transmitters
Beam Phase monitoring
Clock phase adjustment
AD5330x
AD5330x
2. The designs

## Slide 26
Used on the Jlab’s Trigger Interface (TI) modules to generate SYNCHRONIZED /2, /4, /6 and /8 lower frequency clocks.
Analog Devices AD9510
Additive output jitter (rms)
LVPECL: 225 fs
LVDS/CMOS: 275 fs
2.4.1 GTU detailed design: AD9510 synchronous clock divider (clk1 input)

## Slide 27
2.4.2 DAM (FLX155) clock interface
Dedicated Clock input,
up to three MGT lanes (Tx/Rx)
MTP multimode 850µm optical
* These two diagrams are from FLX155 presentations

## Slide 28
3.2 ppRDO clock design
Optic transceiver
RX
TX
1:4 ADCLK944
Out1
Out0
FPGA
GTY
RX
TX
Si5345
Out0
Out2
Out1
IN2
RxRECclk
Phase difference detection
Fiber
optional emergency circuit I2C
ppRDO
(N/M)* 98.5 MHz
197 or
394 MHz
control
ClkRef
pseudoClock
98.5 MHz
Out9
IN3
Zero Delay FB
DAM
W16/Y16
W17/W18
K5/K6
M5/M6
H1/H2
G3/G4
14/15
23/24
27/28
30/31
ePIC_Clock
( Pll_cc )
(reset)
Si53302
RED/RED: FPGA package pins, or Si5345 package pins
Data/control
To/from MGT
TX
RX
ClkRef0
ClkRef1
RxPLL
AA4/AA3
Y6/Y5
P6/P5
V6/V5
Optic transceiver
RX
TX
Si5338
17/18
9/10
SMA cables to oscilloscope
SMA
SMA
SMA
SMA
SMA
SMA
SMA

## Slide 29
2.6.1 GTU  DAM communication (Downlink, example)
packet | One packet at 9.85 MHz, or 10 ( one word at 98.5 MHz) |  |  |  |  |  |  |  |  | 
word | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Bit(9:0) abcdeifghj- | K28.1_3C 0011111001 x0111110xx | K28.2_5C 0011110101 | K28.3_7C 0011110011 | K28.4_9C 0011110010 | K28.5_BC 0011111010 x0111110xx | K28.6_DC 0011110110 | K28.7_FC 0011111000 x0111110xx | K23.7_F7 1110101000 | K27.7_FB 1101101000 | K28.0_1C 0011110100
Bit(19:10) | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC
Bit(29:20) | BX(7:0) | BX(15:8) | Obx(7:0) | Obx(15:8) | Orbit(47:0), BX(63:16), etc. |  |  |  |  | 
Bit(39:30) | DAM | DAM | DAM | DAM | DAM | DAM | DAM | DAM | DAM | DAM
Bit(79:40) | USER | USER | USER | USER | USER | USER | USER | USER | USER | USER
packet | One packet at 9.85 MHz, or ten (single word at 98.5 MHz) |  |  |  |  |  |  |  |  | 
word | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Bit(9:0) abcdeifghj- | K28.1/3C 0011111001 x0111110xx | K28.2/5C 0011110101 | K28.3/7C 0011110011 | K28.4/9C 0011110010 | K28.5/BC 0011111010 x0111110xx | K28.6/DC 0011110110 | K28.7/FC 0011111000 x0111110xx | K23.7/F7 1110101000 | K27.7/FB 1101101000 | K28.0/1C 0011110100
Bit(39:10) | Status | Status | Status | Status | Status | Status | Status | Status | Status | Status
Bit(79:40) | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC
2.6.1 DAM  GTU communication (uplink, for example)

## Slide 30
DAM to GTU:
Bit(9:0): 8b/10b encoded, used as word count, and word alignment in the receiver
Bit(39:10): DAM status, 24-bit at 98.5 MHz
Bit(79:40): RDO/ASIC status, 32-bit at 98.5 MHz
The Streaming Readout time window will be 65530 (or 6553 if counting on 9.85 MHz), instead of 65536 (216) BX.
Available on DAM: (MTP, 8 fibers can be used)
  4 MGT (MultiGigabit Transceivers) (One Rx for Clock)
Design on GTU: (MTP, 5 fibers used)
  Clock,
  1 Tx and 1 Rx using FPGA’s MGT;
  1 Tx and 1 Rx using FPGA’s regular IO (HPIO/XPIO)
GTU to DAM:
Bit(9:0): 8b/10b encoded, used as word count, and word alignment in the receiver
Bit(19:10): GTU run-control, 8-bit at 98.5 MHz
Bit(29:20): Clock sync counters,
BX(63:0): Beam Crossing counter;
Obx(15:0): beam crossing counter within the orbit;
Orbit(47:0): Orbit counter
Bit(39:30): DAM specific, 8-bit at 98.5 MHz;
Bit(79:40): User-specific, 32-bit at 98.5 MHz;
2.6.1 GTU  DAM communication

## Slide 31
2.6.2 DAM  RDO communication (alignment, example)
Packet | (GTU  DAM) One packet at 9.85 MHz, or 10 ( one word at 98.5 MHz) |  |  |  |  |  |  |  |  | 
word | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Bit(9:0) abcdeifghj- | K28.1_3C 0011111001 x0111110xx | K28.2_5C 0011110101 | K28.3_7C 0011110011 | K28.4_9C 0011110010 | K28.5_BC 0011111010 x0111110xx | K28.6_DC 0011110110 | K28.7_FC 0011111000 x0111110xx | K23.7_F7 1110101000 | K27.7_FB 1101101000 | K28.0_1C 0011110100
Bit(19:10) | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC
Bit(29:20) | BX(7:0) | BX(15:8) | Obx(7:0) | Obx(15:8) | Orbit(47:0), BX(63:16), etc. |  |  |  |  | 
Bit(39:30) | DAM | DAM | DAM | DAM | DAM | DAM | DAM | DAM | DAM | DAM
Bit(79:40) | USER | USER | USER | USER | USER | USER | USER | USER | USER | USER
Packet | lpGBT compatible (DAM  RDO) One packet at 9.85 MHz, or 4 ( one word at 39.4 MHz) |  |  | 
word | 1 | 2 | 3 | 4
Bit(63:0) | Downlink#1 | Downlink#2 | Downlink#3 | Downlink#4
Bit(255:0) | Uplink#1 | Uplink#2 | Uplink#3 | Uplink#4
Packet | Non-lpGBT (8b/10b encoded) (DAM  RDO) One packet at 9.85 MHz, or 10 ( one word at 98.5 MHz) |  |  |  |  |  |  |  |  | 
word | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Bit(79:0) | Downlink#1 | Downlink#2 | Downlink#3 | Downlink#4 | Downlink#5 | Downlink#6 | Downlink#7 | Downlink#8 | Downlink#9 | Downlink#10
Bit(79:0) | uplink#1 | uplink#2 | uplink#3 | uplink#4 | uplink#5 | uplink#6 | uplink#7 | uplink#8 | uplink#9 | uplink#10
“DAM  RDO” packets are synchronized (same timing on all the DAMs, and same timing on all the RDOs)
2.5.2 between DAM and non-lpGBT RODs
00: Pseudo-clock (pattern)

## Slide 32
Jitter and Phase measurement using an oscilloscope
EIC/Common Platform/GTU clock: Si5344H as reference;
Oscilloscope Probes
Si5344H
KCU105
Si5394A
FLX182
Clk_98.6
Fiber_7.89
RxRecClk_197.3
ClkSys_98.6
ClkPD_98.6
Phase
Detect
CH#1
CH#2
CH#3
CH#3
MGT
1:2
Beam Crossing/Reference Clock
DAM MGT_TX output: FLX182/KCU105 pseudoClock
Encoded Clock
RDO/FEB Recovered Clock: XEM8320/KCU105 plus Si5394A
Recovered Clock
Phase/Jitter measuring method using a scope (Tektronix MSO64):
Phase difference == WIDTH of the difference of the two signals
Jitter == uncertainty of the WIDTH of the difference of the two signals assuming the reference clock is perfect.

## Slide 33
3.1 Clock distribution
Si5344H
O3: 197 MHz
O1: 9.85 MHz
O2: 98.5 MHz
O0: 39.4 MHz
QSFP
TX0
QSFP
RX0
Si5394A
IN0: 9.85 MHz
O0: 39.4 MHz
O1: 9.85 MHz
O2: 98.5 MHz
O3  IN3 ZDM
MSO64
CH4
CH3
CH2
CH1
MATH1 = CH1 – CH4, 39.4 MHz clock
MATH2 = CH2 – CH3, 98.5 MHz clock
10 M loopback  20 meters
“GTU”
“DAM”
3.1.1 9.85 MHz clock distribution via fiber

## Slide 34
3.1 Clock distribution
Clock: 39.4 MHz
Period: 25.3805ns
MATH1 = CH1 – CH4
Positive width: 2.1725 ns
FWHM: 4 ps
40 µs data: σ: 1.51 ps
Negative width: 2.1788ns
FWHM: 4 ps
40 µs data: σ: 1.56 ps
Clock: 98.5 MHz
Period: 10.1522 ns
MATH2 = CH2 – CH3
Positive width: 2.877ns
FWHM: 3.5ps
40 µs data: σ: 1.64 ps
Positive width: 2.7ns
FWHM: 3 ps
40 µs data: σ: 1.34 ps
* ~ one hour accumulation
3.1.1 9.85 MHz clock distribution via fiber

## Slide 35
3.1.2 long term stability test (>15 hours)
Setup in CC_F110, room (AC) temp 72oF.
No phase drift (differences of Si5394A outputs and Si5344H outputs)  Fiber and QSFP are stable.
3.1 Clock distribution

## Slide 36
Overnight accumulation (9/25-9/26), very stable
The Phase measurement (meas 9/10), and the skew measurement (meas19/20) gave the similar results as MATH widths measurement (meas 5/6/7/8)
3.1.2 long term stability test (>15 hours)
3.1 Clock distribution
σ < 2 ps

## Slide 37
MC100 EP57
AD9510 (/8)
SY58607 1:2
9.85 MHz
TI
Si5394A
Tektronix MSO64
9.85 MHz
9.85 MHz
98.5 MHz
39.4 MHz
Si5344H
MC100 EP90
9.85 MHz
98.5 MHz
39.4 MHz
78.8 MHz
Si5344H @78.8MHz
Phase stability (phase shift and jitter): FWHM < 4 ps
3.1 Clock distribution
3.1.3 AD9510 clock divider

## Slide 38
Meas19: FWHM_Ch1-Ch4 ~ 3.4 ps
Meas20: FWHM_Ch2-Ch3 ~ 3.4 ps
3.1 Clock distribution
3.1.3 AD9510 clock divider

## Slide 39
3.1 Clock distribution
Bypassing the TI and the optic transceivers, Si5344H generates 9.85 MHz, and the Si5394A reconstruct the 98.5 MHz, and 39.4 MHz clock, Phase stability (jitter): ~ 1 ps, P_P: ~ 9 ps.
3.1.4 9.85 MHz clock distribution via SMA cables (best signal integrity)

## Slide 40
RDO clock recovery (non-lpGBT)
RDO clock recovery procedure: During this procedure, the DAM sends pseudo-clock of 98.5MHz
  Step 1: Measure the clock phase difference between the PseudoClock and the clock output from the AD9510.
    Step 2: If the phase difference is not the preset value (nominal serial data UI), do the MGT RxRECclk reset, and go back to step 1. If the phase difference is the preset value, the RDO clock recovery is finished.
Before the run start, the GTU will send a clock_sync command. When the RDO receives this command, the RDO sends the Clock_Sync to the AD9510, so that all the slower clocks are synchronized (by re-align the rising edges of AD9510 outputs).
3.2 Clock distribution

## Slide 41
June 24, 2024: SMA output with ppRDO, at 98.5 MHz, checking with different FLX182 TX patterns
FLX182 TX output
“10” “01”
“11” “00”
The Si5345 output shifted 20ps even after the pattern went back to “00”, pseudoclock.
3.2 non-lpGBT RDO recovered clock

## Slide 42
3.2 non-lpGBT RDO recovered clock
~one hour’s accumulation
Positive Width: 1.557ns ± 2.5ps;
Negative Width: 1.546ns ± 2.7ps;
7.88 Gb/ps
Serial Data,
PseudoClock