## Slide 1
Oscar Cabellos (UPM)
Universidad Politécnica de Madrid (UPM), Madrid, Spain
E-mail: oscar.cabellos@upm.es
ENDF/B-VIII.1
Covariance Testing

## Slide 2
Processing ENDF/B-VIII.1 into JANIS format:
  HENDF + INTER + BOXER (33g and 238g)
1. Processing in JANIS format
NJOY2016.76
BOXER file
VERSION 7.01
MF31/32/33/34 and MF35
Figure 1. Flowchart of processing JANIS database from ENDF tapes
moder /tape20 from MERGER
20 -31
reconr /Reconstruct XS data
-31 -32
' PENDF tape ' /
9437 2 /
.005 /
' MAT=pu239 ENDF Library:JENDL-5.0upd' /
' Processed NJOY2016-UPM,2023 '
0/
broadr /Doppler broaden XS
-31 -32 -33
9437 1 /
.005 /
293.60
0/
thermr / Add thermal scattering data
0 -33 -34
0 9437 12 1 1 0 0 1 221 0
293.60
0.005 10.0
unresr
-31 -34 -35
9437 1 1 0 /
293.60
1.0e+10 /
0/
heatr / Add heating kerma and damage energy
-31 -35 -36 40/
9437 7 0 0 0 2/
302 303 304 318 401 403 407 /
heatr / Add heating kerma and damage energy
-31 -36 -37 41/
9437 6 0 0 0 2 0 1/
442 443 444 445 446 447 /
gaspr /Gas production
-31 -37 -38
moder
-38 26
stop
Figure 2. Example of input deck to process in PENDF format
tape20 = ENDF file
=====================

## Slide 3
Processing ND libraries into JANIS format:
JEFF-4T?, JENDL-5.0-upd, …
ENDF/B-VIII.1
  Logs reported when importing JANIS database
  Covariances for some Tungsten (W) files only in 33 energy groups – 238 failed in covr!
  # - HENDF: Hybrid format ENDF+PENDF including KERMA and DAMAGE cross-sections
  # - INTER
  # - BOXER: covariances MF31, MF32/MF33, MF34 and MF35
  Download at the following links – “UN-OFFICIAL JANIS Databases”:
    ENDF/B-VIII.1 with BOXER in 33g: https://drive.upm.es/s/mzGbRoZt5CBw20G
    ENDF/B-VIII.1 with BOXER in 238g: https://drive.upm.es/s/zNq9ww0JJf0DJUy
    password: janis
  See the “Readme.txt” file, it explains how to download and import the database in JANIS
Import WIZARD tool: Use the “Database > Import Wizard”
Steps:
- Use “JANIS toolbar -> Database –> Load” function
- Set “.h2.db file” to select the downloaded “h2.db” file
- Set “Root Folder” to the folder where the “h2.fb” is located
(Leave the other default options are they are)
1. Processing in JANIS format

## Slide 4
Verification ND Uncertainties in ICSBEP Benchmarks using NDAST Tool
  HENDF - ENDF/B-VIII.1: Uncertainty Quantification in ICSBEP using NDaST
  U233 – U235 - U238 – Pu239
  The impact of uncertainties due to:
    XSs (s)
    Nubar (n)
    P1-elastic
    PFNS (c)
http://www.oecd-nea.org/ndast/
2. Verification ND Uncertainties
with Ein =100keV

## Slide 5
Verification ND uncertainties: PU cases
Fissile material |  | PU | PU |  | 
Spectrum |  | FAST | INTER | MIXED | THERM
Number of Benchmarks |  | 152 | 4 | 9 | 624/637
Experimental Uncertainty (pcm) |  | 334 | 710 | 587 | 426
Total (pcm) | ENDF/B-VIII.1 | 653 | 434 | 387 | 450
 | ENDF/B-VIII.0 | 921 | 1403 | 1055 | 1099
 | ENDF/B-VII.1 | 436 | 565 | 459 | 625
Cross-sections (with correlations) | ENDF/B-VIII.1 | 520 | 248 | 154 | 108
Cross-sections | ENDF/B-VIII.0 | 857 | 1368 | 983 | 998
 | ENDF/B-VII.1 | 409 | 546 | 356 | 500
P1-elastic | ENDF/B-VIII.1 | 66 | - | - | -
P1-elastic | ENDF/B-VIII.0 | 66 | - | - | -
 | ENDF/B-VII.1 | - | - | - | -
nubar | ENDF/B-VIII.1 | 385 | 350 | 349 | 430
nubar | ENDF/B-VIII.0 | 300 | 271 | 275 | 308
 | ENDF/B-VII.1 | 76 | 88 | 114 | 168
PFNS NOTE: Ein=100keV | ENDF/B-VIII.1 | 27 | 25 | 53 | 59
PFNS | ENDF/B-VIII.0 | 117 | 106 | 265 | 297
 | ENDF/B-VII.1 | 118 | 106 | 265 | 297
Uncertainty Quantification with ENDF/B-VIII.1: ICSBEP/Pu cases
Uncertainty Quantification in ICSBEP using NDaST
only Pu239 covariances (33g)








## Slide 6
PU239 covariances
Pu239(n,elastic)
Pu239(n,inelastic)
Pu239(n,fission)
Pu239(n,gamma)
Pu239(nubar)
Pu239(PFNS)
1
2
4
3
Eincident =100keV

## Slide 7
Table 1. Bias and nuclear data uncertainties in PU-MET-FAST-001 (Jezebel)
 | JEFF-3.3 | ENDF/B-VIII.0 | ENDF/B-VIII.1 | ENDF/B-VII.1 | JENDL-5.0
Exp. Uncertainty | ±110 | ±110 | ±110 | ±110 | ±110
¦C-E¦* | 68 | 15 | 68 | 12 | 61
 | UNCERTAINTIES in keff |  |  |  | 
Nubar | 413 | 318 | 417 | 82 | 210
PFNS | 443 | 181*/181+ | 39*/74+ | 182*/182+ | 273
Fission | 305 | 903 | 542 | 330 | 668
Elastic | 90 | 460 | 341 | 435 | 195
Inelastic | 150 | 789 | 651 | 789 | 250
Capture | 30 | 67 | 19 | 74 | 60
elasticP1 | - | 150 | 150 | - | 150
Correlated Sum | 645 | 1054 | 779 | 557 | 832
Note: (values in pcm)
NDAST – Uncertainty Quantification using 1st-order approximation “Sandwich formula”
* Calculations (C) performed with MCNP6-1.0
NOTE: *PFNS covariance Eincident =100keV (default value); + PFNS covariance Eincident =1MeV










## Slide 8
Verification ND uncertainties: U233 cases
Uncertainty Quantification with ENDF/B-VIII.1: ICSBEP/U233 cases
Fissile material |  | U233 | PU |  | 
Spectrum |  | FAST | INTER | MIXED | THERM
Number of Benchmarks |  | 8 | 29 | 8 | 194
Experimental Uncertainty (pcm) |  | 174 | 670 | 601 | 600
Total (pcm) | ENDF/B-VIII.1 | 810 | 1001 | 1026 | 1018
 | ENDF/B-VIII.0 | 810 | 1132 | 1155 | 1131
 | ENDF/B-VII.1 | 754 | 486 | 472 | 495
Cross-sections (with correlations) | ENDF/B-VIII.1 | 640 | 145 | 161 | 347
Cross-sections | ENDF/B-VIII.0 | 640 | 315 | 329 | 514
 | ENDF/B-VII.1 | 724 | 364 | 297 | 206
P1-elastic | ENDF/B-VIII.1 | - | - | - | -
P1-elastic | ENDF/B-VIII.0 | - | - | - | -
 | ENDF/B-VII.1 | - | - | - | -
nubar | ENDF/B-VIII.1 | 475 | 479 | 490 | 539
nubar | ENDF/B-VIII.0 | 484 | 496 | 501 | 508
 | ENDF/B-VII.1 | 211 | 319 | 367 | 447
PFNS NOTE: Ein=100keV | ENDF/B-VIII.1 | 137 | 867 | 887 | 758
PFNS | ENDF/B-VIII.0 | 95 | 967 | 987 | 837
 | ENDF/B-VII.1 | - | - | - | -
Uncertainty Quantification in ICSBEP using NDaST
only U233 covariances (33g)



## Slide 9
U233(n,fission)
U233(n,gamma)
U233(nubar)
U233(PFNS)
U233(n,elastic)
U233(n,inelastic)
U233 covariances
Eincident =100keV

## Slide 10
U233(n,fission)
U233(n,gamma)
U233(nubar)
U233(PFNS)
U233(n,elastic)
U233(n,inelastic)
U233 covariances
Eincident =100keV

## Slide 11
Verification ND uncertainties: HEU cases
  HENDF/ENDF/B-VIII.1: Uncertainty Quantification in ICSBEP using NDaST
Fissile material |  | HEU | PU |  | 
Spectrum |  | FAST | INTER | MIXED | THERM
Number of Benchmarks |  | 477 | 21 | 78 | 798
Experimental Uncertainty (pcm) |  | 225 | 310 | 415 | 473
ENDF/B-VIII.1 only U235 covariances | Total (pcm) | 891 | 638 | 558 | 473
KJE | Cross-sections* | 811 | 514 | 442 | 144
 | P1-elastic | 53 | 13 | 13 | -
 | nubar | 357 | 341 | 322 | 435
 | PFNS+ | 29 | 60 | 61 | 98
ENDF/B-VIII.1 only U238 covariances | Total (pcm) | 52 | 63 | 13 | 6
 | Cross-sections* | 47 | 61 | 11 | 6
 | P1-elastic | 9 | - | - | 
 | nubar | 16 | 10 | 6 | 1
 | PFNS+ | 5 | 3 | 1 | 0
Uncertainty Quantification with ENDF/B-VIII.1: ICSBEP/HEU cases
U235 covariances (33g)
U238 covariances (33g)
Calculations with NDaST: only U235/238 covariances
NOTE: *Cross-sections (with correlations)
NOTE: +PFNS covariance with Ein=100keV

## Slide 12
Verification ND uncertainties: HEU cases
Uncertainty Quantification with ENDF/B-VIII.1: ICSBEP/HEU cases
Fissile material |  | HEU | PU |  | 
Spectrum |  | FAST | INTER | MIXED | THERM
Number of Benchmarks |  | 477 | 21 | 78 | 798
Experimental Uncertainty (pcm) |  | 225 | 310 | 415 | 473
Total (pcm) | ENDF/B-VIII.1 | 891 | 638 | 558 | 473
 | ENDF/B-VIII.0 | 911 | 758 | 649 | 497
 | ENDF/B-VII.1 | 1350 | 1920 | 1266 | 978
Cross-sections (with correlations) | ENDF/B-VIII.1 | 811 | 514 | 442 | 144
Cross-sections | ENDF/B-VIII.0 | 816 | 545 | 470 | 155
 | ENDF/B-VII.1 | 1207 | 1748 | 1062 | 233
P1-elastic | ENDF/B-VIII.1 | 53 | 13 | 13 | -
P1-elastic | ENDF/B-VIII.0 | - | - | - | -
 | ENDF/B-VII.1 | - | - | - | 
nubar | ENDF/B-VIII.1 | 357 | 341 | 322 | 435
nubar | ENDF/B-VIII.0 | 402 | 501 | 435 | 457
 | ENDF/B-VII.1 | 544 | 597 | 550 | 658
PFNS NOTE: Ein=100keV | ENDF/B-VIII.1 | 29 | 60 | 61 | 98
PFNS | ENDF/B-VIII.0 | 29 | 60 | 61 | 98
 | ENDF/B-VII.1 | 210 | 334 | 346 | 622
Uncertainty Quantification in ICSBEP using NDaST
only U235 covariances (33g)
<- Differences in XS-correlations




## Slide 13
U235(n,fission)
U235(n,gamma)
U235(nubar)
U235(PFNS)
U235(n,elastic)
U235(n,inelastic)
U235 covariances
Eincident =100keV

## Slide 14
U238(n,fission)
U238(n,gamma)
U238(nubar)
U238(PFNS)
U238(n,elastic)
U238(n,inelastic)
U238 covariances
Eincident =100keV

## Slide 15
Table 2. Bias and nuclear data uncertainties in HEU-MET-FAST-001 (Godiva)
 | JEFF-3.3 | ENDF/B-VIII.0 | ENDF/B-VIII.1 | ENDF/B-VII.1 | JENDL-5.0
Exp. Uncertainty | ±100 | ±100 | ±100 | ±100 | ±100
¦C-E¦ | 16 | 6 | 0 | 8 | 74
 | UNCERTAINTIES |  |  |  | 
Nubar | 510 | 400 | 388 | 545 | 272
PFNS | 364* | 31*/115+ | 31*/72+ | 257*/257+ | 169*
Fission | 648 | 788 | 788 | 269 | 475
Elastic | 109 | 276 | 276 | 293 | 421
Inelastic | 698 | 244 | 244 | 608 | 679
Capture | 375 | 281 | 282 | 869 | 272
elasticP1 | - | - | 216 | - | 422
Correlated Sum | 1342 | 1036 | 1038 | 1211 | 1104
NOTE: (values in pcm)
NDAST – Uncertainty Quantification using 1st-order approximation “Sandwich formula”
Calculations (C) performed with MCNP6-1.0
NOTE: *PFNS covariance Eincident =100keV (default value); + PFNS covariance Eincident =1MeV

## Slide 16
Fissile material |  | IEU | PU |  | 
Spectrum |  | FAST | INTER | MIXED | THERM
Number of Benchmarks |  | 58 | 8 | 8 | 143
Experimental Uncertainty (pcm) |  | 175 | 166 | 360 | 514
ENDF/B-VIII.1 only U235 covariances | Total (pcm) | 768 | 611 | 450 | 467
KJE | Cross-sections* | 714 | 528 | 220 | 131
 | P1-elastic | - | - | - | -
 | nubar | 277 | 297 | 367 | 430
 | PFNS+ | 65 | 40 | 70 | 121
ENDF/B-VIII.1 only U238 covariances | Total (pcm) | 409 | 292 | 130 | 57
 | Cross-sections* | 336 | 246 | 119 | 55
 | P1-elastic | - | - | - | -
 | nubar | 206 | 149 | 49 | 12
 | PFNS+ | 101 | 41 | 14 | 6
Uncertainty Quantification with ENDF/B-VIII.1: ICSBEP/IEU cases
U235 covariances (33g)
U238 covariances (33g)
Verification ND uncertainties: IEU cases
  HENDF/ENDF/B-VIII.1: Uncertainty Quantification in ICSBEP using NDaST
Calculations with NDaST: only U235/238 covariances
NOTE: *Cross-sections (with correlations)
NOTE: +PFNS covariance with Ein=100keV

## Slide 17
Uncertainty Quantification with ENDF/B-VIII.1: ICSBEP/IEU cases
Verification ND uncertainties: IEU cases
Fissile material |  | IEU | PU |  | 
Spectrum |  | FAST | INTER | MIXED | THERM
Number of Benchmarks |  | 58 | 8 | 8 | 143
Experimental Uncertainty (pcm) |  | 175 | 166 | 360 | 514
Total (pcm) | ENDF/B-VIII.1 | 768 | 611 | 450 | 467
 | ENDF/B-VIII.0 | 800 | 726 | 521 | 492
 | ENDF/B-VII.1 | 1688 | 1853 | 938 | 1045
Cross-sections (with correlations) | ENDF/B-VIII.1 | 714 | 528 | 220 | 131
Cross-sections | ENDF/B-VIII.0 | 716 | 561 | 254 | 143
 | ENDF/B-VII.1 | 1539 | 1740 | 598 | 264
P1-elastic | ENDF/B-VIII.1 | - | - | - | -
P1-elastic | ENDF/B-VIII.0 | - | - | - | -
 | ENDF/B-VII.1 | - | - | - | -
nubar | ENDF/B-VIII.1 | 277 | 297 | 367 | 430
nubar | ENDF/B-VIII.0 | 348 | 454 | 554 | 543
 | ENDF/B-VII.1 | 486 | 540 | 436 | 650
PFNS NOTE: Ein=100keV | ENDF/B-VIII.1 | 65 | 40 | 70 | 121
PFNS | ENDF/B-VIII.0 | 65 | 40 | 70 | 121
 | ENDF/B-VII.1 | 474 | 288 | 413 | 768
Uncertainty Quantification in ICSBEP using NDaST
only U235 covariances (33g)
Differences in XS-correlations




## Slide 18
Uncertainty Quantification with ENDF/B-VIII.1: ICSBEP/IEU cases
Verification ND uncertainties: IEU cases
Fissile material |  | IEU | PU |  | 
Spectrum |  | FAST | INTER | MIXED | THERM
Number of Benchmarks |  | 58 | 8 | 8 | 143
Experimental Uncertainty (pcm) |  | 175 | 166 | 360 | 514
Total (pcm) | ENDF/B-VIII.1 | 409 | 292 | 130 | 57
 | ENDF/B-VIII.0 | 466 | 309 | 157 | 63
 | ENDF/B-VII.1 | 795 | 365 | 365 | 137
Cross-sections (with correlations) | ENDF/B-VIII.1 | 336 | 246 | 119 | 55
Cross-sections | ENDF/B-VIII.0 | 403 | 267 | 148 | 61
 | ENDF/B-VII.1 | 689 | 300 | 360 | 135
P1-elastic | ENDF/B-VIII.1 | - | - | - | -
P1-elastic | ENDF/B-VIII.0 | - | - | - | -
 | ENDF/B-VII.1 | - | - | - | -
nubar | ENDF/B-VIII.1 | 206 | 149 | 49 | 12
nubar | ENDF/B-VIII.0 | 206 | 149 | 49 | 12
 | ENDF/B-VII.1 | 199 | 144 | 48 | 12
PFNS NOTE: Ein=100keV | ENDF/B-VIII.1 | 101 | 41 | 14 | 6
PFNS | ENDF/B-VIII.0 | 101 | 41 | 14 | 6
 | ENDF/B-VII.1 | 320 | 131 | 36 | 18
Uncertainty Quantification in ICSBEP using NDaST
only U238 covariances (33g)

## Slide 19
Verification ND uncertainties: LEU cases
  HENDF/ENDF/B-VIII.1: Uncertainty Quantification in ICSBEP using NDaST
Uncertainty Quantification with ENDF/B-VIII.1: ICSBEP/LEU cases
Fissile material |  | LEU | PU |  | 
Spectrum |  | FAST | INTER | MIXED | THERM
Number of Benchmarks |  | 1 | - | 5 | 1565
Experimental Uncertainty (pcm) |  | 274 | - | 353 | 240
ENDF/B-VIII.1 only U235 covariances | Total (pcm) | 793 | - | 614 | 451
KJE | Cross-sections* | 721 | - | 536 | 156
 | P1-elastic | - | - | - | -
 | nubar | 329 | - | 296 | 419
 | PFNS+ | 29 | - | 25 | 47
ENDF/B-VIII.1 only U238 covariances | Total (pcm) | 125 | - | 158 | 171
 | Cross-sections* | 118 | - | 140 | 160
 | P1-elastic | - | - | - | -
 | nubar | 41 | - | 72 | 59
 | PFNS+ | 7 | - | 11 | 11
Calculations with NDaST: only U235/238 covariances
NOTE: *Cross-sections (with correlations)
U235 covariances (33g)
U238 covariances (33g)
NOTE: +PFNS covariance with Ein=100keV

## Slide 20
Verification ND uncertainties: LEU cases
Uncertainty Quantification with ENDF/B-VIII.1: ICSBEP/LEU cases
Fissile material |  | LEU | PU |  | 
Spectrum |  | FAST | INTER | MIXED | THERM
Number of Benchmarks |  | 1 | - | 5 | 1565
Experimental Uncertainty (pcm) |  | 274 | - | 353 | 240
Total (pcm) | ENDF/B-VIII.1 | 793 | - | 614 | 451
 | ENDF/B-VIII.0 | 832 | - | 685 | 471
 | ENDF/B-VII.1 | 1253 | - | 1019 | 752
Cross-sections (with correlations) | ENDF/B-VIII.1 | 721 | - | 536 | 156
Cross-sections | ENDF/B-VIII.0 | 734 | - | 562 | 163
 | ENDF/B-VII.1 | 1110 | - | 857 | 237
P1-elastic | ENDF/B-VIII.1 | - | - | - | -
P1-elastic | ENDF/B-VIII.0 | - | - | - | -
 | ENDF/B-VII.1 | - | - | - | -
nubar | ENDF/B-VIII.1 | 329 | - | 296 | 419
nubar | ENDF/B-VIII.0 | 392 | - | 388 | 437
 | ENDF/B-VII.1 | 532 | - | 509 | 640
PFNS NOTE: Ein=100keV | ENDF/B-VIII.1 | 29 | - | 25 | 47
PFNS | ENDF/B-VIII.0 | 29 | - | 25 | 47
 | ENDF/B-VII.1 | 231 | - | 203 | 290
Uncertainty Quantification in ICSBEP using NDaST
only U235 covariances (33g)
Differences in XS-correlations




## Slide 21
CONCLUSION
Processing in JANIS format
  ENDF/B-VIII.1 into JANIS Database -> to be used in NDAST (see links in slide 3)
Testing Covariances using NDaST in ICSBEP
How to use the covariance nuclear data of general-purpose nuclear data libraries?
  End-USERS: A–priori covariance data to create specific “application” or industrial ND libraries
  Evaluators: A–priori covariance data for ND adjustment and/or assimilation
  USERS & Evaluators: A-priori covariance data to perform a Target Accuracy Requirement (TAR) to feed HPRL
Pu239 | PFNS | Lower values than E80 ~25-60 pcm
Pu239 | Nubar | Higher values than E80 THERM: Significant change…. 308 pcm → 430 pcm
 | Cross-sections | Ver low values in INTER, MIXED and THERM cases !! < 250 pcm Significant reduction in FAST cases: 857 -> 520
U235 | PFNS | No changes with E80
Pu239 | Nubar | FAST/MIXED/INTER/THERM: lower values than E80
 | Cross-sections | Similar values to E80 … small differences due to cross-correlations
U238 | PFNS/nubar/XSs | Similar values to E80
U233 | PFNS | Large uncertainties in E80 and E81: -> INTER-MIXED-THERM
Pu239 | Nubar | Similar values in E80 and E81
 | Cross-sections | Significant reduction of unc. in fission in E81 -> INTER-MIXED and THERM

## Slide 22
Acknowledgments
This work is part of the APRENDE project (Addressing PRiorities of Evaluated Nuclear Data in Europe) that has received funding from the European Union’s HORIZON-EURATOM
under grant agreement No. 101164596

## Slide 23
Backup slides

## Slide 24
moder /
1 21
'094-Pu-239 '
20 9437 /
0/
reconr /
21 22
'094-Pu-239 '
9437 2 /
0.005 /
'Reconstructed'/
'Processed'/
0/
broadr /
21 22 23
9437 1 0 0 0./
0.005 /
300.0 /
0/
unresr /
21 23 24
9437 1 1 0 /
300.0 /
1.0E+10 /
0 /
groupr /
21 24 0 31/
9437 1 0 2 0 1 1 1 /
'GENDF- 238g' /
300.0
1.E10
238 /
1.00000E-05
1.00000E-04
5.00000E-04
…
1.73300E+07
2.0000E+07 /
3/
3 18/
3 251/
3 452 nubar_t/
3 455 nubar_d/
3 456 nubar_p/
5 455 nubar_spc/
0/
0/
errorr
21 24 0 77 /
9437 1 2 1 1 /
1 300.0 / Just only one temperature
0 33 /
33 /
1.00000E-05
1.00000E-01
…
6.06531E+06
1.00000E+07
1.9640E+07 /
covr
77 0 81 /
1/
/
/
9437 0 0 0 /
viewr
81 82
covr
77 78 /
4 1
'LIB_JENDL-5.0upd ' /
'BOXER format'/
9437 0 0 0 /
stop
Figure 1. Input deck to process MF32/33 covariances
Processing ND/MF32+MF33 in BOXER format
Processing into BOXER format
tape20 = ENDF Pu239
=====================

## Slide 25
Processing ND/MF32+MF33 in BOXER format
Processing into BOXER format

## Slide 26
Processing ND/MF32+MF33 in BOXER format
Processing into BOXER format

## Slide 27
moder
1 21
'017-Cl-35 '
20 1725 /
0/
reconr
21 22
'017-Cl-35 '
1725 2 /
0.005 /
'Reconstructed'/
'Processed'/
0/
broadr
21 22 23
1725 1 0 0 0./
0.005 /
300.0 /
0/
unresr
21 23 24
1725 1 1 0 /
300.0 /
1.0E+10 /
0 /
errorr
999/
21 88/
1 / MT1
2 / MT2
102 / MT102
600 / MT600
0/
errorr
88 24 0 77 /
1725 1 2 1 1 /
1 300.0 / Just only one temperature
0 33 /
33 /
1.00000E-05
1.00000E-01
5.40000E-01
…
1.00000E+07
1.9640E+07 /
covr
77 0 81 /
1/
/
/
1725 0 0 0 /
viewr
81 82
covr
77 78 /
4 1
'LIB_JENDL-5.0upd ' /
'BOXER format'/
1725 0 0 0 /
stop
Figure 2. Input deck to process covariances in files with MF32-only
Processing ND/MF32 “only” in BOXER format
Processing into BOXER format
Materials only MF32
JENDL-5.0:
Cl35, Cr50, Cr54
JEFF-4T2.2
Cl35, Cl37
Cu63, Cu65
Pa231, Pa233
Pu240, Am241
tape20 = ENDF Cl35
==================

## Slide 28
moder /
2 99
' 9437 and 9228' /
91 9437 /
92 9228 /
0/
errorr
21 0 99 26 61 /
9437 1 2 1 1 /
1 300.0 / Just only one temperature
2 33 /
9228 18 /
0 /
33 /
1.00000E-05
1.00000E-01
…
1.00000E+07
1.9640E+07 /
covr
26 0 81 /
1/
/
/
9437 18 9228 18 /
viewr
81 82
covr
26 27 /
4 1
'LIB_JENDL-5.0upd ' /
'BOXER format'/
9437 18 9228 18 /
stop
Processing ND/MF33 –cc in MATs in BOXER format
Figure 3. Input deck to process MF33 covariances between different materials (example JENDL5)
Processing into BOXER format
tape21 = ENDF Pu239
tape91 = GENDF-238g Pu239
tape92 = GENDF-238g U235
tape61 = input cov. tape77(ERRORR output) for U235
=====================================================

## Slide 29
Processing ND/MF31 in BOXER format
groupr /
21 24 0 31/
9437 1 0 2 0 1 1 1 /
'GENDF- 33g' /
300.0
1.E10
33 /
1.00000E-05
1.00000E-01
…
3.67879E+06
6.06531E+06
1.00000E+07
1.9640E+07 /
3/
3 452 nubar_t/
3 455 nubar_d/
3 456 nubar_p/
5 455 nubar_spc/
0/
0/
errorr
21 0 31 41 /
9437 1 2 1 1 /
1 300.0 / Just only one temperature
0 31 /
33 /
1.00000E-05
1.00000E-01
…
6.06531E+06
1.00000E+07
1.9640E+07 /
covr
41 0 81 /
1/
/
/
9437 0 0 0 /
viewr
81 82
covr
41 71 /
4 1
'LIB_JENDL-5.0upd ' /
'BOXER format'/
9437 0 0 0 /
stop
Figure 4. Input deck to process MF31 covariances
Processing into BOXER format
tape21 = ENDF Pu239
tape24 = PENDF Pu239
=====================

## Slide 30
groupr
21 24 0 31/
9437 1 0 2 5 1 1 1 /
'GENDF- 33g' /
300.0
1.E10
33 /
1.00000E-05
1.00000E-01
..
1.00000E+07
1.9640E+07 /
3/
3 251/
0/
0/
errorr
21 0 31 42 /
9437 1 2 1 1 /
1 300.0 / Just only one temperature
0 34 /
33 /
1.00000E-05
1.00000E-01
..
6.06531E+06
1.00000E+07
1.9640E+07 /
covr
42 0 81 /
1/
/
/
9437 0 0 0 /
viewr
81 82
covr
42 72 /
4 1
'LIB_JENDL-5.0upd ' /
'BOXER format'/
9437 0 0 0 /
stop
Figure 5. Input deck to process MF34 covariances
Processing ND/MF34 in BOXER format
Processing into BOXER format
tape21 = ENDF Pu239
tape24 = PENDF Pu239
=====================

## Slide 31
groupr /
21 24 0 31/
9437 1 0 2 0 1 1 1 /
'GENDF- 33g' /
300.0
1.E10
33 /
1.00000E-05
1.00000E-01
..
1.00000E+07
1.9640E+07 /
3/
3 18/
3 452 nubar_t/
3 455 nubar_d/
3 456 nubar_p/
5 455 nubar_spc/
5 18 nubar_spc/
3 452 nubar_t/
3 455 nubar_d/
3 456 nubar_p/
5 455 nubar_spc/
5 18 nubar_spc/
0/
0/
Figure 6. Input deck to process MF35 covariances
errorr
21 0 31 40 /
9437 1 2 1 1 /
1 300.0 / Just only one temperature
0 35 1 1 -1 1.0000E+05 /
33 /
1.00000E-05
1.00000E-01
..
1.00000E+07
1.96400E+07 /
covr
40 0 81 /
1/
/
/
9437 0 0 0 /
viewr
81 82
covr
40 70 /
4 1
'LIB_JENDL-5.0upd ' /
'BOXER format'/
9437 0 0 0 /
stop
Processing ND/MF35 in BOXER
Processing into BOXER format
tape21 = ENDF Pu239
tape24 = PENDF Pu239
=====================