## Slide 1: 88Zr+n: the kick-off to study small radioactive samples with DICER at LANSCE*
Nuclear Data Week, Brookhaven National Laboratory
November 4th – 8th, 2024
LA-UR-24-31649
Experiendo cognoscitur
Th. Stamatopoulos1, P. Koehler1, A. Couture1, B. DiGiovine2, A. Matyskin3, V. Mocko4, J. Morrel4, E. O’Brien4, J. Ullmann1, C. Vermeulen4
Physics Division, Los Alamos National Laboratory, 87545, NM, USA
Weapons Stockpile Modernization Division, 87545, NM, USA
Radiation Science & Engineering Center, College of Engineering, Pennsylvania State University
Chemistry Division, Los Alamos National Laboratory, 87545, NM, USA
*Funded by LANL/LDRD-DR, OES

## Slide 2: Table of Contents
Neutron capture on radionuclides
Traditional neutron transmission measurements
Non-traditional neutron transmission at LANL
The 88Zr experimental campaign

## Slide 3
Neutron capture on radionuclides

## Slide 4
Neutron capture measurements
(n,γ) cross sections are important for:
  Basic nuclear physics
  Astrophysics
  Nuclear criticality safety
  Advanced reactors
  Radiochemical diagnostics
  Safeguards
Gamma detectors are close to the sample and detect the gammas from the de-excitation.
Works fine for stable or moderately radioactive samples.
A new indirect technique is proposed to study radionuclides:
  Neutron transmission experiments to measure the (n,tot) cross section
  R-Matrix fits of the resonances seen in the transmission spectrum
  Fit results to calibrate the Nuclear Statistical Model and tightly constrain (n,γ)

## Slide 5
The technique in a nutshell

## Slide 6
Proof of principle: in brief
Data on 151Sm(n,tot) from Kirouac and Einland (10.1103/PhysRevC.11.895)
Resonance data up to 300 eV (120 resonances)
Resonances were fitted with SAMMY
13 Γγ values were obtained
<Γγ> = 96.5(14) meV
Level spacing D0 = 1.10(7) eV
Strength function 104xS0 = 3.58(59)
TALYS was adjusted to these values and compared with recent (n,γ) data
  Level density parameter α(Sn)
  Optical model potential depth
  Optical model potential diffuseness
  Photon strength function was normalized to give the <Γγ> value https://nds.iaea.org/talys/tutorials/talys.pdf
Good agreement with the data in EXFOR

## Slide 7
Traditional neutron transmission measurements

## Slide 8
Traditional transmission measurements: How to
~10m
~10m
Neutron
detector
Neutron
beam
Collimator
The neutron spectrum (Cout) and backgrounds (Bout) are recorded by a neutron detector (sample out)
A sample, (~cm in diameter), is installed and absorption dips appear (sample in)
The transmission T is the ratio sample in/out
Transmission measurements provide information on the total (Γ) and neutron (Γn) widths and the level spacing (D0) Γ : Transmission dip width Γn : Transmission dip depth D0: Distance between transmission dips
Γ
Γn
D0

## Slide 9
Sample cycling is needed therefore a positioning system must be utilized.
Positioning systems have a finite accuracy and that’s a serious bottleneck, in cycling small and radioactive samples
  Repositioning precision and risk mitigation
Precise repeatability of the sample’s position, relative to the collimation system, is not necessarily ensured.
Traditional transmission measurements: More challenges
What if…the sample didn’t have to move…?

## Slide 10
Binocular mode of operation: Simultaneous measurement of sample in and out
2 non-parallel beam lines, 1mm in diameter that point to the same area on the neutron production target.
No precise repositioning concerns, as long as the sample is precisely positioned beforehand: metrology network ~10μm and ~10 mdeg accuracy
  Knowing where a pencil lead is positioned across the length of a basketball court
Added bonus: measurements are completed in half the time!
Neutron
detectors
Neutron
beam
Collimator
Non-traditional measurements: Binocular approach
Target/moderator
~15m
~15m
Not to scale

## Slide 11
Non-traditional neutron transmission measurements

## Slide 12
The Los Alamos Neutron Science Center - LANSCE
500-800 MeV protons
meV – keV neutrons
keV – MeV neutrons

## Slide 13
800MeV protons impinge on a 3-way split W target.
DICER points to the H2O moderator and the target
Mark-IV (M4) : New neutron target at Lujan, est. 2022
Simulation

## Slide 14
Neutron spectrum
Mark-IV provides an enhanced keV spectrum compared to Mark-III
Mark-IV is expected to improve the neutron energy resolution
Preliminary

## Slide 15
Description of the apparatus:
Device for Indirect Capture Experiments on Radionuclides
A. Stamatopoulos et al., NIMA (1025) 166166, 2022
A. Stamatopoulos et al., IEEE Trans. Nucl. Science 70, (2023)
A. Stamatopoulos et al., Neutron News 33, 12 – 14 (2022)

## Slide 16
The 88Zr experimental campaign

## Slide 17
The curious case of 88Zr (t1/2 = 83.4 days)
LLNL: σγth = 0.861(69) Mb Shusterman et al., Nature 565, p 328 (2019)
LLNL: Iγ = 2.530(280) Mb Shusterman et al., PRC 103 124614 (2021)
Systematic study taking data from Mughabghab reveals that this is an odd combination

## Slide 18
The curious case of 88Zr (t1/2 = 83.4 days)
It’s even hard to model such combination
SAMMY with different combinations didn’t yield such an enormous Iγ.

## Slide 19
DICER - IPF synergy: The 88Zr case
The radioactive sample fabrication relies on the synergy between DICER and IPF
Proton irradiation of a suitable bulk material
Chemical separation and purification (600 mCi, 10 mL 88Zr + D2O●6mol/L DCl )
Gamma spectroscopy
A. Matyskin et al, Scientific Reports 13, 1736 (2023)
A. Stamatopoulos et al., EPJ., Conf. 260, 03006 (2022)
A. Stamatopoulos et al., J. Radioanal. Nucl. Chem. 331, (2022)

## Slide 20
Development of filling station
Operations have to take place in a hot cell with a remote handling capability

## Slide 21
Results
Compatible cross section: σthDICER = 771(31) kb vs σthLLNL = 861(69) kb
Incompatible resonance integral: IDICER = 15.21(67) kb vs ILLNL = 2530.0(280) kb
1 keV MACS in agreement with LANL evaluation MACSDICER = 1.6(12) b. vs MACSLANL = 1.1 b
Phys. Rev. Lett : In press

## Slide 22
The curious case of 88Zr (t1/2 = 83.4 days)

## Slide 23
Thank you for your attention!

## Slide 24
https://exp-astro.de/meetings/dimer/index.php

## Slide 25
9Back-up slides

## Slide 26
Flux monitor
Sanity checks
Binocular collimator
Paddle configuration: should not affect the flux monitor
Does the binocular idea work?
Flux * efficiency: Left vs Right

## Slide 27
Backgrounds

## Slide 28
The technique in a nutshell
Resonances can be used across an energy region ΔΕ to calculate the 3 ingredients needed to extract or constrain the average capture cross section
Average level spacing (N: number of resonances in the ΔΕ interval).
Neutron strength function for s-waves , where
  g is the spin factor for a resonance with spin J
  Γ0n is the reduced neutron width
Average radiation width <Γγ>
The capture cross section is related to these quantities
k : Wave number
W : Width fluctuation factor
Notes: n the Hauser-Feshbach formalism, the width fluctuation factor represents the effect of the statistical fluctuations in the nuclear levels on the width (or probability) of a particular reaction channel. It accounts for the fact that the widths of these levels are not fixed values but can vary due to the uncertainty principle of quantum mechanics. Essentially, it helps to adjust the predicted cross sections for nuclear reactions to better match experimental data.

## Slide 29
Sophisticated collimation system
Rotating beam blocker
Binocular collimator
Aperture stop
Rotating inner cylinder with 3 holes
30 cm in length
Provides 0 - 2 beams
Stepped design to avoid neutron stream paths
Remotely controlled
Divided in a top and bottom part
Sample is installed in the collimator in the Maxwell kinematic stops
1.5 cm length, 1 cm diameter sample envelope
1 mm collimation
Kinematic stops ensure repeatability when installing the top part.
Cuts off the beam penumbra
Ensures two sharp beam spots at a 31 m, 9.5 cm in diameter