## Slide 1: An Upgraded Polarized 3He Atomic Beam Source for Polarimetry at EIC (Dev.: Cryo. nEDM Exp. @ SNS in ORNL)
Prajwal T MohanMurthy
+ J. Kelsey, J. Dodge, R. Redwine, R. Milner
& P. Binns, B. O’Rourke
MIT

## Slide 2: Contents
§0
Why 3He ABS?
Basic Components:
    Cryo-chamber
    MCP & Actuation system
    Quadrupole magnet
Major Upgrades (easier to discuss knowing the components):
  Vertical orientation
  MCP
  Actuation system
Polarimetry @ EIC

## Slide 3: Why polarized 3He?
§1
SQUID loops
HV
Measurement Cells
UCN: 500k
3He: 1016
=
3He/ 4He ~ 10-10
3He is a good: co-magnetometer + neutron detector
n + 3He → p + t
Ideally ~99% polarized: SEOP/MEOP won’t work

## Slide 4: ABS Components
Cryo-vessel
Quadrupole magnet
§2
Produces cold 3He polarized atoms
~ 1.3 K (112 µeV)
Flux ⪆1014 atoms/s

## Slide 5: ABS: Cryo-Vessel
§2
Produces cold 3He polarized atoms
~ 1.3 K (112 µeV)
Flux ⪆1014 atoms/s
4K pot
1K pot
MCP
3He (unpol)
Uses both 4He (for cooling) & 3He ! Not a dilution refrigerator
2D Actuator

## Slide 6: ABS: Quad. Magnet
§2
Shim Magnet
MCP
Skimmers
Quadrupole Magnet

## Slide 7: ABS: Quad. Magnet
§2
Spin-Tracking , Ray-Tracing Simulation
Quadrupole Magnet
Shim Magnet
MCP
Skimmers
UCN: Can be completely reflected
E < 300 neV
ΔE = µm ≈ 60 neV/T
: Only >deflected<
1.3 K ≈ 86 µeV
ΔE = µm ≈ 67 neV/T
Making initial angle very important

## Slide 8: ABS: Multi Channel Plate
§2
Arranged in hexagon (side 25 µm)
Pores at vertex and center of hexagon
Pore diameter: 5 µm
Pore length: 0.5mm
Simulation
Microscope (2 µm)
Schematic
Quartz MCP: Unidirectional 3He beam

## Slide 9: Upgrade: MCP
§3
Before: 3He ABS used a needle valve to effuse
Now: 3He ABS uses a Quartz MCP
Constraints the angular distribution to (before: 1.5o) 0.5o
Microscope (2 µm)
Schematic
Angular distribution set by:
Diameter/length = 0.01/0.5
Angular distribution set by:
Diameter/length = 0.002/0.5

## Slide 10: Upgrade: Actuation
§3
Before: 3He nozzle was fixed
Now: 3He nozzle can be moved – pitch and yaw

## Slide 11: Rotary Stage
§3
1K
4K
Vac
New 2-Axis Actuator System
(i) Rotary Stage
“Yaw” : LR
(ABS: 0.5o acceptance)
Resolution | 0.27 (arc) s
Repeatability | 5 (arc) s
Temperature | [0,50] oC
newmarksystems.com/vacuum-compatible-stages/rm-3-vacuum-compatible-rotary-stage/

## Slide 12: Linear Actuator
§3
1K
4K
Vac
New 2-Axis Actuator System
(i) Linear Actuator
“Pitch” : TB
(ABS: 0.5o acceptance)
Resolution “steps” | 30 nm
Range | 12.7 mm (0.5o)
Temperature | [10,40] oC
newport.com/p/8310-V

## Slide 13: Upgrade: Actuation
§3
Produces cold 3He polarized atoms
~ 1.3 K (112 µeV)
Flux ⪆1014 atoms/s
4K pot
1K pot
MCP
3He (unpol)
2D Actuator
MCP: Unidirectional 3He beam Actuation: Gives direction control

## Slide 14: Mezzanine: Now…
Apr 2023: Mezzanine ++ Electrical outlets, gas lines, electronics rack
§x
Electrical lines
Racks
Gas lines

## Slide 15: Mezzanine: Now…
Apr 2023: Mezzanine ++ Electrical outlets, gas lines, electronics rack
§x
Upstairs
“Things that get shipped”
Downstairs
“Things that don’t get shipped”
Power outlets
Power supply unit is attached to the rack, for upstairs

## Slide 16: Vacuum Schematic + Gas Panel
§x
He-ABS for Pol. @ EIC, Aug 2024: Page 16
1K
4K
y
x
Air
LN2
Air

## Slide 17: Gas Panel
§x
He-ABS for Pol. @ EIC, Aug 2024: Page 17
1K
4K
y
x
Air
LN2
Air

## Slide 18
§x
He-ABS for Pol. @ EIC, Aug 2024: Page 18
1K
4K
y
x
Air
N2
Air
4He-MFC (Bates)
www.mks.com/f/ge50a-mass-flow-controller
Flow Rate ≤ 1400 SCCM
GE50A 007 104 R B V 0 20
GE50A: Multi-gas/range, Elastomer-sealed
007: Hydrogen-Calibrated (OK for He)
104: <10k SCCM (standard cubic-cm per minute)
R B: Swagelok 4 (inlet), 2 (outlet), male
V: Vitron (Elastomer) sealant
0: Normally closed
20: Firmware version

## Slide 19: Valve: Magnetic Fields
§x
He-ABS for Pol. @ EIC, Aug 2024: Page 19
Magnetic Fields
ni.com/en-us/support/model.pxi-2566
Solenoid: 24 V
2-9 µT @ surface [measured]
0.067-0.225 nT @ 1m - MSR [calculated]
(Earth’s magnetic field ~ 5 µT)

## Slide 20: Assembly: Cryo Insert
§x
New 4K pot
New heat shield

## Slide 21: Parts Fabrication: 4K Pot + Torlon
§x
New 4K pot
New heat shield
New skimmer-1
Not in picture: all Torlon pieces have also been fabricated

## Slide 22: Simulation – 1: Spin Tracking
§x
Spin-Tracking , Ray-Tracing Simulation
Quadrupole Magnet
Shim Magnet
MCP
Skimmers
Quadrupole Magnet
@ Surface: 0.9 T dB/dx = 1.125 T/cm
: Transmitted [50%→99.5%]
: Deflected and pumped out [50%→0.5%]
Shim Magnet
Adiabatic transport
d2B/dxdz = 0.39 T/cm2
S. Eckel et al., Phys. Rev. A 85, 032124 (2012).

## Slide 23: Simulation – 2: Mol Flow
§x
M. Broering, E. Tsentalovich, J. Kelsey
Residual Gas Simulation
*No B-field or spin tracking
Helped with design of:
Pumping requirements (+bypass tube)
Geometry/location of turbos
x
y
RGA

## Slide 24: Thermal Modelling
§x
To compensate for change in dimension of height
ΔT ~ 300 K, L ~ 10 cm
α: in/in/K
ΔL = α L ΔT ~ 0.51 mm
ΔL (Thermal Model) = 0.5 mm
wshampshire.com/wp-content/uploads/torlon.pdf

## Slide 25: Preliminary Polarization
§x
Key performance requirement:
  99.5% @ 1.25K
  99% @ 1.55K
From Simulation

## Slide 26: 3He ABS Pol. Measurement
§4
x
y
x
y
A
B
+
-
Polarizer
Analyzer
+
-
: Background/residual gas from simulation [angular diffusion]
: Raw measured profile
~ 1/20 [pre-upgrade]

## Slide 27: 3He—3He Polarimeter
§4
G. Breit, I. I. Rabi, Phys. Rev. 38, 2082 (1931)
R
R
L
L
+
-
+
-
x
y
x
y

## Slide 28: Polarimetry Analyzing Power
§4
N. H. Buttimore, PoS (PSTP2013) 182, 057 (2014)
Calculated, but needs to be measured

## Slide 29: Location in RHIC
§4
R. Abdul Khalek et al, Nucl. Phys. A 1026, 122447 (2022) A. A. Poblaguev, Phys. Rev. C 106, 065203 (2022)
20 m stretch
Location: Right next to polarized H-Jet [also an ABS based absolute p-Polarimeter].
20m: Need to veto nuclear fragments.
Characterization: Explicitly measure the analyzing power of both {p-3He, 3He-3He}
Cross check with HJet {p-3He}.
H-Jet

## Slide 30: Proposed Schedule
§5
3-Year Program:
  @MIT-Bates [Publish instrument paper] (i) Finish out the upgrades, (ii) measure ABS temp. [-profile], (iii) measure polarization, (iii) establish long-term performance
  @MIT-Bates (a) upgrade cold-head [pulse tube → eliminate vibr.], (b) design & build scattered particle detectors
  @BNL [Publish instrument paper] (A) Commission 3He ABS (B) Measure the analyzing power {p-3He, 3He-3He} (C) Cross check with HJet {p-3He}

## Slide 31: Summary
Major upgrades under implementation:
  Redesign of new larger cryo-vessel: vertical orientation
  Use of MCPs
  MCP actuation
3-Year Program to develop and implement absolute 3He-3He Pol.
Ask me about: side-physics quest (Testing charge neutrality)!
New setup will be tested in Year-1
=> Should Deliver Key Param.: flux (1014.3He/s) & Pol. (99.5%)
§5
DOE: DE-SC0019768, DE-SC0014448, DE-SC0018229
NSF:
PHY-1822502
Discuss!

## Slide 32: Backup!

## Slide 33: Why polarized 3He?
§1
SQUID loops
HV
Measurement Cells
UCN: 500k
3He: 1016
3He is a good: co-magnetometer + neutron detector
3He/ 4He ~ 10-10

## Slide 34: Why polarized 3He?
§1
SQUID loops
HV
Measurement Cells
UCN: 500k
3He: 1016
3He/ 4He ~ 10-10
3He is a good: co-magnetometer + neutron detector
UCNs and 3He are moving and precessing

## Slide 35: Why polarized 3He?
§1
SQUID loops
HV
Measurement Cells
UCN: 500k
3He: 1016
=
Spin dependent capture
3He/ 4He ~ 10-10
3He is a good: co-magnetometer + neutron detector
n + 3He → p + t

## Slide 36: ABS Components
§1
! Not to scale!
New component

## Slide 37: Transmission of 3He
§2
MCP: Exaggerated
0.5 mm
Generate 3He within 0.1mm of MCP pore: Molecular flow
Pointing in forward hemisphere: Isotropically
With |V| ∈ Boltzmann distribution for T = 1.3 K

## Slide 38: Reflections
§2
Discrete Time vs. Ray tracing
Initially, discrete Steps of 1 µs
  E.g.: To traverse 500 µm @ 10 m/s takes 50 steps
Updated, Faster!: Ray tracing, on an average 3 steps
  2 bounces @ 100 % bounce rate (initially bounce rate = 0%)
Faster by ~ order of magnitude
MCP: Exaggerated

## Slide 39: ABS: Quadrupole
§1
Quadrupole: Polarizes 3He
MCP
Hexapod
Skimmers
Quadrupole magnet
! MCP Schematic: Not to Scale !

## Slide 40: ABS: Cryo-Vessel
§2
Produces cold 3He polarized atoms
~ 1.3 K (112 µeV)
Flux ⪆1014 atoms/s
4K pot
1K pot
MCP
3He (unpol)
Uses both 4He (for cooling) & 3He ! Not a dilution refrigerator
Hexapod

## Slide 41: ABS: Cryo-Vessel
§2
Produces cold 3He polarized atoms
~ 1.3 K (112 µeV)
Flux ⪆1014 atoms/s
4K pot
1K pot
MCP
3He (unpol)
MCP: Unidirectional 3He beam Hexapod: Gives direction control
Hexapod

## Slide 42: Upgrade: Vertical
§3
Pre HV-cavallo design “Thomas the Tank Engine”
3He ABS came in from the side

## Slide 43: Upgrade: Vertical
§3
Now: 3He ABS comes in vertically down → Major eng. design

## Slide 44: Hexapod Replacement
§3
1K
4K
Vac
1K
4K
Vac

## Slide 45: Rotary Stage + Linear Actuator
§3
1K
4K
Vac
New 2-Axis Actuator System
Restores 2-axis * rotation “Pitch” and “Yaw”
Loss of 3rd axis rotation
Loss of 3 * translations
-Translation: along beam @ mm scale doesn’t affect 3He polarization
-Translation: perpendicular to the beam axis (after ΔT)
  Up-Down: (Thermal Model)
  Left-Right

## Slide 46: Rotary Stage
§3
1K
4K
Vac
New 2-Axis Actuator System
(i) Rotary Stage
“Yaw” : LR
(ABS: 0.5o acceptance)

## Slide 47: Linear Actuator
§3
1K
4K
Vac
New 2-Axis Actuator System
(i) Linear Actuator
“Pitch” : TB
(ABS: 0.5o acceptance)
newport.com/p/8310-V

## Slide 48: Pressure and Mass Flow
§6
Cryo-ABS Review, Apr 2024: Page 48
1K
4K
y
x
Air
N2
Air
(Mass flow rate)2
3He: 0.01 SCCM
4He: 1400 SCCM
(Flow rate)2
Apply: Bernoulli's Principle

## Slide 49: Actuated Valves
§6
Cryo-ABS Review, Apr 2024: Page 49
Swagelok SS-BNS4-C
products.swagelok.com/en/c/straight-pattern/p/SS-BNS4-C
Bates - stock
+Micro-switch (state: on/off)
Pneumatic-Electro Valve
Normally open/closed
Solenoid: 24 V

## Slide 50
§x
Cryo-ABS Review, Apr 2024: Page 50
1K
4K
y
x
Air
N2
Air
3He VAT
VAT 59.0
~$9k
Rated for (10-13, 10) Bar
105 digital encoder resolution (stepper motor)
For 5mm bore: {3,4}He Flow Rate ~ (0.001,100) SCCM
“All metal variable leak valve”
Still need to measure the flow rate!
https://www.vatvalve.com/series/ultra-high-vacuum-all-metal-variable-leak-valve
Already delivered

## Slide 51
Vertical ABS Support
§9
Support system fabrication to be done
Need to secure the quadrupole magnet in vertical orientation
Clean and seal quadrupole magnets
Engineering Design Complete
Vertical support system

## Slide 52: Mezzanine: Then…
Jan 2023: Mezzanine = pillars, platform, stairs
§x

## Slide 53: Actuated Valves - Controller
§ 6
Cryo-ABS Review, Apr 2024: Page 53
8-channel controller
(solenoid power supply + status indicator)

## Slide 54: Controller – Relay
§ 6
Cryo-ABS Review, Apr 2024: Page 54
PXI NI 2566 (single pole double throw - SPDT) Relay Board
ni.com/en-us/support/model.pxi-2566

## Slide 55: Vacuum Test of the Chamber
§x
Reaches 20 n mBar with a small turbo after baking at 180o C overnight (can easily get to 1 nTorr with inline turbo)
!Empty inside!

## Slide 56
Non-magnetic Gate Valve
§x
Candidate Al-Gate Valve
Non-magnetic
vacuumresearch.com

## Slide 57: Placement in the Apparatus
§x
Cryo-ABS Review, Apr 2024: Page 57
Vac
4K
1K
300K
CX10-1
CX10-2
RX102-3
CX10-5
RX102-2
RX102-1
CX10-4
CX10-3

## Slide 58: Types of Sensors: New
§1
Zirconium Oxy-Nitride Thin-Film Resistance
Ruthenium Oxide
Thick-Film Resistance
Silicon Diode
Voltage Drop
(0.1,420) K
(0.05,40) K
(1.4,500) K
www.lakeshore.com
Cernox-CX10
Rox-RX102A
Diode-DT670

## Slide 59: Types of Sensors: New
§1
Zirconium Oxy-Nitride Thin-Film Resistance
(0.1,420) K
www.lakeshore.com
Cernox-CX10

## Slide 60: Types of Sensors: New
§1
Ruthenium Oxide
Thick-Film Resistance
(0.05,40) K
www.lakeshore.com
Rox-RX102A

## Slide 61: !!!Types of Sensors: New
§1
www.lakeshore.com
Silicon Diode
Voltage Drop
(1.4,500) K
Diode-DT670

## Slide 62: Calibration of Test Sample
§3
Cryo-ABS Review, Apr 2024: Page 62
Repeated temperature cycles
Zirconium Oxy-Nitride Thin-Film Resistance
(0.1,420) K
Cernox-CX10
.
.
.
2-point calibration doesn’t really work!
3rd degree polynomial: 4 points required.
Lakeshore basic: 3-point calibration @ {Room temp, Liq. N2, Liq. He}
Can be done in our lab: @ {Ice water, Boiling water, Liq. N2, Liq. He}

## Slide 63: Calibration of Test Sample
§3
Cryo-ABS Review, Apr 2024: Page 63
Needs more resolution than available in a lab!
Can NOT be done in our lab
Ruthenium Oxide
Thick-Film Resistance
(0.05,40) K
Rox-RX102A

## Slide 64: DAQ: LakeShore 224
§ 5
Cryo-ABS Review, Apr 2024: Page 64
We already have…
12 Channels
Can handle mixture of sensors
Compatible with RX102A & DT670

## Slide 65: V-Distribution Change
§x
The distribution of the magnitude of the velocity changes little
This is to be expected, because:
  There is no energy dependent scattering (or η)
  Assumed: elastic collisions

## Slide 66: Angular Dist. Change
§x
Angular distribution is constrained by MCP.
…not by subsequent components ~ 10% level.
Angular allowance of MCP ~ 0.5o
... same from subsequent components (8.8/1010)
8.8 mm
1010 mm

## Slide 67: Angular Dist. Change
§x
Angular distribution is constrained by MCP.
…not by subsequent components ~ 10% level.
Angular allowance of MCP ~ 0.5o
... same from subsequent components (8.8/1010)
8.8 mm
1010 mm
End point set by choice of η

## Slide 68: # Bounces & Choice of η
§x
Eg. η ~ 0.3 → #bounces ~ 3
#bounces sets the limit on angular allowance
#bounces ~ length/(diameter/tan(θz))

## Slide 69: Polarization/Depolarization
§2
Quadrupole gradient ~

## Slide 70: Modification to code
§2
“Dipole Precession”
Gradients (in any combination)
Quadrupole:
Shim:
Shim:
Shim:

## Slide 71: Depolarization
§2
Modes of depolarization
  Bounces Pick: β-Depolarization per bounce
  Magnetic field gradients Known:

## Slide 72: Results: Conservative
§2
Time after shutter close + bounces off shutter

## Slide 73: Initial Velocity
§2
Generate 3He within 0.1mm of MCP pore: Molecular flow
Pointing in forward hemisphere: Isotropically
With |V| ∈ Boltzmann distribution for T = 1.3 K

## Slide 74: η: Loss per bounce coeff.
§2
If, bounce coefficient, η=0 (Everything sticks)
If, bounce coefficient, η=0.3 (30% sticks)
A difference ~ 10% level.
5 µm
500 µm
0.5O

## Slide 75: Angular Dist. Change
§2

## Slide 76: Depolarization from magnetic field gradients
§1
“Dipole Precession”
Gradients (in any combination)
What B field?!
Eg.: [Think on the same lines for transverse direction…]
“ultracold”
“hot”

## Slide 77: Results: Conservative
§2
: C. Gemmel et al., Phys. Rev. D 82, 111901 (2010)
s
Time after shutter close + bounces off shutter

## Slide 78: Modes: Bounces
§3
: C. Gemmel et al., Phys. Rev. D 82, 111901 (2010)
Time after shutter close + bounces off shutter
Mean free path,
Bounce rate,

## Slide 79: Modes: Bounces
§3
: C. Gemmel et al., Phys. Rev. D 82, 111901 (2010)
Time after shutter close + bounces off shutter

## Slide 80: Neutrality of Matter

## Slide 81: Motivation
Charge Quantization?
Micro-charges
Global gauge invariance
Charge conservation
Inflation: Is charge conserved?
Is the charge of neutrinos “0”?
Is ?
If
PDG:
s
§y

## Slide 82: Motivation
Neutrality of matter
Global gauge invariance
Charge conservation
From neutrality of matter
(atoms: ) &
PDG: (95% C.L.)
&
§y

## Slide 83: Previous Efforts
Cold Neutrons:
Deflection Experiments
Neutrality of Matter:
Acoustic Resonator
R. Gähler et al., Phys. Rev. D 25, 2887 (1982).
J. Baumann et al., Phys. Rev. D 37, 3107 (1988).
G. Bressi et al., , Phys. Rev. A 83, 052101 (2011). Using SF6
Neutrality of matter can also be tested with gas efflux and suspended bodies.
§y

## Slide 84: New Proposals: Cold Neutrons
Sensitivity of:
Deflection
Interferometry
@ ESS
§y

## Slide 85: Overview of Current Status
Under review
Under review
§y

## Slide 86: Using Cryo. He-ABS
Perform a beam deflection measurement
Cryo-vessel
Quadrupole magnet
→ Electrode (30 kV/cm)
Produces cold (3He) 4He
(For better systematics)
~ 1.3 K (112 µeV)
Flux ⪆1014 atoms/s
§y

## Slide 87: Using Cryo. He-ABS
Perform a beam deflection measurement
V. W. Hughes et al., Z. Phys. D 10, 145 (1988)
Previous beam deflection experiments used hot oven sources of Cs, K atoms
@ 480 K [HOT!]
≲ 2×10−18 e [90% CL]
ABS: T≈1 K→
X500 better!!!
Measure deflection using RGA (±E,0)
§y

## Slide 88: Measurement Campaign
Measure deflection using RGA (±E,0)
1K
Electrode
Electrode
x
y
RGA
Residual Gas Analyzer
1 ms timing resolution, using 2× RGAs →velocity profile better than 10 m/s →temperature better than 0.3 K [tof]
1 µm/hour (standard error) precision by collecting data on pressure profile
§y

## Slide 89: Best Gases? 2nd Species
Using 2 species of gases, :
&
From neutrality of matter
(atoms: ) &
+
§y

## Slide 90: Best Gases? 2nd Species
Divide by large molar mass
&
From neutrality of matter
(atoms: ) &
+
4He: spin-0
20Ne: spin-0
130Xe: spin-0
§y

## Slide 91: Systematics
Choice of 4He (s=0) motivated by…
Residual Gas Analyzer
1 ms timing resolution, using 2*RGAs →velocity profile better than 10 m/s →temperature better than 0.3 K [tof]
1 µm/hour (standard error) precision by collecting data on pressure profile
v×E effect: both linear and quadratic
Spatial inhomogeneity of E-field: ∂E/E≈10-4
Other systematics from:
AC E-fields ~ ∂E/E≈10-4
§y
R. Gähler et al., Phys. Rev. D 25, 2887 (1982).

## Slide 92: Systematics
Residual Gas Analyzer
1 ms timing resolution, using 2*RGAs →velocity profile better than 10 m/s →temperature better than 0.3 K [tof]
1 µm/hour (standard error) precision by collecting data on pressure profile
If spin=0, then negligible
4He EDM ≈ 0
4He polarizability much smaller compared to alkali atoms & 3He
M. Puchalski et al., Phys. Rev. A 101, 022505 (2020)
Other systematics from:
AC E-fields ~ ∂E/E≈10-4
α4He/4πε0= 8.6×10−25 cm3
§y
Choice of 4He (s=0) motivated by…

## Slide 93: Summary
[1] R. Gähler et al., Phys. Rev. D 25, 2887 (1982)
[2] J. Baumann et al., Phys. Rev. D 37, 3107 (1988)
[3] G. Bressi et al., Phys. Rev. A 83, 052101 (2011)
[4] F. M. Piegsa, Phys. Rev. C 98, 045503 (2018)
[5] G. Bressi et al., Phys. Rev. A 83, 052101 (2011)
[6] V. W. Hughes et al., Z. Phys. D 10, 145 (1988)
[A] M. Puchalski et al., Phys. Rev. A 101, 022505 (2020)
Sensitivity to from current ABS
Current PDG limit
Could improve by x(2-10) by longer averaging and higher E-fields
§y