## Slide 1: Memo from Jim Yeck, Project Director, Dec 11 2024
Optimization of the Electron Injector – The decision was made to remove the Rapid Cycling Synchrotron (RCS) from the RHIC/EIC tunnel. The preliminary RCS concept is a new 1.4-km ring, located near Interaction Region 4. The cost and performance optimization of the entire injector (linac and RCS) will continue into the Spring of 2025. The justification for the decision and the plan for advancing the electron injector design and for addressing the full implication of this important change will be presented at the DOE review in early January. Sergei Nagaitsev, EIC Technical Director, is the primary point of contact for questions.
Strategy for Project Delivery – (not part of this charge)
Early Science Program – (not part of this charge)
Beam Cooling – The project is no longer planning to implement Strong Hadron Cooling within the scope of the line-item construction project. Low Energy Cooling will be added to the scope of the line-item project. These changes are responsive to the concerns raised in earlier DOE reviews and result in lower technical performance risk and reduced construction cost. The justification for these decisions will be presented at the DOE review. Following the DOE review we will implement the changes in our planning documentation.

## Slide 2
Strategy for Electron Injector System
Slides from various draft SC-1 Injector Session
presentations for January 2025 DOE OPA Review

## Slide 3: EIS Performance Goals
Provide bunches with appropriate emittances, charge and polarization at the necessary cycle rate to meet the needs of the Electron Storage Ring (ESR) and the physics program.
  Generate and accelerate polarized electrons to 5, 10 GeV with 85% polarization
  Deliver 7 nC bunches at 5 and 10 GeV ( 1 bunch per second)
    Need to fill ESR in under 20 min 1160 buckets x 1 sec ~ 19.33 min
Provide Path to upgrade:
  Increase bunch charge to 28 nC/bunch at 5 and 10 GeV
  Deliver 11nC at 18 GeV
    290 buckets x 1 sec~ 4.8 min
  Match ESR Emittances

## Slide 4: RCS Issues, in a nutshell…
The EIC needs an RCS in order to deliver on project requirements and expectations.
The RCS placement into the existing RHIC tunnel is leading to a highly non-optimal design. Also, presents a challenge to installation and future EIC operations (maintenance and servicing of the RCS).
Tunnel at Sector 1 (with the 41-GeV bypass)

## Slide 5: Moving RCS out of RHIC Tunnel

## Slide 6: New Concept of the Electron Injector
750 MeV linac @ 1.3 GHz Superconducting RF
ESR
RF
fRF = 591 MHz
7 nC bunch injection
RCS
RF
Improvements from baseline
  Increased RCS dipole field from 56 G to 290 G to avoid large magnetic field error at below 200 G.
    Increased RCS injection energy to reduce beam affected by eddy current induced magnetic field.
  Lower linac frequency to open high charge (>10nC) bunch option
  Add spin rotation option at low energy
400 MeV linac @ 2.8 GHz Normal conducting RF
New Concept
CDR baseline
Frequency ratio 11:5
3.8 km circ.
RCS
RF
fRF = 591 MHz
7 nC bunch injection
In RHIC tunnel
ESR
RF
In RHIC tunnel
Swap out
Swap out
Swap out
1.4 km circ.

## Slide 7: EIS Approach with RCS out of RHIC tunnel
Pre-injector: Front End  delivers up 7.5 nC of bunch charge with 88% polarization
Pre-injector: SRF LINAC  accelerates 1 bunch to 750 MeV
RCS: Accelerate from 750 MeV to 5 and 10 GeV energy delivering one bunch of 7 nC every second. This will fill ESR in under 20 min.
EIS is capable of being cycled up to 4 times per acceleration cycle (5Hz)
Path to 18 GeV and 28 nC bunch charge:
Path to reach 18 GeV with 11nC and high polarization  RF installation and Power supply upgrade
Path to achieve 28 nC/bunch in the RCS using accumulator ring: BAR (Beam Accumulator Ring)

## Slide 8: Introduction to the New Pre-injector
Envelop:
From polarized electron gun to end of the Linac to RCS (LTR) transfer line
Scope interface defined at RCS septum entrance
The major components of the electron pre-injector are listed in the picture above
IR04

## Slide 9: RCS Lattice Layout and Spin Transparent Design
Need room for the ability to install up to 130 MV of RF voltage and accommodate injection and extraction
However this will spoil the high periodicity of we need to avoid the impact of depolarizing spin resonances i.e. with a race track design the periodicity “P” would be 2 and we would see intrinsic and strong imperfections in our range of energy acceleration.
To avoid breaking spin periodicity the vertical phase advance across straight to 2*PI*N. (the original RCS spin transparent concept). We choose 4PI.

## Slide 10
Strategy for Hadron Cooling
Slides from S. Nagaitsev (Technical Director) draft plenary
for January 2025 DOE OPA Review
(Basically the same as presented at November 2024 Director’s Review)

## Slide 11: Recommendations from Nov 2023 DOE Review
Develop a plan in case strong hadron cooling (both SHC-CeC and SHC-REC) performance falls below expectations; present at the next OPA Review. ​ We concur. See next slides ​
Develop a plan for a focused program of the RHIC end-of-run beam studies as part of APEX with a goal to address potential issues and provide input to further mitigation of the EIC performance risks; report to NP by May 2024.
See V. Ptitsyn’s talk (SC2)​ at CD-3B DOE OPA Review (January 2025)

## Slide 12: Why is beam cooling so important for the EIC?
Compared to HERA, the EIC design implements two new critical ideas:
  Flat proton bunches at collisions (to match the electron beam dimensions) – this helps with the peak luminosity
  Continuous proton beam cooling during collisions to maintain matched beam dimensions – this helps with the average luminosity
EIC main parameters

## Slide 13: SHC: Background Info
2021: The EIC CDR focuses on SHC as a preferred alternative to (1) create flat bunches and (2) maintain emittance during collisions.
2023: We realize that SHC is too slow to create flat bunches at collision energy. Added a low-energy electron cooler (13 MeV) at injection, combined with SHC-CEC.
2024: SHC has remaining unresolved technical challenges. We developed a detailed luminosity model with and without SHC at collisions. Model assumes flat bunches, created by a low-energy electron cooler.
SHC 55-150 MeV
PreCooler 13 MeV
SHC/Precooler shared returning ERL loop
CS1 ~60m
(SHC Modulator)
CS2 ~60m
(SHC Kicker)
HSR SHC Chicane
HSR Magnets
IP2
HSR Magnets
HSR Magnets
U- turn
E=13, 55, 150 MeV
Electron beam direction
Electron beam direction
Notes: Challenges: 1. cooling theory has been done in longitudinal plane. However transverse emittance effect on cooling rate is not fully understood yet.
2. Cooling requires the generating and preservation of low shot noise electron beam, which has not been fully demonstrated
3. The requirement for synchronization of both beam is crucial for high bandwidth strong hadron cooling, which has not been fully demonstrated

## Slide 14: Luminosities w/wo SHC for 275 GeV p on 10 GeV e (example)
Each store starts with 30 min precooling and 30 min to fill the ESR ring (~1200 bunches);
In addition, we assume a 2-hour turnaround time for filling hadrons, precooling, and ramping
ESR fill
SHC
SHC
See W. Bergan’s talk in SC2
Starting collisions with “flat” proton bunches

## Slide 15: Producing ‘flat’ Proton Bunches
DC Gun
400kV
e-
Laser
197 MHz
900 kW Beam Dump
16x 197 MHz
NCRF LINAC
extraction
injection
cooling
HSR
4x 591 MHz
NCRF correction Cavities
180° Dipole
Spectrometer
Quad
Cathode transport
Mu-metal shielding
24MHz
RF cavity
SC Quad
130 kW Beam Dump
Extraction line
Injector/linac
Test line
Solenoids
LEReC Cooling Solenoids
180°Dipole
(U-turn)
transport
PM
PM
PM
RF diagnostics line with Deflecting cavity
Injector test
e-
HSR
hadron
hadron
hadron
e-
RF diagnostic
Not to scale
See A. Fedotov’s talk in SC2 at January 2025 DOE OPA Review
IR2 layout
(all within the
existing RHIC
Tunnel)

## Slide 16: Strategy for Hadron Cooling
The SHC-related risk was identified as ‘HIGH’; much attention to SHC at previous reviews.
To mitigate this risk, we are adding an injection electron cooler for hadrons (at 25 GeV/u) to create ‘flat’ bunches. This is a proven and tested technology. We propose to remove the SHC system from the project baseline.
  The average luminosity would drop by a factor of 2 per our model, but the CD0 luminosity goals (1033 – 1034 cm-2sec-1) can still be met even without the SHC system.
This downgrades the hadron cooling risk from HIGH (SHC) to LOW (Injection cooler).
The High-Energy Cooling technology development will continue as an R&D program, supported by the EIC Accelerator Collaboration. Will remain as an injection cooler performance risk mitigation strategy to be funded with project contingency, if triggered.